## Slide 1: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1 creator: Tom Alber
UC Multicampus Research Programs and Initiatives (MRPI)
UCSF Program for Breakthrough Biomedical Research (PBBR)
one-time NIH-DOE Inter-agency agreement (IAA)
Integrated Diffraction Analysis Technologies (IDAT)
Plexxikon, Inc.
M D Anderson CRC
Synchrotron Radiation Structural Biology Resource (SLAC)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser Aina Cohen Ana Gonzalez
Axel Brunger Monarin Uervirojnangkoorn Artem Lyubimov David Case Nick Sauter

## Slide 2: Major points for today
Radiation damage
Signal vs noise
Noise vs systematic error
Simulation of diffraction

## Slide 3: Structural Biologists Want:
Resolution
Phases

## Slide 4: Resolution
http://bl831.als.lbl.gov/~jamesh/movies/resolution.mpeg

## Slide 5: Phases
http://bl831.als.lbl.gov/~jamesh/movies/dephase.mpeg

## Slide 6: Structural Biologists Want:
Resolution
Phases
  problem: fractional errors

## Slide 7: 100% SeMet incorporation
Trivial to solve

## Slide 8: 100% S -Met incorporation
Impossible to solve

## Slide 9: Is it Real? Or is it MLFSOM
simulated
real

## Slide 10: Simulated diffraction image (2008)
simulated
real

## Slide 11
Simulated | statistic | Real
5.4% | Rmerge | 6.2%
18.9 | I/sd | 16.2
1.9 | I/sd (1.4 Ǻ) | 1.6
1.7 4.0 0.020 | SDCORR | 1.0 2.2 0.065
36.8 | PADFPH | 31.46
3.871 | mlphare f” | 3.476
0.178 | FOM | 0.192
0.545 | FOMDM | 0.664
0.6270 | CC(1H87) | 0.6090
0.070 | Rwork | 0.184
0.080 | Rfree | 0.231

## Slide 12: Global Challenge: Se phasing
fraction Sulfur
correlation coefficient

## Slide 13: Global Challenge: Se phasing
fraction Sulfur
correlation coefficient

## Slide 14: Global Challenge: Se phasing
fraction Sulfur
correlation coefficient

## Slide 15: Global Challenge: Se phasing
fraction Sulfur
correlation coefficient

## Slide 16: Global Challenge: Se phasing
fraction Sulfur
correlation coefficient

## Slide 17: How to install: MLFSOM
wget http://bl831.als.lbl.gov/~jamesh/
mlfsom/development_snapshot.tgz
tar xvzf development_snapshot.tgz
wget http://ftp.esrf.eu/pub/expg/FIT2D/
fit2d_10.132_i686_linuxV2.2.10
ln –sf fit2d_* fit2d
yum install gnuplot
gedit example.com mlfsom.params
./ano_sfall.com lysozyme.pdb
mv ideal_ano.mtz pristine.mtz
./mlfsom.com frames=100

## Slide 18: mosaic spread
Ewald sphere
diffracted ray
F(h,k,l)
d*
λ*
λ*
F(0,0,0)

## Slide 19: mosaic spread
Ewald sphere
diffracted ray
λ*
λ*
d*
d*
F(h,k,l)
F(0,0,0)

## Slide 20: mosaic spread = 0 º

## Slide 21: mosaic spread = 0.1º

## Slide 22: mosaic spread = 0.2º

## Slide 23: mosaic spread = 0.4º

## Slide 24: mosaic spread = 0.6º

## Slide 25: mosaic spread = 0.8º

## Slide 26: mosaic spread = 1.0º

## Slide 27: mosaic spread = 1.5º

## Slide 28: mosaic spread = 2.0º

## Slide 29: mosaic spread = 2.5º

## Slide 30: mosaic spread = 3.2º

## Slide 31: mosaic spread = 6.4º

## Slide 32: mosaic spread = 12.8º

## Slide 33: beam divergence
F(h,k,l)
F(0,0,0)
Ewald sphere
diffracted ray
d*
λ*
λ*

## Slide 34: beam divergence
Ewald sphere
λ*
λ*
F(0,0,0)
d*
diffracted ray

## Slide 35: divergence = 0 º

## Slide 36: divergence = 0.3 º

## Slide 37: spectral dispersion
Ewald sphere
diffracted ray
d*
λ*
λ*
F(h,k,l)
F(0,0,0)

## Slide 38: spectral dispersion
Ewald sphere
diffracted ray
λ’*
λ’*
F(h,k,l)
F(0,0,0)
d*

## Slide 39: dispersion = 0

## Slide 40: dispersion = 0.014% (Si 111)

## Slide 41: dispersion = 0.25% (CuKα)

## Slide 42: dispersion = 0.6%

## Slide 43: dispersion = 1.3%

## Slide 44: dispersion = 2.6%

## Slide 45: dispersion = 5.1%

## Slide 46: spot shape
Ewald sphere
diffracted ray
d*
λ’*
λ’*
Ewald sphere
diffracted ray
d*
λ*
λ*
diffracted ray
d*
Ewald sphere
λ*
λ*
Ewald sphere
diffracted rays
d*
d*

## Slide 47: Detector Point-spread function
http://bl831.als.lbl.gov/~jamesh/bin_stuff/noisify.html

## Slide 48: How to install: noisify
wget http://bl831.als.lbl.gov/
~jamesh/fastBragg/noisify.c
wget http://bl831.als.lbl.gov/
~jamesh/fastBragg/float_add.c
wget http://bl831.als.lbl.gov/
~jamesh/fastBragg/float_func.c
gcc –o noisify noisify.c –lm
gcc –o float_add float_add.c –lm
gcc –o float_func float_func.c –lm

## Slide 49
Source of error | realistic simulation | No SHSSS | Perfect detector
Photon counting | + | + | +
Shutter jitter | + | + | -
Beam flicker | + | + | -
Sample absorption | + | + | -
Radiation damage | + | + | -
Imperfect spindle | + | + | -
vignette | + | + | -
Corner correction | + | + | -
SHSSS | + | - | -
Rmeas (∞-10 Å) | 2.8% | 0.7% | 0.7%
I/σ asymptotic | 26.8 | 74.2 | 81.0
Threshold of a revolution in phasing
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 50
Required signal-to-noise (I/σ)
Solve-able proteins (%)
Current
technology
Goal
Threshold of a revolution in phasing

## Slide 51: Can you count to 1,000,000 ?
= 0.1%
sqrt(1,000,000)
1,000,000
= 3%
sqrt(1,000)
1,000
> 1000 is a waste!
photon
spot
Theoretically:
In reality:
ISa ~ 33
Rmeas ≈ 0.1% ?
ISa = 1000
Rmeas = ≈ 3%

## Slide 52
Gd edge-contrast map of ADSC Q315r detector
10% high
average
10% low

## Slide 53
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel
Pilatus: subtract smooth baseline

## Slide 54
3.5
3.0
2.5
2.0
1.5
1.0
0.5
SHSSS
Systematic component of Rsseparate (%)
distance between spots (mm)
0.1 1 10 100
CCD detector
anomalous mates are always on
different modules
different
modules
Pilatus
SN113
Pilatus
SN001
Notes: Comparision of SHSSS measured by the detector-shift experiment on three different detectors:
The Q315R in ALS 8.3.1
The first Pilatus detector at the Swiss Light Soruce
A newer Pilatus detector at Stanford
Improvements in calibration technology have finally made
Pilatus competitive with calibration on CCDs

## Slide 55
Photon Energy (eV)
Anomalous f” (electrons)
2472.7 2473.5
Bohic et al. Anal. Chem. 2008; 80(24):9557. doi: 10.1021/ac801817k

## Slide 56: S-MAD Sample size Dilemma

## Slide 57: Small, soft beams

## Slide 58: Small, soft beams
Diamond
($100, reusable)

## Slide 59: Small, soft beams
Diamond
($100, reusable)
oil ?

## Slide 60: Small, soft beams
Diamond
($100, reusable)
oil ?

## Slide 61: Small, soft beams
oil ?
λ=2d sinθ
2.5 Å data
with 5 Å X-rays
Only analytic absorption correction:
International Tables for Crystallography, Vol. C, 2nd ed., chapter 6.3

## Slide 62
Ewald sphere 2
diffracted ray
λ*
λ*
θ
1
Ewald sphere
λ*
(h,k,l)
diffracted ray
λ*
θ
d*
(-h,-k,-l)
d*

## Slide 63
h,k,l
-h,-k,-l
Detector
Detector
Detector
Detector
λ = 5 Å
sample
injector
Si(111)
52.87deg
Si(111)
Si(111)
Si(111)
Si(111)
Si(111)
2 Multilayer mirrors
d=2nm, W/B4C
KB Horiz focus
KB vertical focus
~ 1m
Notes: Proposed 5-crystal monochromator for colliding-beam crystallography. The generation of two opposing Ewald spheres means that for every h,k,l index reflected from the protein crystal, the Friedel mate is reflected in the opposite direction, allowing for very accurate anomalous difference measurements. The wavelength need not be set precisely at the sulfur or phosphorous edge, but merely at a wavelength where the f” of those elements are strong. For fs-class pulses, the distances above will have to be precise to withing ~3 microns, and for accurate reproduction of the partiality of the Friedel mates, the angular precision of the colliding beams must be within ~1% of the sample crystal’s rocking width, or ~100 microrads.

## Slide 64: Structural Biologists Want:
Resolution
  problem: background & disorder
Phases
  problem: fractional errors

## Slide 65: X-ray scattering “rules”:
1 μm crystal ≈ 1 μm water
≈ 1 μm plastic
≈ 0.1 μm glass
≈ 1000 μm air
~ 50 mm He
≈ 370 mm sat water vapor @ 4C
Optimum: support thickness = crystal thickness

## Slide 66: Background scattering

## Slide 67: Background scattering
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
real estate is
expensive
use it!

## Slide 68: Mosquito tips cost $0.15 each
So do Pilatus pixels!
We bought 6,224,001
Use them!
(they are reusable)

## Slide 69: Structural Biologists Want:
Resolution
  problem: background & disorder
Phases
  problem: fractional errors
Problem for both: radiation damage

## Slide 70
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.
No flux
No symmetry

## Slide 71
Crystal diameter (micron)
Resolution (Å)
B = 0
B = 20
B = 60
B = 170
B = 330
B = 560
B = 850
Bigger is better, but not by much

## Slide 72: B factor from image analysis
B = 500

## Slide 73: B factor from image analysis
B = 20

## Slide 74
The number of photons scattered
before crystal is dead
is independent
of data collection time
1 um3 = 105 photons (roomT)
1 um3 = 106 photons (synch)
1 um3 = 108 photons (XFEL)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009
(synch)

## Slide 75
Synchrotron Resolution (Å)
XFEL Resolution (Å)
Predicting resolution limits

## Slide 76: Dose slicing
crystal’s useful life
N
photons
N
photons
N
photons
Low
completeness
unacceptable
readout noise?

## Slide 77: Completeness: random deletion
http://bl831.als.lbl.gov/~jamesh/movies/completeness.mpeg

## Slide 78: Completeness: missing wedge
http://bl831.als.lbl.gov/~jamesh/movies/osc.mpeg

## Slide 79: Overloads
http://bl831.als.lbl.gov/~jamesh/movies/overloads.mpeg

## Slide 80: Resolution: low-angle cutoff
http://bl831.als.lbl.gov/~jamesh/movies/lo_cut.mpeg

## Slide 81: Can radiation damage be “outrun”?

## Slide 82: Dose-rate effect at Room Temp?
Warkentin M, Badeau R, Hopkins JB, Mulichak AM, Keefe LJ & Thorne RE (2012)."Global radiation damage at 300 and 260 K with dose rates approaching 1 MGy s-1", Acta Cryst. D 68, 124-133.
Owen RL, Axford D, Nettleship JE, Owens RJ, Robinson JI, Morgan AW, Dore AS, Lebon G, Tate CG, Fry EE, Ren J, Stuart DI & Evans G (2012)."Outrunning free radicals in room-temperature macromolecular crystallography", Acta Cryst. D 68, 810-818.

## Slide 83: Pilatus pile-up for RT MX? same photons, different speeds
Sum of 193 shots with
193-fold attenuation
SLOW

## Slide 84: Pilatus pile-up for RT MX? same photons, different speeds
1 shot with
no attenuation
FAST

## Slide 85: Pilatus pile-up for RT MX? same photons, different speeds

## Slide 86: Do we expect this with protein?
Mosaic spread (η) < 0.02°
20°/s rotation
50x50x50 μm lysozyme crystal
Istill = 0.07*(F/mosaic)2
F=130 → 3e6 photons/s/spot
Max Eiger count rate = 3e6 photons/s/spot
35% of Fs > 130 (lysozyme @ 2.0 Å)
45% under-counting expected

## Slide 87: What is a “streak camera”?

## Slide 88: What is a “streak camera”?
0.1 mm/pixel
= 4 ms/pixel
25 mm/s

## Slide 91: Individual spots at 768 kGy/s
Intensity (photons)
Dose (kGy)
0
Same xtal, different spots

## Slide 92: Double-tap: no dark progression at 675 kGy/s
Intensity (photons)
Dose (kGy)

## Slide 93: Xtal5_t1 graph

## Slide 94: How much H2 are we making?
Meents et al. (2010) claimed:
"400 molecules of H2 for every 12.5 keV photon“
= 3.3x10-7 mol/J
200 kGy to 100 um3 = 0.24 J
= 1.2x10-8 mol H2
100 um3 of water = 6.7x10-8 mol
→ 18% of water has reacted!

## Slide 95: Dose-rate dependence of damage
dose rate (kGy/s)
maximum useful dose (MGy)

## Slide 96: Elastic scattering

## Slide 97: Elastic scattering

## Slide 98: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
Protein
1A x-rays

## Slide 99: Elastic scattering

## Slide 100: Inelastic scattering

## Slide 101: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
Protein
1A x-rays

## Slide 102: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays

## Slide 103: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 104: Photoelectric absorption

## Slide 105: Photoelectric absorption
e-
+

## Slide 106: Fluorescence
+

## Slide 107: Fluorescence
e-
+

## Slide 108: Metal identification

## Slide 109: Auger emission
+

## Slide 110: Auger emission
++
e-

## Slide 111: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 112: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 113: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (~0%)
Absorbed (99%)
Re-emitted (99%)
Absorbed (~0%)

## Slide 114: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
useful/absorbed energy: 7.3%
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (~0%)
Absorbed (99%)
Re-emitted (99%)
Absorbed (~0%)

## Slide 115: Photoelectric absorption

## Slide 116: Photoelectric absorption
e-
+

## Slide 117: Secondary ionization
e-

## Slide 118: Secondary ionization
e-
e-
+

## Slide 119: Excitation
e-

## Slide 120: Excitation
e-

## Slide 121: Excitation
e-

## Slide 122: Excitation

## Slide 123: Electron attachment
e-

## Slide 124: Electron attachment
-

## Slide 125: Sample atoms

## Slide 126: Sample atoms

## Slide 127: Primary ionization
e-
+

## Slide 128: Secondary ionizations
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+

## Slide 129: Ionization track
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 130: Ionization track
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 131: Ionization track

## Slide 132: Ionization track

## Slide 133: Ionization track
3 μm

## Slide 134: Ionization track
Linear Energy Transfer

## Slide 135: Ionization track
initial effects

## Slide 136: Ionization track
Homogeneous reactions
initial effects

## Slide 137: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 138: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
neutralization
e-
+

## Slide 139: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
neutralization
e-
+

## Slide 140: initial effects
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
neutralization
neutralization
+

## Slide 141: initial effects
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
attachment
+

## Slide 142: initial effects
e-
e-
e-
e-
-
e-
e-
+
+
+
+
+
+
attachment
+

## Slide 143: initial effects
e-
e-
e-
e-
-
e-
e-
+
+
+
+
+
+
attachment
attachment
+

## Slide 144: initial effects
e-
e-
-
e-
e-
+
+
+
+
+
+
-
-
+

## Slide 145: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 146: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+
solvation

## Slide 147: initial effects
-
e-
+
+
+
+
+
-
-
-
-
solvation
+

## Slide 148: Solvated electron
e-

## Slide 149: Solvated electron
e-

## Slide 152: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 153: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 154: initial effects
-
e-
+
+
+
+
-
-
-
+

## Slide 155: initial effects
-
e-
+
+
-
+

## Slide 156: initial effects
-
e-
+
+

## Slide 157: Excitation transfer

## Slide 158: Excitation transfer
UV photon

## Slide 159: Excitation transfer

## Slide 160: Excitation transfer
Förster transfer
r-6

## Slide 161: Excitation transfer

## Slide 162: t = 0 s

## Slide 163: t ≈ 10-15 s
-
e-
+
+

## Slide 164: Timescales of radiation damage
Garret et. al. (2005) Chem. Rev. 105, 355-389

## Slide 165: Timescales of radiation damage
Garret et. al. (2005) Chem. Rev. 105, 355-389
LCLS
ALS
bunch

## Slide 166: Ionization track
Heterogeneous reactions
Homogeneous reactions

## Slide 167: Rough values of energy quanta
1 MeV 100 GJ/mol Medical radiation therapy
100 keV 10 GJ/mol Medical imaging
10 keV 1 GJ/mol X-ray crystallography
1 keV 100 MJ/mol S and P K-edges
100 eV 10 MJ/mol “water window”
10 eV 1 MJ/mol C≡C bond
1 eV 100 kJ/mol C-C bond, visible light
100 meV 10 kJ/mol hydrogen bond
10 meV 1 kJ/mol heat (~300 K)

## Slide 168: Energy Transfer Analogy
37 C

## Slide 169
Damage at 100K is done
by dose (MGy)
proportional to photons/area
not time
not heat
Sliz P, Harrison SC & Rosenbaum G (2003). Structure 11, 13-19.
Garman EF & McSweeney SM (2006). J. Sync. Rad. 14, 1-3.
Owen RL, Rudino-Pinera E & Garman EF (2006). PNAS 103, 4912-4917.
Leiros et al. (2006). Acta Cryst. D 62, 125-132.
Holton JM (2007). J. Synch Rad. 14, 51-72.

## Slide 170: what the is a MGy?
http://bl831.als.lbl.gov/
damage_rates.pdf
Holton J. M. (2009) J. Synchrotron Rad. 16 133-42
energy
mass

## Slide 171
How long will my crystal last?
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
ALS 4.2.2 MAD 2.2e11 75x80 3.7e+07 27.3 kGy/s 18 m 73 s
ALS 5.0.1 mono 1.6e11 100 2.0e+07 10.4 kGy/s 48 m 3.2 m
ALS 5.0.2 MAD 8e11 100 1.0e+08 51.8 kGy/s 9.6 m 39 s
ALS 5.0.3 mono 1.7e11 100 2.2e+07 11 kGy/s 45 m 3 m
ALS 8.2.1 MAD 1.8e11 100 2.3e+07 11.7 kGy/s 43 m 2.9 m
ALS 8.2.2 MAD 2.3e11 100 2.9e+07 14.9 kGy/s 34 m 2.2 m
ALS 8.3.1 MAD 9e11 70 2.3e+08 119 kGy/s 4.2 m 17 s
ALS 8.3.1 typical 6e11 70 1.6e+08 115 kGy/s 4.3 m 17 s
ALS 12.3.1 MAD 1.8e11 100 2.3e+07 11.7 kGy/s 43 m 2.9 m
ALS 12.3.1 ML 4.0e12 100 5.1e+08 513 kGy/s 58 s 3.9 s
APS 8-BM MAD 1e11 200 2.5e+06 1.27 kGy/s 6.6 h 26 m
APS 14-BM-C mono 5.8e10 200 1.4e+06 738 Gy/s 11 h 45 m
APS 14-BM-D MAD 3.3e9 200 8.2e+04 42 Gy/s 8.3 d 13 h
APS 14-ID-B MAD 6.0e10 200 1.5e+06 763 Gy/s 11 h 44 m
APS 17-BM MAD 1.1e11 200 2.8e+06 1.4 kGy/s 6 h 24 m
APS 17-ID MAD 2.3e11 200 5.8e+06 2.93 kGy/s 2.8 h 11 m
APS 19-BM MAD 2.0e11 70x60 4.8e+07 24.2 kGy/s 21 m 83 s
APS 19-ID MAD 1.3e13 80x40 4.1e+09 2.07 MGy/s 15 s 0.97 s
APS 19-ID typical 5.5e11 100x100 5.5e+07 28 kGy/s 18 m 71 s
APS 22-BM MAD 7e12 80x40 2.2e+09 1.23 MGy/s 24 s 1.6 s
APS 22-ID MAD 7e12 80x40 2.2e+09 1.23 MGy/s 24 s 1.6 s
APS 22-ID typical 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
APS 23-ID-B MAD 1e13 75x25 5.3e+09 3.01 MGy/s 10 s 0.66 s
APS 23-ID typical 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
APS 24-ID-C MAD 1.3e13 20x60 1.1e+10 5.23 MGy/s 5.7 s 0.38 s
APS 24-ID-E MAD 0.5e13 20x100 2.5e+09 1.19 MGy/s 25 s 1.7 s
APS 31-ID MAD 2e12 70 4.1e+08 194 kGy/s 2.6 m 10 s

## Slide 173
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 174: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12

## Slide 175: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12
10 MGy/Å

## Slide 176: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.

## Slide 177: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.
Riso ≈ 0.7 %/MGy

## Slide 178: Dose-doubling concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 179: Dose-doubling concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 180
Holton (2009) J. Synchrotron Rad. 16 133-42
Specific Damage
World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 181: Structural Biologists Want:
Resolution
  problem: background
Phases
  problem: fractional errors
Publications
  problem: R factors

## Slide 182: R-factor
http://bl831.als.lbl.gov/~jamesh/movies/rfactor.mpeg

## Slide 183: Is this good enough?
dmax = 4.5 Å
Rcryst = 27%
Rfree = 38%

## Slide 184: Is this good enough?
3a8n 4.5 Å Rmerge = 0.15 R/Rfree = 0.306/0.396
1grz 5 Å Rmerge = 0.052 R/Rfree = 0.369/0.428
1qzv 4.44 Å Rmerge = 0.099 R/Rfree = 0.41/0.42

## Slide 185: The R-factor Gap
Holton et al. (2014). FEBS J. 281, 4046-60.
R1 < 2*Rsigma
Publication criterion for chemical crystallography:
R1 = Fo vs Fc for I/σ(I) > 3
Rsigma = <σ(I)>/<I>
There are no PDB entries that pass this test!

## Slide 186: The R-factor Gap
Rmerge = 3%
Rwork = 20%
Rfree = 24%
Experimental
error
“systematic”
error
20% of carbon atom = 1.2 e-
5% of carbon atom = 0.3 e-
Closing the R-factor gap will enable study of 1-electron changes

## Slide 187: The R-factor Gap
MLFSOM
Elves
Rmerge = 6%
Rcryst = 17%
Rfree = 20%
multi-conformer PDB file
1H87
Holton, Classen, Frankel & Tainer (2014)."The R-factor gap in macromolecular crystallography: an untapped potential for insights on accurate structures", FEBS J. 281, 4046-4060.

## Slide 188: The R-factor Gap
MLFSOM
Elves
Rmerge = 6%
Rcryst = 7%
Rfree = 8%
multi-conformer PDB file
1H87
Holton, Classen, Frankel & Tainer (2014)."The R-factor gap in macromolecular crystallography: an untapped potential for insights on accurate structures", FEBS J. 281, 4046-4060.

## Slide 189: The R-factor Gap
single-conformer PDB file
1H87; conf “A”
Holton, Classen, Frankel & Tainer (2014)."The R-factor gap in macromolecular crystallography: an untapped potential for insights on accurate structures", FEBS J. 281, 4046-4060.
MLFSOM
Elves
Rmerge = 6%
Rcryst = 7%
Rfree = 8%
ARP/wARP

## Slide 190: The R-factor Gap
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.

## Slide 191: 2Fsim-Fcalc and Fsim-Fcalc maps
1.0 Å data
Rcryst= 0.137
Rfree = 0.159
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc

## Slide 192: 2Fsim-Fcalc and (Fsim Φsim) - (Fcalc Φcalc) maps
1 “sigma” 2Fsim-Fc
Fright – (2Fsim-Fc)
1.0 Å data
Rcryst= 0.137
Rfree = 0.159

## Slide 193: 30 conformers from 24,000

## Slide 194: How many conformers are there?
Rcryst = 0.0441
Rfree = 0.0516
vs Fsim
Answer: 2-14

## Slide 195: How many conformers are there?
Rcryst = 0.1546
Rfree = 0.1749
vs Fobs
1aho:
Rcryst = 0.1630
Rfree = n/d
Answer: 1-7

## Slide 196: How many conformers are there?
All difference
features
are in
the solvent!
real data

## Slide 197: The R-factor Gap
MX data quality is not limiting
Hypotheses:
  Hidden systematic error?
  Model-building problem?
  Representation problem?

## Slide 198: RISM model for “bulk” solvent
Method | Rwork | Rfree
Default refmac5: flat bulk solvent | .1784 | .1898
RISM – self-consistent density field based on electrostatics | .1640 | .1808
Explicit MD solvent, protein fixed | .1523 | .1690
RISM – protein fixed multi-conformer weighted | .1578 | .1739
Explicit – protein fixed multi-conformer weighted | .1440 | .1666

## Slide 199: Systematic error does not “average out”

## Slide 200: non-isomorphism

## Slide 201
0.5% cell change → 15%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.
Same structure, different cell

## Slide 202
Same structure, different cell
0.5% cell change → 15%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 203
Same cell, rotated protein
0.5° rotation → 16%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 204
Same cell, rotated protein
0.5° rotation → 16%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 205
Uniform stretch
5% change → 0%

## Slide 206
5% change → 0%
Uniform stretch

## Slide 207
Dear James
The story of the two forms of lysozyme crystals goes back to about 1964 when it was found that the diffraction patterns from different crystals could be placed in one of two classes depending on their intensities. This discovery was a big set back at the time and I can remember a lecture title being changed from the 'The structure of lysozyme' to 'The structure of lysozyme two steps forward and one step back'. Thereafter the crystals were screened based on intensities of the (11,11,l) rows to distinguish them (e.g. 11,11,4 > 11,11,5 in one form and vice versa in another). Data were collected only for those that fulfilled the Type II criteria. (These reflections were easy to measure on the linear diffractometer because crystals were mounted to rotate about the diagonal axis). As I recall both Type I and Type II could be found in the same crystallisation batch . Although sometimes the external morphology allowed recognition this was not infallible.
The structure was based on Type II crystals. Later a graduate student Helen Handoll examined Type I. The work, which was in the early days and before refinement programmes, seemed to suggest that the differences lay in the arrangement of water or chloride molecules (Lysozyme was crystallised from NaCl). But the work was never written up. Keith Wilson at one stage was following this up as lysozyme was being used to test data collection strategies but I do not know the outcome.
An account of this is given in International Table Volume F (Rossmann and Arnold edited 2001) p760.
Tony North was much involved in sorting this out and if you wanted more info he would be the person to contact. I hope this is helpful. Do let me know if you need more.
Best wishes
Louise
Non-isomorphism in lysozyme

## Slide 208: Non-isomorphism in lysozyme
RH: 84.2%
vs 71.9%
Riso = 44.5%
3aw6
3aw7
Δcell = 0.7 %
RMSD = 0.18 Å

## Slide 209
h,k,l | structure factors (F) |  |  | 
 | #1 | #2 | #3 | #4
5,3,4 | 523.7 | 559.8 | 579.9 | 603.2
5,4,4 | 168.2 | 166.6 | 177.2 | 196.1
5,5,4 | 34.9 | 26.4 | 19.2 | 17.3
6,1,4 | 305.7 | 301.1 | 298.1 | 296.3
6,2,4 | 353.0 | 353.9 | 356.2 | 366.9
6,3,4 | 300.9 | 285.3 | 273.5 | 259.4
6,3,5 | 223.8 | 226.3 | 234.6 | 251.4
… | … | … | … | …
X-ray Data Sets
h,k,l | 100% | 17 % | 13 % | 9 %
 | 1st | 2nd | 3rd | 4th
5,3,4 | -1.46 | -0.02 | 1.84 | -0.72
5,4,4 | -0.88 | -0.29 | -0.34 | 0.15
5,5,4 | -0.42 | -0.65 | 1.02 | 1.47
6,1,4 | -0.90 | -0.85 | 1.44 | -0.40
6,2,4 | -1.20 | -0.37 | 0.67 | 0.01
6,3,4 | -0.75 | 0.31 | 0.48 | 0.00
6,3,5 | -0.75 | -0.85 | 0.72 | -0.82
… | … | … | … | …
data
set
Singular value decomp.
SVD
vector
value
Singular values & vectors
Correlation
Coefficients
-0.68
CC2
CC3
CC1
CC1 CC2 CC3
data set #1
Data sets
Positioned
in
“Correlation
Space”
-0.24
data set #2
data set #3
0.32 …

## Slide 211
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 212
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 213
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 214: Bragg’s “minimum wavelength principle”
Perutz (1985). “Early Days of Cryst…” Methods in Enzymology, Vol. 114, 3-18.
Bragg & Perutz (1952)."external form haemoglobin I", Acta Cryst. 5, 277-283.

## Slide 215: DMMULTI – fake data 4 deg rotation: 8 “xtals”: before
CC = 0.02

## Slide 216
CC = 0.8
DMMULTI – fake data 4 deg rotation: 8 “xtals”: after

## Slide 217: Systematic error can “average out” if you can change up the source

## Slide 218: Partiality > 25% error per spot!
Kabsch W (2014)."Processing of X-ray snapshots from crystals in random orientations", Acta Cryst D 70, 2204-2216.

## Slide 219: What is “partiality”?
Ewald sphere

## Slide 220: What is “partiality”?
Ewald sphere

## Slide 221: The “partiality problem”
0.006°
1 μm xtal
1 Å x-rays

## Slide 222: Multiplicity required to phase
Monte Carlo
  100% /obs → 10,000 fold
nXDS
  25% /obs → 625 fold
Synchrotron
  3% /obs → 9 fold
  Assuming ΔF/F ~ 1%
Beam time:
$2/s

## Slide 223: Can’t we just rotate the crystal?
1 μm
1°
100 fs
= 90 km/s
9 nm
17.26 km/s
(90 km/s)2
0.5 μm
= 1.5 x 1015 G
= 0.5 nN

## Slide 224: Can’t we just rotate the crystal?
NO
Why do we want to rotate the crystal?

## Slide 225: The “nanocrystal advantage”
Ispot = k Ncells
Ewald sphere
range
2
caveat: 100% error!

## Slide 226: nearBragg program
http://bl831.als.lbl.gov/~jamesh/nearBragg/
“assumption-free” total scattering
no Fourier Transform
no unit cells
no “mosaicity”
arbitrary “atoms”
arbitrary “source”
coherent or not

## Slide 227: How to install: nearBragg
wget http://bl831.als.lbl.gov/
~jamesh/nearBragg/nearBragg.c
gcc –o nearBragg nearBragg.c –lm
./nearBragg

## Slide 228: What has been learned from nearBragg?
Fundamentals of scattering
What is “molecular transform”?
What is “Coherence length”?
Diffuse scatter vs unit cell
Inter-Bragg is not what you think
Phases from non-isomorphism

## Slide 229: What has been learned from nearBragg?
Fundamentals of scattering
What is “molecular transform”?
What is “Coherence length”?
Diffuse scatter vs unit cell
Inter-Bragg is not what you think
Phases from non-isomorphism

## Slide 232
scattering from a structure
sample
detector

## Slide 233
forward Fourier Transform
inverse Fourier Transform
no phase

## Slide 234
scattering from a structure
colored by phase
sample
detector
inverse Fourier Transform

## Slide 235
scattering from a lattice
colored by phase
sample
detector

## Slide 236
scattering from a lattice
colored by phase
sample
detector

## Slide 237
scattering from a lattice
colored by phase
sample
detector

## Slide 238
scattering from a crystal structure
colored by phase
sample
detector

## Slide 239: What has been learned from nearBragg?
Fundamentals of scattering
What is “molecular transform”?
What is “Coherence length”?
Diffuse scatter vs unit cell
Inter-Bragg is not what you think
Phases from non-isomorphism

## Slide 240
Definition of unit cell defines MT
False color intensity
sample
detector

## Slide 241
Definition of unit cell defines MT
False color intensity
sample
detector

## Slide 242
Definition of unit cell defines MT
False color intensity
sample
detector

## Slide 243
Definition of unit cell defines DS
False color intensity
sample
detector

## Slide 244: What has been learned from nearBragg?
Fundamentals of scattering
What is “molecular transform”?
What is “Coherence length”?
Diffuse scatter vs unit cell
Inter-Bragg is not what you think
Phases from non-isomorphism

## Slide 245: Meaning of “coherence length”

## Slide 246: What has been learned from nearBragg?
Fundamentals of scattering
What is “molecular transform”?
What is “Coherence length”?
Diffuse scatter vs unit cell
Inter-Bragg is not what you think
Phases from non-isomorphism

## Slide 247
Total scattering from a structure
Move one atom
sample
detector

## Slide 248
Total scattering from a structure
Intensity sum: F12+F22
sample
detector

## Slide 249
Total scattering from a structure
Coherent sum: (F1+F2)2
sample
detector

## Slide 250
Total scattering from a structure
Incoherent – coherent difference: ( F12+F22) - (F1+F2)2
sample
detector

## Slide 251
Total scattering from one atom
Intensity sum: F12+F22
sample
detector

## Slide 252
Total scattering from two ½ atoms
sample
detector
Coherent sum: (F1+F2)2

## Slide 253
Total scattering from one atom
sample
detector
Incoherent – coherent difference: ( F12+F22) - (F1+F2)2

## Slide 254
Total scattering from a structure
Incoherent – coherent difference: ( F12+F22) - (F1+F2)2
sample
detector

## Slide 255
Total scattering from a lattice
sample
detector
Intensity sum: F12+F22

## Slide 256
Total scattering from a crystal
sample
detector
Intensity sum: F12+F22

## Slide 257
Total scattering from a crystal
sample
detector
Coherent sum: (F1+F2)2

## Slide 258
Total scattering from a crystal
sample
detector
Incoherent – coherent difference: ( F12+F22) - (F1+F2)2

## Slide 259
Total scattering from a crystal
sample
detector
Intensity: random fluctuations

## Slide 260
Total scattering from a crystal
sample
detector
Intensity sum: F12+F22+F32+F42+ …

## Slide 261
Total scattering from a crystal
sample
detector
Random fluctuations - Coherent average

## Slide 262
Total scattering from a crystal
sample
detector
Incoherent-coherent difference:
(F12+F22+F32+F42+ …) - (F1+F2+F3+F4+ …)2

## Slide 263
Total scattering from one atom
sample
detector
Incoherent – coherent difference: ( F12+F22) - (F1+F2)2

## Slide 264
Total scattering from a crystal
sample
detector
“Dilatation” movements

## Slide 265
Total scattering from a crystal
sample
detector
Incoherent-coherent difference:
(F12+F22+F32+F42+ …) - (F1+F2+F3+F4+ …)2

## Slide 266: Super-cell formalism for diffuse scatter
sinθ/λ
intensity (F2)
Notes: one cell

## Slide 267: Super-cell formalism for diffuse scatter
sinθ/λ
intensity (F2)
Notes: 9 cells – same cell contents so diffraction pattern is the same

## Slide 268: Super-cell formalism for diffuse scatter
sinθ/λ
intensity (F2)
Notes: Supercell – don’t change the atoms, just remove the cell borders – diffraction pattern is, of course, the same

## Slide 269: Super-cell formalism for diffuse scatter
sinθ/λ
intensity (F2)
Notes: supercell with disorder – by jiggling the atoms around a bit they become non-equivalent and off-Bragg scattering is apparent.

## Slide 270: Super-cell formalism for diffuse scatter
sinθ/λ
intensity (F2)
Notes: average electron density – translate all these “disordered” atoms back into the original cell, however, and the inter-Bragg stuff goes away. This is because the FFT can only report on the average electron density in a single unit cell

## Slide 271: Super-cell formalism for diffuse scatter
intensity (F2)
one-cell hkl index
Notes: By repeating the “jiggle the atoms in a supercell” trick many times and averaging, the relative intensity of the diffuse scatter becomes apparent.

## Slide 272: Super-cell formalism for diffuse scatter
intensity (F2)
one-cell hkl index
Notes: Here we show the average supercell scattering over many atomic “jiggles”, superimposed on the average electron density. The intensity at the integral structure factors is the same in both cases.

## Slide 273: Super-cell formalism for diffuse scatter
intensity (F2)
one-cell hkl index
Notes: average cell intensity is relative to “zero”. Here we zoom in on the diffuse scattering. The 1-exp(-x^2) shape of the scattering left over
After subtracting a B factor is apparent.

## Slide 274: Super-cell formalism for diffuse scatter
intensity (F2)
one-cell hkl index
Notes: supercell density gives clue to diffuse scatter, but Bragg peaks are still relative to zero

## Slide 275: Super-cell formalism for diffuse scatter
one-cell hkl index
intensity (F2)
Notes: supercell density gives clue to diffuse scatter, but Bragg peaks are still relative to zero

## Slide 276: Super-cell formalism for diffuse scatter
one-cell hkl index
intensity (F2)
“Caspar hole” ???
Notes: high-angle Brragg peaks have zero intensity and so create “holes” is the background?! This is an artefact of the Supercell formalism.

## Slide 277: average total scattering from points
deviation from Bragg angle
intensity (relative to one atom)
Notes: when nearBragg is used instead of supercell, the Bragg peaks “ride” on the background and do NOT produce “holes”. This is consistent with the background-subtracted spot intensities being related directly to the structure factor of the average electron density, which is as expected.
Unfortunately, nearBragg is very slow, but extrapolating this “riding spot” behavior from a supercell formalism is tricky.

## Slide 278: Diffuse Scatter Challenge
http://bl831.als.lbl.gov/example_data_sets/Illuin/lyso_DS

## Slide 279: What has been learned from nearBragg?
Fundamentals of scattering
What is “molecular transform”?
What is “Coherence length”?
Diffuse scatter vs unit cell
Inter-Bragg is not what you think
Phases from non-isomorphism

## Slide 280: Inter-Bragg spots over-sample unit cell

## Slide 281: square

## Slide 282: round

## Slide 283: fastBragg program
http://bl831.als.lbl.gov/~jamesh/fastBragg/
Optimized for nanocrystals
Square or round
Takes h,k,l and F
Supports 1 unit cell
no “mosaicity”
arbitrary “source”
arbitrary “phi” steps

## Slide 284: fastBragg program
http://bl831.als.lbl.gov/~jamesh/fastBragg/

## Slide 285: fastBragg program
http://bl831.als.lbl.gov/~jamesh/fastBragg/

## Slide 286: fastBragg program
http://bl831.als.lbl.gov/~jamesh/fastBragg/

## Slide 287: fastBragg program
http://bl831.als.lbl.gov/~jamesh/fastBragg/

## Slide 288: fastBragg program
http://bl831.als.lbl.gov/~jamesh/fastBragg/
8x larger

## Slide 289: fastBragg program
http://bl831.als.lbl.gov/~jamesh/fastBragg/
64x larger

## Slide 290: nonBragg for background

## Slide 291: How to run: nonBragg for SAXS
pdbset xyzin lysozyme.pdb xyzout bigcell.pdb << EOF
CELL 250 250 250 90 90 90
SPACEGROUP 1
EOF
phenix.fmodel bigcell.pdb high_resolution=10 k_sol=0.35 b_sol=46.5 mask.solvent_radius=0.5 mask.shrink_truncation_radius=0.16
mtz_to_stol.com bigcell.pdb.mtz
nonBragg -stol mtz.stol -lambda 1 -dispersion 0 \
-distance 1000 -detsize 100 -pixel 0.172 \
-flux 1e13 -thick 1.2 -MW 14000 -density 0.01
adxv noiseimage.img

## Slide 292: How to install: nonBragg
wget http://bl831.als.lbl.gov/
~jamesh/nonBragg/nonBragg.c
gcc –o nonBragg nonBragg.c –lm
./nonBragg

## Slide 293: “fit” simulation to reality
Dispersion
Divergence
Mosaicity
Wavelength
Unit cell parameters (3)
Crystal orientation (3)
Mosaic domain size (3)
Beam center (2)
Beam direction (2)
Detector distance

## Slide 294
Real XFEL still

## Slide 295: Simulation of XFEL stills

## Slide 296
phiz
Simulation of XFEL stills
phiy
phiz
phix
phix
phiy
VS
real

## Slide 297
Angle about y axis (°)
Fraction pixels predicted
Fitting individual “mosaic domains”
Best of
262,140 trials

## Slide 298: The “Lorentz zone”

## Slide 299: The “partiality problem”
0.006°
1 μm xtal
1 Å x-rays
Lovelace et al. (2006)."topography", J. Appl. Cryst. 39, 425-432.

## Slide 300
Simulation of XFEL stills
Beam center from autoindexing
Sauter (2015). JSR 22, 239.

## Slide 301
Simulation of XFEL stills
Beam center from autoindexing
Sauter (2015). JSR 22, 239.
Color is
time

## Slide 302: Sanity check on beam position?
~1000 m
0.3 m
100 μm
~1 m
pinhole

## Slide 303: How to install: fastBragg
wget http://bl831.als.lbl.gov/
~jamesh/fastBragg/fastBragg.c
gcc –o fastBragg fastBragg.c –lm
./fastBragg

## Slide 304: How to run: fastBragg for single particle
pdbset xyzin lysozyme.pdb xyzout bigcell.pdb << EOF
CELL 250 250 250 90 90 90
SPACEGROUP 1
EOF
phenix.fmodel bigcell.pdb high_resolution=10 k_sol=0.35 b_sol=46.5 mask.solvent_radius=0.5 mask.shrink_truncation_radius=0.16
mtz_to_P1hkl.com bigcell.pdb.mtz
fastBragg –cell 250 250 250 90 90 90 –misset 10 20 30 -hkl P1.hkl -lambda 1 -distance 1000 -detsize 100 -fluence 1e32 -N 1
adxv noiseimage.img

## Slide 305: How to run: fastBragg for single particle
UBtoA.awk << EOF > A.mat
CELL 250 250 250 90 90 90
RANDOM
EOF
fastBragg -hkl P1.hkl -lambda 1 -distance 1000 -detsize 100 -fluence 1e32 -N 1 –mat A.mat
adxv noiseimage.img
UBtoA.awk << EOF > A.mat
CELL 250 250 250 90 90 90
MISSET 10 20 30
RANDOM 1 12345
EOF

## Slide 306: How to run: nearBragg for single particle
egrep “^ATOM|^HETAT” lysozyme.pdb |\
awk ‘{print substr($0,31,36)}’ |\
cat >! atoms.txt
./rotate.awk -v phix=10 -v phiy=20 -v phiz=30 atoms.txt >! rotated.txt
nearBragg –atoms rotated.txt -lambda 1 -distance 1000 -detsize 100 -fluence 1e32
(200s)
adxv intimage.img

## Slide 307: How to run: nearBragg for single particle
egrep “^ATOM|^HETAT” lysozyme.pdb |\
awk ‘{print substr($0,31,36)}’ |\
cat >! atoms.txt
./rotate.awk -v phix=10 -v phiy=20 -v phiz=30 atoms.txt >! rotated.txt
nearBragg –atoms rotated.txt -lambda 1 -distance 1000 -detsize 100 -fluence 1e32
(200s)
noisify –header intimage.bin –floatfile floatimage.bin
adxv noiseimage.img

## Slide 308: Realistic single-particle prediction
1012 photon/pulse
100 nm focus

## Slide 309: Realistic single-particle prediction
1012 photon/pulse
3 nm focus

## Slide 310: lysozyme: real and reciprocal

## Slide 311: lysozyme: thermal motion

## Slide 312: Muybridge’s galloping horse (1878)
Real space
reciprocal
“Time-resolved” diffraction

## Slide 313: Muybridge’s galloping horse (1878)
Real space
reciprocal
Average electron density

## Slide 314: Muybridge’s galloping horse (1878)
Real space
reciprocal
Average electron density: 1 sigma contour

## Slide 315: Sparse validation supporting a 4D model with 2D data

## Slide 316: URLs & Summary
Phasing is limited by detectors
R-factors limited by model complexity
Resolution limited by disorder
Use simulation to predict your experiment!
How do we make our molecules sit still?
http://bl831.als.lbl.gov/~jamesh/powerpoint/
SLAC_uxss_2016.pptx
http://bl831.als.lbl.gov/~jamesh/bin_stuff/
http://bl831.als.lbl.gov/~jamesh/mlfsom/