## Slide 1: PowerPoint File available:
http://bl831.als.lbl.gov/
~jamesh/powerpoint/
AS_SvN_2014.pptx

## Slide 2: Acknowledgements
Tom Peat Janet Newman Christine Gee
Jason Price Kay Diederichs Tom Caradoc-Davies
Pavel Janowski David Cerutti David Case
Center for Structure of Membrane Proteins
Membrane Protein Expression Center II
Center for HIV Accessory and Regulatory Complexes
W. M. Keck Foundation
Plexxikon, Inc.
M D Anderson CRC
University of California Berkeley
University of California San Francisco
National Science Foundation
University of California Campus-Laboratory Collaboration Grant
Henry Wheeler
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.

## Slide 3: signal vs noise
“If you don’t have good data, then you have no data at all.”
-Sung-Hou Kim

## Slide 4: signal vs noise
easy
hard
impossible

## Slide 5: signal vs noise
easy
hard
impossible
threshold of “solvability”

## Slide 6: The “success rate” of structure determination
100 s/dataset
200 days/year
~150 beamlines
~26,000,000 datasets/year
9597 PDBs in 2013

## Slide 7: Grand Challenges in Structural Biology
Phase Problem
spots, but no maps
Amplitude Problem
    Crystals, but no spots
R-factor Gap
    Can’t/shouldn’t publish

## Slide 8: “Success rate” of structures
~2500 datasets/year
~100 PDBs/year

## Slide 9: 100% SeMet incorporation
Trivial to solve

## Slide 10: 100% S -Met incorporation
Impossible to solve

## Slide 11: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 12: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 13: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 14: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 15: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 16: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 17: Molecular Replacement
Rmsd from perfect search model (Å)
corrupted model
Correlation coefficient to correct density

## Slide 18: The transition is sharp!
How can we predict success/failure?
Phase Problem

## Slide 19
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 20: signal vs noise
“If you don’t have good data, then you must learn statistics.”
-James Holton

## Slide 21: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 22: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 23: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
102 + 12 = 10.052

## Slide 24
anomalous signal
Crick, F. H. C. & Magdoff, B. S. (1956) Acta Crystallogr. 9, 901-908.
Hendrickson, W. A. & Teeter, M. M. (1981) Nature 290, 107-113.
# sites
MW (Da)
ΔF
F
≈ 1.2 f”
√

## Slide 25
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 26: Sources of error for anomalous differences
Shutter jitter (rms 0.5 ms)
Beam flicker (0.15%/sqrt(Hz))
Attenuation correction (< 2%)
Radiation damage (1%/MGy)
Detector calibration (3%)

## Slide 27: Sources of error for anomalous differences
Shutter jitter (rms 0.5 ms)
Beam flicker (0.15%/sqrt(Hz))
Attenuation correction (< 2%)
Radiation damage (1%/MGy)
Detector calibration (3%)

## Slide 28: Detector calibration: 7235 eV

## Slide 29: Detector calibration: 7247 eV

## Slide 30: Gadox calibration vs energy
photon energy (keV)
Relative absorption depth
same = good!
bad!

## Slide 31
Dan Schuette PhD Thesis (2008) Fig 6.22 page 198, Gruner Lab, Cornell University.
Pilatus is not immune!
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 32: Spatial Heterogeneity in Sharp Spot Sensitivity (SHSSS): Q315r vs Pilatus
3.5
3.0
2.5
2.0
1.5
1.0
0.5
average change in spot intensity (%)
distance between spots (mm)
0.1 1 10 100
Pilatus
Q315r
anomalous mates typically
> 100 mm apart
different
modules

## Slide 33: Required multiplicity
mult > (—)2
~3%
<ΔF/F>

## Slide 34
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 35
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 36: Multi-crystal strategies
Kendrew et al. (1960) "Structure of Myoglobin” Nature 185, 422-427.

## Slide 37
A
B
E297
P351
G353
E347
Metal site: is it Mg++ ? Or Na+ ?
Peat, TS et al. (2013) Cyanuric acid hydrolase: evolutionary innovation by structural concatenation, Mol Microbiol. 88, 1149-1163.

## Slide 38: Data collection parameters:
16 crystals
360° each, inverse beam
7235 eV photon energy
< 1 MGy per xtal
Australian Synchrotron MX1
  35 kGy/s into 100 μm x 100 μm

## Slide 39
RESOLUTION COMPLETENESS R-FACTOR I/SIGMA R-meas CC(1/2) Anomal SigAno Nano
LIMIT OF DATA observed Corr
9.17 99.1% 3.9% 257.47 3.9% 100.0* 91* 5.024 450
6.49 100.0% 5.2% 214.33 5.2% 100.0* 86* 3.836 882
5.30 100.0% 7.2% 165.13 7.2% 100.0* 76* 3.257 1175
4.59 100.0% 7.2% 175.42 7.3% 100.0* 67* 2.589 1403
4.10 99.9% 7.7% 174.13 7.7% 100.0* 59* 2.264 1594
3.74 99.9% 9.4% 143.09 9.4% 100.0* 49* 1.953 1783
3.47 100.0% 11.2% 120.17 11.2% 100.0* 39* 1.696 1942
3.24 100.0% 14.1% 91.14 14.1% 100.0* 30* 1.333 2103
3.06 99.9% 19.5% 65.79 19.5% 100.0* 23* 1.117 2214
2.90 99.9% 29.0% 44.85 29.1% 99.9* 17* 1.008 2369
2.77 99.9% 40.5% 32.58 40.6% 99.8* 11* 0.901 2493
2.65 99.9% 52.8% 25.16 52.9% 99.8* 10* 0.866 2605
2.54 100.0% 67.4% 19.47 67.6% 99.6* 2 0.804 2705
2.45 100.0% 88.9% 14.58 89.2% 99.2* 4 0.831 2859
2.37 100.0% 109.3% 9.97 109.7% 98.1* 5 0.829 2925
2.29 100.0% 138.2% 6.87 138.9% 96.1* 1 0.760 3037
2.22 100.0% 197.1% 4.03 198.6% 83.5* -1 0.721 3159
2.16 100.0% 227.3% 2.41 230.8% 46.9* -1 0.677 3224
2.10 61.2% 154.4% 1.28 163.6% 47.0* -2 0.660 1999
2.05 47.9% 170.1% 0.68 196.5% 25.7* 3 0.629 1578
total 93.3% 15.7% 54.30 15.8% 100.0* 12* 1.217 42499
140-fold multiplicity: 16 crystals, 360° each, inverse beam, 7235 eV

## Slide 40: 140-fold multiplicity
18 σ
Phased anomalous difference Fourier
16 σ

## Slide 41: 140-fold multiplicity
15σ = PO4
Phased anomalous difference Fourier

## Slide 42: 140-fold multiplicity
~2σ = Mg?
Phased anomalous difference Fourier

## Slide 43: 140-fold multiplicity
8.2σ = Mg?
DELFAN residual anomalous difference

## Slide 44: 140-fold multiplicity
7.4σ = Mg?
DELFAN residual anomalous difference

## Slide 45: How do you do it ?
Reproducibility!
Careful with humidity
All mounts exactly same time
Blow on the cryo
Low dose!
7-8 σ is enough for phasing!
Implications

## Slide 46: How do you do it ?
Reproducibility!
Careful with humidity
All mounts exactly same time
Blow on the cryo
Low dose!
7-8 σ is enough for phasing!
Implications

## Slide 47: Sources of error for anomalous differences
Shutter jitter (rms 0.5 ms)
Beam flicker (0.15%/sqrt(Hz))
Attenuation correction (< 2%)
Radiation damage (1%/MGy)
Detector calibration (3%)

## Slide 48: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.

## Slide 49: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.
Riso ≈ 0.7 %/MGy

## Slide 50
How long will my crystal last?
http://bl831.als.lbl.gov/damage_rates.pdf

## Slide 51: How do you do it ?
Reproducibility!
Careful with humidity
All mounts exactly same time
Blow on the cryo
Low dose!
7-8 σ is enough for phasing!
Implications

## Slide 52: plunge cooling
foam insulation
warm, moist air
cold N2
liquid N2
ice

## Slide 53: plunge cooling
foam insulation
warm, moist air
cold N2
liquid N2
ice

## Slide 54: plunge cooling
cold N2
foam insulation
warm, moist air
liquid N2
ice

## Slide 55: Warkentin method
foam insulation
liquid N2
Warkentin (2006) J. Appl. Crystallogr. 39, 805-811.

## Slide 56: How do you do it ?
Reproducibility!
Careful with humidity
All mounts exactly same time
Blow on the cryo
Low dose!
7-8 σ is enough for phasing!
Implications

## Slide 57: First diffraction from protein xtal
Bernal, J. & Crowfoot, D. (1934). "X-ray photographs of crystalline pepsin", Nature 133, 794-795.
1934

## Slide 58: Non-isomorphism in lysozyme
RH 84.2% vs 71.9%
Riso = 44.5%
RMSD = 0.18 Å

## Slide 59: Elastic deformation = non-isomorphism

## Slide 60: Elastic deformation = non-isomorphism

## Slide 61: Plastic deformation = poor diffraction

## Slide 62: Plastic deformation = poor diffraction

## Slide 63: Dehydration: 1934
100 μm
2 mm
= 1.5 μL
= 1.0 nL
10 μm
= 1.0 pL
and 2014?

## Slide 64: Grand Challenges in Structural Biology
Phase Problem
spots, but no maps
Amplitude Problem
    Crystals, but no spots
R-factor Gap
    Can’t/shouldn’t publish

## Slide 65: Now What?
10 Å

## Slide 66: Ways to improve diffraction
New crystal form
Purify
  - add a column
  - heat shock
Bind something
  - Known ligand
  - Silver bullets
Change the clone
  - chop off floppy bits
  - homolog
  - Ala -> Lys mutants
Make Protein Sit Still!!!
Newman J. (2006) Acta Cryst. D62 27-31.

## Slide 67: Sources of error for weak spots
Beam intensity sqrt(seconds)
Radiation damage (10 MGy/Å)
Crystal size (size3)
Background sqrt(Ispot+Ibg)
Disorder (e-B)

## Slide 68: Darwin’s Formula
Ispot - photons/spot (fully-recorded)
Ibeam - incident (photons/s/m2 )
re - classical electron radius (2.818x10-15 m)
Vxtal - volume of crystal (in m3)
Vcell - volume of unit cell (in m3)
λ - x-ray wavelength (in meters!)
ω - rotation speed (radians/s)
L - Lorentz factor (speed/speed)
P - polarization factor
A - attenuation factor
F0 - structure factor at T = 0
B - Debye-Waller-Ott factor
s - 0.5/d-spacing
C. G. Darwin (1914)
P A | F0e-Bs2 |2
Ispot = Ibeam re2
Vxtal
Vcell
λ3 L
ωVcell

## Slide 69: Darwin’s Formula
Ispot - photons/spot (fully-recorded)
Ibeam - incident (photons/s/m2 )
re - classical electron radius (2.818x10-15 m)
Vxtal - volume of crystal (in m3)
Vcell - volume of unit cell (in m3)
λ - x-ray wavelength (in meters!)
ω - rotation speed (radians/s)
L - Lorentz factor (speed/speed)
P - polarization factor
A - attenuation factor
F0 - structure factor at T = 0
B - Debye-Waller-Ott factor
s - 0.5/d-spacing
C. G. Darwin (1914)
P A | F0e-Bs2 |2
Ispot = Ibeam re2
Vxtal
Vcell
λ3 L
ωVcell

## Slide 70: Darwin’s Formula
Ispot - photons/spot (fully-recorded)
Ibeam - incident (photons/s/m2 )
re - classical electron radius (2.818x10-15 m)
Vxtal - volume of crystal (in m3)
Vcell - volume of unit cell (in m3)
λ - x-ray wavelength (in meters!)
ω - rotation speed (radians/s)
L - Lorentz factor (speed/speed)
P - polarization factor
A - attenuation factor
F0 - structure factor at T = 0
B - Debye-Waller-Ott factor
s - 0.5/d-spacing
C. G. Darwin (1914)
P A | F0e-Bs2 |2
Ispot = Ibeam re2
Vxtal
Vcell
λ3 L
ωVcell

## Slide 71
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
resolution (Å)
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12
Cryo damage

## Slide 72
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12
Cryo damage
10 MGy/Å

## Slide 73
How long will my crystal last?
http://bl831.als.lbl.gov/damage_rates.pdf

## Slide 74
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.
No flux
No symmetry

## Slide 75
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 76: Sources of error for weak spots
Beam intensity sqrt(seconds)
Radiation damage (10 MGy/Å)
Crystal size (size3)
Background sqrt(Ispot+Ibg)
Disorder (e-B)

## Slide 77: Sources of error for weak spots
Beam intensity sqrt(seconds)
Radiation damage (10 MGy/Å)
Crystal size (size3)
Background sqrt(Ispot+Ibg)
Disorder (e-B)

## Slide 78
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 79: Darwin’s Formula
Ispot - photons/spot (fully-recorded)
Ibeam - incident (photons/s/m2 )
re - classical electron radius (2.818x10-15 m)
Vxtal - volume of crystal (in m3)
Vcell - volume of unit cell (in m3)
λ - x-ray wavelength (in meters!)
ω - rotation speed (radians/s)
L - Lorentz factor (speed/speed)
P - polarization factor
A - attenuation factor
F0 - structure factor at T = 0
B - Debye-Waller-Ott factor
s - 0.5/d-spacing
C. G. Darwin (1914)
P A | F0e-Bs2 |2
Ispot = Ibeam re2
Vxtal
Vcell
λ3 L
ωVcell

## Slide 80
Disorder
Trumps
Everything!
Diffraction Take-Home Lesson:

## Slide 81: What Causes Disorder?
Function
Radiation damage
Mosaicity
Strain
Xtal abuse
Dehydration

## Slide 82: What Causes Disorder?
Function
Radiation damage
Mosaicity
Strain
Xtal abuse
Dehydration

## Slide 83: Muybridge’s galloping horse (1878)

## Slide 84: realistic “crystal” of horses

## Slide 85: average structure: galloping horse

## Slide 86: average structure: 1-sigma contour

## Slide 87: lysozyme: real and reciprocal

## Slide 88: lysozyme: thermal motion
RMS displacement from B factors

## Slide 89: Sources of error for weak spots
Beam intensity sqrt(seconds)
Radiation damage (10 MGy/Å)
Crystal size (size3)
Background sqrt(Ispot+Ibg)
Disorder (e-B)

## Slide 90: Sources of error for weak spots
Beam intensity sqrt(seconds)
Radiation damage (10 MGy/Å)
Crystal size (size3)
Background sqrt(Ispot+Ibg)
Disorder (e-B)

## Slide 91: Background scattering
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
real estate is
expensive
use it!

## Slide 92: Background scattering

## Slide 93: Fine Slicing
Pflugrath, J. W. (1999)."The finer things in X-ray diffraction data collection", Acta Cryst. D 55, 1718-1725.
background
background

## Slide 94: X-ray scattering “rules”:
1 μm crystal ≈ 1 μm water
≈ 1 μm plastic
≈ 0.1 μm glass
≈ 1000 μm air
you want:
air gap < 1000x xtal size

## Slide 95: Non-crystal stuff in the beam
Too much
Too little
Just right

## Slide 96: Sources of error for weak spots
Beam intensity sqrt(seconds)
Radiation damage (10 MGy/Å)
Crystal size (size3)
Background sqrt(Ispot+Ibg)
Disorder (e-B)

## Slide 97: Sources of error for weak spots
Beam intensity sqrt(seconds)
Radiation damage (10 MGy/Å)
Crystal size (size3)
Background sqrt(Ispot+Ibg)
Disorder (e-B)

## Slide 98: Exposure time problem:
Too long = radiation damage
Too short = read-out noise
Solution: “dose slicing”

## Slide 99: Exposure time: “dose slicing”
crystal’s useful life
N
photons
N
photons
N
photons
unacceptable
damage
unacceptable
read noise

## Slide 100: Optimal exposure time (faint spots)
thr Optimal exposure time for data set (s)
tref exposure time of reference image (s)
bgref background level near weak spots on
reference image (ADU)
bg0 ADC offset of detector (ADU)
bghr optimal background level (via thr)
σ0 rms read-out noise (ADU)
gain ADU/photon
m multiplicity of data set (including partials)
adjust exposure
so this is ~100

## Slide 101: Grand Challenges in Structural Biology
Phase Problem
spots, but no maps
Amplitude Problem
    Crystals, but no spots
R-factor Gap
    Can’t/shouldn’t publish

## Slide 102: R-factor Gap?
Holton et al. (2014). FEBS J. 281, 4046-60.
R1 < 2*Rsigma
Publication criterion for chemical crystallography:
R1 = Fo vs Fc for I/σ(I) > 3
Rsigma = <σ(I)>/<I>
There are no PDB entries that pass this test!

## Slide 103: Is this good enough?
dmax = 4.5 Å
Rcryst = 27%
Rfree = 38%

## Slide 104: Is this good enough?
3a8n 4.5 Å Rmerge = 0.15 R/Rfree = 0.306/0.396
1grz 5 Å Rmerge = 0.052 R/Rfree = 0.369/0.428
1qzv 4.44 Å Rmerge = 0.099 R/Rfree = 0.41/0.42

## Slide 105: Is this good enough?
1hvu 4.75 Å Rmerge = 0.064 R/Rfree = 0.34/0.413
2r6e 5.02 Å Rmerge = 0.058 R/Rfree = 0.394/0.397
1n8e 4.5 Å Rmerge = 0.138 R/Rfree = 0.415/0.416

## Slide 106: Molecular Dynamics Simulation
1aho
Scorpion toxin
0.96 Å resolution
64 residues
Solvent: H20 + acetate
Cerutti et al. (2010).J. Phys. Chem. B 114, 12811-12824.
using real
crystal’s lattice

## Slide 107: 30 conformers from 24,000

## Slide 108: Electron density from 24,000 conformers

## Slide 109: Electron density from 24,000 conformers

## Slide 110: 2Fsim-Fcalc and Fsim-Fcalc maps
1.0 Å data
Rcryst= 0.137
Rfree = 0.159
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc

## Slide 111: 2Fsim-Fcalc and (Fsim Φsim) - (Fcalc Φcalc) maps
1 “sigma” 2Fsim-Fc
Fright – (2Fsim-Fc)
1.0 Å data
Rcryst= 0.137
Rfree = 0.159

## Slide 112: Regular model with real data!
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc
1.0 Å data
Rcryst= 0.116
Rfree = 0.135

## Slide 113: MD: predicted density for one atom

## Slide 114: How many conformers are there?
Answer: 40
Rcryst = 0.0506
Rfree = 0.0556
vs Fsim

## Slide 115: How many conformers are there?
Answer: 8
Rcryst = 0.0297
Rfree = 0.0293
vs Fsim

## Slide 116: How many conformers are there?
Rcryst = 0.0441
Rfree = 0.0516
vs Fsim
Answer: 2-14

## Slide 117: How many conformers are there?
Rcryst = 0.1546
Rfree = 0.1749
vs Fobs
1aho:
Rcryst = 0.1630
Rfree = n/d
Answer: 1-7

## Slide 118: How many conformers are there?
All difference
features
are in
the solvent!
real data

## Slide 119: How “rough” is the solvent?
Rcryst = 0.0309
Rfree = 0.0678
vs Fsim

## Slide 120: Molecular Dynamics vs Observation
Fsim
Fcalc
Rcryst= 0.137
refined_vs_Fsim.pdb
1aho 64-residue scorpion toxin in water to 1.0 Å resolution

## Slide 121: Molecular Dynamics vs Observation
Fobs
1aho.cif
1aho.pdb
Fsim
Fcalc
Fcalc
Rcryst= 0.137
Rcryst= 0.116
Rfree = 0.69
refined_vs_Fsim.pdb
LSQ rmsd = 0.43Å
rmsd = 1.05 Å
1aho 64-residue scorpion toxin in water to 1.0 Å resolution
Rfree = 0.48 to 4 Å
Rfree =

## Slide 122: Molecular Dynamics vs Observation
RMSD
1.05 Å

## Slide 123: Molecular Dynamics vs Observation
RMSD
0.45 Å
aligned

## Slide 124: Molecular Dynamics vs Observation
Sodium acetate trihydrate
5 atoms
3 waters
0.9 Å resolution
C2/c
Rfree = 0.03

## Slide 125: Molecular Dynamics vs Observation
fav8
8 residues
4 waters
1.0 Å resolution
P1

## Slide 126: Molecular Dynamics vs Observation
Fobs
fav8.fcf
fav8.cif
Fsim
Fcalc
Fcalc
Rcryst= 0.13
Rcryst= 0.16
Rfree= 0.23
refined_vs_Fsim.pdb
LSQ rmsd = 0.091Å & 0.15 Å
rmsd = 0.20 Å
“fav8” 8-residue aromatic peptide with 4 waters to 1.0 Å resolution
R1 = 0.041
With 4σ cutoff!
Rfree = 0.20 to 2Å

## Slide 127: MD-predicted water structure
Simulated
density
Janowski et al (2013) JACS 135, 7938-7948

## Slide 128: MD-predicted water structure
Simulated
density
2mFo-DFc
Janowski et al (2013) JACS 135, 7938-7948

## Slide 129: MD-predicted Val rotamer
Janowski et al (2013) JACS 135, 7938-7948

## Slide 130: MD-predicted Val rotamer
confs | Rwork | Rfree
one | 4.11% | 5.84%
A & B | 3.89% | 5.53%
Janowski et al (2013) JACS 135, 7938-7948

## Slide 131: Grand Challenges in Structural Biology
Phase Problem
super-high multiplicity isomorphous crystals
Amplitude Problem
Disorder trumps everything
Revolution in sample handling?
R-factor Gap
There is “life” below 1 sigma
MD-inspired models on horizon?
http://bl831.als.lbl.gov/~jamesh/powerpoint/AS_SvN_2014.pptx

## Slide 132: Summary
http://bl831.als.lbl.gov/xtalsize.html
http://bl831.als.lbl.gov/~jamesh/powerpoint/AS_SvN_2014.pptx
100 ADU/pixel
dose slicing
~3% error per spot, 1%/MGy
7235 eV for S-SAD
There is “life” below 1 sigma