## Slide 2: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1: TomAlberTron
NIH NIGMS R01 GM124149
NIH NIAID P50 AI150476
NIH NIGMS P30 GM124169
DOE-BER Integrated Diffraction Analysis Technologies (IDAT)
NIH NIGMS P30 GM133894
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser Nevan Krogan
Paul Adams John Tainer Greg Hura Nick Sauter
Aina Cohen Art Lyubimov Jeney Wierman
http://bl831.als.lbl.gov/~jamesh/powerpoint/CBMS_WB_2022.pptx

## Slide 3: Systematic Errors! … and how to eliminate them
Radiation Damage
Non-isomorphism
Bulk(-ish) solvent
Tangled refinement

## Slide 4: Systematic error: Illumination contrast appears to “reverse” damage
0.35 MGy
Cys6
Cys127
Room temperature high-dose rate series
de la Mora, et al. (2020) PNAS USA 117, 4142-4151

## Slide 5: False “Damage reversal”: from beam profile
X-ray beam
crystal

## Slide 6: False “Damage reversal”: from beam profile
Cold beam
Hot beam
crystal

## Slide 7: False “Damage reversal”: from beam profile
Cold beam
Hot beam
crystal

## Slide 8: False “Damage reversal”: from beam profile
Cold beam
Hot beam
crystal

## Slide 9: False “Damage reversal”: from beam profile
Cold beam
Hot beam
crystal

## Slide 10: False “Damage reversal”: from beam profile
Cold beam
Hot beam
crystal

## Slide 11: False “Damage reversal”: from drift
X-ray beam
crystal

## Slide 12: Systematic error: Illumination contrast appears to “reverse” damage
Room temperature high-dose rate series
de la Mora, et al. (2020) PNAS USA 117, 4142-4151
occupancy
time
0
1
observed
cold
hot

## Slide 13: 0 Gy

## Slide 14: 100 MGy

## Slide 15: What is the dose?
50 MGy ?

## Slide 16
Holton (2009) J. Synchrotron Rad. 16 133-42
Radiation Damage World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
10/Å global damage Howells et al. (2009)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
4 R-C-COOH Garman et al. (2015)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
~1? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.06 putidaredoxin Corbett et al. (2007)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 17
Take home:
“dose contrast”
makes rad dam
Hard to correct

## Slide 18: Beam Shape Dichotomy
Flat-top beam
  Uniform dose in illuminated region
  Sharp edges: sensitive to drift
Gaussian beam
  Softer edges
  High dose contrast
Best of both?
  “dose flattening”

## Slide 19: “rastering” to find the crystal
Membrane
protein crystal
X-ray beam
ice

## Slide 20: “rastering” for flat dose

## Slide 21: “rastering” for virtual beam

## Slide 22
phi
position along crystal
360°
0°
Old way: shoot and scoot

## Slide 23
phi
position along crystal
360°
0°
Old way: shoot and scoot

## Slide 24
phi
position along crystal
360°
0°
Old way: shoot and scoot

## Slide 25
phi
position along crystal
360°
0°
phi
1080°
0°
Painting mode: raster as collection

## Slide 26
phi
position along crystal
360°
0°
phi
1080°
0°
Painting mode: raster as collection

## Slide 27
phi
position along crystal
360°
0°
phi
1080°
0°
Painting mode: raster as collection

## Slide 28
phi
position along crystal
360°
0°
phi
1080°
0°
Painting mode: raster as collection

## Slide 29: How many images?
360° / 0.1° * ( 100 µm / 1 µm )2
= 36x106
28,000 photons/image

## Slide 30: Lossless data rate
The 1.2e-5 scattered photons per incident photon can be derived form the cross section of oxygen (0.2 cm^2/g) and the rough density of protein crystals (1.2 g/cm^3), and the fact that about half of all scattered photons hit a flat detector: 0.2*1.2*1e-4/2 = 1.155e-5 That is, flux*thickness*1.2e-5 is the rate of photon arrivals and log2(pixels) is the number of bits required to store the location of one photon in the entropy-limited regime. Lossless compression cannot be better than this because individual photon arrivals are genuinely random.
bits
s
= log2(pixels) * flux * thick * 1.2x10-5
where: bits/s = entropy-limited compressed data rate
pixels = number of pixels in the detector
flux = photons/s onto the sample thick = sample thickness in microns
EG: 1e12 ph/s * 100um thick = 3.4 GBytes/s

## Slide 31: How to lose information
long exposures
  >1 photon/image = order of arrivals
Wide phi slice
  sum over angle
Large beams
  sum over profile area
Pink/divergent beam
  sum over lambda/angle
Background
  non-crystal stuff
Systematics
  Dose contrast, drift, read-out gap

## Slide 32: Dose slicing: is that a spot?

## Slide 33: Dose slicing: is that a spot?

## Slide 34: Dose slicing: is that a spot?

## Slide 35: Dose slicing: is that a spot?

## Slide 36: Dose slicing: is that a spot?

## Slide 37: Dose slicing: is that a spot?

## Slide 38
photons
0
4
photons
0
4
time
photons
0
4
time
photons
0
4
Single Photons Carry Information
About Radiation Damage

## Slide 39
Take home:
“dose flattening”
makes rad dam
correctable
(if we can use weak images)

## Slide 40: Systematic Errors! … and how to eliminate them
Radiation Damage
Non-isomorphism
Bulk(-ish) solvent
Tangled refinement

## Slide 41: Non-isomorphism
is annoying
Caused by:
rad dam
humidity
temperature
Growth conditions
Cryo-cooling
Everything
means you:
can’t merge
can’t
add
can’t
subtract

## Slide 42: Cell clustering: 100 datasets
Reality:
Perfect isomorphism
(simulated data)
Holton, J. (2019). Acta Cryst. D 75, 113-122.

## Slide 43
0.5% cell change → 15%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.
Same structure, different cell

## Slide 44
Same structure, different cell
0.5% cell change → 15%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 45
Uniform stretch
5% change → 0%

## Slide 46
5% change → 0%
Uniform stretch

## Slide 47: Hygrostatic gradients
loop
jet
high
water activity
low

## Slide 48: Non-isomorphism in lysozyme
RH: 84.2%
vs 71.9%
Riso = 44.5%
3aw6
3aw7
Δcell = 0.7 %
RMSD = 1.70 Å
RMSD = 0.18 Å LSQ

## Slide 49: 3aw6

## Slide 50: 3aw6 3aw7

## Slide 51
Periodic Spatial Distortion Vector Field

## Slide 52: 3aw6 3aw7

## Slide 53: 3aw6, 3aw7, “bent” 3aw6

## Slide 54: 3aw7, “bent” 3aw6

## Slide 55: 3aw7

## Slide 56: “bent” 3aw7

## Slide 57: 3aw6

## Slide 58
Fobs-Fobs difference
3σ 1.8 Å
“unbent”

## Slide 59
Fobs-Fobs difference
3σ 1.8 Å
old way

## Slide 60
Take home:
Non-isomorphism
is now correctable
(in real space)

## Slide 61: Downloading “map bender”

## Slide 62: Systematic Errors! … and how to eliminate them
Radiation Damage
Non-isomorphism
Bulk(-ish) solvent
Tangled refinement

## Slide 63: Refined
Rwork = 0.17023
Rfree = 0.19309
3si4
waters = 401

## Slide 64: Watershed-ed
Rwork = 0.17727
Rfree = 0.19281
3si4
waters = 291

## Slide 65: Fo-Fc peak in solvent but “water” makes it worse…
Rwork 11.71
Rfree 13.46
bond 0.007 Å
angle 1.78°

## Slide 66: After solvent “touch-up”
Rwork 11.10
Rfree 12.97
bond 0.006 Å
angle 1.49°

## Slide 67: Probability that it’s not noise
P() probability
ρ electron density
σ(ρ) rms value of difference map
erf() error function – integral of a Gaussian
Vasu volume of asymmetric unit
Vshan volume of “Shannon voxel”
d true resolution
B Debye-Waller factor
9.484 intrinsic width of C atom
B = 8π2rms2 exp(-x2) has rms = 1
fwhm = 2*sqrt(2*log(2))*rms

## Slide 68: “Bulk” solvent average from 100 ns MD
Rwork 11.10
Rfree 12.97
bond 0.006 Å
angle 1.49°

## Slide 69: Best so far
8564 waters for AMBER
Rwork 11.94
Rfree 21.13
bond 0.005 Å
angle 1.29°

## Slide 70
Chart: 
Phenix macro-cycle
R factor (%)
Explicit solvent: refinement is unstable

## Slide 71: Model complexity vs Rfree
Method of refinement | Rwork | Rfree
Refmac5: defaults, isotropic B | .1617 | .1797
1aho

## Slide 72: Model complexity vs Rfree
Method of refinement | Rwork | Rfree
Refmac5: defaults, isotropic B | .1617 | .1797
3D-RISM solvent | .1578 | .1739
1aho

## Slide 73: Model complexity vs Rfree
Method of refinement | Rwork | Rfree
Refmac5: defaults, isotropic B | .1617 | .1797
3D-RISM solvent | .1578 | .1739
100 ns averaged MD solvent protein fixed | .1440 | .1666
1aho

## Slide 74: Model complexity vs Rfree
Method of refinement | Rwork | Rfree
Refmac5: defaults, isotropic B | .1617 | .1797
3D-RISM solvent | .1578 | .1739
100 ns averaged MD solvent protein fixed | .1440 | .1666
2-8 conformers/residue Iterative solvent from restrained MD | .1089 | .1239
1aho

## Slide 75: Model complexity vs Rfree
Method of refinement | Rwork | Rfree
Refmac5: defaults, isotropic B | .1617 | .1797
3D-RISM solvent | .1578 | .1739
100 ns averaged MD solvent protein fixed | .1440 | .1666
2-8 conformers/residue Iterative solvent from restrained MD | .1089 | .1239
48-copy supercell refinement mixed MD & ordered + watershed + touchup | .0928 | .1161
1aho

## Slide 76
Take home:
Solvent region contains error
(but not all of it)

## Slide 77: Why does ensemble refinement suck? (3 parameters/observation and Rwork still high!) The chains are “tangled”

## Slide 78: Systematic Errors! … and how to eliminate them
Radiation Damage
Non-isomorphism
Bulk(-ish) solvent
Tangled refinement

## Slide 79: Is it Real? Or is it MLFSOM
simulated
real
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 80
Simulated | statistic | Real
5.4% | Rmerge | 6.2%
18.9 | I/sd | 16.2
1.9 | I/sd (1.4 Ǻ) | 1.6
1.7 4.0 0.020 | SDCORR | 1.0 2.2 0.065
36.8 | PADFPH | 31.46
3.871 | mlphare f” | 3.476
0.178 | FOM | 0.192
0.545 | FOMDM | 0.664
0.6270 | CC(1H87) | 0.6090

## Slide 81
Simulated | statistic | Real
5.4% | Rmerge | 6.2%
18.9 | I/sd | 16.2
1.9 | I/sd (1.4 Ǻ) | 1.6
1.7 4.0 0.020 | SDCORR | 1.0 2.2 0.065
36.8 | PADFPH | 31.46
3.871 | mlphare f” | 3.476
0.178 | FOM | 0.192
0.545 | FOMDM | 0.664
0.6270 | CC(1H87) | 0.6090
0.050 | Rcryst | 0.184
0.070 | Rfree | 0.231

## Slide 82: Model building: real vs sim data
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.

## Slide 83
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.
Fo-Fc difference map peak height
Model building: real vs sim data

## Slide 84
Rwork = 0.04
Rfree = 0.05
dmin = 3.5 Å
6σ = 1 e-
Simulation:
Realistic noise
“perfect” model
Hydrogen: visible at 3.5 Å resolution!

## Slide 85
Big Question:
Why doesn’t this work
with real data?

## Slide 88: Right answer
R = 0.8%
rms bond = 0.0002

## Slide 89: swap assignments
R = 0.8%
rms bond = 0.04

## Slide 90: Refine – low x-ray weight
R = 14.3%
rms bond = 0.0002

## Slide 91: Refine – step 61
R = 6.8%
rms bond = 0.001

## Slide 92: Refine – step 62
R = 5.7%
rms bond = 0.003

## Slide 93: Refine – high x-ray weight
R = 1.2%
rms bond = 0.06

## Slide 94: Final compromise
R = 7.07%
rms bond = 0.001

## Slide 95: Right answer
R = 0.8%
rms bond = 0.0002

## Slide 96: What if … ?
Exactly two conformations
50:50
Geometry/energy excellent
Solvent model-able
Can correct assignments be found?
If so, what would Rfree be?
  ~4%

## Slide 97
flipme.pdb
control
Flip_1
Flip_2
Refine
Score & Sort
Multiply together:
Rwork Clashscore
VdW_Energy Cβdev
Worst & average Z-scores:
rama rotamer
sin(ω)
bonds angles planes
Chirals dihedrals
Flip_3 …
Flip_4 …

## Slide 98
Rwork: 0.1226
Rfree: 0.1385
bond: 0.0319
Angle: 3.57
MoPro: 2.12
Clash: 6.52
Cβdev: 11
Rota: 2.78
Rama: 1.61

## Slide 99
Rwork: 0.1107
Rfree: 0.1250
bond: 0.024
Angle: 4.11
MoPro: 0.89
Clash: 0.54
Cβdev: 1
Rota: 0.93
Rama: 0

## Slide 100
Rwork: 0.0815
Rfree: 0.0805
bond: 0.0101
Angle: 1.83
MoPro: 0.72
Clash: 0
Cβdev: 0
Rota: 0
Rama: 0

## Slide 101
Rwork: 0.0815
Rfree: 0.0805
bond: 0.0101
Angle: 1.83
MoPro: 0.72
Clash: 0
Cβdev: 0
Rota: 0
Rama: 0

## Slide 102
Take home:
Single-electron changes
are visible at 3.5 Å
(but only if Rfree ~ 5%)

## Slide 103: Summary
“dose contrast” avoided with dose flattening
Two photons are better than two
Non-isomorphism is correctable (real space)
Solvent “touch up” doesn’t hurt
Ensemble tangling limits refinement
Hydrogens at 3.5 Å
http://bl831.als.lbl.gov/~jamesh/powerpoint/
CBMS_WB_2022.pptx