## Slide 1: Acknowledgements
http://bl831.als.lbl.gov/~jamesh/powerpoint/CSHL_raddam_2022.pptx
UCSF LBNL SLAC
ALS 8.3.1: TomAlberTron
NIH NIGMS R01 GM124149 to Holton
NIH NIAID P50 AI150476 to Krogan
NIH NIAID U19 AI171110 to Krogan
NIH NIGMS P30 GM124169 to Adams
DOE-BER IDAT to Hura
NIH NIGMS P41 GM103393 to Hodgson
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser
Paul Adams Greg Hura
Aina Cohen Keith Hodgson

## Slide 2: PowerPoint File available:
http://bl831.als.lbl.gov/
~jamesh/powerpoint/
CSHL_raddam_2022.pptx

## Slide 3: Radiation damage

## Slide 4: Radiation damage

## Slide 5: What you need to know:
Limits “data photons”
Caveat for active site
Can be corrected
Can be predicted
Cannot be prevented
Cannot be outrun

## Slide 6: Where do photons go?
beamstop
Transmitted (98%)
Protein
1A x-rays

## Slide 7: Elastic scattering

## Slide 8: Elastic scattering

## Slide 9: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
Protein
1A x-rays

## Slide 10: Elastic scattering

## Slide 11: Inelastic scattering

## Slide 12: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
Protein
1A x-rays

## Slide 13: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays

## Slide 14: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 15: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 16: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 17: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (~0%)
Absorbed (99%)
Re-emitted (99%)
Absorbed (~0%)

## Slide 18: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
useful/absorbed energy: 7.3%
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (~0%)
Absorbed (99%)
Re-emitted (99%)
Absorbed (~0%)

## Slide 19: Photoelectric absorption

## Slide 20: Photoelectric absorption
e-
+

## Slide 21: Secondary ionization
e-

## Slide 22: Secondary ionization
e-
e-
+

## Slide 23: Excitation
e-

## Slide 24: Excitation
e-

## Slide 25: Excitation
e-

## Slide 26: Excitation

## Slide 27: Electron attachment
e-

## Slide 28: Electron attachment
-

## Slide 29: Sample atoms

## Slide 30: Sample atoms

## Slide 31: Primary ionization
e-
+

## Slide 32: Secondary ionizations
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+

## Slide 33: Ionization track
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 34: Ionization track
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 35: Ionization track

## Slide 36: Ionization track

## Slide 37: Ionization track
3 μm

## Slide 38: Ionization track
Linear Energy Transfer

## Slide 39: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 40: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
neutralization
e-
+

## Slide 41: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
neutralization
e-
+

## Slide 42: initial effects
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
neutralization
neutralization
+

## Slide 43: initial effects
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
attachment
+

## Slide 44: initial effects
e-
e-
e-
e-
-
e-
e-
+
+
+
+
+
+
attachment
+

## Slide 45: initial effects
e-
e-
e-
e-
-
e-
e-
+
+
+
+
+
+
attachment
attachment
+

## Slide 46: initial effects
e-
e-
-
e-
e-
+
+
+
+
+
+
-
-
+

## Slide 47: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 48: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+
solvation

## Slide 49: initial effects
-
e-
+
+
+
+
+
-
-
-
-
solvation
+

## Slide 50: Solvated electron
e-

## Slide 51: Solvated electron
e-

## Slide 54: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 55: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 56: initial effects
-
e-
+
+
+
+
-
-
-
+

## Slide 57: initial effects
-
e-
+
+
-
+

## Slide 58: initial effects
-
e-
+
+

## Slide 59: Excitation transfer

## Slide 60: Excitation transfer
UV photon

## Slide 61: Excitation transfer

## Slide 62: Excitation transfer
Förster transfer
r-6

## Slide 63: Excitation transfer

## Slide 64: t = 0 s

## Slide 65: t ≈ 10-14 s
-
e-
+
+

## Slide 66: Timescales of radiation damage
Garret et. al. (2005) Chem. Rev. 105, 355-389

## Slide 67: Timescales of radiation damage
Garret et. al. (2005) Chem. Rev. 105, 355-389
XFEL
synch
bunch

## Slide 68: Ionization track
Heterogeneous reactions
Homogeneous reactions

## Slide 69: Rough values of energy quanta
1 MeV 100 GJ/mol Medical radiation therapy
100 keV 10 GJ/mol Medical imaging
10 keV 1 GJ/mol X-ray crystallography
1 keV 100 MJ/mol S and P K-edges
100 eV 10 MJ/mol “water window”
10 eV 1 MJ/mol C≡C bond
1 eV 100 kJ/mol C-C bond, visible light
100 meV 10 kJ/mol hydrogen bond
10 meV 1 kJ/mol heat (~300 K)

## Slide 70: Types of radiation damage
Global
Specific

## Slide 71: Types of radiation damage
Global
Specific
  depends on chemistry

## Slide 72: Specific damage
final, refined phases

## Slide 73: Specific damage
experimentally-obtained phases

## Slide 74: Types of radiation damage
Global
Specific
  depends on chemistry
  destroys phasing signal

## Slide 75
Holton, J. M. (2007) J. Synch. Rad. 14, 51-72.

## Slide 76
1.0
0.0
fraction
unconverted
Holton, J. M. (2007) J. Synch. Rad. 14, 51-72.

## Slide 77: what the is a MGy?
http://bl831.als.lbl.gov/
damage_rates.pdf
Holton J. M. (2009) J. Synchrotron Rad. 16 133-42
1 MGy = 106 J/kg

## Slide 78
https://bl831.als.lbl.gov/~jamesh/dose2dose.html

## Slide 79
Holton (2009) J. Synchrotron Rad. 16 133-42
Radiation Damage World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
10/Å global damage Howells et al. (2009)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
4 R-C-COOH Garman et al. (2015)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
~1? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.06 putidaredoxin Corbett et al. (2007)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 80: What if I’m not on the list?
Rule of thumb:
is it a “good leaving group” ?
  Br
  COO-
  S-CH2-
  CH3
  H2

## Slide 81: Radiation damage

## Slide 82: Xtal5_t1 graph

## Slide 83: How much water are we burning?
Meents et al. (2010) claimed:
"400 molecules of H2 for every 12.5 keV photon“
= 3.3x10-7 mol/J
200 kGy to 100 um3 = 0.24 J
= 1.2x10-8 mol H2
100 um3 of water = 6.7x10-8 mol
→ 18% of water has reacted!

## Slide 84
Global damage
Howells, et al. (2009) J. Electron Spectrosc. Relat. Phenom. 170, 4-12.

## Slide 85: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12

## Slide 86: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12
10 MGy/Å

## Slide 87
How long will my crystal last?
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
APS 5ID-B POWDER 5e12 1000x300 1.7e+07 8.25 kGy/s 61 m 4 m
APS 8-BM MAD 1e11 200 2.5e+06 858 Gy/s 9.7 h 39 m
APS 14-BM-C MONO 6e11 130x200 2.3e+07 11 kGy/s 46 m 3 m
APS 14-ID-B LAUE 7e13 15x20 2.3e+11 132 MGy/s 0.23 s 0.015 s
APS 17-BM POWDER 8e11 200 2.0e+07 8.72 kGy/s 57 m 3.8 m
APS 17-ID MAD 7e11 200 1.8e+07 9.87 kGy/s 51 m 3.4 m
APS 18-ID SAXS 2e13 50x150 2.7e+09 2.69 MGy/s 11 s 0.74 s
APS 19-BM MAD 6e+08 60x50 2.0e+05 77.3 Gy/s 4.5 d 7.2 h
APS 19-ID MAD 3e+10 100x20 1.5e+07 7.81 kGy/s 64 m 4.3 m
APS 21-ID-D MAD 5e12 50 2.0e+09 1.13 MGy/s 27 s 1.8 s
APS 21-ID-F MONO 1e12 50 4.0e+08 190 kGy/s 2.6 m 11 s
APS 21-ID-G MONO 1e12 50 4.0e+08 190 kGy/s 2.6 m 11 s
APS 22-BM MAD 7e12 40x80 2.2e+09 750 kGy/s 40 s 2.7 s
APS 22-ID MAD 7e12 40x80 2.2e+09 750 kGy/s 40 s 2.7 s
APS 23-BM-B MAD 2e11 200? 5.0e+06 2.47 kGy/s 3.4 h 13 m
APS 23-ID-B MAD 6e12 80x20 3.8e+09 2.11 MGy/s 14 s 0.95 s
APS 23-ID-D MAD 1e13 75x25 5.3e+09 3.01 MGy/s 10 s 0.66 s
APS 24-ID-C MAD 2.5e12 40x60 1.0e+09 357 kGy/s 84 s 5.6 s
APS 24-ID-E MONO 2.85e12 20x120 1.2e+09 563 kGy/s 53 s 3.5 s
APS 31-ID MAD 2.6e12 120x80 2.7e+08 105 kGy/s 4.8 m 19 s
NSLS-II 17-ID-1 MAD 5e12 7x5 1.4e+11 67 MGy/s 0.45 s 0.03 s
NSLS-II 17-ID-2 MAD 2e12 1x1 1.3e+12 626 MGy/s 0.048 s 0.0032 s
NSLS X3A MAD 3.8e10 200 9.5e+05 451 Gy/s 18 h 74 m
NSLS X3B EXAFS 9e11 200x700 6.4e+06 6.48 kGy/s 77 m 5.1 m
NSLS X4A MAD 2e10 300 2.2e+05 136 Gy/s 61 h 4.1 h
NSLS X6A MAD 1.5e12 100x500 3.0e+07 10.3 kGy/s 49 m 3.2 m
NSLS X8C MAD 1.1e10 200? 2.8e+05 204 Gy/s 41 h 2.7 h

## Slide 88: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 89: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 90
Chart: minimum required crystal size
wavelength dependence of required crystal size
crystal diameter (μm)
Å
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 91: Does wavelength make a difference? not really

## Slide 92
660%
Protective Measure
Holton, J. M. (2007) J. Synch. Rad. 14, 51-72.

## Slide 93: Can radiation damage be prevented?
Yes! By keeping dose low

## Slide 95
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 96: Multi-crystal strategies
Kendrew et al. (1960) "Structure of Myoglobin” Nature 185, 422-427.

## Slide 97: Can radiation damage be “outrun”?

## Slide 98: No Damage in the Dark!
Experiment time (hours)
Peak absorbance (electrons)
4.6 5.0 5.4 5.8 6.2 6.6
0 5 10 15 20 25

## Slide 99: Double-tap: no dark progression at 675 kGy/s
Intensity (photons)
Time (seconds)

## Slide 100: Dose-rate dependence of damage
dose rate (kGy/s)
maximum useful dose (MGy)

## Slide 101: Dose-rate effect at Room Temp?
Warkentin M, Badeau R, Hopkins JB, Mulichak AM, Keefe LJ & Thorne RE (2012)."Global radiation damage at 300 and 260 K with dose rates approaching 1 MGy s-1", Acta Cryst. D 68, 124-133.
Owen RL, Axford D, Nettleship JE, Owens RJ, Robinson JI, Morgan AW, Dore AS, Lebon G, Tate CG, Fry EE, Ren J, Stuart DI & Evans G (2012)."Outrunning free radicals in room-temperature macromolecular crystallography", Acta Cryst. D 68, 810-818.

## Slide 102: Gaussian beam
50% of flux
the other 50%

## Slide 103: Collimated beam
100% of flux
0%

## Slide 104: Tipping point for µfocus:
10 µm
~10 mm
~1 mrad =0.06°

## Slide 105: Can radiation damage be “outrun”?
not really

## Slide 106
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.
No flux
No symmetry
No exposure time

## Slide 107
The number of photons scattered
before crystal is dead
is independent
of flux & time
1 um3 = 105 photons (roomT)
1 um3 = 106 photons (synch)
1 um3 = 108 photons (XFEL)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009
(synch)

## Slide 108: Dose slicing
crystal’s useful life
N
photons
N
photons
N
photons
unacceptable
completeness
unacceptable
read noise

## Slide 109: Data collection “strategy”
Dauter, Z. (1999). "Data-collection strategies." Acta Cryst. D 55(10): 1703-1717.
The “American Method”:
360° no matter what
(shoot first, questions later)

## Slide 110: Dose slicing: is that a spot?

## Slide 111: Dose slicing: is that a spot?

## Slide 112: Dose slicing: is that a spot?

## Slide 113: Dose slicing: is that a spot?

## Slide 114: Dose slicing: is that a spot?

## Slide 115: Dose slicing: is that a spot?

## Slide 116: What if?
You only have a few small crystals…
Should you:
  Collect 360° from each?
  Collect 10° from each at 36x exposure?
  Glue 36 xtals together, then collect 360° ?

## Slide 117
Chart: 
Resolution (Å)
CC vs right answer
“true” resolution limit

## Slide 118
Dose slice collection scenario |  | 
fine | coarse | glue
3.17700 | 3.14057 | 3.17604
“true” resolution vs strategy
301,640,334 photons/xtal

## Slide 119
processing procedure | resolution limit |  |  | 
 | fine | coarse | glue | glue&fine
XDS/XSCALE | 3.17700 | 3.14057 | 3.17604 | 3.12086
XDS/aimless | 3.16251 | 3.15922 | 3.16675 | 3.12162
XDS/noscale | 3.27289 | 3.15617 | 3.38929 | 3.12162
MOSFLM-defaults | x | x | x | x
MOSFLM-cheat | 3.19755 | 3.18166 | 3.20354 | 3.19755
HKL2000-defaults | x | x | x | x
HKL2000-expert | 3.21803 | 3.12646 | 3.11551 | 3.21803
HKL2000-cheat | 3.16119 | 3.10338 | 3.10338 | 3.16300
DIALS-defaults | x | x | 3.42125 | x
DIALS-expert | 3.10296 | 3.09547 | 3.07653 | 3.08465
d*Trek | ? | ? | 4.34076 | ?
EVAL15 | 3.14352 | 3.10383 | 3.09936 | 3.14105
EVAL15-sadabs | 3.13920 | 3.10797 | 3.10171 | 3.13700

## Slide 120: Minimum exposure time:
~1 photon/pixel
  PAD w XDS, DIALS
~10 photon/pixel
PAD w HKL2k, MOSFLM
~30 photon/pixel
CCD detector

## Slide 121: Can radiation damage be corrected?
Yes, if you have enough information

## Slide 122: Zero-dose extrapolation (ZDE)
Diederichs, K. (2006). "Some aspects of quantitative analysis and correction of radiation damage." Acta Cryst. D 62(1): 96-101.

## Slide 123: How to lose information
long exposures
  >1 photon/image = order of arrivals
Wide phi slice
  sum over angle
Large beams
  sum over area
Pink/divergent beam
  sum over lambda/angle
Background
  non-crystal stuff
Systematics
  Dose contrast

## Slide 124: The Entropy Limit
= log2(Npixels) * flux * tsample * 1.2x10-5
minimum data rate with no information loss
Npixels = 4150*4371 for Eiger
flux = photons/s onto the sample
tsample = sample thickness in µm
1.2x10-5 = 10-4 cm/µm * cross section of oxygen (0.2 cm2/g)
* density of protein crystal (1.2 g/cm3 )
* ~1/2 of total scattering intersects detector
E.G. 34 GByte/s for 1013 photons/s and 100 µm thick
bits
s

## Slide 125: Optimal exposure time
Dose of dataset (MGy) <= half-reaction point

## Slide 126: Types of radiation damage
Global
  scale factor
  B factor
  non-isomorphism
Specific
  depends on chemistry
  destroys phasing signal

## Slide 127: Types of radiation damage
Global
  scale factor
  B factor
  non-isomorphism
Specific
  depends on chemistry
  destroys phasing signal

## Slide 128: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.

## Slide 129: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.
Riso ≈ 0.7 %/MGy

## Slide 130
anomalous signal
Crick, F. H. C. & Magdoff, B. S. (1956) Acta Crystallogr. 9, 901-908.
Hendrickson, W. A. & Teeter, M. M. (1981) Nature 290, 107-113.
# sites
MW (Da)
ΔF
F
≈ 1.2 f”
√
World record!
ΔF/F = 0.5%
Wang, Dauter & Dauter (2006) Acta Cryst. D 62, 1475-1483.

## Slide 131: Optimal exposure time
Dose of dataset (MGy)
<=
anomalous signal (%)

## Slide 132: Radiation Damage
Know your dose! (MGy)
Avoid World Records
disorder dominates everything
“Attenu-wait”: dose slicing
Stay hydrated!
http://bl831.als.lbl.gov/xtalsize.html
http://bl831.als.lbl.gov/xtallife.html
http://bl831.als.lbl.gov/~jamesh/powerpoint/Rapidata_raddam_2022.pptx

## Slide 133: … but does it work for membrane proteins?
Efremov, R. G. & Sazanov, L. A. (2011)."Structure of the membrane domain of respiratory complex I", Nature 476, 414-420.
“To improve diffraction properties, crystals were slowly cooled to 4 C, placed into micro-dialysis buttons, and mother liquor was exchanged by dialysis for 0.1 M sodium acetate (pH 4.8), 0.15 M sodium tartrate (pH 5.0), 30% PEG4000, 0.1% sodium cholate and 12.5% glycerol over a period of 5 days.”
CCP4BB:
“We used it for a large membrane protein complex and diffraction improved from ~7 to 2.7 A. The crystal is fished out and put into mother liquor solution in the button, sealed with dialysis membrane and the button is then placed into about 5 mls of mother liquor with slightly higher PEG concentration. Then you just exchange outside buffer every day or so for solutions containing higher concentrations of PEG. We went from ~9 to 30 % PEG4000 in about a week. You can easily observe crystal under microscope and if it cracks - you went too far/too quickly with PEG and need to use a bit less next time. Also, this method allows you to control all other components of the dehydrating solution - we needed to decrease salt concentration at the same time as increasing PEG. You can also introduce/increase cryo-protectant concentration at the same time. With these crystals, otherwise excellent dehydration machines already mentioned did not work, possibly because the process had to be really slow.”