## Slide 1: Acknowledgements
http://bl831.als.lbl.gov/~jamesh/powerpoint/CSHL_raddam_2023.pptx
UCSF LBNL SLAC
ALS 8.3.1: TomAlberTron
NIH NIGMS R01 GM124149 to Holton
NIH NIAID P50 AI150476 to Krogan
NIH NIAID U19 AI171110 to Krogan
NIH NIGMS P30 GM124169 to Adams
DOE-BER IDAT to Hura
NIH NIGMS P41 GM103393 to Hodgson
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser
Paul Adams Greg Hura
Aina Cohen Keith Hodgson

## Slide 2: PowerPoint File available:
http://bl831.als.lbl.gov/
~jamesh/powerpoint/
CSHL_raddam_2023.pptx

## Slide 3: Radiation damage

## Slide 4: Radiation damage

## Slide 5: What you need to know:
Limits “data photons”
Caveat for active site
Cannot be outrun
Cannot be prevented
Can be corrected
Can be predicted

## Slide 6: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge (RADDOSE)
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23
Holton JSR 2009

## Slide 7
Holton (2009) J. Synchrotron Rad. 16 133-42
Radiation Damage World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
10/Å global damage Howells et al. (2009)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
4 R-C-COOH Garman et al. (2015)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
~1? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.06 putidaredoxin Corbett et al. (2007)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 8: What if I’m not on the list?
Rule of thumb:
is it a “good leaving group” ?
  Br
  COO-
  S-CH2-
  CH3
  H2

## Slide 9: what the is a MGy?
http://bl831.als.lbl.gov/
damage_rates.pdf
Holton J. M. (2009) J. Synch Rad. 16 133-42
1 MGy = 106 J/kg

## Slide 10
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
home FR-E+ Cu 1.2e9 100 1.5e+05 310 Gy/s 27 h 1.8 h
ALS 2.0.1 MAD 2e12 15x15 8.9e+09 4.5 MGy/s 6.7 s 0.44 s
ALS 4.2.2 MAD 1e12 85x55 2.1e+08 108 kGy/s 4.6 m 18 s
ALS 5.0.1 MONO 3.0e11 100 3.8e+07 19.4 kGy/s 26 m 1.7 m
ALS 5.0.2 MAD 1.5e12 100 1.5e+08 130 kGy/s 3.9 m 15 s
ALS 5.0.3 MONO 5.0e11 100 6.4e+07 32.3 kGy/s 15 m 62 s
ALS 8.2.1 MAD 2e12 100x50 4.0e+08 203 kGy/s 2.5 m 9.9 s
ALS 8.2.2 MAD 6e11 75x40 2.0e+08 101 kGy/s 4.9 m 20 s
ALS 8.3.1 MAD 1.0e12 60x80 2.1e+08 154 kGy/s 3.3 m 13 s
ALS 12.3.1 SAXS 4e13 200? 1.0e+09 707 kGy/s 42 s 2.8 s
SSRL BL6-2 XAFS 2e13 400x150 3.3e+08 241 kGy/s 2.1 m 8.3 s
SSRL BL7-1 MAD 3e10 200 7.5e+05 558 Gy/s 15 h 60 m
SSRL BL7-3 XAS 1e12 20x2 2.5e+10 4.07 MGy/s 7.4 s 0.49 s
SSRL BL9-2 MAD 8e11 200 2.0e+07 9.66 kGy/s 52 m 3.5 m
SSRL BL9-3 EXAFS 2e12 20x300 3.3e+08 469 kGy/s 64 s 4.3 s
SSRL BL12-2 MAD 4.0e12 100x200 2.0e+08 96.6 kGy/s 5.2 m 21 s
SSRL BL11-3 MONO 5e10 200 1.2e+06 582 Gy/s 14 h 57 m
SSRL BL14-1 MAD 2e11 200 5.0e+06 4.32 kGy/s 1.9 h 7.7 m
SSRL BL4-3 XAFS 1e12 20x20 2.5e+09 769 kGy/s 39 s 2.6 s
SSRL BL2-3 EXAFS 1e10 2 2.5e+09 804 kGy/s 37 s 2.5 s
SSRL BL14-3 EXAFS 2e10 5 8.0e+08 6.99 MGy/s 4.3 s 0.29 s
CHESS F1 MONO 3.0e11 100 3.0e+07 14.2 kGy/s 35 m 2.3 m
CHESS F2 MAD 8e11 3x944 2.3e+08 148 kGy/s 3.4 m 14 s
CHESS F3 SAD 4e9 300 4.4e+04 37.8 Gy/s 9.2 d 15 h
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
How long will my crystal last?

## Slide 11
How long will my crystal last?
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
APS 5ID-B POWDER 5e12 1000x300 1.7e+07 8.25 kGy/s 61 m 4 m
APS 8-BM MAD 1e11 200 2.5e+06 858 Gy/s 9.7 h 39 m
APS 14-BM-C MONO 6e11 130x200 2.3e+07 11 kGy/s 46 m 3 m
APS 14-ID-B LAUE 7e13 15x20 2.3e+11 132 MGy/s 0.23 s 0.015 s
APS 17-BM POWDER 8e11 200 2.0e+07 8.72 kGy/s 57 m 3.8 m
APS 17-ID MAD 7e11 200 1.8e+07 9.87 kGy/s 51 m 3.4 m
APS 18-ID SAXS 2e13 50x150 2.7e+09 2.69 MGy/s 11 s 0.74 s
APS 19-BM MAD 6e+08 60x50 2.0e+05 77.3 Gy/s 4.5 d 7.2 h
APS 19-ID MAD 3e+10 100x20 1.5e+07 7.81 kGy/s 64 m 4.3 m
APS 21-ID-D MAD 5e12 50 2.0e+09 1.13 MGy/s 27 s 1.8 s
APS 21-ID-F MONO 1e12 50 4.0e+08 190 kGy/s 2.6 m 11 s
APS 21-ID-G MONO 1e12 50 4.0e+08 190 kGy/s 2.6 m 11 s
APS 22-BM MAD 7e12 40x80 2.2e+09 750 kGy/s 40 s 2.7 s
APS 22-ID MAD 7e12 40x80 2.2e+09 750 kGy/s 40 s 2.7 s
APS 23-BM-B MAD 2e11 200? 5.0e+06 2.47 kGy/s 3.4 h 13 m
APS 23-ID-B MAD 6e12 80x20 3.8e+09 2.11 MGy/s 14 s 0.95 s
APS 23-ID-D MAD 1e13 75x25 5.3e+09 3.01 MGy/s 10 s 0.66 s
APS 24-ID-C MAD 2.5e12 40x60 1.0e+09 357 kGy/s 84 s 5.6 s
APS 24-ID-E MONO 2.85e12 20x120 1.2e+09 563 kGy/s 53 s 3.5 s
APS 31-ID MAD 2.6e12 120x80 2.7e+08 105 kGy/s 4.8 m 19 s
NSLS-II 17-ID-1 MAD 5e12 7x5 1.4e+11 67 MGy/s 0.45 s 0.03 s
NSLS-II 17-ID-2 MAD 2e12 1x1 1.3e+12 626 MGy/s 0.048 s 0.0032 s
NSLS X3A MAD 3.8e10 200 9.5e+05 451 Gy/s 18 h 74 m
NSLS X3B EXAFS 9e11 200x700 6.4e+06 6.48 kGy/s 77 m 5.1 m
NSLS X4A MAD 2e10 300 2.2e+05 136 Gy/s 61 h 4.1 h
NSLS X6A MAD 1.5e12 100x500 3.0e+07 10.3 kGy/s 49 m 3.2 m
NSLS X8C MAD 1.1e10 200? 2.8e+05 204 Gy/s 41 h 2.7 h

## Slide 13
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 14
https://bl831.als.lbl.gov/~jamesh/dose2dose.html

## Slide 15
The number of photons scattered
before crystal is dead
is independent
of flux & time
1 um3 = 105 photons (roomT)
1 um3 = 106 photons (synch)
1 um3 = 108 photons (XFEL)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009
(synch)

## Slide 16: Dose slicing
crystal’s useful life
N
photons
N
photons
N
photons
low
completeness
Can’t process?

## Slide 17: Dose slicing: is that a spot?

## Slide 18: Dose slicing: is that a spot?

## Slide 19: Dose slicing: is that a spot?

## Slide 20: Dose slicing: is that a spot?

## Slide 21: Fine dose slicing

## Slide 22: Coarse dose slicing

## Slide 23
Same number of photons | 
fine | coarse
3.177 | 3.140
Damage correctable | Damage uncorrectable
resolution vs dose slice

## Slide 24: Optimal exposure time:
~1 photon/pixel
PAD detector
Processing with XDS or DIALS

## Slide 25: Where do photons go?
beamstop
Transmitted (98%)
Protein
1A x-rays

## Slide 26: Elastic scattering

## Slide 27: Elastic scattering

## Slide 28: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
Protein
1A x-rays

## Slide 29: Elastic scattering

## Slide 30: Inelastic scattering

## Slide 31: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
Protein
1A x-rays

## Slide 32: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays

## Slide 33: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 34: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 35: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 36: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (~0%)
Absorbed (99%)
Re-emitted (99%)
Absorbed (~0%)

## Slide 37: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
useful/absorbed energy: 7.3%
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (~0%)
Absorbed (99%)
Re-emitted (99%)
Absorbed (~0%)

## Slide 38: Photoelectric absorption

## Slide 39: Photoelectric absorption
e-
+

## Slide 40: Secondary ionization
e-

## Slide 41: Secondary ionization
e-
e-
+

## Slide 42: Excitation
e-

## Slide 43: Excitation
e-

## Slide 44: Excitation
e-

## Slide 45: Excitation

## Slide 46: Electron attachment
e-

## Slide 47: Electron attachment
-

## Slide 48: Sample atoms

## Slide 49: Sample atoms

## Slide 50: Primary ionization
e-
+

## Slide 51: Secondary ionizations
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+

## Slide 52: Ionization track
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 53: Ionization track
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 54: Ionization track

## Slide 55: Ionization track

## Slide 56: Ionization track
3 μm

## Slide 57: Ionization track
Linear Energy Transfer

## Slide 58: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 59: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
neutralization
e-
+

## Slide 60: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
neutralization
e-
+

## Slide 61: initial effects
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
neutralization
neutralization
+

## Slide 62: initial effects
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
attachment
+

## Slide 63: initial effects
e-
e-
e-
e-
-
e-
e-
+
+
+
+
+
+
attachment
+

## Slide 64: initial effects
e-
e-
e-
e-
-
e-
e-
+
+
+
+
+
+
attachment
attachment
+

## Slide 65: initial effects
e-
e-
-
e-
e-
+
+
+
+
+
+
-
-
+

## Slide 66: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 67: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+
solvation

## Slide 68: initial effects
-
e-
+
+
+
+
+
-
-
-
-
solvation
+

## Slide 69: Solvated electron
e-

## Slide 70: Solvated electron
e-

## Slide 73: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 74: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 75: initial effects
-
e-
+
+
+
+
-
-
-
+

## Slide 76: initial effects
-
e-
+
+
-
+

## Slide 77: initial effects
-
e-
+
+

## Slide 78: Excitation transfer

## Slide 79: Excitation transfer
UV photon

## Slide 80: Excitation transfer

## Slide 81: Excitation transfer
Förster transfer
r-6

## Slide 82: Excitation transfer

## Slide 83: t = 0 s

## Slide 84: t ≈ 10-14 s
-
e-
+
+

## Slide 85: Timescales of radiation damage
Garret et. al. (2005) Chem. Rev. 105, 355-389

## Slide 86: Timescales of radiation damage
Garret et. al. (2005) Chem. Rev. 105, 355-389
XFEL
synch
bunch

## Slide 87: Ionization track
Heterogeneous reactions
Homogeneous reactions

## Slide 88: Rough values of energy quanta
1 MeV 100 GJ/mol Medical radiation therapy
100 keV 10 GJ/mol Medical imaging
10 keV 1 GJ/mol X-ray crystallography
1 keV 100 MJ/mol S and P K-edges
100 eV 10 MJ/mol “water window”
10 eV 1 MJ/mol C≡C bond
1 eV 100 kJ/mol C-C bond, visible light
100 meV 10 kJ/mol hydrogen bond
10 meV 1 kJ/mol heat (~300 K)

## Slide 89: Types of radiation damage
Global
Specific

## Slide 90: Types of radiation damage
Global
Specific
  depends on chemistry

## Slide 91: Specific damage
final, refined phases

## Slide 92: Specific damage
experimentally-obtained phases

## Slide 93: Types of radiation damage
Global
Specific
  depends on chemistry
  destroys phasing signal

## Slide 94
Holton, J. M. (2007) J. Synch. Rad. 14, 51-72.

## Slide 95
1.0
0.0
fraction
unconverted
Holton, J. M. (2007) J. Synch. Rad. 14, 51-72.

## Slide 96
Global damage
Howells, et al. (2009) J. Electron Spectrosc. Relat. Phenom. 170, 4-12.

## Slide 97: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12

## Slide 98: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12
10 MGy/Å

## Slide 99: what the is a MGy?
http://bl831.als.lbl.gov/
damage_rates.pdf
Holton J. M. (2009) J. Synchrotron Rad. 16 133-42
1 MGy = 106 J/kg

## Slide 100
Holton (2009) J. Synchrotron Rad. 16 133-42
Radiation Damage World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
10/Å global damage Howells et al. (2009)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
4 R-C-COOH Garman et al. (2015)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
~1? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.06 putidaredoxin Corbett et al. (2007)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 101: Radiation damage

## Slide 102: Xtal5_t1 graph

## Slide 103: How much water are we burning?
Meents et al. (2010) claimed:
"400 molecules of H2 for every 12.5 keV photon“
= 3.3x10-7 mol/J
200 kGy to 100 um3 = 0.24 J
= 1.2x10-8 mol H2
100 um3 of water = 6.7x10-8 mol
→ 18% of water has reacted!

## Slide 104: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 105: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 106
Chart: minimum required crystal size
wavelength dependence of required crystal size
crystal diameter (μm)
Å
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 107: Does wavelength make a difference? not really

## Slide 108
660%
Protective Measure
Holton, J. M. (2007) J. Synch. Rad. 14, 51-72.

## Slide 109: Can radiation damage be prevented?
Yes! By keeping dose low

## Slide 110: Multi-crystal strategies
Kendrew et al. (1960) "Structure of Myoglobin” Nature 185, 422-427.

## Slide 111: Can radiation damage be “outrun”?

## Slide 112: No Damage in the Dark!
Experiment time (hours)
Peak absorbance (electrons)
4.6 5.0 5.4 5.8 6.2 6.6
0 5 10 15 20 25

## Slide 113: Double-tap: no dark progression at 675 kGy/s
Intensity (photons)
Time (seconds)

## Slide 114: Dose-rate dependence of damage
dose rate (kGy/s)
maximum useful dose (MGy)

## Slide 115: Dose-rate effect at Room Temp?
Warkentin M, Badeau R, Hopkins JB, Mulichak AM, Keefe LJ & Thorne RE (2012)."Global radiation damage at 300 and 260 K with dose rates approaching 1 MGy s-1", Acta Cryst. D 68, 124-133.
Owen RL, Axford D, Nettleship JE, Owens RJ, Robinson JI, Morgan AW, Dore AS, Lebon G, Tate CG, Fry EE, Ren J, Stuart DI & Evans G (2012)."Outrunning free radicals in room-temperature macromolecular crystallography", Acta Cryst. D 68, 810-818.

## Slide 116: Damage reversal? No.
https://doi.org/10.1073/pnas.1821522117

## Slide 117: Gaussian beam
50% of flux
the other 50%

## Slide 118: Collimated beam
100% of flux
0%

## Slide 119: Tipping point for µfocus:
10 µm
~10 mm
~1 mrad =0.06°

## Slide 120: Can radiation damage be “outrun”?
not really

## Slide 121: Can radiation damage be corrected?
Yes, if you have enough information

## Slide 122: Zero-dose extrapolation (ZDE)
Diederichs, K. (2006). "Some aspects of quantitative analysis and correction of radiation damage." Acta Cryst. D 62(1): 96-101.

## Slide 123: How to lose information
long exposures
  >1 photon/image = order of arrivals
Wide phi slice
  sum over angle
Large beams
  sum over area
Pink/divergent beam
  sum over lambda/angle
Background
  non-crystal stuff
Systematics
  Dose contrast

## Slide 124: The Entropy Limit
= log2(Npixels) * flux * tsample * 1.2x10-5
minimum data rate with no information loss
Npixels = 4150*4371 for Eiger
flux = photons/s onto the sample
tsample = sample thickness in µm
1.2x10-5 = 10-4 cm/µm * cross section of oxygen (0.2 cm2/g)
* density of protein crystal (1.2 g/cm3 )
* ~1/2 of total scattering intersects detector
E.G. 34 GByte/s for 1013 photons/s and 100 µm thick
bits
s

## Slide 125: Optimal exposure time
Dose of dataset (MGy) <= half-reaction point

## Slide 126: Types of radiation damage
Global
  scale factor
  B factor
  non-isomorphism
Specific
  depends on chemistry
  destroys phasing signal

## Slide 127: Types of radiation damage
Global
  scale factor
  B factor
  non-isomorphism
Specific
  depends on chemistry
  destroys phasing signal

## Slide 128: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.

## Slide 129: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.
Riso ≈ 0.7 %/MGy

## Slide 130
anomalous signal
Crick, F. H. C. & Magdoff, B. S. (1956) Acta Crystallogr. 9, 901-908.
Hendrickson, W. A. & Teeter, M. M. (1981) Nature 290, 107-113.
# sites
MW (Da)
ΔF
F
≈ 1.2 f”
√
World record!
ΔF/F = 0.5%
Wang, Dauter & Dauter (2006) Acta Cryst. D 62, 1475-1483.

## Slide 131: Optimal exposure time
Dose of dataset (MGy)
<=
anomalous signal (%)

## Slide 132: Radiation Damage
Know your dose! (MGy)
Avoid World Records
disorder dominates everything
“Attenu-wait”: dose slicing
Stay hydrated!
http://bl831.als.lbl.gov/xtalsize.html
http://bl831.als.lbl.gov/xtallife.html
http://bl831.als.lbl.gov/~jamesh/powerpoint/Rapidata_raddam_2023.pptx

## Slide 133: Radiation Damage
Know your dose! (MGy)
Avoid World Records
Keep your atoms light
“Attenu-wait”: fine dose slicing
Keep on spinning

## Slide 134: … but does it work for membrane proteins?
Efremov, R. G. & Sazanov, L. A. (2011)."Structure of the membrane domain of respiratory complex I", Nature 476, 414-420.
“To improve diffraction properties, crystals were slowly cooled to 4 C, placed into micro-dialysis buttons, and mother liquor was exchanged by dialysis for 0.1 M sodium acetate (pH 4.8), 0.15 M sodium tartrate (pH 5.0), 30% PEG4000, 0.1% sodium cholate and 12.5% glycerol over a period of 5 days.”
CCP4BB:
“We used it for a large membrane protein complex and diffraction improved from ~7 to 2.7 A. The crystal is fished out and put into mother liquor solution in the button, sealed with dialysis membrane and the button is then placed into about 5 mls of mother liquor with slightly higher PEG concentration. Then you just exchange outside buffer every day or so for solutions containing higher concentrations of PEG. We went from ~9 to 30 % PEG4000 in about a week. You can easily observe crystal under microscope and if it cracks - you went too far/too quickly with PEG and need to use a bit less next time. Also, this method allows you to control all other components of the dehydrating solution - we needed to decrease salt concentration at the same time as increasing PEG. You can also introduce/increase cryo-protectant concentration at the same time. With these crystals, otherwise excellent dehydration machines already mentioned did not work, possibly because the process had to be really slow.”