## Slide 1: The Future of Structural Biology
NGLS is dead
ALS 2?
  Much smaller beams
  Need optics upgrades
  New kind of sample handling?
at the ALS

## Slide 2
Beamline | 8.3.1 |  | 12.3.1 | 
Lattice | New | Old | New | Old
Horiz FWHM (μm) | 60 | 137 | 59 | 121
Vert FWHM (μm) | 176 | 183 | 105 | 109
Flux (1011 Ph/s) | 3.0 | 2.1 | 3.2 | 2.0
Flicker (%/√Hz) | 0.37 | 0.66 | n/d | 0.37
aperture | 100 μm round |  | 100 μm square | 
Unattenuated No aperture |  |  |  | 
120 μm Cu |  |  |  | 
apertures open to 400 μm
11.1 keV, convergence slits “wide” (3 x 0.3 mRad), pixel = 0.83 μm, FWHM from knife edge
June 2013 ALS emittance upgrade

## Slide 3: Knife edge scans
3 mm
curve fit to integral
add residual to differentiated curve
¼” tungsten carbide ball

## Slide 4: 8.3.1 12.3.1

## Slide 5: ALS 8.3.1 optics
ADSC Quantum 315r
Superbend
Pt & Rh
on invar
Plane
Parabolic
M1 mirror
Pt & Rh
on Si
Torroidal
M2 mirror
two flat
Si(111)
monochromator
Protein Crystal
100 μm
aperture
Scatter
guard
convergence
angle slits
MacDowell et. al. (2004) J. Sync. Rad. 11 447-455
Notes: 5
Most notable acheivements are high brightness with very little “wasted” light. The discovery made by Howard Padmore? At ALS showed that a 2:1 demagnification cancels nearly all of the spherical abberations in the parabolic/torroid system. 30-50% of the total x-ray intensity passes through the 100um pinhole. The flux through the 100um pinhole at the superbend beamlines is comparable to that of the 5.0.2 wiggler or an APS bending magnet, but only 150 Watts of power must be dissipated by the beamline optics. In contrast, wiggler beamlines must disipate kilowatts. The optics here are much simpler and not exotic in any way. The system is stable and robust. There is never a need to re-focus the beam at a new wavelength. Only a 2-minute automatic tuneup is recommended for very large energy changes (more than 1-2 keV).

## Slide 6: ALS 12.3.1 optics
ADSC Quantum 315r
Superbend
Pt & Rh
on invar
Plane
Parabolic
M1 mirror
Pt & Rh
on Si
Torroidal
M2 mirror
two flat
Si(111)
monochromator
Protein Crystal
100 μm
aperture
Scatter
guard
convergence
angle slits
MacDowell et. al. (2004) J. Sync. Rad. 11 447-455
Notes: 6
Most notable acheivements are high brightness with very little “wasted” light. The discovery made by Howard Padmore? At ALS showed that a 2:1 demagnification cancels nearly all of the spherical abberations in the parabolic/torroid system. 30-50% of the total x-ray intensity passes through the 100um pinhole. The flux through the 100um pinhole at the superbend beamlines is comparable to that of the 5.0.2 wiggler or an APS bending magnet, but only 150 Watts of power must be dissipated by the beamline optics. In contrast, wiggler beamlines must disipate kilowatts. The optics here are much simpler and not exotic in any way. The system is stable and robust. There is never a need to re-focus the beam at a new wavelength. Only a 2-minute automatic tuneup is recommended for very large energy changes (more than 1-2 keV).

## Slide 7: Carbon on mono xtal

## Slide 8: Carbon on mono xtal

## Slide 9: Cleaning mono xtal
Relative intensity

## Slide 10: Cleaning mono xtal
500 μm Si
~10 μm C

## Slide 11: Silicon photodiode (111)
Tilt angle (arc seconds)
Relative intensity

## Slide 12: Silicon ground w 5 um
Tilt angle (arc seconds)
Relative intensity

## Slide 13: Silicon ground w 5 um
Tilt angle (arc seconds)
Relative intensity

## Slide 14: Silicon NaOH etch 2 days
Tilt angle (arc seconds)
Relative intensity

## Slide 15: Silicon NaOH etch 2 hours
Tilt angle (arc seconds)
Relative intensity

## Slide 16: ALS 2 in a nutshell
100 μm
10 μm
48 min
30 sec

## Slide 17: Dose-rate dependence of damage
dose rate (kGy/s)
maximum useful dose (MGy)
8.3.1
12.3.1

## Slide 18: Si(111) vs multilayers
0.014%
Si(111)
1%
multilayer
4 Å
1.9 Å
resolution
spectral
dispersion

## Slide 19: Wide-bandpass MX?
Mono | Si(111) | multilayer | Difference (%) | good
Energy (eV) | 11111 | 12027.5 | +8.2 | Same
Scale | 1.0000 | 1.0964 | +9.6 | Yes
Rmerge (%) | 7.5 | 8.4 | +12 | No
Ranom (%) | 5.6 | 5.5 | -1.8 | Same
I/sd | 13.2 | 12.3 | -6.8 | Same
I/sd (1.5Å) | 2.3 | 1.8 | -21.7 | No
Ano Patt | 5.96 | 4.75 | -20.3 | Same
Ano Phased | 41 | 39.33 | -4.1 | Same
FOM | 0.238 | 0.192 | -19.3 | Same
CC | 0.555 | 0.647 | -6.1 | Yes
Rcryst (%) | 26.70 | 26.48 | -0.2 | Same
Ligand peak | 8.213 | 8.250 | +0.4 | Same

## Slide 20: Adjustable bandpass
Si(111)
Si(111)
Existing mono
Ge(11 1 1)
Ge(11 1 1)
3 mm
16.26°
d = 0.51 Å
2θ = 147.478°
For 12660 eV
6 mm
0.0007 % (8 hours)

## Slide 21: Adjustable bandpass
Si(111)
Si(111)
Existing mono
3 mm
Ge(11 1 1)
Ge(11 1 1)
0.014 % (30 min)

## Slide 22: Adjustable bandpass
ML
ML
Existing mono
3 mm
Ge(11 1 1)
Ge(11 1 1)
1 % (~1 second)

## Slide 23: Adjustable bandpass
Existing mono
Ge(11 1 1)
Ge(11 1 1)
3 mm
16.26°
d = 0.51 Å
2θ = 147.478°
For 12660 eV
6 mm
ML
ML
0.0007 % (8 hours)

## Slide 24: Measuring bandpass
Si(111)
Si(111)
~32.5°
d = 0.51 Å
2θ = 147.478°
For 12660 eV
PIN diode
vertical
divergence
< 5 arcsec
(24 μRad)
15 μm
pinhole
Ge(11 1 1)
Chart: Photon energy (eV)

## Slide 25: Measuring bandpass
~32.5°
d = 0.51 Å
2θ = 147.478°
For 12660 eV
PIN diode
vertical
divergence
< 5 arcsec
(24 μRad)
15 μm
pinhole
Ge(11 1 1)
Chart: Photon energy (eV)
Si(333)
Si(333)
Al
absorber

## Slide 26: Measuring bandpass
Vortex
Chart: Photon energy (eV)
Se
vertical
divergence
< 5 arcsec
(24 μRad)
15 μm
pinhole
Si(333)
Si(333)
Al
absorber

## Slide 27: Bandpass vs anomalous signal?
Chart: Photon energy (eV)
| 12656 | 12657 | 12658 | 12658.1 | 12658.2 | 12658.6 | 12658.9 | 12659 | 12659.1 | 12659.2 | 12659.3 | 12659.4 | 12659.6 | 12659.7 | 12659.9 | 12660.4 | 12660.5 | 12660.6 | 12661 | 12656 | 12657 | 12658 | 12658.1 | 12658.2 | 12658.6 | 12658.9 | 12659 | 12659.1 | 12659.2 | 12659.3 | 12659.4 | 12659.6 | 12659.7 | 12659.9 | 12660.4 | 12660.5 | 12660.6 | 12661
I(+) | 159900 | 171800 | 190300 | 193800 | 195000 | 228800 | 232700 | 240200 | 253200 | 241400 | 260200 | 267800 | 243300 | 256400 | 251000 | 260200 | 233100 | 234600 | 247000
I(-) | 131500 | 100900 | 81560 | 76100 | 83960 | 69860 | 50120 | 60980 | 74270 | 66830 | 85140 | 76810 | 82330 | 69980 | 103800 | 106000 | 89630 | 108800 | 110400
vertical
divergence
(240 μRad)
100 μm
pinhole
Si(333)
Si(333)
Al
absorber
1rb5

## Slide 28: The Future of Structural Biology
Problem:
XFELs cannot solve the “resolution problem”
overfitting
non-isomorphism
radiation damage
small & fast = noisy
What can we do?
4D modelling
probe weak density
more accurate data
humidity control during growth

## Slide 29: Minimum exposure time
Exposure time (ms)
Overall I/σ(I)
Same dose
for each
data set

## Slide 30: Beam Flicker
time (seconds)
normalized flux

## Slide 31: Beam Flicker
time (seconds)
normalized flux
pinhole
removed

## Slide 32
Steel pipe
Surgical tubing
Memory foam
Normal tubing
Swagelock?
Acrylic
Pie wedges

## Slide 33: The Future of Structural Biology
10 Å

## Slide 34: What is the structure of “disorder” ?
a grand challenge for structural biology in the 21st century

## Slide 35: Anything is possible … with the right tools.

## Slide 36: Big Question:
When a horse gallops, is there ever a moment where all four hooves leave the ground?
AD 1872

## Slide 37: Muybridge’s multi-camera

## Slide 38: Muybridge’s galloping horse (1878)

## Slide 39: not enough signal

## Slide 40: brighter light

## Slide 41: even brighter

## Slide 42: very bright light

## Slide 43: a “crystal” of horses

## Slide 44: realistic “crystal” of horses

## Slide 45: average structure: galloping horse

## Slide 46: average structure: 1-sigma contour

## Slide 47: 21st Century Big Question: how do biomolecules work?
Beernink, Endrizzi, Alber & Schachman (1999). PNAS USA 96, 5388-5393.

## Slide 48: Averaging destroys resolution
10 Å

## Slide 49: Promise of Single-molecule Imaging
R. Neutze et al., Nature 406, pp. 752-757 (2000)

## Slide 50: lysozyme: real and reciprocal

## Slide 51: lysozyme: thermal motion
RMS displacement from B factors

## Slide 52: The Future of Structural Biology
Problem:
XFELs cannot solve the “resolution problem”
What can we do?
modelling

## Slide 53: Muybridge’s galloping horse (1878)
Real space
reciprocal
“Time-resolved” diffraction

## Slide 54: Muybridge’s galloping horse (1878)
Real space
reciprocal
Diffract and Destroy

## Slide 55: Muybridge’s galloping horse (1878)
Real space
reciprocal
Average electron density

## Slide 56: Muybridge’s galloping horse (1878)
Real space
reciprocal
Sum(intensity) – Sum(density) = diffuse scatter

## Slide 57: Muybridge’s galloping horse (1878)
Real space
reciprocal
Fincoh – Fcoherent with density phases

## Slide 58: Muybridge’s galloping horse (1878)
Real space
reciprocal
RMS variation in density

## Slide 59: Supporting a model with data

## Slide 60: That’ll be in 20 years What can we do now?

## Slide 61: Molecular Dynamics Simulation
1aho
Scorpion toxin
0.96 Å resolution
64 residues
Solvent: H20 + acetate
Cerutti et al. (2010).J. Phys. Chem. B 114, 12811-12824.
using real
crystal’s lattice

## Slide 62: 30 conformers from 24,000

## Slide 63: Electron density from 24,000 conformers

## Slide 64: Electron density from 24,000 conformers

## Slide 65: Molecular Dynamics vs Observation
Fsim
Fcalc
Rcryst= 0.137
refined_vs_Fsim.pdb
1aho 64-residue scorpion toxin in water to 1.0 Å resolution

## Slide 66: Molecular Dynamics vs Observation
Fobs
1aho.cif
1aho.pdb
Fsim
Fcalc
Fcalc
Rcryst= 0.137
Rcryst= 0.116
Rfree = 0.69
refined_vs_Fsim.pdb
LSQ rmsd = 0.43Å
rmsd = 1.05 Å
1aho 64-residue scorpion toxin in water to 1.0 Å resolution
Rfree = 0.48 to 4 Å
Rfree =

## Slide 67: Molecular Dynamics vs Observation
RMSD
1.05 Å

## Slide 68: Molecular Dynamics vs Observation
RMSD
0.45 Å
aligned

## Slide 69: Molecular Dynamics vs Observation
Sodium acetate trihydrate
5 atoms
3 waters
0.9 Å resolution
C2/c
Rvault = 0.03

## Slide 70: Molecular Dynamics vs Observation
fav8
8 residues
4 waters
1.0 Å resolution
P1

## Slide 71: Molecular Dynamics vs Observation
Fobs
fav8.fcf
fav8.cif
Fsim
Fcalc
Fcalc
Rcryst= 0.13
Rcryst= 0.16
Rfree= 0.23
refined_vs_Fsim.pdb
LSQ rmsd = 0.091Å & 0.15 Å
rmsd = 0.20 Å
“fav8” 8-residue aromatic peptide with 4 waters to 1.0 Å resolution
R1 = 0.041
With 4σ cutoff!
Rfree = 0.20 to 2Å

## Slide 72: MD-predicted water structure
Simulated
density
Janowski et al (2013) JACS 135, 7938-7948

## Slide 73: MD-predicted water structure
Simulated
density
2mFo-DFc
Janowski et al (2013) JACS 135, 7938-7948

## Slide 74: MD-predicted Val rotamer
Janowski et al (2013) JACS 135, 7938-7948

## Slide 75: MD-predicted Val rotamer
confs | Rwork | Rfree
one | 4.11% | 5.84%
A & B | 3.89% | 5.53%
Janowski et al (2013) JACS 135, 7938-7948

## Slide 76: The Future of Structural Biology
Problem:
XFELs cannot solve the “resolution problem”
What can we do?
modelling
probe weak density

## Slide 77: average structure: 1-sigma contour

## Slide 78: Disorder is not “noise”

## Slide 79: Ringer: systematic map sampling
Lang et al. (2010) Protein Sci. 19, 1420-31.
Fraser, et al. (2009) Nature 462, 669-73.

## Slide 80: Ringer: systematic map sampling
electron density (e-/Å3)
χ1 angle (degrees)

## Slide 81: Ringer: systematic map sampling
electron density (e-/Å3)
χ1 angle (degrees)

## Slide 82: Ringer: systematic map sampling
electron density (e-/Å3)
χ1 angle (degrees)

## Slide 83: Ringer: systematic map sampling
electron density (e-/Å3)
χ1 angle (degrees)

## Slide 84: Independent estimates of F000
--
PDB | Method | F000 | diff
3DKE | Matthews et. al. (2008) | 121700 | +6.7%
 | END map estimate | 130500 | 
2NVH | Matthews et. al. (2006) | 92800 | +3.0%
 | END map estimate | 95656 | 
1AHO | Cerutti et. al. (2010) | 23177 | -5.0%
 | END map estimate | 22020 | 
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 85: Ringer: systematic map sampling
electron density (e-/Å3)
χ1 angle (degrees)

## Slide 86: Ringer: systematic map sampling
electron density (e-/Å3)
χ1 angle (degrees)

## Slide 87: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 88: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 89: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 90: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 91: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 92: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 93: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 94: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 95: "error bar" for electron density
fractional coordinate
electron density (e-/Å3)
Refinement
Against
Perturbed
Input
Data
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 96: How does the “error” compare to “sigma”?
Electron Number Density (e-/Å3)
normalized counts
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 97: How does the “error” compare to “sigma”?
Electron Number Density (e-/Å3)
normalized counts
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 98: 1 “sigma” is not a good criterion
Electron Number Density (e-/Å3)
normalized counts
Lang et al. (2014) PNAS USA 111, 237-242.

## Slide 99: Molecular Dynamics Simulation
1aho
Scorpion toxin
0.96 Å resolution
64 residues
Solvent: H20 + acetate
Cerutti et al. (2010).J. Phys. Chem. B 114, 12811-12824.
using real
crystal’s lattice

## Slide 100: MLFSOM simulation

## Slide 101: Electron density from 24,000 conformers

## Slide 102: 2Fsim-Fcalc and Fsim-Fcalc maps
1.0 Å data
Rcryst= 0.137
Rfree = 0.159
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc

## Slide 103: 2Fsim-Fcalc and (Fsim Φsim) - (Fcalc Φcalc) maps
1 “sigma” 2Fsim-Fc
Fright – (2Fsim-Fc)
1.0 Å data
Rcryst= 0.137
Rfree = 0.159

## Slide 104: Regular model with real data!
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc
1.0 Å data
Rcryst= 0.116
Rfree = 0.135

## Slide 105: How many conformers are there?

## Slide 106: How many conformers are there?
40 explain density to 3% error

## Slide 107: How many conformers are there?
8 explain density to 3% error

## Slide 108: The Future of Structural Biology
Problem:
XFELs cannot solve the “resolution problem”
overfitting
What can we do?
4D modelling
probe weak density
more accurate data

## Slide 109: 100% SeMet incorporation
Trivial to solve

## Slide 110: 100% S -Met incorporation
Impossible to solve

## Slide 111: Model building performance
fraction Sulfur
correlation coefficient

## Slide 112: Model building performance
fraction Sulfur
correlation coefficient

## Slide 113
29% Se 71% S

## Slide 114
28% Se 72% S

## Slide 115: ARP/wARP performance
fraction Sulfur
correlation coefficient

## Slide 116
21% Se 79% S

## Slide 117: ARP/wARP performance
fraction Sulfur
correlation coefficient

## Slide 118: ARP/wARP performance
fraction Sulfur
correlation coefficient

## Slide 119
11% Se 89% S

## Slide 120: Finding sites
fraction Sulfur
Number of correct sites

## Slide 121: Finding sites
fraction Sulfur
Number of correct sites

## Slide 122: Finding sites
fraction Sulfur
Number of correct sites

## Slide 123: Finding sites
fraction Sulfur
Number of correct sites
25
20
15
10
5
0
peak height ()

## Slide 124: Finding sites
fraction Sulfur
Number of correct sites

## Slide 125: Finding sites
fraction Sulfur
Number of correct sites

## Slide 126: MR simulation
Rmsd from perfect search model (Å)
corrupted model
Correlation coefficient to correct density

## Slide 127: signal vs noise
“If you don’t have good data, then you have no data at all.”
-Sung-Hou Kim

## Slide 128: signal vs noise
easy
hard
impossible

## Slide 129: signal vs noise
easy
hard
impossible
threshold of “solvability”

## Slide 130: signal vs noise
“If you don’t have good data, then you must learn statistics.”
-James Holton

## Slide 131: Adding noise

## Slide 132: Adding noise
12 + 12 = 1.42

## Slide 133: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 134: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 135: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 136: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
102 + 12 = 10.052

## Slide 137: Optimal exposure time (faint spots)
thr Optimal exposure time for data set (s)
tref exposure time of reference image (s)
bgref background level near weak spots on
reference image (ADU)
bg0 ADC offset of detector (ADU)
bghr optimal background level (via thr)
σ0 rms read-out noise (ADU)
gain ADU/photon
m multiplicity of data set (including partials)
adjust exposure
so this is ~100

## Slide 138
RESOLUTION COMPLETENESS R-FACTOR I/SIGMA R-meas CC(1/2) Anomal SigAno Nano
LIMIT OF DATA observed Corr
9.17 99.1% 3.9% 257.47 3.9% 100.0* 91* 5.024 450
6.49 100.0% 5.2% 214.33 5.2% 100.0* 86* 3.836 882
5.30 100.0% 7.2% 165.13 7.2% 100.0* 76* 3.257 1175
4.59 100.0% 7.2% 175.42 7.3% 100.0* 67* 2.589 1403
4.10 99.9% 7.7% 174.13 7.7% 100.0* 59* 2.264 1594
3.74 99.9% 9.4% 143.09 9.4% 100.0* 49* 1.953 1783
3.47 100.0% 11.2% 120.17 11.2% 100.0* 39* 1.696 1942
3.24 100.0% 14.1% 91.14 14.1% 100.0* 30* 1.333 2103
3.06 99.9% 19.5% 65.79 19.5% 100.0* 23* 1.117 2214
2.90 99.9% 29.0% 44.85 29.1% 99.9* 17* 1.008 2369
2.77 99.9% 40.5% 32.58 40.6% 99.8* 11* 0.901 2493
2.65 99.9% 52.8% 25.16 52.9% 99.8* 10* 0.866 2605
2.54 100.0% 67.4% 19.47 67.6% 99.6* 2 0.804 2705
2.45 100.0% 88.9% 14.58 89.2% 99.2* 4 0.831 2859
2.37 100.0% 109.3% 9.97 109.7% 98.1* 5 0.829 2925
2.29 100.0% 138.2% 6.87 138.9% 96.1* 1 0.760 3037
2.22 100.0% 197.1% 4.03 198.6% 83.5* -1 0.721 3159
2.16 100.0% 227.3% 2.41 230.8% 46.9* -1 0.677 3224
2.10 61.2% 154.4% 1.28 163.6% 47.0* -2 0.660 1999
2.05 47.9% 170.1% 0.68 196.5% 25.7* 3 0.629 1578
total 93.3% 15.7% 54.30 15.8% 100.0* 12* 1.217 42499
140-fold multiplicity: 16 crystals, 360° each, inverse beam, 7235 eV

## Slide 139: 140-fold multiplicity
8.2σ = Mg?
DELFAN residual anomalous difference
data Courtesy of Tom Peat & Janet Newman

## Slide 140: Discerning Na+ from Mg++
f’’ (electrons)
DELFAN peak height (σ)
Mg
Ne
Na
F
O
N

## Slide 141: 140-fold multiplicity
7.4σ = Na
DELFAN residual anomalous difference
data Courtesy of Tom Peat & Janet Newman

## Slide 142: Detector calibration: 7247 eV
target:
oil
distance:
900 mm
2θ: 12°

## Slide 143: Detector calibration: 7235 eV
target:
oil
distance:
900 mm
2θ: 12°

## Slide 144: Detector calibration: ALS 8.3.1

## Slide 145: Detector calibration errors: detector 2

## Slide 146: Detector calibration errors: detector 3

## Slide 147: Detector calibration errors
Dan Schuette PhD Thesis (2008) Fig 6.22 page 198, Gruner Lab, Cornell University.
Pixel arrays are not immune!

## Slide 148: Detector calibration
photon energy (keV)
calibration error (%)
good!
good!
bad!

## Slide 149
7247 eV

## Slide 150
7235 eV

## Slide 151: Detector calibration
7223 eV

## Slide 152
Great! We have lots of crystals
but we have a problem with
non-isomorphism

## Slide 153
Dear James
The story of the two forms of lysozyme crystals goes back to about 1964 when it was found that the diffraction patterns from different crystals could be placed in one of two classes depending on their intensities. This discovery was a big set back at the time and I can remember a lecture title being changed from the 'The structure of lysozyme' to 'The structure of lysozyme two steps forward and one step back'. Thereafter the crystals were screened based on intensities of the (11,11,l) rows to distinguish them (e.g. 11,11,4 > 11,11,5 in one form and vice versa in another). Data were collected only for those that fulfilled the Type II criteria. (These reflections were easy to measure on the linear diffractometer because crystals were mounted to rotate about the diagonal axis). As I recall both Type I and Type II could be found in the same crystallisation batch . Although sometimes the external morphology allowed recognition this was not infallible.
The structure was based on Type II crystals. Later a graduate student Helen Handoll examined Type I. The work, which was in the early days and before refinement programmes, seemed to suggest that the differences lay in the arrangement of water or chloride molecules (Lysozyme was crystallised from NaCl). But the work was never written up. Keith Wilson at one stage was following this up as lysozyme was being used to test data collection strategies but I do not know the outcome.
An account of this is given in International Table Volume F (Rossmann and Arnold edited 2001) p760.
Tony North was much involved in sorting this out and if you wanted more info he would be the person to contact. I hope this is helpful. Do let me know if you need more.
Best wishes
Louise
Non-isomorphism in lysozyme

## Slide 154
Johnson’s ratio
Structure factor (e-)
Non-isomorphism in lysozyme

## Slide 155
Johnson’s ratio
Structure factor (e-)
Non-isomorphism in lysozyme

## Slide 157
Dear James
The story of the two forms of lysozyme crystals goes back to about 1964 when it was found that the diffraction patterns from different crystals could be placed in one of two classes depending on their intensities. This discovery was a big set back at the time and I can remember a lecture title being changed from the 'The structure of lysozyme' to 'The structure of lysozyme two steps forward and one step back'. Thereafter the crystals were screened based on intensities of the (11,11,l) rows to distinguish them (e.g. 11,11,4 > 11,11,5 in one form and vice versa in another). Data were collected only for those that fulfilled the Type II criteria. (These reflections were easy to measure on the linear diffractometer because crystals were mounted to rotate about the diagonal axis). As I recall both Type I and Type II could be found in the same crystallisation batch . Although sometimes the external morphology allowed recognition this was not infallible.
The structure was based on Type II crystals. Later a graduate student Helen Handoll examined Type I. The work, which was in the early days and before refinement programmes, seemed to suggest that the differences lay in the arrangement of water or chloride molecules (Lysozyme was crystallised from NaCl). But the work was never written up. Keith Wilson at one stage was following this up as lysozyme was being used to test data collection strategies but I do not know the outcome.
An account of this is given in International Table Volume F (Rossmann and Arnold edited 2001) p760.
Tony North was much involved in sorting this out and if you wanted more info he would be the person to contact. I hope this is helpful. Do let me know if you need more.
Best wishes
Louise
Non-isomorphism in lysozyme

## Slide 158: Non-isomorphism in lysozyme
RH 84.2% vs 71.9%
Riso = 44.5%
RMSD = 0.18 Å

## Slide 159: Non-isomorphism = dehydration?
= 1 nL
100 μm

## Slide 160: Elastic deformation = non-isomorphism

## Slide 161: Elastic deformation = non-isomorphism

## Slide 162: Plastic deformation = poor diffraction

## Slide 163: Plastic deformation = poor diffraction

## Slide 164: The Future of Structural Biology
Problem:
XFELs cannot solve the “resolution problem”
overfitting
non-isomorphism
radiation damage
What can we do?
4D modelling
probe weak density
more accurate data
humidity control during growth

## Slide 165: The Future of Structural Biology
Will be noisy
Averaging destroys resolution
Multi-crystal data – isomorphism
structures of the future must be 4D
There is “life” below 1 σ

## Slide 166: The Future of Structural Biology
Multi-crystal data sets
There is “life” below 1 σ
Averaging destroys resolution
structures of the future must be 4D

## Slide 167: 100 fs damage “threshold”
Lomb et al. (2011) Phys Rev B 84, 214111

## Slide 168: Single-molecule imaging result
200 nm
Resolution ~2 mm
2.5 eV 0.1 s Michelin P255/70R18 LTX A/S 112T BSW
to what
resolution
is this
interesting?
Notes: what limits single-particle resolution ?
get 100 times more photons/shot if correctly focussed beam
get 100 times more with submicron beam focus on CXI chamber
Problem – scattering goes from N^2 to N (Wilson statistics).
So use a-priori information – modelling Axel Brummer
Make beam smaller than jet to elliminate streak
168

## Slide 169: Snapshot from single virus particle
TEM
2 keV LCLS 200 fs Mimi virus single-shot.
200 nm
Reconstructed image
Resolution 20nm
Seibert, et al. (2011). Nature 470, 78-81.
Notes: what limits single-particle resolution ?
get 100 times more photons/shot if correctly focussed beam
get 100 times more with submicron beam focus on CXI chamber
Problem – scattering goes from N^2 to N (Wilson statistics).
So use a-priori information – modelling Axel Brummer
Make beam smaller than jet to elliminate streak
169