## Slide 1: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1 creator: Tom Alber
UC Multicampus Research Programs and Initiatives (MRPI)
UCSF Program for Breakthrough Biomedical Research (PBBR)
one-time NIH-DOE Inter-agency agreement (IAA)
Integrated Diffraction Analysis Technologies (IDAT)
Plexxikon, Inc.
M D Anderson CRC
Synchrotron Radiation Structural Biology Resource (SLAC)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser Aina Cohen Ana Gonzalez
Axel Brunger Monarin Uervirojnangkoorn Artem Lyubimov Nick Sauter

## Slide 2: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1 creator: Tom Alber
UC Multicampus Research Programs and Initiatives (MRPI)
UCSF Program for Breakthrough Biomedical Research (PBBR)
one-time NIH-DOE Inter-agency agreement (IAA)
Integrated Diffraction Analysis Technologies (IDAT)
Plexxikon, Inc.
M D Anderson CRC
Synchrotron Radiation Structural Biology Resource (SLAC)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser Aina Cohen Ana Gonzalez
Axel Brunger Monarin Uervirojnangkoorn Artem Lyubimov Nick Sauter

## Slide 3: Systematic Error vs Random Noise

## Slide 4: Is it Real? Or is it MLFSOM
simulated
real
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 5
Source of error | realistic simulation | No SHSSS | Perfect detector
Photon counting | + | + | +
Shutter jitter | + | + | -
Beam flicker | + | + | -
Sample absorption | + | + | -
Radiation damage | + | + | -
Imperfect spindle | + | + | -
vignette | + | + | -
Corner correction | + | + | -
SHSSS | + | - | -
Rmeas (∞-10 Å) | 2.8% | 0.7% | 0.7%
I/σ asymptotic | 26.8 | 74.2 | 81.0
Sources of error
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 6
Spot centroid position (pixels)
Relative spot intensity
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 7
Spot centroid position (pixels)
Relative spot intensity
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 8
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel
Pilatus: subtract smooth baseline

## Slide 9
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 10
down
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 11
down
up
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 12
down
up
Rseparate
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 13
odd
even
Rmixed
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 14
separate:
2.5%
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 15
separate:
mixed:
2.5%
0.9%
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 16
separate:
mixed:
2.5%
0.9%
2.5%2-0.9%2 = 2.3%2
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 17
Required signal-to-noise (I/σ)
Solve-able proteins (%)
Current
technology
Goal
Threshold of a revolution in phasing

## Slide 18: What if…
we knew everything?
  how would we store it?
we had a hotter beam?
we had more coherence?
we had a perfect detector?
…
we knew what we are doing wrong?

## Slide 19: Diffraction Simulators
1. MLFSOM
- rotation data with maximum realism in noise
2. nearBragg
- first-principles scattering from atoms in space
3. nanoBragg
- optimized for nanocrystal/single-particle stills
4. nonBragg
- non-crystalline, centrosymmetric (SAXS)

## Slide 20: nearBragg program
http://bl831.als.lbl.gov/~jamesh/nearBragg/
“assumption-free” total scattering
no Fourier Transform
no unit cells
no “mosaicity”
arbitrary “atoms”
arbitrary “source”
coherent or not

## Slide 23: Meaning of “coherence length”
http://bl831.als.lbl.gov/~jamesh/nearBragg/collision/

## Slide 24: Meaning of “coherence length”
http://bl831.als.lbl.gov/~jamesh/nearBragg/collision/

## Slide 25: Meaning of “coherence length”
http://bl831.als.lbl.gov/~jamesh/nearBragg/collision/

## Slide 26: Meaning of “coherence length”
http://bl831.als.lbl.gov/~jamesh/nearBragg/collision/

## Slide 27
Meaning of “Molecular Transform”
False color intensity
sample
detector

## Slide 28
Definition of unit cell defines DS
False color intensity
sample
detector

## Slide 29
Definition of unit cell defines MT
False color intensity
sample
detector

## Slide 30
Definition of unit cell defines MT
False color intensity
sample
detector

## Slide 31: How to install: nearBragg
wget http://bl831.als.lbl.gov/
~jamesh/nearBragg/nearBragg.c
gcc –o nearBragg nearBragg.c –lm
./nearBragg
usage: nearBragg -file atom_list.txt
options:
-file filename.txt text file containing point scatterer coordinates in Angstrom relative to the origin.
-distance from origin to detector center in mm
-detsize detector size in mm. may also use -detsize_x -detsize_y
-detpixels detector size in pixels. may also use -detpixels_x -detpixels_y
-pixel detector pixel size in mm.

## Slide 32: How to run: nearBragg for single particle
egrep “^ATOM|^HETAT” lysozyme.pdb |\
awk ‘{print substr($0,31,36)}’ |\
cat >! atoms.txt
wget bl831.als.lbl.gov/~jamesh/nearBragg/rotate.awk
./rotate.awk -v phix=10 -v phiy=20 -v phiz=30 atoms.txt >! rotated.txt
nearBragg –atoms rotated.txt -lambda 1 -distance 1000 -detsize 100 -fluence 1e32
(200s)
adxv intimage.img

## Slide 33: How to run: nearBragg for single particle
egrep “^ATOM|^HETAT” lysozyme.pdb |\
awk ‘{print substr($0,31,36)}’ |\
cat >! atoms.txt
wget bl831.als.lbl.gov/~jamesh/nearBragg/rotate.awk
./rotate.awk -v phix=10 -v phiy=20 -v phiz=30 atoms.txt >! rotated.txt
nearBragg –atoms rotated.txt -lambda 1 -distance 1000 -detsize 100 -fluence 1e32
(200s)
adxv intimage.img

## Slide 34: How to run: nearBragg for single particle
egrep “^ATOM|^HETAT” lysozyme.pdb |\
awk ‘{print substr($0,31,36)}’ |\
cat >! atoms.txt
wget bl831.als.lbl.gov/~jamesh/nearBragg/rotate.awk
./rotate.awk -v phix=10 -v phiy=20 -v phiz=30 atoms.txt >! rotated.txt
nearBragg –atoms rotated.txt -lambda 1 -distance 1000 -detsize 100 -fluence 1e32
(200s)
adxv noiseimage.img

## Slide 35: nanoBragg program
http://bl831.als.lbl.gov/~jamesh/nanoBragg/
Optimized for nanocrystals
Square or round
Takes h,k,l and F
Supports 1 unit cell
explicit “mosaicity”
arbitrary source
explicit “phi” steps

## Slide 36: square

## Slide 37: round

## Slide 38: How to run: nanoBragg for single particle
pdbset xyzin lysozyme.pdb xyzout bigcell.pdb << EOF
CELL 250 250 250 90 90 90
SPACEGROUP 1
EOF
phenix.fmodel bigcell.pdb high_resolution=10 k_sol=0.35 b_sol=46.5 mask.solvent_radius=0.5 mask.shrink_truncation_radius=0.16
mtz_to_P1hkl.com bigcell.pdb.mtz
nanoBragg –cell 250 250 250 90 90 90 –misset 10 20 30 -hkl P1.hkl -lambda 1 -distance 1000 -detsize 100 -fluence 1e32 -N 1
adxv noiseimage.img

## Slide 39: How to run: nanoBragg for single particle
pdbset xyzin lysozyme.pdb xyzout bigcell.pdb << EOF
CELL 250 250 250 90 90 90
SPACEGROUP 1
EOF
phenix.fmodel bigcell.pdb high_resolution=10 k_sol=0.35 b_sol=46.5 mask.solvent_radius=0.5 mask.shrink_truncation_radius=0.16
mtz_to_P1hkl.com bigcell.pdb.mtz
nanoBragg –cell 250 250 250 90 90 90 –misset 10 20 30 -hkl P1.hkl -lambda 1 -distance 1000 -detsize 100 -fluence 1e32 -N 1
adxv noiseimage.img

## Slide 40: Realistic single-particle prediction
1012 photon/pulse
100 nm focus

## Slide 41: Realistic single-particle prediction
1012 photon/pulse
3 nm focus

## Slide 42: How to run: nonBragg for SAXS
pdbset xyzin lysozyme.pdb xyzout bigcell.pdb << EOF
CELL 250 250 250 90 90 90
SPACEGROUP 1
EOF
phenix.fmodel bigcell.pdb high_resolution=10 k_sol=0.35 b_sol=46.5 mask.solvent_radius=0.5 mask.shrink_truncation_radius=0.16
mtz_to_stol.com bigcell.pdb.mtz
nonBragg -stol mtz.stol -lambda 1 -dispersion 0 \
-distance 1000 -detsize 100 -pixel 0.172 \
-flux 1e13 -thick 1.2 -MW 14000 -density 0.01
adxv noiseimage.img

## Slide 43: How to run: nonBragg for SAXS
pdbset xyzin lysozyme.pdb xyzout bigcell.pdb << EOF
CELL 250 250 250 90 90 90
SPACEGROUP 1
EOF
phenix.fmodel bigcell.pdb high_resolution=10 k_sol=0.35 b_sol=46.5 mask.solvent_radius=0.5 mask.shrink_truncation_radius=0.16
mtz_to_stol.com bigcell.pdb.mtz
nonBragg -stol mtz.stol -lambda 1 -dispersion 0 \
-distance 1000 -detsize 100 -pixel 0.172 \
-flux 1e13 -thick 1.2 -MW 14000 -density 0.01
adxv noiseimage.img

## Slide 44: nonBragg extracts background
Flux
Exposure
Density
Thickness
Gain, offset
spot remover

## Slide 45
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel
Pilatus: subtract smooth baseline

## Slide 46: “fit” simulation to reality
Dispersion
Divergence
Mosaicity
Wavelength
Unit cell parameters (3)
Crystal orientation (3)
Mosaic domain size (3)
Beam center (2)
Beam direction (2)
Detector distance

## Slide 47
Real XFEL still

## Slide 48: Simulation of XFEL still

## Slide 49
phiz
Simulation of XFEL still
phiy
phiz
phix
phix
phiy
VS
real

## Slide 50
Angle about y axis (°)
Fraction pixels predicted
Fitting individual “mosaic domains”
Best of
262,140 trials

## Slide 51: The “Lorentz zone”

## Slide 52
Simulation of XFEL stills
Beam center from autoindexing
Sauter (2015). JSR 22, 239.

## Slide 53: Now What?
10 Å

## Slide 54
The number of photons scattered
before crystal is dead
is independent
of data collection time
1 um3 = 105 photons (roomT)
1 um3 = 106 photons (synch)
1 um3 = 108 photons (XFEL)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009
(synch)

## Slide 55
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.
No flux
No symmetry

## Slide 56
Crystal diameter (micron)
Resolution (Å)
B = 0
B = 20
B = 60
B = 170
B = 330
B = 560
B = 850
Bigger is better, but not by much

## Slide 57: B factor from image analysis
B = 500

## Slide 58: B factor from image analysis
B = 20

## Slide 59
Synchrotron Resolution (Å)
XFEL Resolution (Å)
Predicting resolution limits

## Slide 60: Is it Real? Or is it MLFSOM
simulated
real
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 61: The R-factor Gap
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.

## Slide 62: The R-factor Gap
Last “right”
atom added
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.

## Slide 63: 30 conformers from 24,000

## Slide 64: 2Fsim-Fcalc and Fsim-Fcalc maps
1.0 Å data
Rcryst= 0.137
Rfree = 0.159
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc

## Slide 65: 2Fsim-Fcalc and (Fsim Φsim) - (Fcalc Φcalc) maps
1 “sigma” 2Fsim-Fc
Fright – (2Fsim-Fc)
1.0 Å data
Rcryst= 0.137
Rfree = 0.159

## Slide 66: 30 conformers from 24,000

## Slide 67: Muybridge’s galloping horse (1878)
Real space
reciprocal
Structural and Dynamical Information Beyond Bragg

## Slide 68: Muybridge’s multi-camera

## Slide 69: Muybridge’s galloping horse (1878)
Real space
reciprocal
Average electron density

## Slide 70: Muybridge’s galloping horse (1878)
Real space
reciprocal
Average electron density: 1 sigma contour

## Slide 71: lysozyme: real and reciprocal

## Slide 72: lysozyme: thermal motion

## Slide 73: Supporting a model with data

## Slide 74: URLs & Summary
MLFSOM for rotation data
nonBragg for background
nanoBragg for stills
nearBragg for coherence
Phasing limit is calibration
Resolution limited by “disorder”
http://bl831.als.lbl.gov/~jamesh/powerpoint/
IGBMC_XFELsim_2016.pptx
http://bl831.als.lbl.gov/~jamesh/bin_stuff/
http://bl831.als.lbl.gov/~jamesh/mlfsom/

## Slide 75: How to install: MLFSOM
wget http://bl831.als.lbl.gov/~jamesh/
mlfsom/development_snapshot.tgz
tar xvzf development_snapshot.tgz
wget http://ftp.esrf.eu/pub/expg/FIT2D/
fit2d_10.132_i686_linuxV2.2.10
ln –sf fit2d_* fit2d
yum install gnuplot
gedit example.com mlfsom.params
./ano_sfall.com lysozyme.pdb
mv ideal_ano.mtz pristine.mtz
./mlfsom.com frames=100

## Slide 76: What if…
You only have a few small crystals?
Should you:
  Collect 360° from each?
  Collect 10° from each at 36x exposure?
  Glue 36 xtals together, then collect 360° ?
  Glue together and do 12960° ?

## Slide 77
processing procedure | collection scenario |  |  | 
 | fine | coarse | glue | glue_fine
XDS/XSCALE | 3.03874 | 3.02970 | 3.0270 | 3.02948
XDS/aimless | 3.13351 | 3.03531 | 3.02638 | 3.05292
XDS/noscale | 3.01449 | 3.03048 | 3.02576 | 3.31013
MOSFLM-defaults | x | x | x | x
MOSFLM-cheat | 3.51254 | 3.04355 | 3.08244 | x
MOSFLM/noscale | 3.51311 | 3.04287 | 3.21664 | x
HKL2000-defaults | x | x | x | x
HKL2000-cheat | 3.04147 | 3.01415 | 3.01415 | 3.03948
DIALS-defaults | x | x | 3.32378 | x
DIALS-cheat | 2.92007 | x | 2.98204 | 2.92007
DIALS-noscale | 2.96392 | x | 3.26126 | 5.14852
d*Trek | ? | ? | ? | ?
EVAL15 | ? | ? | ? | ?

## Slide 78: 30 conformers from 24,000

## Slide 79: How many conformers are there?
Rcryst = 0.0441
Rfree = 0.0516
vs Fsim
Answer: 2-14

## Slide 80: How many conformers are there?
Rcryst = 0.1546
Rfree = 0.1749
vs Fobs
1aho:
Rcryst = 0.1630
Rfree = n/d
Answer: 1-7

## Slide 81: How many conformers are there?
All difference
features
are in
the solvent!
real data

## Slide 82: The R-factor Gap
MX data quality is not limiting
Hypotheses:
  Hidden systematic error?
  Model-building problem?
  Representation problem?

## Slide 83: RISM model for “bulk” solvent
Method | Rwork | Rfree
Default refmac5: flat bulk solvent | .1784 | .1898
RISM – self-consistent density field based on electrostatics | .1640 | .1808
Explicit MD solvent, protein fixed | .1523 | .1690
RISM – protein fixed multi-conformer weighted | .1578 | .1739
Explicit – protein fixed multi-conformer weighted | .1440 | .1666

## Slide 84: How to install: nanoBragg
wget http://bl831.als.lbl.gov/
~jamesh/nanoBragg/nanoBragg.c
gcc –o nanoBragg nanoBragg.c -lm

## Slide 85: How to install: nonBragg
wget http://bl831.als.lbl.gov/
~jamesh/nonBragg/nonBragg.c
gcc –o nonBragg nonBragg.c -lm

## Slide 86: How to install: ancillaries
wget http://bl831.als.lbl.gov/
~jamesh/nanoBragg/noisify.c
wget http://bl831.als.lbl.gov/
~jamesh/nanoBragg/float_add.c
wget http://bl831.als.lbl.gov/
~jamesh/nanoBragg/float_func.c
gcc –o noisify noisify.c –lm
gcc –o float_add float_add.c –lm
gcc –o float_func float_func.c –lm

## Slide 87: How to run: nanoBragg for single particle
UBtoA.awk << EOF > A.mat
CELL 250 250 250 90 90 90
RANDOM
EOF
nanoBragg -hkl P1.hkl -lambda 1 -distance 1000 -detsize 100 -fluence 1e32 -N 1 –mat A.mat
adxv noiseimage.img
UBtoA.awk << EOF > A.mat
CELL 250 250 250 90 90 90
MISSET 10 20 30
RANDOM 1 12345
EOF