## Slide 1: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1 creator: Tom Alber
Center for Structure of Membrane Proteins (CSMP)
Membrane Protein Expression Center II (MPEC)
Center for HIV Accessory and Regulatory Complexes (HARC)
UC Multicampus Research Programs and Initiatives (MRPI)
UCSF Program for Breakthrough Biomedical Research (PBBR) Integrated Diffraction Analysis Technologies (IDAT)
Plexxikon, Inc.
M D Anderson CRC
Synchrotron Radiation Structural Biology Resource (SLAC)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser John Spence
Chris Nielsen Clemens Schulze-Briese Aina Cohen Ana Gonzalez

## Slide 2: Grand Challenges in Structural Biology
Phase Problem
native elements - universally
Amplitude Problem
    Improving resolution
R-factor Gap
    Publishing / being right

## Slide 3: Grand Challenges in Structural Biology
Phase Problem
detector calibration
Amplitude Problem
    disorder
R-factor Gap
    Limited representation

## Slide 4: Grand Challenges in Structural Biology
Phase Problem
detector calibration
Amplitude Problem
    disorder
R-factor Gap
    Limited representation

## Slide 5: Can you count to 1,000,000 ?
= 0.1%
sqrt(1,000,000)
1,000,000
= 3%
sqrt(1,000)
1,000
> 1000 is a waste!
photon
spot
Theoretically:
In reality:
ISa ~ 33
Rmeas ≈ 0.1% ?
ISa = 1000
Rmeas = ≈ 3%

## Slide 6
Required signal-to-noise (I/σ)
Solve-able proteins (%)
Current
technology
Goal
Threshold of a revolution in phasing

## Slide 7
Source of error | realistic simulation | No SHSSS | Perfect detector
Photon counting | + | + | +
Shutter jitter | + | + | -
Beam flicker | + | + | -
Sample absorption | + | + | -
Radiation damage | + | + | -
Imperfect spindle | + | + | -
vignette | + | + | -
Corner correction | + | + | -
SHSSS | + | - | -
Rmeas (∞-10 Å) | 2.8% | 0.7% | 0.7%
I/σ asymptotic | 26.8 | 74.2 | 81.0
Threshold of a revolution in phasing
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 8
Spot centroid position (pixels)
Relative spot intensity
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 9
Spot centroid position (pixels)
Relative spot intensity
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 10: Pilatus: 1-module shift

## Slide 11
Pilatus: 1-module shift

## Slide 12
Pilatus: 1-module shift

## Slide 13
Pilatus: 1-module shift - aligned

## Slide 14
3% high
average
3% low
Pilatus: 1-module shift - ratio

## Slide 15
3.5
3.0
2.5
2.0
1.5
1.0
0.5
SHSSS
Systematic component of Rsseparate (%)
distance between spots (mm)
0.1 1 10 100
CCD detector
anomalous mates are always on
different modules
different
modules
Pilatus
SN113
Pilatus
SN001

## Slide 16
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel
Pilatus: subtract smooth baseline

## Slide 17
N
N
N
θ
λ
detection
event
incoming
photon
PAD: need more than flood-field

## Slide 18
thickness
width
N
N
N
Bragg
glitch
oxygen
inclusion
θ
λ
detection
event
incoming
photon
PAD: need more than flood-field

## Slide 19
charge-
sharing
zone
thickness
width
N
N
N
trim
trim
trim
Bragg
glitch
oxygen
inclusion
θ
λ
detection
event
incoming
photon
PAD: need more than flood-field

## Slide 20: Grand Challenges in Structural Biology
Phase Problem
Calibrate it out boost the signal average over it
Amplitude Problem
R-factor Gap
http://bl831.als.lbl.gov/~jamesh/powerpoint/Janelia_thresholds_2015.pptx

## Slide 21: Grand Challenges in Structural Biology
Phase Problem
Calibrate it out boost the signal average over it
Amplitude Problem
R-factor Gap
http://bl831.als.lbl.gov/~jamesh/powerpoint/Janelia_thresholds_2015.pptx

## Slide 22
Photon Energy (eV)
Anomalous f” (electrons)
2472.7 2473.5
Bohic et al. Anal. Chem. 2008; 80(24):9557. doi: 10.1021/ac801817k

## Slide 23
Required signal-to-noise (I/σ)
Solve-able proteins (%)
Current
detectors

## Slide 24: Where do photons go?
beamstop
97%
transmitted
1 Å x-rays
attenuation correction
error cannot be > ~3%
100 μm
thick
protein

## Slide 25: Where do photons go?
beamstop
2%
transmitted
5 Å x-rays
attenuation correction
error can be ~98%
100 μm
thick
protein

## Slide 26: Where do photons go?
beamstop
96%
transmitted
5 Å x-rays
attenuation correction
error cannot be > ~4%
1 μm
thick
protein

## Slide 29: “sweet spot” for sample size ?
2 Å
2sin(90°)
3 Å
2sin(90°)
S
P
Mg
Na
C
F
N
O
Cl
Ar
K
Ca
Ne
Se
4 Å
2sin(90°)

## Slide 30: Dose-rate dependence of damage
dose rate (kGy/s)
maximum useful dose (MGy)

## Slide 31: The “partiality problem”
0.006°
1 μm xtal
1 Å x-rays

## Slide 32
The true nature of “mosaic spread”
Lovelace JJ, Murphy CR, Pahl R, Brister K & Borgstahl GEO (2006)."Tracking reflections through cryogenic cooling with topography", J. Appl. Cryst. 39, 425-432.
Any function can be approximated by a family of Gaussians

## Slide 33
Ewald sphere 2
diffracted ray
λ*
λ*
θ
1
Ewald sphere
λ*
(h,k,l)
diffracted ray
λ*
θ
d*
(-h,-k,-l)
d*

## Slide 34
h,k,l
-h,-k,-l
Detector
Detector
Detector
Detector
λ = 5 Å
sample
injector
Si(111)
52.87deg
Si(111)
Si(111)
Si(111)
Si(111)
Si(111)
2 Multilayer mirrors
d=2nm, W/B4C
KB Horiz focus
KB vertical focus
~ 1m
Notes: Proposed 5-crystal monochromator for colliding-beam crystallography. The generation of two opposing Ewald spheres means that for every h,k,l index reflected from the protein crystal, the Friedel mate is reflected in the opposite direction, allowing for very accurate anomalous difference measurements. The wavelength need not be set precisely at the sulfur or phosphorous edge, but merely at a wavelength where the f” of those elements are strong. For fs-class pulses, the distances above will have to be precise to withing ~3 microns, and for accurate reproduction of the partiality of the Friedel mates, the angular precision of the colliding beams must be within ~1% of the sample crystal’s rocking width, or ~100 microrads.

## Slide 35: Grand Challenges in Structural Biology
Phase Problem
Calibrate it out boost the signal average over it
Amplitude Problem
R-factor Gap
http://bl831.als.lbl.gov/~jamesh/powerpoint/Janelia_thresholds_2015.pptx

## Slide 36: Systematic error does not “average out”

## Slide 37: Required averaging for anomalous
mult > (—)2
~3%
<ΔF/F>

## Slide 38
RESOLUTION COMPLETENESS R-FACTOR I/SIGMA R-meas CC(1/2) Anomal SigAno Nano
LIMIT OF DATA observed Corr
9.17 99.1% 3.9% 257.47 3.9% 100.0* 91* 5.024 450
6.49 100.0% 5.2% 214.33 5.2% 100.0* 86* 3.836 882
5.30 100.0% 7.2% 165.13 7.2% 100.0* 76* 3.257 1175
4.59 100.0% 7.2% 175.42 7.3% 100.0* 67* 2.589 1403
4.10 99.9% 7.7% 174.13 7.7% 100.0* 59* 2.264 1594
3.74 99.9% 9.4% 143.09 9.4% 100.0* 49* 1.953 1783
3.47 100.0% 11.2% 120.17 11.2% 100.0* 39* 1.696 1942
3.24 100.0% 14.1% 91.14 14.1% 100.0* 30* 1.333 2103
3.06 99.9% 19.5% 65.79 19.5% 100.0* 23* 1.117 2214
2.90 99.9% 29.0% 44.85 29.1% 99.9* 17* 1.008 2369
2.77 99.9% 40.5% 32.58 40.6% 99.8* 11* 0.901 2493
2.65 99.9% 52.8% 25.16 52.9% 99.8* 10* 0.866 2605
2.54 100.0% 67.4% 19.47 67.6% 99.6* 2 0.804 2705
2.45 100.0% 88.9% 14.58 89.2% 99.2* 4 0.831 2859
2.37 100.0% 109.3% 9.97 109.7% 98.1* 5 0.829 2925
2.29 100.0% 138.2% 6.87 138.9% 96.1* 1 0.760 3037
2.22 100.0% 197.1% 4.03 198.6% 83.5* -1 0.721 3159
2.16 100.0% 227.3% 2.41 230.8% 46.9* -1 0.677 3224
2.10 61.2% 154.4% 1.28 163.6% 47.0* -2 0.660 1999
2.05 47.9% 170.1% 0.68 196.5% 25.7* 3 0.629 1578
total 93.3% 15.7% 54.30 15.8% 100.0* 12* 1.217 42499
140-fold multiplicity: 16 crystals, 360° each, inverse beam, 7235 eV

## Slide 39
RESOLUTION COMPLETENESS R-FACTOR I/SIGMA R-meas CC(1/2) Anomal SigAno Nano
LIMIT OF DATA observed Corr
9.17 99.1% 3.9% 257.47 3.9% 100.0* 91* 5.024 450
6.49 100.0% 5.2% 214.33 5.2% 100.0* 86* 3.836 882
5.30 100.0% 7.2% 165.13 7.2% 100.0* 76* 3.257 1175
4.59 100.0% 7.2% 175.42 7.3% 100.0* 67* 2.589 1403
4.10 99.9% 7.7% 174.13 7.7% 100.0* 59* 2.264 1594
3.74 99.9% 9.4% 143.09 9.4% 100.0* 49* 1.953 1783
3.47 100.0% 11.2% 120.17 11.2% 100.0* 39* 1.696 1942
3.24 100.0% 14.1% 91.14 14.1% 100.0* 30* 1.333 2103
3.06 99.9% 19.5% 65.79 19.5% 100.0* 23* 1.117 2214
2.90 99.9% 29.0% 44.85 29.1% 99.9* 17* 1.008 2369
2.77 99.9% 40.5% 32.58 40.6% 99.8* 11* 0.901 2493
2.65 99.9% 52.8% 25.16 52.9% 99.8* 10* 0.866 2605
2.54 100.0% 67.4% 19.47 67.6% 99.6* 2 0.804 2705
2.45 100.0% 88.9% 14.58 89.2% 99.2* 4 0.831 2859
2.37 100.0% 109.3% 9.97 109.7% 98.1* 5 0.829 2925
2.29 100.0% 138.2% 6.87 138.9% 96.1* 1 0.760 3037
2.22 100.0% 197.1% 4.03 198.6% 83.5* -1 0.721 3159
2.16 100.0% 227.3% 2.41 230.8% 46.9* -1 0.677 3224
2.10 61.2% 154.4% 1.28 163.6% 47.0* -2 0.660 1999
2.05 47.9% 170.1% 0.68 196.5% 25.7* 3 0.629 1578
total 93.3% 15.7% 54.30 15.8% 100.0* 12* 1.217 42499
140-fold multiplicity: 16 crystals, 360° each, inverse beam, 7235 eV

## Slide 40: Gadox calibration vs energy
photon energy (keV)
Relative absorption depth
same = good!
bad!

## Slide 41: 140-fold multiplicity
18 σ
Phased anomalous difference Fourier
16 σ

## Slide 42: 140-fold multiplicity
8.2σ = Mg?
DELFAN residual anomalous difference

## Slide 43
A
B
Metal site: is it Mg++ ? Or Na+ ?
Position (Å)
Electron density (e-/ Å3)

## Slide 44
f’’ (electrons)
DELFAN peak height (σ)
Mg
Ne
Na
F
O
N
Metal site: is it Mg++ ? Or Na+ ?

## Slide 45: non-isomorphism
Why doesn’t everyone do this?

## Slide 46: non-isomorphism
not same structure thing
Why doesn’t everyone do this?

## Slide 47
0.5% cell change → 15%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.
Same structure, different cell

## Slide 48
Same structure, different cell
0.5% cell change → 15%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 49
Same cell, rotated protein
0.5° rotation → 16%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 50
Same cell, rotated protein
0.5° rotation → 16%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 51
Uniform stretch
5% change → 0%

## Slide 52
5% change → 0%
Uniform stretch

## Slide 53: Non-isomorphism in lysozyme
RH: 84.2%
vs 71.9%
Riso = 44.5%
3aw6
3aw7
Δcell = 0.7 %
RMSD = 0.18 Å

## Slide 54
h,k,l | structure factors (F) |  |  | 
 | #1 | #2 | #3 | #4
5,3,4 | 523.7 | 559.8 | 579.9 | 603.2
5,4,4 | 168.2 | 166.6 | 177.2 | 196.1
5,5,4 | 34.9 | 26.4 | 19.2 | 17.3
6,1,4 | 305.7 | 301.1 | 298.1 | 296.3
6,2,4 | 353.0 | 353.9 | 356.2 | 366.9
6,3,4 | 300.9 | 285.3 | 273.5 | 259.4
6,3,5 | 223.8 | 226.3 | 234.6 | 251.4
… | … | … | … | …
X-ray Data Sets
h,k,l | 100% | 17 % | 13 % | 9 %
 | 1st | 2nd | 3rd | 4th
5,3,4 | -1.46 | -0.02 | 1.84 | -0.72
5,4,4 | -0.88 | -0.29 | -0.34 | 0.15
5,5,4 | -0.42 | -0.65 | 1.02 | 1.47
6,1,4 | -0.90 | -0.85 | 1.44 | -0.40
6,2,4 | -1.20 | -0.37 | 0.67 | 0.01
6,3,4 | -0.75 | 0.31 | 0.48 | 0.00
6,3,5 | -0.75 | -0.85 | 0.72 | -0.82
… | … | … | … | …
data
set
Singular value decomp.
SVD
vector
value
Singular values & vectors
Correlation
Coefficients
-0.68
CC2
CC3
CC1
CC1 CC2 CC3
data set #1
Data sets
Positioned
in
“Correlation
Space”
-0.24
data set #2
data set #3
0.32 …

## Slide 56
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 57
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 58
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 59: Bragg’s “minimum wavelength principle”
Perutz (1985). “Early Days of Cryst…” Methods in Enzymology, Vol. 114, 3-18.
Bragg & Perutz (1952)."external form haemoglobin I", Acta Cryst. 5, 277-283.

## Slide 60: DMMULTI – fake data 4 deg rotation: 8 “xtals”: before
CC = 0.02

## Slide 61
CC = 0.8
DMMULTI – fake data 4 deg rotation: 8 “xtals”: after

## Slide 62: Grand Challenges in Structural Biology
Phase Problem
detector calibration
Amplitude Problem
    disorder
R-factor Gap
    Limited representation

## Slide 63: The Amplitude Problem
10 Å

## Slide 64
X-ray beam size (μm)
Resolution (Å)
too big
too small
just right
Match beam size to crystal size

## Slide 65
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.
No flux
No symmetry

## Slide 66
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 67
Crystal diameter (micron)
Resolution (Å)
B = 0
B = 20
B = 60
B = 170
B = 330
B = 560
B = 850
Bigger is better, but not by much

## Slide 68
Home Lab Resolution (Å)
Synchrotron Resolution (Å)
Predicting resolution limits

## Slide 69
Synchrotron Resolution (Å)
XFEL Resolution (Å)
Predicting resolution limits

## Slide 70
Disorder
Trumps
Everything!
Diffraction Take-Home Lesson:

## Slide 71: lysozyme: real and reciprocal

## Slide 72: lysozyme: thermal motion

## Slide 73: Muybridge’s galloping horse (1878)
Real space
reciprocal
“Time-resolved” diffraction

## Slide 74: Muybridge’s galloping horse (1878)
Real space
reciprocal
Average intensity

## Slide 75: Muybridge’s galloping horse (1878)
Real space
reciprocal
Average electron density

## Slide 76: Supporting a model with data

## Slide 77
Dissecting the Amplitude Problem
purify
protein
grow
crystal
cryo
MX
micro
beam
XFEL
Give up

## Slide 78
Dissecting the Amplitude Problem
purify
protein
grow
crystal
cryo
MX
micro
beam
design
new clone /
conditions
+
-
traditional
approach
high
low
SAXS
order/disorder
In solution
XFP
xtal packing
interfaces
in-situ MX
Control for handling
RT MX
Control for cryo
B factor

## Slide 79
SAXS assay for intrinsic order

## Slide 80
Dissecting the Amplitude Problem
purify
protein
grow
crystal
cryo
MX
micro
beam
design
new clone /
conditions
+
-
traditional
approach
high
low
SAXS
order/disorder
In solution
XFP
xtal packing
interfaces
in-situ MX
Control for handling
XFEL
Rapid RT
high multiplicity
RT MX
Control for cryo
B factor

## Slide 81
ADSC
area
detector
Cu foil
x-ray beam
beam center
3%
2%
1%
0
X-ray excited
fluorescent
X-ray source
crystal in loop

## Slide 82: Cone-Beam Online X-ray Absorption Radiograph

## Slide 83
Dissecting the Amplitude Problem
purify
protein
grow
crystal
cryo
MX
micro
beam
XFEL
design
new clone /
conditions
+
-
traditional
approach
high
low
AUORA
auto optical
re-alignment
CBOXAR
& raster
xtal size, shape & location
SAXS
order/disorder
In solution
XFP
xtal packing
interfaces
in-situ MX
Control for handling
Rapid RT
high multiplicity
RT MX
Control for cryo
B factor

## Slide 84: Grand Challenges in Structural Biology
Phase Problem
detector calibration
Amplitude Problem
    disorder
R-factor Gap
    Limited representation

## Slide 85: Is this good enough?
dmax = 4.5 Å
Rcryst = 27%
Rfree = 38%

## Slide 86: Is this good enough?
3a8n 4.5 Å Rmerge = 0.15 R/Rfree = 0.306/0.396
1grz 5 Å Rmerge = 0.052 R/Rfree = 0.369/0.428
1qzv 4.44 Å Rmerge = 0.099 R/Rfree = 0.41/0.42

## Slide 87: Is this good enough?
1hvu 4.75 Å Rmerge = 0.064 R/Rfree = 0.34/0.413
2r6e 5.02 Å Rmerge = 0.058 R/Rfree = 0.394/0.397
1n8e 4.5 Å Rmerge = 0.138 R/Rfree = 0.415/0.416

## Slide 88: The R-factor Gap
Holton et al. (2014). FEBS J. 281, 4046-60.
R1 < 2*Rsigma
Publication criterion for chemical crystallography:
R1 = Fo vs Fc for I/σ(I) > 3
Rsigma = <σ(I)>/<I>
There are no PDB entries that pass this test!

## Slide 89: The R-factor Gap
Rmerge = 3%
Rwork = 20%
Rfree = 24%
Experimental
error
“systematic”
error
20% of carbon atom = 1.2 e-
5% of carbon atom = 0.3 e-
Closing the R-factor gap will enable study of 1-electron changes

## Slide 90: The R-factor Gap
MLFSOM
Elves
Rmerge = 6%
Rcryst = 17%
Rfree = 20%
multi-conformer PDB file
1H87
Holton, Classen, Frankel & Tainer (2014)."The R-factor gap in macromolecular crystallography: an untapped potential for insights on accurate structures", FEBS J. 281, 4046-4060.

## Slide 91: The R-factor Gap
MLFSOM
Elves
Rmerge = 6%
Rcryst = 7%
Rfree = 8%
multi-conformer PDB file
1H87
Holton, Classen, Frankel & Tainer (2014)."The R-factor gap in macromolecular crystallography: an untapped potential for insights on accurate structures", FEBS J. 281, 4046-4060.

## Slide 92: The R-factor Gap
single-conformer PDB file
1H87; conf “A”
Holton, Classen, Frankel & Tainer (2014)."The R-factor gap in macromolecular crystallography: an untapped potential for insights on accurate structures", FEBS J. 281, 4046-4060.
MLFSOM
Elves
Rmerge = 6%
Rcryst = 7%
Rfree = 8%
ARP/wARP

## Slide 93: The R-factor Gap
MX data quality is not limiting
Hypotheses:
  Hidden systematic error?
  Model-building problem?
  Representation problem?

## Slide 94: Molecular Dynamics Simulation
1aho
Scorpion toxin
0.96 Å resolution
64 residues
Solvent: H20 + acetate
Cerutti et al. (2010).J. Phys. Chem. B 114, 12811-12824.
using real
crystal’s lattice

## Slide 95: 30 conformers from 24,000

## Slide 96: Electron density from 24,000 conformers

## Slide 97: Electron density from 24,000 conformers

## Slide 98: 2Fsim-Fcalc and Fsim-Fcalc maps
1.0 Å data
Rcryst= 0.137
Rfree = 0.159
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc

## Slide 99: 2Fsim-Fcalc and (Fsim Φsim) - (Fcalc Φcalc) maps
1 “sigma” 2Fsim-Fc
Fright – (2Fsim-Fc)
1.0 Å data
Rcryst= 0.137
Rfree = 0.159

## Slide 100: 30 conformers from 24,000

## Slide 101: Regular model with real data!
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc
1.0 Å data
Rcryst= 0.116
Rfree = 0.135

## Slide 102: MD: predicted density for one atom

## Slide 103: How many conformers are there?
Answer: 8
Rcryst = 0.0297
Rfree = 0.0293
vs Fsim

## Slide 104: How many conformers are there?
Rcryst = 0.0441
Rfree = 0.0516
vs Fsim
Answer: 2-14

## Slide 105: How many conformers are there?
Rcryst = 0.1546
Rfree = 0.1749
vs Fobs
1aho:
Rcryst = 0.1630
Rfree = n/d
Answer: 1-7

## Slide 106: How many conformers are there?
All difference
features
are in
the solvent!
real data

## Slide 107: How “rough” is the solvent?
Rcryst = 0.0309
Rfree = 0.0678
vs Fsim

## Slide 108: RISM model for “bulk” solvent
Method | Rwork | Rfree
Default refmac5: flat bulk solvent | .1784 | .1898
RISM – self-consistent density field based on electrostatics | .1640 | .1808
Explicit MD solvent, protein fixed | .1523 | .1690
RISM – protein fixed multi-conformer weighted | .1578 | .1739
Explicit – protein fixed multi-conformer weighted | .1440 | .1666

## Slide 109: Grand Challenges in Structural Biology
Phase Problem
Calibrate it out boost the signal average over it
Non-isomorphism phasing (NIP)
Amplitude Problem
Disorder > everything Dissect sample prep
Revolution in sample handling?
R-factor Gap
1 electron =chemistry validate dynamics
2D data vs 4D models
http://bl831.als.lbl.gov/~jamesh/powerpoint/Janelia_thresholds_2015.pptx

## Slide 110: What good are low energies?
Carbon 284
Nitrogen 402
Oxygen 537
Fluorine 685
Neon 866
Sodium 1072
Magnesium 1304
Aluminum 1559
Silicon 1838
Phosphorous 2148
Sulfur 2475
Chlorine 2825
Argon 3205
Potassium 3610
Calcium 4041
Scandium 4495

## Slide 111
What is the “molecular transform”?
False color intensity
sample
detector

## Slide 112
What is the “molecular transform”?
False color intensity
sample
detector

## Slide 113
What is the “molecular transform”?
False color intensity
sample
detector

## Slide 114
Two-color experiment (1930)

## Slide 115
Two-color experiment (ca 1914)
20 eV
aka “rotating anode”