## Slide 1: PowerPoint File available:
http://bl831.als.lbl.gov/~jamesh/powerpoint/
LBLSCW_SvN_2017.pptx

## Slide 2: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1 creator: Tom Alber
UC Multicampus Research Programs and Initiatives (MRPI)
UCSF Program for Breakthrough Biomedical Research (PBBR)
one-time NIH-DOE Inter-agency agreement (IAA)
GM117126 to Sauter (DIALS)
Integrated Diffraction Analysis Technologies (IDAT)
Plexxikon, Inc.
Synchrotron Radiation Structural Biology Resource (SLAC)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser Aina Cohen Ana Gonzalez
Nick Sauter Axel Brunger Monarin Uervirojnangkoorn
Artem Lyubimov

## Slide 3: At-scale diffraction simulation
simulated
real
MLFSOM
Holton et al (2014) “R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 4
Simulated | statistic | Real
5.4% | Rmerge | 6.2%
18.9 | I/sd | 16.2
1.9 | I/sd (1.4 Ǻ) | 1.6
1.7 4.0 0.020 | SDCORR | 1.0 2.2 0.065
36.8 | PADFPH | 31.46
3.871 | mlphare f” | 3.476
0.178 | FOM | 0.192
0.545 | FOMDM | 0.664
0.6270 | CC(1H87) | 0.6090
0.170 | Rcryst | 0.184
0.205 | Rfree | 0.231

## Slide 5: The R-factor Gap
MLFSOM
Elves
Rmerge = 6%
Rcryst = 7%
Rfree = 8%
single-conformer PDB file
Elves
Rmerge = 6%
Rcryst = 17%
Rfree = 20%
real
data
Holton et al (2014) “R-factor gap", FEBS Journal 281, 4046-4060.
Notes: Typically, when atomic models are refined against macromolecular crystallographic data, the model-data agreement statistics (Rcryst and Rfree) are many times higher than the internal self-consistency of the observations (exemplified by Rmerge here). The diffraction image simulation program MLFSOM includes all known sources of experimental error (including the systematic errors of sample absorption and detector calibration), and when the simulated images are processed with common data reduction packages such as Elves, the data quality statistics (such as Rmerge, I/sigma, and phasing power) obtained are essentially identical to those obtained from real data. The only exceptions are Rcryst and Rfree, which rapidly refine down to where the calculated and “observed” structure factors agree to within experimental error. Essentially, this result implies that experimental noise is not the cause of the large disagreements that persist between observed spot intensities and our molecular models. Indeed, if this were the case, then averaging over many crystals should result in significantly lower Rcryst/Rfree.

## Slide 6: Systematic Error vs Random Noise

## Slide 7: Three types of error
Relative
  Proportional to signal
    Shutter jitter, beam flicker, vibration, calibration
    Partiality, isomorphism, Fobs vs Fcalc (Rwork & Rfree)
Photon count
  Proportional to sqrt(signal)
Baseline
  Independent of signal
    Detector read-out noise

## Slide 8: Partiality > 25% error per spot!
Kabsch W (2014)."Processing of X-ray snapshots from crystals in random orientations", Acta Cryst D 70, 2204-2216.

## Slide 9: What is “partiality”?
Ewald sphere

## Slide 10: What is “partiality”?
Ewald sphere

## Slide 11: The “partiality problem”
0.006°
1 μm xtal
1 Å x-rays

## Slide 12
Real XFEL still
Lyubimov et al. (2016).
eLife 5, e18740.

## Slide 13: XFEL: “fit” simulation to reality
Dispersion
Divergence
Mosaicity
Wavelength
Unit cell parameters (3)
Crystal orientation (3)
Mosaic domain size (3)
Beam center (2)
Beam direction (2)
Detector distance

## Slide 14: Simulation of XFEL still
Lyubimov et al. (2016).
eLife 5, e18740.

## Slide 15
Real XFEL still
Lyubimov et al. (2016).
eLife 5, e18740.

## Slide 16
phiz
Simulation of XFEL still
phiy
phiz
phix
phix
phiy
VS
real

## Slide 17
Angle about y axis (°)
Fraction pixels predicted
Fitting individual “mosaic domains”
Best of
262,140 trials

## Slide 18: 3-domain Simulation of XFEL still

## Slide 19
Real XFEL still
Lyubimov et al. (2016).
eLife 5, e18740.

## Slide 20: 1-domain Simulation of XFEL still

## Slide 21
The true nature of “mosaic spread”
Lovelace JJ, Murphy CR, Pahl R, Brister K & Borgstahl GEO (2006)."Tracking reflections through cryogenic cooling with topography", J. Appl. Cryst. 39, 425-432.
Any function can be approximated by a family of Gaussians

## Slide 22: The “Lorentz zone”

## Slide 23: Coming Soon in CCTBX / DIALS!
At-scale simulation coupled to
data processing
https://github.com/cctbx

## Slide 24: Can’t we just rotate the crystal?
1 μm
1°
100 fs
= 90 km/s
9 nm
17.26 km/s
(90 km/s)2
0.5 μm
= 1.5 x 1015 G
= 0.5 nN

## Slide 25: Can’t we just rotate the crystal?
NO
Why do we want to rotate the crystal?

## Slide 26: Can’t we just widen the bandpass?

## Slide 27: Si(111) vs multilayers
0.014%
Si(111)
1%
multilayer
4 Å
1.9 Å
resolution
spectral
dispersion

## Slide 28: Wide-bandpass MX?
Mono | Si(111) | multilayer | Difference (%) | good
Energy (eV) | 11111 | 12027.5 | +8.2 | Same
Scale | 1.0000 | 1.0964 | +9.6 | Yes
Rmerge (%) | 7.5 | 8.4 | +12 | No
Ranom (%) | 5.6 | 5.5 | -1.8 | Same
I/sd | 13.2 | 12.3 | -6.8 | Same
I/sd (1.5Å) | 2.3 | 1.8 | -21.7 | No
Ano Patt | 5.96 | 4.75 | -20.3 | Same
Ano Phased | 41 | 39.33 | -4.1 | Same
FOM | 0.238 | 0.192 | -19.3 | Same
CC | 0.555 | 0.647 | -6.1 | Yes
Rcryst (%) | 26.70 | 26.48 | -0.2 | Same
Ligand peak | 8.213 | 8.250 | +0.4 | Same

## Slide 29: Wide bandpass reveals mosaicity from a still
Snell EH, Weisgerber S, Helliwell JR, Holzer K & Schroer K (1995)."Improvements in lysozyme protein crystal perfection through microgravity growth", Acta crystallographica. Section D, Biological crystallography 51, 1099-1102.
low mosaic
high mosaic
Δradial = 2ηD/cos22θ

## Slide 30: Narrow bandpass does not improve anomalous signal
Chart: Photon energy (eV)
| 12656 | 12657 | 12658 | 12658.1 | 12658.2 | 12658.6 | 12658.9 | 12659 | 12659.1 | 12659.2 | 12659.3 | 12659.4 | 12659.6 | 12659.7 | 12659.9 | 12660.4 | 12660.5 | 12660.6 | 12661 | 12656 | 12657 | 12658 | 12658.1 | 12658.2 | 12658.6 | 12658.9 | 12659 | 12659.1 | 12659.2 | 12659.3 | 12659.4 | 12659.6 | 12659.7 | 12659.9 | 12660.4 | 12660.5 | 12660.6 | 12661
I(+) | 159900 | 171800 | 190300 | 193800 | 195000 | 228800 | 232700 | 240200 | 253200 | 241400 | 260200 | 267800 | 243300 | 256400 | 251000 | 260200 | 233100 | 234600 | 247000
I(-) | 131500 | 100900 | 81560 | 76100 | 83960 | 69860 | 50120 | 60980 | 74270 | 66830 | 85140 | 76810 | 82330 | 69980 | 103800 | 106000 | 89630 | 108800 | 110400
vertical
divergence
(240 μRad)
100 μm
pinhole
Si(333)
Si(333)
Al
absorber
1rb5
h,k,l = 5,5,0

## Slide 31: The “nanocrystal advantage”
Ispot = k Ncells
Ewald sphere
range
2
caveat: 100% error!

## Slide 32: signal vs noise
“If you don’t have good data, then you have no data at all.”
-Sung-Hou Kim

## Slide 33: signal vs noise
easy
hard
impossible

## Slide 34: signal vs noise
easy
hard
impossible
threshold of “solvability”

## Slide 35: signal vs noise
“If you don’t have good data, then you must learn statistics.”
-James Holton

## Slide 36: Adding noise

## Slide 37: Adding noise
12 + 12 = 1.42

## Slide 38: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 39: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 40: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 41: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
102 + 12 = 10.052

## Slide 42: Reducing error with averaging
mult > (—)2
error
<ΔF/F>

## Slide 43: Multiplicity required to phase
Monte Carlo
  100% /obs → 10,000 fold
nXDS
  25% /obs → 625 fold
Synchrotron
  3% /obs → 9 fold
  Assuming ΔF/F ~ 1%
Beam time:
$2/s

## Slide 44: 100% SeMet incorporation
Trivial to solve

## Slide 45: 100% S -Met incorporation
Impossible to solve

## Slide 46: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 47: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 48: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 49: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 50: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 51: MR simulation
Rmsd from perfect search model (Å)
corrupted model
Correlation coefficient to correct density

## Slide 52: The transitions are sharp!
How can we predict success/failure?
Know Thy Experiment

## Slide 53: What if…
You only have a few small crystals?
Should you:
  Collect 360° from each?
  Collect 10° from each at 36x exposure?
  Glue 36 xtals together, then collect 360° ?
  Glue together and do 12960° ?
  http://bl1231.als.lbl.gov/~jamesh/dose_slice/results.html

## Slide 54
The number of photons scattered
before crystal is dead
is independent
of data collection time
1 um3 = 105 photons (roomT)
1 um3 = 106 photons (synch)
1 um3 = 108 photons (XFEL)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009
(synch)

## Slide 55: Dose slicing
crystal’s useful life
N
photons
N
photons
N
photons
unacceptable
damage
unacceptable
read noise

## Slide 56: Dose slicing: is that a spot?

## Slide 57: Dose slicing: is that a spot?

## Slide 58: Dose slicing: is that a spot?

## Slide 59: Dose slicing: is that a spot?

## Slide 60: Dose slicing: is that a spot?

## Slide 61: Dose slicing: is that a spot?

## Slide 62
Resolution (Å)
CC vs right answer
“true” resolution limit

## Slide 63
Dose slice collection scenario |  |  | 
fine | coarse | glue | Glue & fine
3.17700 | 3.14057 | 3.17604 | 3.12086
“true” resolution vs strategy
301,640,334 photons/xtal

## Slide 64
processing procedure | resolution limit |  |  | 
 | fine | coarse | glue | glue&fine
XDS/XSCALE | 3.17700 | 3.14057 | 3.17604 | 3.12086
XDS/aimless | 3.16251 | 3.15922 | 3.16675 | 3.12162
XDS/noscale | 3.27289 | 3.15617 | 3.38929 | 3.12162
MOSFLM-defaults | x | x | x | x
MOSFLM-cheat | 3.19755 | 3.18166 | 3.20354 | 3.19755
HKL2000-defaults | x | x | x | x
HKL2000-expert | 3.21803 | 3.12646 | 3.11551 | 3.21803
HKL2000-cheat | 3.16119 | 3.10338 | 3.10338 | 3.16300
DIALS-defaults | x | x | 3.42125 | x
DIALS-expert | 3.10296 | 3.09547 | 3.07653 | 3.08465
d*Trek | ? | ? | 4.34076 | ?
EVAL15 | 3.14352 | 3.10383 | 3.09936 | 3.14105
EVAL15-sadabs | 3.13920 | 3.10797 | 3.10171 | 3.13700

## Slide 65: X-ray scattering “rules”:
1 μm crystal ≈ 1 μm water
≈ 1 μm plastic
≈ 0.1 μm glass
≈ 1000 μm air
~ 50 mm He
≈ 370 mm sat water vapor @ 4C
Optimum: support thickness = crystal thickness

## Slide 66: "error bar" for electron density
structure factor (e-/cell)
spot index

## Slide 67: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 68: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 69: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 70: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 71: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 72: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 73: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 74: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 75: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 76: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 77: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 78: "error bar" for electron density
fractional coordinate
electron density (e-/Å3)
Refinement
Against
Perturbed
Input
Data

## Slide 79: How does the “error” compare to “sigma”?
Electron Number Density (e-/Å3)
normalized counts

## Slide 80: How does the “error” compare to “sigma”?
Electron Number Density (e-/Å3)
normalized counts

## Slide 81: How does the “error” compare to “sigma”?
Electron Number Density (e-/Å3)
normalized counts

## Slide 82: What is the “error” in 2Fo-Fc “sigma” units?
traditional “sigma” units (multples of rms(-) relative to )
normalized counts

## Slide 83: What is the “error” in Fo-Fc “sigma” units?
traditional “sigma” units (multples of rms(-) relative to )
normalized counts

## Slide 84: Tradition
fractional coordinate
electron density (e-/Å3)

## Slide 85: Break with Tradition
fractional coordinate
electron density (e-/Å3)

## Slide 86: Optimum resolution cutoff is:
Too optimistic: add nothing but noise
Too pessimistic: series-termination error
Happy medium?
Simulate:
  Random atoms, compute F2
  Add Gaussian noise, RMS = 1
  Truncate
  Subtract “right” map, RMS difference

## Slide 92: Optimum resolution cutoff is:
0.0 Å

## Slide 93: At the beamline…
Resolution
  problem: background
  solution: use as few pixels as possible
Phases
  problem: fractional errors
  solution: use as many pixels as possible

## Slide 94
anomalous signal
Crick, F. H. C. & Magdoff, B. S. (1956) Acta Crystallogr. 9, 901-908.
Hendrickson, W. A. & Teeter, M. M. (1981) Nature 290, 107-113.
# sites
MW (Da)
ΔF
F
≈ 1.2 f”
√
World record!
ΔF/F = 0.5%
Wang, Dauter & Dauter (2006) Acta Cryst. D 62, 1475-1483.

## Slide 95: Fractional error
mult > (—)2
~3%
<ΔF/F>

## Slide 96: Can you count to 1,000,000 ?
= 0.1%
sqrt(1,000,000)
1,000,000
= 3%
sqrt(1,000)
1,000
> 1000 is a waste!
photon
spot
Theoretically:
In reality:
ISa ~ 33
Rmeas ≈ 0.1% ?
ISa = 1000
Rmeas = ≈ 3%

## Slide 97
Required signal-to-noise (I/σ)
Solve-able proteins (%)
Current
technology
Goal
Threshold of a revolution in phasing

## Slide 98
Source of error | realistic simulation | No SHSSS | Perfect detector
Photon counting | + | + | +
Shutter jitter | + | + | -
Beam flicker | + | + | -
Sample absorption | + | + | -
Radiation damage | + | + | -
Imperfect spindle | + | + | -
vignette | + | + | -
Corner correction | + | + | -
SHSSS | + | - | -
Rmeas (∞-10 Å) | 2.8% | 0.7% | 0.7%
I/σ asymptotic | 26.8 | 74.2 | 81.0
Threshold of a revolution in phasing
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 99
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel
Pilatus: subtract smooth baseline

## Slide 100: nonBragg extracts background
Flux
Exposure
Density
Thickness
Gain, offset
spot remover

## Slide 101
FOM from “dm”
Correlation to final map
Phasing success vs Figure of Merit
Hunter et al. (2016)."Selenium anomalous phasing XFEL", Nature Comm. 7, 13388.
http://cxidb.org/id54-SfjMJjaBny/id-54.html http://cxidb.org/id55-BWuBDSUrBy/id-55.html
Adjusting:
Solvent content
Resolution
SDfac Sdadd
Cycles of dm
“mode”
“scheme”
NCS radius
NCS cycles
Phase blur

## Slide 102
Number of counts/pixel
frequency
Gaussian vs Poisson distributions
Long-term average:
1 photon/pixel

## Slide 103
Number of counts/pixel
frequency
Central limit theorem fails on weak images
Expect: ~6
“9-sigma outliers”
On 6x106 pixel detector
at 1 photon/pixel

## Slide 104: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.
Riso ≈ 0.7 %/MGy