## Slide 3: I’m hiring!
UCSF Beamline Engineer
Sole member of “Holton Lab” – (replacing retiree)
Methods development
Inventing devices
Software and HPC
All things structure
User support
$106k - $225k /y

## Slide 4: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1: TomAlberTron
NIH NIGMS R01 GM124149 (Holton)
NIH NIAID P50 AI150476 (Krogan)
NIH NIGMS P30 GM124169 (Adams)
DOE-BER IDAT (Hura)
NIH NIGMS P30 GM133894 (Hodgson)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
James Fraser Nevan Krogan
Paul Adams John Tainer Greg Hura Nick Sauter
Pavel Afonine Tom Terwilliger
Aina Cohen
https://bl831.als.lbl.gov/~jamesh/powerpoint/PDC_tangle_2024.pptx

## Slide 5: Why is a beamline guy doing refinement things?
Because: the future of crystallography has alternate conformations
Single-conf models
poor resolution
Low signal/noise
Phase Problem
Dynamics?
Mechanism?
Small signal?
Overlapping states?
https://bl831.als.lbl.gov/~jamesh/powerpoint/PDC_tangle_2024.pptx

## Slide 6: The UNTANGLE Challenge
11) Build better than the best:
as-good or better wE, Rfree as best.pdb
non-equivalent ensemble
10) Recover best.pdb from refme.mtz
true phases, auto-building allowed
no cheating (don’t use best.pdb as guide)
Prove: true ensemble is unique and can be recovered
best.pdb
refme.mtz
$1000
$500
https://github.com/jmholton/UnTangle

## Slide 7: verified Score sheet
wE | Rwork | Rfree | method
185 | 20.6 | 21.4 | Alphafold2
109.6 | 8.87 | 9.44 | Phenix.ensemble_refine
97.3 | 8.84 | 9.27 | qFit best
91.7 | 3.64 | 4.27 | manual
80.5 | 4.31 | 4.75 | lotswrong
65.2 | 6.35 | 6.93 | Amber24
54.6 | 5.87 | 6.57 | single conf w aniso B
33.5 | 2.94 | 3.32 | One thing wrong: Ala39
23.5 | 2.95 | 3.31 | One thing wrong: Val1
21.4 | 3.12 | 3.48 | Rectified Simulated annealing
18.1 | 17.9 | 18.4 | Phenix autobuild
18.2 | 2.79 | 3.14 | best (ground truth)

## Slide 8: Map Noise: via Parseval’s Theorem
e- number of electrons in peak
7 number of electrons in typical atom
R Riso or Rfree
ρ electron density peak
σ rms deviation expected

## Slide 9
Rwork = 0.04
Rfree = 0.05
6σ = 1 e-
Simulation:
Realistic noise
“perfect” model
Hydrogen: visible at 3.5 Å resolution!
cut at 5 Å :
Rfree = 0.01

## Slide 10: Model building: real vs sim data
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.
multi
multi
multi
multi
single
single
single
single

## Slide 11: Model building: real vs sim data
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.
multi
single conf
Multi conf ground truth
Single conf ground

## Slide 12
Rwork: 0.0823
Rfree: 0.1106
bond: 0.014 Å
angle: 1.92°
6σ
MoPro: 1.15
Clash: 0.49
Cβdev: 20
Rota: 1.7%
Rama: 0.03%
reso: 1.0 Å
Real Data
1.2 σ
48-copy ensemble
3 params
per observation

## Slide 13
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3 | 3.1 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.8 | 3.9 | 4 | 4.0999999999999996 | 4.2 | 4.3 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.7 | 4.8 | 4.9000000000000004 | 5 | 5.0999999999999996 | 5.2 | 5.3 | 5.4 | 5.5 | 5.6 | 5.7 | 5.8 | 5.9 | 6 | 6.1 | 6.2 | 6.3 | 6.4 | 6.5 | 6.6 | 6.7 | 6.8 | 6.9 | 7 | 7.1 | 7.2 | 7.3 | 7.4 | 7.5 | 7.6 | 7.7 | 7.8 | 7.9 | 8 | 8.1 | 8.1999999999999993 | 8.3000000000000007 | 8.4 | 8.5 | 8.6 | 8.6999999999999993 | 8.8000000000000007 | 8.9 | 9 | 9.1 | 9.1999999999999993 | 9.3000000000000007 | 9.4 | 9.5 | 9.6 | 9.6999999999999993 | 9.8000000000000007 | 9.9
data | 0.0045981 | 0.29107 | 0.84581 | 0.15221 | 0.58554 | 0.19348 | 0.81062 | 0.17353 | 0.48498 | 0.15186
Over-Fitting data
Map density
position

## Slide 14
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3 | 3.1 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.8 | 3.9 | 4 | 4.0999999999999996 | 4.2 | 4.3 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.7 | 4.8 | 4.9000000000000004 | 5 | 5.0999999999999996 | 5.2 | 5.3 | 5.4 | 5.5 | 5.6 | 5.7 | 5.8 | 5.9 | 6 | 6.1 | 6.2 | 6.3 | 6.4 | 6.5 | 6.6 | 6.7 | 6.8 | 6.9 | 7 | 7.1 | 7.2 | 7.3 | 7.4 | 7.5 | 7.6 | 7.7 | 7.8 | 7.9 | 8 | 8.1 | 8.1999999999999993 | 8.3000000000000007 | 8.4 | 8.5 | 8.6 | 8.6999999999999993 | 8.8000000000000007 | 8.9 | 9 | 9.1 | 9.1999999999999993 | 9.3000000000000007 | 9.4 | 9.5 | 9.6 | 9.6999999999999993 | 9.8000000000000007 | 9.9
data | 0.0045981 | 0.29107 | 0.84581 | 0.15221 | 0.58554 | 0.19348 | 0.81062 | 0.17353 | 0.48498 | 0.15186
1 param | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269
Over-Fitting data
Map density
position

## Slide 15
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3 | 3.1 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.8 | 3.9 | 4 | 4.0999999999999996 | 4.2 | 4.3 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.7 | 4.8 | 4.9000000000000004 | 5 | 5.0999999999999996 | 5.2 | 5.3 | 5.4 | 5.5 | 5.6 | 5.7 | 5.8 | 5.9 | 6 | 6.1 | 6.2 | 6.3 | 6.4 | 6.5 | 6.6 | 6.7 | 6.8 | 6.9 | 7 | 7.1 | 7.2 | 7.3 | 7.4 | 7.5 | 7.6 | 7.7 | 7.8 | 7.9 | 8 | 8.1 | 8.1999999999999993 | 8.3000000000000007 | 8.4 | 8.5 | 8.6 | 8.6999999999999993 | 8.8000000000000007 | 8.9 | 9 | 9.1 | 9.1999999999999993 | 9.3000000000000007 | 9.4 | 9.5 | 9.6 | 9.6999999999999993 | 9.8000000000000007 | 9.9
data | 0.0045981 | 0.29107 | 0.84581 | 0.15221 | 0.58554 | 0.19348 | 0.81062 | 0.17353 | 0.48498 | 0.15186
1 param | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269
3 params | 0.28281 | 0.37054 | 0.43452 | 0.47477 | 0.49127 | 0.48404 | 0.45306 | 0.39834 | 0.31988 | 0.21767
Over-Fitting data
Map density
position

## Slide 16
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3 | 3.1 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.8 | 3.9 | 4 | 4.0999999999999996 | 4.2 | 4.3 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.7 | 4.8 | 4.9000000000000004 | 5 | 5.0999999999999996 | 5.2 | 5.3 | 5.4 | 5.5 | 5.6 | 5.7 | 5.8 | 5.9 | 6 | 6.1 | 6.2 | 6.3 | 6.4 | 6.5 | 6.6 | 6.7 | 6.8 | 6.9 | 7 | 7.1 | 7.2 | 7.3 | 7.4 | 7.5 | 7.6 | 7.7 | 7.8 | 7.9 | 8 | 8.1 | 8.1999999999999993 | 8.3000000000000007 | 8.4 | 8.5 | 8.6 | 8.6999999999999993 | 8.8000000000000007 | 8.9 | 9 | 9.1 | 9.1999999999999993 | 9.3000000000000007 | 9.4 | 9.5 | 9.6 | 9.6999999999999993 | 9.8000000000000007 | 9.9
data | 0.0045981 | 0.29107 | 0.84581 | 0.15221 | 0.58554 | 0.19348 | 0.81062 | 0.17353 | 0.48498 | 0.15186
1 param | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269 | 0.39269
3 params | 0.28281 | 0.37054 | 0.43452 | 0.47477 | 0.49127 | 0.48404 | 0.45306 | 0.39834 | 0.31988 | 0.21767
Over-Fitting data
Map density
position
Rwork ≈ 0
Nparams= Nobs

## Slide 17
Under-Fitting data
Map density
position
Rwork > 0
Nparams> Nobs

## Slide 18
Rwork: 0.0823
Rfree: 0.1106
bond: 0.014 Å
angle: 1.92°
6σ
MoPro: 1.15
Clash: 0.49
Cβdev: 20
Rota: 1.7%
Rama: 0.03%
reso: 1.0 Å
under-fitting:
Rwork > 0

## Slide 19
What is holding it back?
30°
peptide
bond twist
48-copy ensemble
3 parameters
per observation!

## Slide 20: Why does ensemble refinement suck? (3 parameters/observation and Rwork still high!)
The chains are “tangled”

## Slide 21
Local Minimum
Ground Truth
What do you mean, “tangled”?

## Slide 22
A
B
A
B
B
A
It takes two to tangle
Chemical
strain
density
fit
energy
tangled
barrier
untangled

## Slide 23: Right answer
R = 0.8%
rms bond = 0.0002

## Slide 24: swap assignments
R = 0.8%
rms bond = 0.04

## Slide 25: Refine – low x-ray weight
R = 14.3%
rms bond = 0.0002

## Slide 26: Refine – step 61
R = 6.8%
rms bond = 0.001

## Slide 27: Refine – high x-ray weight
R = 1.2%
rms bond = 0.06

## Slide 28: Refine – low x-ray weight
R = 14.3%
rms bond = 0.0002

## Slide 29: Final compromise
R = 7.07%
rms bond = 0.001

## Slide 30: Right answer
R = 0.8%
rms bond = 0.0002

## Slide 31: UNTANGLE: sim-data Ground Truth
As simple as possible:
  2 conformers
  50:50 occupancy
Accessible
  64 residues
  78 waters
Every chance of success
  1.0 Å reso
  “one thing wrong”
  flat bulk solvent
  no false outliers
  phenix, refmac, shelxl
  clear score
  Experimental error only
  perfect phases

## Slide 32
Ala39
wE=18.2
-0.3σ
-0.2σ
0.8σ
angle
N-Cα
bond
A B conformers
Sim challenge data

## Slide 33
Ala39
wE=63.5
-9σ
+11σ
5σ
angle
N-Cα
bond
A B conformers
Sim challenge data: “otw39”

## Slide 34
Ala39
wE=63.5
-9σ
+11σ
5σ
angle
N-Cα
bond
A B conformers
Sim challenge data: “otw39”

## Slide 35
Arg62
wE=63.5
A B conformers
4σ
Cγ-Cδ
bond
2.8 Å
2.7σ torsion
sim data

## Slide 36
Arg62
wE=50.7
A B conformers
2.8 Å
2σ
angle
sim data

## Slide 37
Arg62
wE=18.2
A B conformers
3.0 Å
1σ
angle
0.3σ
Cγ-Cδ
bond
1.6σ torsion
sim data

## Slide 38
Tyr14
wE=33.1
A B conformers
3.0 Å
sim data

## Slide 39
Tyr14
A B conformers
3.2 Å
wE=18.2
sim data

## Slide 40
Cys16
A B conformers
wE=21.4
2.7σ
angle
sim data

## Slide 41
Cys16
A B conformers
wE=18.2
1.5σ
angle
sim data

## Slide 42: Statistical Potential
E “energy”
v model value
v0 ideal value
σ rms deviation expected
Outlier problem:
1 x 6σ ≈ 36x 1σ
solution: weight by
“probability its not noise”

## Slide 43: wE score: key concepts
Energy ↔ dev/sigma ↔ Probability
Probability outlier is not noise
  “clip” outlier energy at “10”
  Not so sharp transition to outlier
Tighter Non-bond (Leonard-Jones)

## Slide 44
real data
-80°
Torsion outlier
Glu32
Genuine outlier
in ground truth

## Slide 45
A B conformers
real data
-107°
torsion outlier
Cys12
Genuine outlier
in ground truth

## Slide 46: New Tools!
phenix.holton_geometry_validation test.pdb
phenix.create_alt_conf phenix_autobuild.pdb refme.mtz \
nproc=48
phenix.refine \
model.pdb refme.mtz \
main.number_of_mac=10 \
fit_altlocs_method=masking \
ordered_solvent=true \
include_altlocs=true \
ordered_solvent.mode=every_macro_cycle_after_first \
refine_oat=true
Tom
Terwilliger
Pavel Afonine

## Slide 47: Summary
Rfree < 3% → single e-
  Not over-fitting
Main barrier: tangled ensemble
Sensible scoring function
  Probability its not noise
  some outliers are real
Recover underlying ensemble
  Might be required!
Cooperative motions
$1000
$500
https://bl831.als.lbl.gov/~jamesh/powerpoint/PDC_tangle_2024.pptx

## Slide 48: verified Score sheet
wE | Rwork | Rfree | method
185 | 20.6 | 21.4 | Alphafold2
109.6 | 8.87 | 9.44 | Phenix.ensemble_refine
97.3 | 8.84 | 9.27 | qFit best
91.7 | 3.64 | 4.27 | manual
80.5 | 4.31 | 4.75 | lotswrong
65.2 | 6.35 | 6.93 | Amber24
54.6 | 5.87 | 6.57 | single conf w aniso B
33.5 | 2.94 | 3.32 | One thing wrong: Ala39
23.5 | 2.95 | 3.31 | One thing wrong: Val1
21.4 | 3.12 | 3.48 | Rectified Simulated annealing
18.1 | 17.9 | 18.4 | Phenix autobuild
18.2 | 2.79 | 3.14 | best (ground truth)

## Slide 49: Statistical Potential
E “energy”
v model value
v0 ideal value
σ rms deviation expected
Outlier problem:
1 x 6σ ≈ 36x 1σ
solution: weight by
“probability its not noise”

## Slide 50: wE score: key concepts
Probability outlier is not noise
  “clip” outlier energy at “10”
  Not so sharp transition to outlier
Tighter Non-bond (Leonard-Jones)

## Slide 51: Probability that it’s not noise
Pnn probability
v-v0 deviation from ideal
σ rms deviation expected
erf() integral of a Gaussian
Nthings number of trials
erf() = 68%
erf() = 95%
= 2%
= 63%
= 53%

## Slide 52: Probability that it’s not noise softer
Pnn probability
v-v0 deviation from ideal
σ rms deviation expected
inverf() inverse erf()
Nthings number of trials
1
0.5
0
3
6
N=1
N=1 soft
max sigma deviate
P
4
5
2
1
N=10,000
N=10,000
soft

## Slide 53: Probability that it’s not noise average/sum of Nthings
χ2 test
Probability
That its
Gaussian
tie breaker
Nthings

## Slide 54: Sensible scoring function
  Statistical potential
    bonds, angles, planes, torsions, chiral
  Leonard-Jones vdW
    non-bond and clashes
  Probability -> σ dev
    - Rota, rama
  Peptide bond
    σ → 5°
  Cβdev
    σ = 0.05 Å
4
2
0
3
4
5
van der Waals
Phenix/refmac
Atomic separation (Å)
Energy
-1
2
1

## Slide 55: weighted Energy scoring function
clip(E)
10
5
0
3
6
8
N=10
N=10,000
max sigma deviate
wE
max() = worst outlier
validation types
Nbonds
wE
phenix.holton_geometry_validation

## Slide 56
real data
-80°
Torsion outlier
Glu32
Genuine outlier
in ground truth

## Slide 57
A B conformers
real data
-107°
torsion outlier
Cys12
Genuine outlier
in ground truth

## Slide 58: UNTANGLE scoring function
score UNTANGLE Challenge score
wE weighted energy avg + worst
σR experimental error (2%)
https://github.com/jmholton/UnTangle

## Slide 59
wE=18.2

## Slide 60
wE=21.4

## Slide 61: Muybridge’s galloping horse (1872)

## Slide 62: average structure: galloping horse

## Slide 63: Horses have bones
+/- 0.01

## Slide 64: Horses have bones

## Slide 65: Muybridge’s galloping horse 0

## Slide 66: Muybridge’s galloping horse 1

## Slide 67: Muybridge’s galloping horse 2

## Slide 68: Muybridge’s galloping horse 3

## Slide 69: Muybridge’s galloping horse 4

## Slide 70: Muybridge’s galloping horse 5

## Slide 71: Muybridge’s galloping horse 6

## Slide 72: Muybridge’s galloping horse 7

## Slide 73: Muybridge’s galloping horse 8

## Slide 74: Muybridge’s galloping horse 9

## Slide 75: Muybridge’s galloping horse 10

## Slide 76: Muybridge’s galloping horse 11

## Slide 77: Muybridge’s galloping horse 12

## Slide 78: Muybridge’s galloping horse 13

## Slide 79: Muybridge’s galloping horse 14

## Slide 80: ensemble refine ???

## Slide 81: Differences
horse
~2 m
Stiff backbone
Bone sigma ~ 1 mm
4 joints/leg
Continuous angle
No torision
Concerted motion
molecule
~100 Å
Stiff backbone
Bond sigma = 0.01 Å
0-4 chi angles
Angle sigma ~ 1°
Rotamers
Concerted motion