## Slide 1: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1: TomAlberTron
NIH NIAID P50 AI150476
NIH NIGMS P30 GM124169
DOE-BER Integrated Diffraction Analysis Technologies (IDAT)
NIH NIGMS P30 GM133894
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser Nevan Krogan
Paul Adams John Tainer Greg Hura Nick Sauter
Aina Cohen Art Lyubimov Jeney Wierman

## Slide 2
ber
structural
bio
portal.org

## Slide 3: Powerpoint file available:
https://bl831.als.lbl.gov/~jamesh/powerpoint/RapiData_XDS_2022.pptx
JMHolton@lbl.gov

## Slide 4: XDS X-ray diffraction data reduction engine
Diffraction image data
List of spot intensities (text)

## Slide 5
XDS native user interface: a text file!

## Slide 7
XDS native user interface

## Slide 8
The “prompt”
Cursor
does not move
with mouse
Mouse
can be used
To select and paste
But all pasted text
Goes to the cursor

## Slide 9: How to start XDS
~]$ cd
~]$ mkdir xds_tutorial
~]$ cd xds_tutorial
~]$ ln –sf /data/holton/demo .
~]$ pxproc_dialog.sh
~]$ ssh pxproc12
@pxproc ~]$ cd xds_tutorial
]$ xdsgui
Space!
underscore
prompt
Do not type!
Enter
Space!

## Slide 10
xdsgui – a graphical interface for XDS

## Slide 11
xdsgui – load an image

## Slide 12
xdsgui – a GUI for text!

## Slide 13
xdsconv – make an “mtz” file
output_file_name.mtz

## Slide 14
xdsgui – nuts, bolts, bells & whistles

## Slide 15
XYCORR– setting things up

## Slide 16: Beam center vs “origin”
direct beam

## Slide 17: Beam center vs “origin”
origin
direct beam

## Slide 18: Correct beam center
155.063 155.647
159.353 155.063
159.301 155.011
1512.73 1554.57
155.063 159.356 -250
ADXV
HKL2000
MOSFLM
XDS
DIALS

## Slide 19
XYCORR– setting things up

## Slide 20
XYCORR– setting things up

## Slide 21: Pilatus: 1-module shift

## Slide 22
Pilatus: 1-module shift

## Slide 23
Pilatus: 1-module shift

## Slide 24: Detector pixels are 3D
51 μm
31 μm thick
17%
loss
Typical CCD
Mean Penetration depth 12 keV:
17.5 μm Gd2O2S 237 μm Si
8%
side
loss
172 μm
26% loss
320 μm thick
Pilatus
53%
side
loss
photon
75 μm
15%
loss
450 μm thick
Eiger
76%
side
loss
photon
Arrival angle of 2 Å spot: 29°

## Slide 25
XYCORR– setting things up

## Slide 26
INIT – look at the background

## Slide 27
INIT – look at the background

## Slide 28
COLSPOT – the spot picker

## Slide 29
COLSPOT – the spot picker

## Slide 30
IDXREF – auto-indexing

## Slide 31: XPARM.XDS
XPARM.XDS VERSION Feb 5, 2021 BUILT=20210323
1 270.0000 0.2000 0.999971 0.007404 -0.001831
0.979460 0.000711 0.000291 1.020970
96 78.8215 78.8215 37.1784 90.000 90.000 90.000
36.338257 9.327419 -69.320709
26.357738 70.532730 23.307367
30.559622 -16.002089 13.866352
1 2463 2527 0.172000 0.172000
1231.500000 1263.500000 189.160004
1.000000 0.000000 0.000000
0.000000 1.000000 0.000000
0.000000 0.000000 1.000000
1 1 2463 1 2527
0.00 0.00 0.00 1.00000 0.00000 0.00000 0.00000 1.00000 0.00000
First image number
Starting phi
Delta-phi
spindle vector
beam vector
unit cell
a
b
c
space
group
number
wavelen
cell vectors
real space
det panels
origin
distance
pixels
pixel size
x
y
z
Detector fast/slow
Panel #

## Slide 32
IDXREF – auto-indexing
BRAVAIS- POSSIBLE SPACE-GROUPS FOR PROTEIN CRYSTALS
TYPE [SPACE GROUP NUMBER,SYMBOL]
aP [1,P1]
mP [3,P2] [4,P2(1)]
mC,mI [5,C2]
oP [16,P222] [17,P222(1)] [18,P2(1)2(1)2] [19,P2(1)2(1)2(1)]
oC [21,C222] [20,C222(1)]
oF [22,F222]
oI [23,I222] [24,I2(1)2(1)2(1)]
tP [75,P4] [76,P4(1)] [77,P4(2)] [78,P4(3)] [89,P422] [90,P42(1)2]
[91,P4(1)22] [92,P4(1)2(1)2] [93,P4(2)22] [94,P4(2)2(1)2]
[95,P4(3)22] [96,P4(3)2(1)2]
tI [79,I4] [80,I4(1)] [97,I422] [98,I4(1)22]
hP [143,P3] [144,P3(1)] [145,P3(2)] [149,P312] [150,P321] [151,P3(1)12]
[152,P3(1)21] [153,P3(2)12] [154,P3(2)21] [168,P6] [169,P6(1)]
[170,P6(5)] [171,P6(2)] [172,P6(4)] [173,P6(3)] [177,P622]
[178,P6(1)22] [179,P6(5)22] [180,P6(2)22] [181,P6(4)22] [182,P6(3)22]
hR [146,R3] [155,R32]
cP [195,P23] [198,P2(1)3] [207,P432] [208,P4(2)32] [212,P4(3)32]
[213,P4(1)32]
cF [196,F23] [209,F432] [210,F4(1)32]
cI [197,I23] [199,I2(1)3] [211,I432] [214,I4(1)32]

## Slide 33: Trick Question: What is the space group?
a = 63 b = 63 c = 63
α = 90 β = 90 γ = 90

## Slide 34: What you know when:
Autoindexing: Lattice (14)
Scaling: Point Group (43)
Phasing: Space Group (84)

## Slide 35: Pitfalls: sub-space groups
P622
What else?
P6122 P6522 P6222 P6422 P6322
P6 P61 P65 P62 P64 P63
P312 P321 P3112 P3121 P3212 P3221
P3 P31 P32
P2 P21 C2 C222 C2221
P1
zanuda

## Slide 36: Asymmetric Unit (ASU)
Smallest part of the crystal
that you can use to build up the rest of the crystal
with symmetry operations
Unit Cell
Smallest part of the crystal
that you can use to build up the rest of the crystal
with translation symmetry only
“NCS ASU”
Builds ASU with Non-crystallographic symmetry operations

## Slide 37: Frequency of Space Groups in PDB
13007 | P212121 | 566 | R32 | 191 | P6322 | 74 | P4322 | 36 | P3212
9629 | P21 | 491 | P6522 | 187 | P213 | 71 | P4122 | 30 | P622
5300 | C2 | 474 | P61 | 161 | P6 | 70 | P64 | 24 | F4132
3021 | P21212 | 421 | P65 | 144 | P4212 | 70 | P6222 | 22 | P4332
2543 | C2221 | 353 | P41 | 142 | I23 | 67 | P6422 | 22 | P422
2109 | P1 | 351 | P63 | 132 | F432 | 66 | F222 | 22 | P23
2030 | P43212 | 286 | P31 | 124 | P321 | 63 | P62 | 19 | P3112
1565 | P3221 | 257 | I422 | 115 | I41 | 59 | P4132 | 18 | P4222
1359 | P41212 | 253 | P42212 | 103 | P3 | 46 | P2221 | 18 | I4132
1198 | P3121 | 249 | I4 | 99 | I213 | 43 | P4 | 16 | P432
1147 | I222 | 246 | P43 | 94 | C222 | 43 | I432 | 8 | P4232
825 | R3 | 239 | I4122 | 93 | P2 | 40 | P42 | 3 | P222
620 | P6122 | 193 | P32 | 82 | I212121 | 37 | F23 | 2 | P312

## Slide 38
DEFPIX – pixels good and bad

## Slide 39
DEFPIX – pixels good and bad

## Slide 40
INTEGRATE – measure the spots!

## Slide 41
INTEGRATE – measure the spots!

## Slide 42
Ewald’s “mosaic” picture

## Slide 43
Ewald’s “mosaic” picture

## Slide 44
Ewald’s “mosaic” picture
What is
this stuff?

## Slide 45
Darwin’s original picture

## Slide 46
“mosaicity” with visible light

## Slide 47: mosaic spread = 0 º

## Slide 48: mosaic spread = 0.1º

## Slide 49: mosaic spread = 0.2º

## Slide 50: mosaic spread = 0.4º

## Slide 51: mosaic spread = 0.6º

## Slide 52: mosaic spread = 0.8º

## Slide 53: mosaic spread = 1.0º

## Slide 54: mosaic spread = 1.5º

## Slide 55: mosaic spread = 2.0º

## Slide 56: mosaic spread = 2.5º

## Slide 57: mosaic spread = 3.2º

## Slide 58: mosaic spread = 6.4º

## Slide 59: mosaic spread = 12.8º

## Slide 60: Spot Shape
Ewald sphere
(h,k,l)

## Slide 61: Spot Shape
Ewald sphere
(h,k,l)
d*

## Slide 62: Spot Shape
Ewald sphere
spindle axis
(h,k,l)
d*

## Slide 63: Spot Shape
Ewald sphere
spindle axis
Φ circle
(h,k,l)

## Slide 64: Spot Shape
Ewald sphere
spindle axis
Φ circle
(h,k,l)

## Slide 65: Spot Shape
Ewald sphere
spindle axis
Φ circle
diffracted ray
(h,k,l)

## Slide 66: Spot Shape
Ewald sphere
spindle axis
Φ circle
diffracted ray
(h,k,l)
d*
λ*
λ*

## Slide 67: Spot Shape
Ewald sphere
spindle axis
Φ circle
diffracted ray
(h,k,l)
d*
λ*
λ*
θ
λ = 2 d sin(θ)

## Slide 68: mosaic spread
Ewald sphere
spindle axis
Φ circle
diffracted ray
(h,k,l)
λ*
λ*
d*
d*

## Slide 69: mosaic spread
Ewald sphere
spindle axis
Φ circle
diffracted rays
(h,k,l)
d*
d*

## Slide 70
INTEGRATE – measure the spots!

## Slide 71: beam divergence
Ewald sphere
spindle axis
Φ circle
diffracted ray
(h,k,l)
d*
λ*
λ*

## Slide 72: beam divergence
spindle axis
Φ circle
diffracted ray
(h,k,l)
d*
Ewald sphere
λ*
λ*

## Slide 73: divergence = 0 º

## Slide 74: divergence = 0.3 º

## Slide 75: spectral dispersion
Ewald sphere
spindle axis
Φ circle
diffracted ray
(h,k,l)
d*
λ*
λ*

## Slide 76: spectral dispersion
Ewald sphere
spindle axis
Φ circle
diffracted ray
(h,k,l)
d*
λ’*
λ’*

## Slide 77: dispersion = 0

## Slide 78: dispersion = 0.014% (Si 111)

## Slide 79: dispersion = 0.25% (CuKα)

## Slide 80: dispersion = 0.6%

## Slide 81: dispersion = 1.3%

## Slide 82: dispersion = 2.6%

## Slide 83: dispersion = 5.1%

## Slide 84: spot shape
Ewald sphere
spindle axis
Φ circle
diffracted ray
(h,k,l)
d*
λ’*
λ’*
Ewald sphere
spindle axis
Φ circle
diffracted ray
(h,k,l)
d*
λ*
λ*
spindle axis
Φ circle
diffracted ray
(h,k,l)
d*
Ewald sphere
λ*
λ*
Ewald sphere
spindle axis
Φ circle
diffracted rays
(h,k,l)
d*
d*

## Slide 85
CORRECT – scale all the “factors”

## Slide 86: Polarization factor
1.0
0.45
+

## Slide 87: Lorentz factor
+
50x
1.2x
550x
3x
10x

## Slide 88: The “Lorentz zone”

## Slide 89: A few other corrections…
Meisburger, et. al. Nat Commun 11, 1271 (2020). https://doi.org/10.1038

## Slide 90: attenuation factor
Bouguer, P. (1729). Essai d'optique sur la gradation de la lumière.
Lambert, J. H. (1760). Photometria: sive De mensura et gradibus luminis, colorum et umbrae. E. Klett.
Beer, A. (1852)."Bestimmung der Absorption des rothen Lichts in farbigen Flüssigkeiten", Ann. Phys. Chem 86, 78-90.
A = = exp[-μxtal(txi+ txo)
-μsolvent(tsi + tso)]
IT
Ibeam
μxtal
txi
txo
tsi
tso
txi
txo
tsi
tso
txi
txo
tsi
tso
μsolvent

## Slide 91: B factor from image gazing
B = 500

## Slide 92: B factor from image gazing
B = 20

## Slide 93
CORRECT – after all the “factors”

## Slide 94
xdscc12 – any outlier images?

## Slide 95
xdsstat – radiation damage “limit”

## Slide 96
xdsconv – make an “mtz” file

## Slide 97
xscale – merge multiple runs

## Slide 98
CORRECT – scale all the “factors”

## Slide 99: Re-indexing cheat sheet
Dauter, Z. (1999). "Data-collection strategies." Acta Cryst. D 55(10): 1703-1717.

## Slide 100: Zero-dose extrapolation (ZDE)
Diederichs, K. (2006). "Some aspects of quantitative analysis and correction of radiation damage." Acta Cryst. D 62(1): 96-101.
OUTPUT_FILE= multi-merge.hkl
INPUT_FILE= ../xds_1/XDS_ASCII.HKL
CRYSTAL_NAME= ip
INPUT_FILE= ../xds_2/XDS_ASCII.HKL
! same crystal, but translated
CRYSTAL_NAME= ip

## Slide 101
xscale – final stats

## Slide 102: XDS: CORRECT.LP or XSCALE.LP
SUBSET OF INTENSITY DATA WITH SIGNAL/NOISE >= -3.0 AS FUNCTION OF RESOLUTION
RESOLUTION NUMBER OF REFLECTIONS COMPLETENESS R-FACTOR R-FACTOR COMPARED I/SIGMA R-meas CC(1/2) Anomal SigAno Nano
LIMIT OBSERVED UNIQUE POSSIBLE OF DATA observed expected Corr
6.39 4103 2517 3135 80.3% 1.7% 1.8% 3018 33.77 2.3% 99.9* 21* 1.012 533
4.54 7339 4970 5544 89.6% 2.6% 2.6% 4585 22.56 3.6% 99.8* 9 0.914 796
3.72 9442 6724 7186 93.6% 2.8% 2.9% 5327 19.99 4.0% 99.7* 9 0.859 877
3.22 11077 7997 8486 94.2% 4.8% 4.9% 6094 12.27 6.8% 99.3* -1 0.784 913
2.88 12408 8851 9595 92.2% 10.0% 10.1% 7068 6.01 14.2% 97.8* -2 0.799 1012
2.63 13673 9561 10662 89.7% 20.8% 20.8% 8185 3.10 29.4% 88.8* -4 0.776 1274
2.44 14360 9852 11510 85.6% 34.5% 34.7% 8981 1.90 48.8% 75.9* 2 0.765 1525
2.28 9501 6495 12416 52.3% 61.8% 59.6% 5991 1.14 87.3% 53.5* -2 0.722 1031
2.15 4567 3307 13210 25.0% 120.5% 120.3% 2520 0.59 170.4% 21.9* 4 0.693 408
total 86470 60274 81744 73.7% 6.7% 6.7% 51769 8.97 9.5% 99.5* 2 0.804 8369

## Slide 103: XDS: CORRECT.LP or XSCALE.LP
******************************************************************************
CORRECTION PARAMETERS FOR THE STANDARD ERROR OF REFLECTION INTENSITIES
******************************************************************************
The variance v0(I) of the intensity I obtained from counting statistics is
replaced by v(I)=a*(v0(I)+b*I^2). The model parameters a, b are chosen to
minimize the discrepancies between v(I) and the variance estimated from
sample statistics of symmetry related reflections. This model implicates
an asymptotic limit ISa=1/SQRT(a*b) for the highest I/Sigma(I) that the
experimental setup can produce (Diederichs (2010) Acta Cryst D66, 733-740).
a b ISa
3.806E+00 1.080E-04 49.32

## Slide 104: CCP4: aimless log
$TABLE: Analysis against resolution, XDSdataset:
$GRAPHS:I/sigma, Mean Mn(I)/sd(Mn(I)):0|0.216023x0|137.14:2,13,14:
:Rmerge, Rfull, Rmeas, Rpim v Resolution:0|0.216023x0|1.70834:2,4,5,6,7:
:Average I, RMSdeviation and Sd:0|0.216023x0|1650.8:2,10,11,12:
:Fractional bias:0|0.216023x0|0:2,15:
$$
N 1/d^2 Dmid Rmrg Rfull Rcum Rmeas Rpim Nmeas AvI RMSdev sd I/RMS Mn(I/sd) FrcBias $$ $$
1 0.0064 12.55 0.020 0.020 0.020 0.021 0.006 13115 1651 57 42 29.2 137.1 -
2 0.0191 7.24 0.027 0.027 0.024 0.028 0.008 24753 1171 47 42 25.0 105.2 -
3 0.0318 5.61 0.038 0.038 0.029 0.040 0.012 32197 857 46 43 18.4 79.6 -
4 0.0445 4.74 0.034 0.034 0.031 0.035 0.010 37743 1212 57 53 21.4 91.2 -
5 0.0572 4.18 0.036 0.036 0.032 0.038 0.011 42642 1181 59 57 19.9 83.8 -
6 0.0699 3.78 0.049 0.049 0.036 0.052 0.015 47224 883 59 57 15.1 65.1 -
7 0.0826 3.48 0.065 0.065 0.040 0.068 0.020 51052 685 59 58 11.7 50.9 -
8 0.0953 3.24 0.096 0.096 0.045 0.100 0.029 54636 448 56 56 8.0 35.0 -
9 0.1080 3.04 0.151 0.151 0.050 0.158 0.046 58072 268 53 53 5.1 22.7 -
10 0.1207 2.88 0.229 0.229 0.056 0.240 0.070 60731 171 51 51 3.3 15.4 -
11 0.1334 2.74 0.314 0.314 0.063 0.329 0.097 63807 125 51 51 2.4 11.3 -
12 0.1461 2.62 0.406 0.406 0.070 0.425 0.125 66241 98 51 52 1.9 8.7 -
13 0.1588 2.51 0.537 0.537 0.078 0.562 0.166 68272 76 53 53 1.4 6.5 -
14 0.1715 2.41 0.685 0.685 0.084 0.727 0.237 54170 61 53 54 1.1 4.4 -
15 0.1843 2.33 0.886 0.886 0.088 0.950 0.333 39781 48 55 56 0.9 3.1 -
16 0.1970 2.25 1.249 1.249 0.092 1.355 0.508 29754 35 57 59 0.6 2.1 -

## Slide 105: CCP4: aimless log
$TABLE: Correlations CC(1/2) within dataset, XDSdataset:
$GRAPHS: Anom & Imean CCs v resolution:0|0.216023x0|1:2,4,7:
: RMS correlation ratio :0|0.216023x0|2.20344:2,6:
$$
N 1/d^2 Dmid CCanom Nanom RCRanom CC1/2 NImean $$ $$
1 0.0064 12.55 0.659 499 2.203 1.000 669
2 0.0191 7.24 0.550 975 1.853 1.000 1155
3 0.0318 5.61 0.527 1295 1.798 1.000 1479
16 0.1970 2.25 0.037 2123 1.038 0.711 2275
17 0.2097 2.18 0.043 1682 1.044 0.460 1877

## Slide 106: CC = 0.999
Chart: 

## Slide 107: CC = 0.0
Chart: 

## Slide 108: CC = 0.9
Chart: 

## Slide 109: CC = 0.8
Chart: 

## Slide 110: CC = 0.7
Chart: 

## Slide 111: CC = 0.6
Chart: 

## Slide 112: CC = 0.5
Chart: 

## Slide 113: CC = 0.4
Chart: 

## Slide 114: CC = 0.3
Chart: 

## Slide 115: CC = 0.2
Chart: 

## Slide 116: CC = 0.1
Chart: 

## Slide 117: CC = 0.1
Chart: 

## Slide 118: CC = 0.0
Chart: 

## Slide 119: Summary
XYCORR
INIT
COLSPOT
IDXREF
DEFPIX
INTEGRATE
CORRECT

## Slide 120: Supply & Demand:

## Slide 121
Nov 2020- Dec 2021
20-Nov
20-Dec
21-Jan
21-Feb
21-Mar
21-Apr
21-May
21-Jun
21-Jul
21-Aug
21-Sep
21-Oct
21-Nov
21-Dec

## Slide 122
Nov 2022- Dec 2023
22-Nov
22-Dec
23-Jan
23-Feb
23-Mar
23-Apr
23-May
23-Jun
23-Jul
23-Aug
23-Sep
23-Oct
23-Nov
23-Dec
assuming here that basis schedules from 2021 will repeat

## Slide 123
Nov 2023- Dec 2024
23-Nov
23-Dec
24-Jan
24-Feb
24-Mar
24-Apr
24-May
24-Jun
24-Jul
24-Aug
24-Sep
24-Oct
24-Nov
24-Dec
assuming here that basis schedules from 2021 will repeat

## Slide 124: 100% SeMet incorporation
Trivial to solve

## Slide 125: 100% S -Met incorporation
Impossible to solve

## Slide 126: Systematic error does not “average out”
Unless you can randomize their source

## Slide 127
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel → 0.3% error
Pilatus: subtract smooth baseline
Gollwitzer & Krumrey (2014)
J. Appl. Cryst. 47, 378

## Slide 128: Fractional error
mult > (—)2
~3%
<ΔF/F>

## Slide 129
anomalous signal
Crick, F. H. C. & Magdoff, B. S. (1956) Acta Crystallogr. 9, 901-908.
Hendrickson, W. A. & Teeter, M. M. (1981) Nature 290, 107-113.
# sites
MW (Da)
ΔF
F
≈ 1.2 f”
√
World record!
ΔF/F = 0.5%
Wang, Dauter & Dauter (2006) Acta Cryst. D 62, 1475-1483.

## Slide 130
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 131: what the is a MGy?
http://bl831.als.lbl.gov/
damage_rates.pdf
Holton J. M. (2009) J. Synchrotron Rad. 16 133-42
1 MGy = 106 J/kg

## Slide 132
How long will my crystal last?
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
ALS 4.2.2 MAD 2.2e11 75x80 3.7e+07 27.3 kGy/s 18 m 73 s
ALS 5.0.1 mono 1.6e11 100 2.0e+07 10.4 kGy/s 48 m 3.2 m
ALS 5.0.2 MAD 8e11 100 1.0e+08 51.8 kGy/s 9.6 m 39 s
ALS 5.0.3 mono 1.7e11 100 2.2e+07 11 kGy/s 45 m 3 m
ALS 8.2.1 MAD 1.8e11 100 2.3e+07 11.7 kGy/s 43 m 2.9 m
ALS 8.2.2 MAD 2.3e11 100 2.9e+07 14.9 kGy/s 34 m 2.2 m
ALS 8.3.1 MAD 9e11 70 2.3e+08 119 kGy/s 4.2 m 17 s
ALS 8.3.1 typical 6e11 70 1.6e+08 115 kGy/s 4.3 m 17 s
ALS 12.3.1 MAD 1.8e11 100 2.3e+07 11.7 kGy/s 43 m 2.9 m
ALS 12.3.1 ML 4.0e12 100 5.1e+08 513 kGy/s 58 s 3.9 s
APS 8-BM MAD 1e11 200 2.5e+06 1.27 kGy/s 6.6 h 26 m
APS 14-BM-C mono 5.8e10 200 1.4e+06 738 Gy/s 11 h 45 m
APS 14-BM-D MAD 3.3e9 200 8.2e+04 42 Gy/s 8.3 d 13 h
APS 14-ID-B MAD 6.0e10 200 1.5e+06 763 Gy/s 11 h 44 m
APS 17-BM MAD 1.1e11 200 2.8e+06 1.4 kGy/s 6 h 24 m
APS 17-ID MAD 2.3e11 200 5.8e+06 2.93 kGy/s 2.8 h 11 m
APS 19-BM MAD 2.0e11 70x60 4.8e+07 24.2 kGy/s 21 m 83 s
APS 19-ID MAD 1.3e13 80x40 4.1e+09 2.07 MGy/s 15 s 0.97 s
APS 19-ID typical 5.5e11 100x100 5.5e+07 28 kGy/s 18 m 71 s
APS 22-BM MAD 7e12 80x40 2.2e+09 1.23 MGy/s 24 s 1.6 s
APS 22-ID MAD 7e12 80x40 2.2e+09 1.23 MGy/s 24 s 1.6 s
APS 22-ID typical 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
APS 23-ID-B MAD 1e13 75x25 5.3e+09 3.01 MGy/s 10 s 0.66 s
APS 23-ID typical 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
APS 24-ID-C MAD 1.3e13 20x60 1.1e+10 5.23 MGy/s 5.7 s 0.38 s
APS 24-ID-E MAD 0.5e13 20x100 2.5e+09 1.19 MGy/s 25 s 1.7 s
APS 31-ID MAD 2e12 70 4.1e+08 194 kGy/s 2.6 m 10 s

## Slide 134
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 135
Holton (2009) J. Synchrotron Rad. 16 133-42
Radiation Damage World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
10/Å global damage Howells et al. (2009)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
4 R-C-COOH Garman et al. (2015)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
~1? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.06 putidaredoxin Corbett et al. (2007)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 136: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 137: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 138
The number of photons scattered
before crystal is dead
is independent
of flux & time
1 um3 = 105 photons (roomT)
1 um3 = 106 photons (synch)
1 um3 = 108 photons (XFEL)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009
(synch)