## Slide 1: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1: TomAlberTron
NIH NIGMS R01 GM124149 (Holton)
NIH NIAID P50 AI150476 (Krogan)
NIH NIGMS P30 GM124169 (Adams)
DOE-BER IDAT (Hura)
NIH NIGMS P30 GM133894 (Hodgson)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser Nevan Krogan
Paul Adams John Tainer Greg Hura Nick Sauter
Aina Cohen Art Lyubimov Jeney Wierman
http://bl831.als.lbl.gov/~jamesh/powerpoint/SLAC_lossy_2023.pptx

## Slide 2: Why keep “blanks”?
Lan et al. “EMC” IUCrJ (2018)
“blank” images

## Slide 3
Why keep pixels?
Because we can’t model mosaicity (yet)
Lovelace JJ, Murphy CR, Pahl R, Brister K & Borgstahl GEO (2006)."Tracking reflections through cryogenic cooling with topography", J. Appl. Cryst. 39, 425-432.
Any function can be approximated by a family of Gaussians

## Slide 4
Real XFEL still
Lyubimov et al. (2016).
eLife 5, e18740.

## Slide 5: “fit” simulation to real image
Dispersion
Divergence
Mosaicity
Wavelength
Unit cell parameters (3)
Crystal orientation (3)
Mosaic domain size (3)
Beam center (2)
Beam direction (2)
Detector distance
Why keep pixels ?

## Slide 6: Simulation of XFEL still

## Slide 7
Real XFEL still
Lyubimov et al. (2016).
eLife 5, e18740.

## Slide 8
phiz
Simulation of XFEL still
phiy
phiz
phix
phix
phiy
VS
real

## Slide 9
Angle about y axis (°)
Fraction pixels predicted
Fitting individual “mosaic domains”
Best of
262,140 trials

## Slide 10: 3-domain Simulation of XFEL still

## Slide 11
Real XFEL still

## Slide 12: 1-domain Simulation of XFEL still

## Slide 13: 3-cluster mosaic simulation

## Slide 14
Real XFEL still
Lyubimov et al. (2016).
eLife 5, e18740.

## Slide 15: 1-cluster Simulation of XFEL still

## Slide 16
3 domains within 1°

## Slide 17
3 domains within 0.2°

## Slide 18: Texture sufficient for poor stats
texture | 1 cluster | 3 clusters
Rtrue* | 4% | 16%
500 images Results from iota: cctbx & prime
*Agreement with F value fed into simulation

## Slide 19: Texture sufficient for poor stats
texture | 1 cluster | 3 clusters
Rtrue* | 4% | 16%
Rmerge | 23% | 66%
500 images Results from iota: cctbx & prime
*Agreement with F value fed into simulation

## Slide 20: Texture sufficient for poor stats
texture | 1 cluster | 3 clusters
Rtrue* | 4% | 16%
Rmerge | 23% | 66%
I/σ | 32 (1.1) | 19 (1.2)
500 images Results from iota: cctbx & prime
*Agreement with F value fed into simulation

## Slide 21: Texture sufficient for poor stats
texture | 1 cluster | 3 clusters
Rtrue* | 4% | 16%
Rmerge | 23% | 66%
I/σ | 32 (1.1) | 19 (1.2)
CC1/2 | 99 (69) | 99 (58)
500 images Results from iota: cctbx & prime
*Agreement with F value fed into simulation

## Slide 22: Texture sufficient for poor stats
texture | 1 cluster | 3 clusters
Rtrue* | 4% | 16%
Rmerge | 23% | 66%
I/σ | 32 (1.1) | 19 (1.2)
CC1/2 | 99 (69) | 99 (58)
resolution | 1.55 | 1.94
500 images Results from iota: cctbx & prime
*Agreement with F value fed into simulation

## Slide 23: How to lose information
long exposures
  >1 photon/image = order of arrivals
Wide phi slice
  sum over angle
Large beams
  sum over area
Pink/divergent beam
  sum over lambda/angle
Background
  non-crystal stuff
Systematics
  Dose contrast

## Slide 24: Lossless compression: data rate
= log2(Npixels) * flux * tsample * 1.2x10-5
minimum data rate with no information loss
Npixels = 4150*4371 for Eiger
flux = photons/s onto the sample
tsample = sample thickness in µm
1.2x10-5 = 10-4 cm/µm * cross section of oxygen (0.2 cm2/g)
* density of protein crystal (1.2 g/cm3 )
* ~1/2 of total scattering intersects detector
E.G. 34 GByte/s for 1013 photons/s and 100 µm thick
bits
s

## Slide 25: Lossless compression: data rate
calibrated using modern lossless algorithms
bits/s = compressed data rate
pixels = number of pixels in the detector
RMSD = RMS deviation of pixels from mean
E.G. ~4 GByte/s for ~1 photon/pixel at 18M 100 Hz
bits
s
= pixels/s * (2 + log2(RMSD))

## Slide 26
compresses 4.2x
Notes: Test data set: ADSC Q315r ccd. No loss, compresses 4.2x with gzip, etc.

## Slide 27
compresses 337x
Notes: Isolate spots by looking for peaks. Set everything else to zero, compresses almost 100x better!

## Slide 28
compresses 5x, but only one per dataset!
Notes: Median background and median absolute deviation from that background, store this separately as two images, compression is > 100x if you consider that there were 100 images in this data set.

## Slide 29
compresses 3.5x
Notes: Subtract meidan background and spots, left with difference between original image and everything we have compressed so far (spots, median background and median background noize level). This compresses less well than original image because all the “information” in the background is in here.

## Slide 30
compressed ~50x
Notes: After doing lossy compression on background, the image can be re-assembled by adding the spots to the median background and then finally adding the lossy-compressed difference image. So, we have only modified background pixels, but achieved 10x more compression!

## Slide 31
compresses 5.2x
Notes: Difference between the 50x lossy-compressed image and the original image. Note that the spots are “blank” because they were not modified by the lossy compression. This difference image contains most of the entropy of the original data set, as evidence by how it doesn’t compress very well. Theoretically, the difference data set could be stored separately from the 50x lossy-compressed data. Perhaps on tape or other slow long-term media. That way if anyone wants the original data back they can still get it. But for quick online storage the 50x compressed data can be used.

## Slide 32: Lossy compression vs R/Rfree
Chart: 
| 1 | 2.4604499999999998 | 2.9380700000000002 | 3.6034999999999999 | 4.5767100000000003 | 5.1109600000000004 | 5.8552499999999998 | 6.8164100000000003 | 7.9383400000000002 | 9.7207000000000008 | 12.778600000000001 | 17.469899999999999 | 26.965800000000002 | 45.728299999999997 | 71.243600000000001 | 97.009200000000007 | 122.298
R_cryst | 0.213 | 0.2034 | 0.2059 | 0.2046 | 0.2012 | 0.2095 | 0.2063 | 0.2009 | 0.2076 | 0.2056 | 0.2238 | 0.2132 | 0.2039 | 0.205 | 0.1997 | 0.2687 | 0.2756
R_free | 0.287 | 0.2939 | 0.2851 | 0.2949 | 0.2831 | 0.2898 | 0.2816 | 0.2798 | 0.2835 | 0.2979 | 0.313 | 0.2958 | 0.2831 | 0.2844 | 0.2783 | 0.353 | 0.3566
R factor
compression ratio
Background
“too smooth”
Notes: By adjusting the h264 lossy compression ratio of the background pixels the impact of the compression on crystallographic statistics can be evaluated. Note that some of these points are actually better than the uncompessed data! This is due to random noise, but could be a misguided argument for lossy compression: it can improve your Rfree

## Slide 33: Why keep “background”?
http://bl831.als.lbl.gov/example_data_sets/Illuin/lyso_DS

## Slide 34: Noise “compression”
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
data | 0 | 1.2367 | -1.1664 | -1.0012 | 1.1142 | 0.71023 | -0.53135 | -1.2617 | 1.9239 | 0.70035 | -0.20686 | 0.49062 | -0.055327 | 0.42495 | -1.0775 | 0.73394 | -1.5961 | -1.3752 | -0.026926 | 2.6872 | -0.85155
seed=22 | 0 | 0.79819 | -0.57356 | 0.30788 | 0.9442 | 1.7603 | 0.44643 | -1.289 | 1.7426 | -0.1881 | 0.38585 | 1.1985 | 0.32985 | -0.68314 | -0.54357 | 1.3617 | -2.4914 | -0.25795 | 0.03555 | 1.0677 | -0.99946
intensity
pixel
Find best-fit pseudo-random sequence to real noise
Notes: By adjusting the h264 lossy compression ratio of the background pixels the impact of the compression on crystallographic statistics can be evaluated. Note that some of these points are actually better than the uncompessed data! This is due to random noise, but could be a misguided argument for lossy compression: it can improve your Rfree

## Slide 35: Noise “compression”
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
data | 0 | 1.2367 | -1.1664 | -1.0012 | 1.1142 | 0.71023 | -0.53135 | -1.2617 | 1.9239 | 0.70035 | -0.20686 | 0.49062 | -0.055327 | 0.42495 | -1.0775 | 0.73394 | -1.5961 | -1.3752 | -0.026926 | 2.6872 | -0.85155
seed=22 | 0 | 0.79819 | -0.57356 | 0.30788 | 0.9442 | 1.7603 | 0.44643 | -1.289 | 1.7426 | -0.1881 | 0.38585 | 1.1985 | 0.32985 | -0.68314 | -0.54357 | 1.3617 | -2.4914 | -0.25795 | 0.03555 | 1.0677 | -0.99946
seed=26945 | 0 | 0.66062 | -0.95195 | -2.0348 | 1.4142 | -0.26449 | -0.64432 | -0.87076 | 0.34532 | -0.19221 | -1.29 | -0.082517 | -0.12876 | -0.43924 | -1.6562 | -0.085877 | -0.4976 | -1.0517 | -0.042587 | 1.2112 | -0.56369
intensity
pixel
Find best-fit pseudo-random sequence to real noise

## Slide 36
3-year service contract
$180k / 400 TB
$450 / TB / 3 years
$150,000 / PB / year

## Slide 37
$12,000 / PB / year
“At just $0.00099 per GB-month”

## Slide 38
Bare
drives
$300 / 18 TB
$17 / TB / 5 years
$3400 / PB / year

## Slide 39
“petabyte”
90 drive bays
SSG-640SP-E1CR90
600 W
= $1k/y
$57k / 1.8 PB
$32 / TB / 5 years
$7400 / PB / year
HDD life:
4-7 years

## Slide 40
$54 / 12 TB
$4.5 / TB / 15 years
$300 / PB / year
Shelf life:
15-30 years
8
$4k
Write speed:
360 MB/s

## Slide 41: 1 GB/s – direct to tape?
LTO-10

## Slide 42
clay tablet ca. 2000 BC
$0.3/lb ; 1 bit = 1 mm3
$2.7 / TB / 4000 years
$0.3 / PB / year

## Slide 43: DVD data archive: ~100 TB
$0.2 / 4.7 GB
$42 / TB / 20 years
$2000 / PB / year
Shelf life:
> 20 years

## Slide 44: Which data go with which PDB?
260,000 images are called “test”
cell: 48 62 84 90 101 104
  is within 5 Å and 5° of 16,000 PDBs
focusing on 2001-2006
490 PDBs credit ALS 8.3.1 with data
44 of these didn’t actually collect data
64 collected data, but no credit

## Slide 45: Which data go with which PDB?
images from 2001-2006
collected “near” edges
find “runs” of >10 images
unify multi-wedge sets
run labelit & XDS
>70% complete?
I/σ > 10
reduced cell vs PDB
1,604,031
682,712
3602
3331
2524
1479
1054
1 to 200+

## Slide 46: Responses to inquiries
“I have to find my old note book as I have no idea what that is.”
“I have changed jobs a few times since and am really far away from crystallography now.”
“Will see what I can find.”
“We solved it but never published it. Sorry!”

## Slide 47: DVD data archive

## Slide 50: Primary failure mode of DVDs

## Slide 53: dataset identification protocol
images from 2001-2006
collected “near” edges
find “runs” of >10 images
sort out multi-wedge sets
run XDS
>70% complete?
I/σ > 10
reduced cell vs PDB
1,604,031
682,712
3602
3331
2524
1479
1054
1 to 200+

## Slide 54: Unit Cell: 90.9 90.9 46.8 90 90 120
best Rcryst after rigid-body refinement
RMS unit cell length deviation (Å)
1hh7 M. TB CSOR
1rb5
myoglobin

## Slide 55: MAD/SAD datasets
Riso vs PDB deposit
best Rcryst after rigid-body refinement
Published
non-isomorphous
Unsolved?

## Slide 56: EGDA
Dec 01 19:45:12 2001 egda46_*1_E#_###.img (1112 images, Se MAD) Dec 02 15:10:06 2001 egda27_*1_###.img (180, 1A, native?) Dec 02 19:21:55 2001 egdau1_*1_###.img (427, 8000eV (U?) SAD) Dec 02 20:58:26 2001 egdau1_*2_###.img (360, 8000eV (U?) SAD) Jun 01 14:07:43 2002 egda60_*1_###.img (360, Lutetium SAD)
“I think that these EGDA data sets are very likely some of xxx’s data sets, he was working on E.coli guanine deaminase, something he brought from yyy. No structure was ever published James, xxx was unable to solve the structure from these data.”

## Slide 57
~2.9 Å
P21212
R = 0.32
Rfree = 0.39
PDB ID: ????
E. coli
guanine
deaminase
Identical
sequence:
6ohc (2019)

## Slide 58: Summary
Old data can age well
Smooth the background?
Bare LTO tape = $300/PB/year
metadata: trust, but verify?