## Slide 1: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1 creator: Tom Alber
UC Multicampus Research Programs and Initiatives (MRPI)
UCSF Program for Breakthrough Biomedical Research (PBBR)
one-time NIH-DOE Inter-agency agreement (IAA)
Integrated Diffraction Analysis Technologies (IDAT)
Plexxikon, Inc.
M D Anderson CRC
Synchrotron Radiation Structural Biology Resource (SLAC)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser Aina Cohen Ana Gonzalez
Axel Brunger Monarin Uervirojnangkoorn Artem Lyubimov Nick Sauter

## Slide 2: Structural Biologists Want:
Resolution
Phases

## Slide 3: Resolution
http://bl831.als.lbl.gov/~jamesh/movies/resolution.mpeg

## Slide 4: Phases
http://bl831.als.lbl.gov/~jamesh/movies/dephase.mpeg

## Slide 5: Structural Biologists Want:
Resolution
  problem: background
  solution: use as few pixels as possible
Phases
  problem: fractional errors
  solution: use as many pixels as possible
Problem for both: radiation damage

## Slide 6: Can radiation damage be “outrun”?

## Slide 7: Dose-rate dependence of damage
dose rate (kGy/s)
maximum useful dose (MGy)

## Slide 8: Dose-rate effect at Room Temp?
Warkentin M, Badeau R, Hopkins JB, Mulichak AM, Keefe LJ & Thorne RE (2012)."Global radiation damage at 300 and 260 K with dose rates approaching 1 MGy s-1", Acta Cryst. D 68, 124-133.
Owen RL, Axford D, Nettleship JE, Owens RJ, Robinson JI, Morgan AW, Dore AS, Lebon G, Tate CG, Fry EE, Ren J, Stuart DI & Evans G (2012)."Outrunning free radicals in room-temperature macromolecular crystallography", Acta Cryst. D 68, 810-818.

## Slide 9: Attenu-wait: same photons, different time
Integrated photons in spot
Exposure time (seconds) for 1° osc
100 20 10 6.7 5
Incident beam transmittance (%)

## Slide 10: Attenu-wait: same photons, different time
Integrated photons in spot
Exposure time (seconds) for 1° osc
100 20 10 6.7 5
Incident beam transmittance (%)

## Slide 11: What could be better than photon-counting?
Count rate (photons/s)
phi position (degrees)

## Slide 12: What could be better than photon-counting?
Count rate (photons/s)
phi position (degrees)
Dead times:
1000 ns Oxford
200 ns Pilatus

## Slide 13: Pilatus pile-up for RT MX? same photons, different speeds
Sum of 193 shots with
193-fold attenuation
SLOW

## Slide 14: Pilatus pile-up for RT MX? same photons, different speeds
1 shot with
no attenuation
FAST

## Slide 15: Pilatus pile-up for RT MX? same photons, different speeds

## Slide 16: Pilatus pile-up for RT MX? same photons, different speeds
20 deg/s
0.016 deg
mosaic

## Slide 17: Pilatus pile-up for RT MX? same photons, different speeds

## Slide 18: Do we expect this with protein?
Mosaic spread (η) < 0.02°
20°/s rotation
50x50x50 μm lysozyme crystal
Istill = 0.07*(F/mosaic)2
F=130 → 3e6 photons/s/spot
Max Eiger count rate = 3e6 photons/s/spot
35% of Fs > 130 (lysozyme @ 2.0 Å)
45% under-counting expected

## Slide 19: What is a “streak camera”?

## Slide 20: What is a “streak camera”?
0.1 mm/pixel
= 4 ms/pixel
25 mm/s

## Slide 23: Individual spots at 768 kGy/s
Intensity (photons)
Dose (kGy)
0
Same xtal, different spots

## Slide 24: Individual spots at 768 kGy/s
Intensity (photons)
Dose (kGy)
0
Same xtal, different spots

## Slide 25: Individual spots at 768 kGy/s
Intensity (photons)
Dose (kGy)
0
Same xtal, different spots

## Slide 26: Individual spots at 768 kGy/s
Intensity (photons)
Dose (kGy)
0
Same xtal, different spots

## Slide 27: Individual spots at 768 kGy/s
Intensity (photons)
Dose (kGy)
0
Same xtal, different spots

## Slide 28: Individual spots at 768 kGy/s
Intensity (photons)
Dose (kGy)
0
Same xtal, different spots

## Slide 29: Individual spots at 768 kGy/s
Intensity (photons)
Dose (kGy)
0
Same xtal, different spots

## Slide 30: Wiggle to get fulls
Ewald sphere

## Slide 31: Slow wiggle

## Slide 32: Dose rate: same hkl, same xtal
Intensity (photons)
Dose (kGy)

## Slide 33: Dose rate: same hkl, same xtal
Intensity (photons)
Dose (kGy)

## Slide 34: xtal24big
Real time at 674 kGy/s

## Slide 35: xtal12
Double tap: 0.4 s on + 1 s off + on again

## Slide 36: Double-tap: no dark progression at 675 kGy/s
Intensity (photons)
Dose (kGy)

## Slide 37: Double-tap: no dark progression at 675 kGy/s
Intensity (photons)
Dose (kGy)

## Slide 38: xtal14
Double tap: 0.4 s on + 1 s off + on again

## Slide 39: Xtal15 slow
Double tap lite: 5 s on + 12.6 s off + on again

## Slide 40: Xtal15 fast
Double tap lite: 5 s on + 12.6 s off + on again

## Slide 41: Individual spots at 44.3 kGy/s
Intensity (photons)
Time (seconds)

## Slide 42: Individual spots at 44.3 kGy/s
Intensity (photons)
Time (seconds)

## Slide 43: Individual spots at 44.3 kGy/s
Intensity (photons)
Time (seconds)

## Slide 44: Dose rate: same hkl, same xtal
Intensity (photons)
Dose (kGy)

## Slide 45: Dose rate: same hkl, same xtal
Intensity (photons)
Dose (kGy)

## Slide 46: Dose rate: same hkl, same xtal
Intensity (photons)
Dose (kGy)

## Slide 47: Dose rate: same hkl, same xtal
Intensity (photons)
Dose (kGy)

## Slide 48: Xtal12 before & after
morphological dose-rate effect?
110 kGy/s
720 kGy/s

## Slide 49: Xtal4_t1
Solvent “reaction” at 764 kGy/s

## Slide 50: xtal4_t2
Solvent “reaction” at 764 kGy/s

## Slide 51: xtal13
Double tap: 0.4 s on + 1 s off + on again

## Slide 52: xtal13
Double tap: 0.4 s on + 1 s off + on again

## Slide 53: xtal5_t1
Crystal “shrinks?” at 764 kGy/s

## Slide 54: xtal5_t2
Crystal “shrinks?” at 764 kGy/s

## Slide 55: Xtal5_t1 graph

## Slide 56: How much H2 are we making?
Meents et al. (2010) claimed:
"400 molecules of H2 for every 12.5 keV photon“
= 3.3x10-7 mol/J
200 kGy to 100 um3 = 0.24 J
= 1.2x10-8 mol H2
100 um3 of water = 6.7x10-8 mol
→ 18% of water has reacted!

## Slide 57
Damage at 100K is done
by dose (MGy)
proportional to photons/area
not time
not heat
Sliz P, Harrison SC & Rosenbaum G (2003). Structure 11, 13-19.
Garman EF & McSweeney SM (2006). J. Sync. Rad. 14, 1-3.
Owen RL, Rudino-Pinera E & Garman EF (2006). PNAS 103, 4912-4917.
Leiros et al. (2006). Acta Cryst. D 62, 125-132.
Holton JM (2007). J. Synch Rad. 14, 51-72.

## Slide 58: what the is a MGy?
http://bl831.als.lbl.gov/
damage_rates.pdf
Holton J. M. (2009) J. Synchrotron Rad. 16 133-42
energy
mass

## Slide 59
How long will my crystal last?
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
ALS 4.2.2 MAD 2.2e11 75x80 3.7e+07 27.3 kGy/s 18 m 73 s
ALS 5.0.1 mono 1.6e11 100 2.0e+07 10.4 kGy/s 48 m 3.2 m
ALS 5.0.2 MAD 8e11 100 1.0e+08 51.8 kGy/s 9.6 m 39 s
ALS 5.0.3 mono 1.7e11 100 2.2e+07 11 kGy/s 45 m 3 m
ALS 8.2.1 MAD 1.8e11 100 2.3e+07 11.7 kGy/s 43 m 2.9 m
ALS 8.2.2 MAD 2.3e11 100 2.9e+07 14.9 kGy/s 34 m 2.2 m
ALS 8.3.1 MAD 9e11 70 2.3e+08 119 kGy/s 4.2 m 17 s
ALS 8.3.1 typical 6e11 70 1.6e+08 115 kGy/s 4.3 m 17 s
ALS 12.3.1 MAD 1.8e11 100 2.3e+07 11.7 kGy/s 43 m 2.9 m
ALS 12.3.1 ML 4.0e12 100 5.1e+08 513 kGy/s 58 s 3.9 s
APS 8-BM MAD 1e11 200 2.5e+06 1.27 kGy/s 6.6 h 26 m
APS 14-BM-C mono 5.8e10 200 1.4e+06 738 Gy/s 11 h 45 m
APS 14-BM-D MAD 3.3e9 200 8.2e+04 42 Gy/s 8.3 d 13 h
APS 14-ID-B MAD 6.0e10 200 1.5e+06 763 Gy/s 11 h 44 m
APS 17-BM MAD 1.1e11 200 2.8e+06 1.4 kGy/s 6 h 24 m
APS 17-ID MAD 2.3e11 200 5.8e+06 2.93 kGy/s 2.8 h 11 m
APS 19-BM MAD 2.0e11 70x60 4.8e+07 24.2 kGy/s 21 m 83 s
APS 19-ID MAD 1.3e13 80x40 4.1e+09 2.07 MGy/s 15 s 0.97 s
APS 19-ID typical 5.5e11 100x100 5.5e+07 28 kGy/s 18 m 71 s
APS 22-BM MAD 7e12 80x40 2.2e+09 1.23 MGy/s 24 s 1.6 s
APS 22-ID MAD 7e12 80x40 2.2e+09 1.23 MGy/s 24 s 1.6 s
APS 22-ID typical 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
APS 23-ID-B MAD 1e13 75x25 5.3e+09 3.01 MGy/s 10 s 0.66 s
APS 23-ID typical 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
APS 24-ID-C MAD 1.3e13 20x60 1.1e+10 5.23 MGy/s 5.7 s 0.38 s
APS 24-ID-E MAD 0.5e13 20x100 2.5e+09 1.19 MGy/s 25 s 1.7 s
APS 31-ID MAD 2e12 70 4.1e+08 194 kGy/s 2.6 m 10 s

## Slide 60: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12

## Slide 61: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12
10 MGy/Å

## Slide 62: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.

## Slide 63: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.
Riso ≈ 0.7 %/MGy

## Slide 64: Dose-doubling concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 65: Dose-doubling concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 66
Holton (2009) J. Synchrotron Rad. 16 133-42
Specific Damage
World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 67: Elastic scattering

## Slide 68: Elastic scattering

## Slide 69: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
Protein
1A x-rays

## Slide 70: Elastic scattering

## Slide 71: Inelastic scattering

## Slide 72: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
Protein
1A x-rays

## Slide 73: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays

## Slide 74: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 75: Photoelectric absorption

## Slide 76: Photoelectric absorption
e-
+

## Slide 77: Fluorescence
+

## Slide 78: Fluorescence
e-
+

## Slide 79: Metal identification

## Slide 80: Auger emission
+

## Slide 81: Auger emission
++
e-

## Slide 82: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 83: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 84: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (~0%)
Absorbed (99%)
Re-emitted (99%)
Absorbed (~0%)

## Slide 85: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
useful/absorbed energy: 7.3%
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (~0%)
Absorbed (99%)
Re-emitted (99%)
Absorbed (~0%)

## Slide 86: Photoelectric absorption

## Slide 87: Photoelectric absorption
e-
+

## Slide 88: Secondary ionization
e-

## Slide 89: Secondary ionization
e-
e-
+

## Slide 90: Excitation
e-

## Slide 91: Excitation
e-

## Slide 92: Excitation
e-

## Slide 93: Excitation

## Slide 94: Electron attachment
e-

## Slide 95: Electron attachment
-

## Slide 96: Sample atoms

## Slide 97: Sample atoms

## Slide 98: Primary ionization
e-
+

## Slide 99: Secondary ionizations
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+

## Slide 100: Ionization track
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 101: Ionization track
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 102: Ionization track

## Slide 103: Ionization track

## Slide 104: Ionization track
3 μm

## Slide 105: Ionization track
Linear Energy Transfer

## Slide 106: Ionization track
initial effects

## Slide 107: Ionization track
Homogeneous reactions
initial effects

## Slide 108: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 109: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
neutralization
e-
+

## Slide 110: initial effects
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
neutralization
e-
+

## Slide 111: initial effects
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
neutralization
neutralization
+

## Slide 112: initial effects
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
attachment
+

## Slide 113: initial effects
e-
e-
e-
e-
-
e-
e-
+
+
+
+
+
+
attachment
+

## Slide 114: initial effects
e-
e-
e-
e-
-
e-
e-
+
+
+
+
+
+
attachment
attachment
+

## Slide 115: initial effects
e-
e-
-
e-
e-
+
+
+
+
+
+
-
-
+

## Slide 116: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 117: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+
solvation

## Slide 118: initial effects
-
e-
+
+
+
+
+
-
-
-
-
solvation
+

## Slide 119: Solvated electron
e-

## Slide 120: Solvated electron
e-

## Slide 123: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 124: initial effects
-
e-
+
+
+
+
+
-
-
-
-
+

## Slide 125: initial effects
-
e-
+
+
+
+
-
-
-
+

## Slide 126: initial effects
-
e-
+
+
-
+

## Slide 127: initial effects
-
e-
+
+

## Slide 128: Excitation transfer

## Slide 129: Excitation transfer
UV photon

## Slide 130: Excitation transfer

## Slide 131: Excitation transfer
Förster transfer
r-6

## Slide 132: Excitation transfer

## Slide 133: t = 0 s

## Slide 134: t ≈ 10-15 s
-
e-
+
+

## Slide 135: Timescales of radiation damage
Garret et. al. (2005) Chem. Rev. 105, 355-389

## Slide 136: Timescales of radiation damage
Garret et. al. (2005) Chem. Rev. 105, 355-389
LCLS
ALS
bunch

## Slide 137: Ionization track
Heterogeneous reactions
Homogeneous reactions

## Slide 138: Rough values of energy quanta
1 MeV 100 GJ/mol Medical radiation therapy
100 keV 10 GJ/mol Medical imaging
10 keV 1 GJ/mol X-ray crystallography
1 keV 100 MJ/mol S and P K-edges
100 eV 10 MJ/mol “water window”
10 eV 1 MJ/mol C≡C bond
1 eV 100 kJ/mol C-C bond, visible light
100 meV 10 kJ/mol hydrogen bond
10 meV 1 kJ/mol heat (~300 K)

## Slide 139: Energy Transfer Analogy
37 C

## Slide 140: Systematic Error vs Random Noise

## Slide 141: Completeness: random deletion
http://bl831.als.lbl.gov/~jamesh/movies/completeness.mpeg

## Slide 142: Completeness: missing wedge
http://bl831.als.lbl.gov/~jamesh/movies/osc.mpeg

## Slide 143: Overloads
http://bl831.als.lbl.gov/~jamesh/movies/overloads.mpeg

## Slide 144: Resolution: low-angle cutoff
http://bl831.als.lbl.gov/~jamesh/movies/lo_cut.mpeg

## Slide 145: R-factor
http://bl831.als.lbl.gov/~jamesh/movies/rfactor.mpeg

## Slide 146: The R-factor Gap
Rmerge = 3%
Rwork = 20%
Rfree = 24%
Experimental
error
“systematic”
error
20% of carbon atom = 1.2 e-
5% of carbon atom = 0.3 e-
Closing the R-factor gap will enable study of 1-electron changes

## Slide 147: The R-factor Gap
Holton et al. (2014). FEBS J. 281, 4046-60.
R1 < 2*Rsigma
Publication criterion for chemical crystallography:
R1 = Fo vs Fc for I/σ(I) > 3
Rsigma = <σ(I)>/<I>
There are no PDB entries that pass this test!

## Slide 148: The R-factor Gap
MLFSOM
Elves
Rmerge = 6%
Rcryst = 17%
Rfree = 20%
multi-conformer PDB file
1H87
Holton, Classen, Frankel & Tainer (2014)."The R-factor gap in macromolecular crystallography: an untapped potential for insights on accurate structures", FEBS J. 281, 4046-4060.

## Slide 149: The R-factor Gap
MLFSOM
Elves
Rmerge = 6%
Rcryst = 7%
Rfree = 8%
multi-conformer PDB file
1H87
Holton, Classen, Frankel & Tainer (2014)."The R-factor gap in macromolecular crystallography: an untapped potential for insights on accurate structures", FEBS J. 281, 4046-4060.

## Slide 150: The R-factor Gap
single-conformer PDB file
1H87; conf “A”
Holton, Classen, Frankel & Tainer (2014)."The R-factor gap in macromolecular crystallography: an untapped potential for insights on accurate structures", FEBS J. 281, 4046-4060.
MLFSOM
Elves
Rmerge = 6%
Rcryst = 7%
Rfree = 8%
ARP/wARP

## Slide 151: Is this good enough?
dmax = 4.5 Å
Rcryst = 27%
Rfree = 38%

## Slide 152: Is this good enough?
3a8n 4.5 Å Rmerge = 0.15 R/Rfree = 0.306/0.396
1grz 5 Å Rmerge = 0.052 R/Rfree = 0.369/0.428
1qzv 4.44 Å Rmerge = 0.099 R/Rfree = 0.41/0.42

## Slide 153: 2Fsim-Fcalc and Fsim-Fcalc maps
1.0 Å data
Rcryst= 0.137
Rfree = 0.159
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc

## Slide 154: 2Fsim-Fcalc and (Fsim Φsim) - (Fcalc Φcalc) maps
1 “sigma” 2Fsim-Fc
Fright – (2Fsim-Fc)
1.0 Å data
Rcryst= 0.137
Rfree = 0.159

## Slide 155: 30 conformers from 24,000

## Slide 156: How many conformers are there?
Rcryst = 0.0441
Rfree = 0.0516
vs Fsim
Answer: 2-14

## Slide 157: How many conformers are there?
Rcryst = 0.1546
Rfree = 0.1749
vs Fobs
1aho:
Rcryst = 0.1630
Rfree = n/d
Answer: 1-7

## Slide 158: How many conformers are there?
All difference
features
are in
the solvent!
real data

## Slide 159: The R-factor Gap
MX data quality is not limiting
Hypotheses:
  Hidden systematic error?
  Model-building problem?
  Representation problem?

## Slide 160: RISM model for “bulk” solvent
Method | Rwork | Rfree
Default refmac5: flat bulk solvent | .1784 | .1898
RISM – self-consistent density field based on electrostatics | .1640 | .1808
Explicit MD solvent, protein fixed | .1523 | .1690
RISM – protein fixed multi-conformer weighted | .1578 | .1739
Explicit – protein fixed multi-conformer weighted | .1440 | .1666

## Slide 161: Phases
http://bl831.als.lbl.gov/~jamesh/movies/dephase.mpeg

## Slide 162: 100% SeMet incorporation
Trivial to solve

## Slide 163: 100% S -Met incorporation
Impossible to solve

## Slide 164: Can you count to 1,000,000 ?
= 0.1%
sqrt(1,000,000)
1,000,000
= 3%
sqrt(1,000)
1,000
> 1000 is a waste!
photon
spot
Theoretically:
In reality:
ISa ~ 33
Rmeas ≈ 0.1% ?
ISa = 1000
Rmeas = ≈ 3%

## Slide 165
Required signal-to-noise (I/σ)
Solve-able proteins (%)
Current
technology
Goal
Threshold of a revolution in phasing

## Slide 166
Source of error | realistic simulation | No SHSSS | Perfect detector
Photon counting | + | + | +
Shutter jitter | + | + | -
Beam flicker | + | + | -
Sample absorption | + | + | -
Radiation damage | + | + | -
Imperfect spindle | + | + | -
vignette | + | + | -
Corner correction | + | + | -
SHSSS | + | - | -
Rmeas (∞-10 Å) | 2.8% | 0.7% | 0.7%
I/σ asymptotic | 26.8 | 74.2 | 81.0
Threshold of a revolution in phasing
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 167
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 168
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 169
Spot centroid position (pixels)
Relative spot intensity
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 170
Spot centroid position (pixels)
Relative spot intensity
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 171: SHSSS! The dominant source of error for anomalous difference measurements
Spatial
Heterogeneity in
Sharp
Spot
Sensitivity
Flat
Field

## Slide 172: SHSSS! The dominant source of error for anomalous difference measurements
Spatial
Heterogeneity in
Sharp
Spot
Sensitivity
Flat
Field
90%
110%
x 1.11 =
x 0.91 =
100%
100%

## Slide 173: SHSSS! The dominant source of error for anomalous difference measurements
Spatial
Heterogeneity in
Sharp
Spot
Sensitivity
Sharp
Spot
20%
110%
x 1.11 =
x 0.91 =
100%
22%

## Slide 174: SHSSS! The dominant source of error for anomalous difference measurements
Spatial
Heterogeneity in
Sharp
Spot
Sensitivity
Sharp
Spot
90%
30%
x 1.11 =
x 0.91 =
27.3%
100%
Integral: 127.3

## Slide 175: SHSSS! The dominant source of error for anomalous difference measurements
Spatial
Heterogeneity in
Sharp
Spot
Sensitivity
Sharp
Spot
20%
110%
x 1.11 =
x 0.91 =
100%
22.2%
Integral: 122.2

## Slide 176: SHSSS! The dominant source of error for anomalous difference measurements
Spatial
Heterogeneity in
Sharp
Spot
Sensitivity
Sharp
Spot
90%
30%
x 1.11 =
x 0.91 =
27.3%
100%
Integral: 127.3

## Slide 177
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 178
down
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 179
down
up
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 180
down
up
Rseparate
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 181
odd
even
Rmixed
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 182
separate:
2.5%
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 183
separate:
mixed:
2.5%
0.9%
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 187
separate:
mixed:
2.5%
0.9%
2.5%2-0.9%2 = 2.3%2
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 188
3.5
3.0
2.5
2.0
1.5
1.0
0.5
SHSSS
Systematic component of Rsseparate (%)
distance between spots (mm)
0.1 1 10 100
CCD detector
anomalous mates are always on
different modules
different
modules
Pilatus
SN001
Spatial Heterogeneity in Sharp Spot Sensitivity
Notes: Comparision of SHSSS measured by the detector-shift experiment on three different detectors:
The Q315R in ALS 8.3.1
The first Pilatus detector at the Swiss Light Soruce
A newer Pilatus detector at Stanford
Improvements in calibration technology have finally made
Pilatus competitive with calibration on CCDs

## Slide 189: Pilatus: 1-module shift
Notes: Insulin diffraction recorded at Swiss light source detector centered on beam

## Slide 190
Pilatus: 1-module shift
Notes: Same insulin pattern, but with detector raised by one module width. This image can then be “digitally shifted” to overlay the same spots on top of one another, but recorded by different pixels.

## Slide 191
Pilatus: 1-module shift
Notes: Subtraction of equivalent pixels after shifting the detector
Note that some modules are mis-aligned relative to a perfect grid. These sub-pixel shifts can be resolved with “triangle binning”

## Slide 192
Pilatus: 1-module shift - aligned
Notes: Subtracted image after correcting for sub-pixel shifts

## Slide 193
3% high
average
3% low
Pilatus: 1-module shift - ratio
Notes: Ratio image: difference divided by average, again after correcting for sub-pixel shifts
Note: range of calibration error from module to module is RMS 3%

## Slide 194
3.5
3.0
2.5
2.0
1.5
1.0
0.5
SHSSS
Systematic component of Rsseparate (%)
distance between spots (mm)
0.1 1 10 100
CCD detector
anomalous mates are always on
different modules
different
modules
Pilatus
SN113
Pilatus
SN001
Notes: Comparision of SHSSS measured by the detector-shift experiment on three different detectors:
The Q315R in ALS 8.3.1
The first Pilatus detector at the Swiss Light Soruce
A newer Pilatus detector at Stanford
Improvements in calibration technology have finally made
Pilatus competitive with calibration on CCDs

## Slide 195
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel
Pilatus: subtract smooth baseline

## Slide 196
N
N
N
θ
λ
detection
event
incoming
photon
PAD: need more than flood-field

## Slide 197
thickness
width
N
N
N
Bragg
glitch
oxygen
inclusion
θ
λ
detection
event
incoming
photon
PAD: need more than flood-field

## Slide 198: CCD calibration: 7235 eV

## Slide 199: CCD calibration: 7247 eV

## Slide 200: Gadox calibration vs energy
photon energy (keV)
Relative absorption depth
same = good!
bad!

## Slide 201: Systematic Error vs Random Noise

## Slide 202: Data collection parameters:
16 crystals
360° each, inverse beam
7235 eV photon energy
< 1 MGy per xtal
Australian Synchrotron MX1
  35 kGy/s into 100 μm x 100 μm

## Slide 203
RESOLUTION COMPLETENESS R-FACTOR I/SIGMA R-meas CC(1/2) Anomal SigAno Nano
LIMIT OF DATA observed Corr
9.17 99.1% 3.9% 257.47 3.9% 100.0* 91* 5.024 450
6.49 100.0% 5.2% 214.33 5.2% 100.0* 86* 3.836 882
5.30 100.0% 7.2% 165.13 7.2% 100.0* 76* 3.257 1175
4.59 100.0% 7.2% 175.42 7.3% 100.0* 67* 2.589 1403
4.10 99.9% 7.7% 174.13 7.7% 100.0* 59* 2.264 1594
3.74 99.9% 9.4% 143.09 9.4% 100.0* 49* 1.953 1783
3.47 100.0% 11.2% 120.17 11.2% 100.0* 39* 1.696 1942
3.24 100.0% 14.1% 91.14 14.1% 100.0* 30* 1.333 2103
3.06 99.9% 19.5% 65.79 19.5% 100.0* 23* 1.117 2214
2.90 99.9% 29.0% 44.85 29.1% 99.9* 17* 1.008 2369
2.77 99.9% 40.5% 32.58 40.6% 99.8* 11* 0.901 2493
2.65 99.9% 52.8% 25.16 52.9% 99.8* 10* 0.866 2605
2.54 100.0% 67.4% 19.47 67.6% 99.6* 2 0.804 2705
2.45 100.0% 88.9% 14.58 89.2% 99.2* 4 0.831 2859
2.37 100.0% 109.3% 9.97 109.7% 98.1* 5 0.829 2925
2.29 100.0% 138.2% 6.87 138.9% 96.1* 1 0.760 3037
2.22 100.0% 197.1% 4.03 198.6% 83.5* -1 0.721 3159
2.16 100.0% 227.3% 2.41 230.8% 46.9* -1 0.677 3224
2.10 61.2% 154.4% 1.28 163.6% 47.0* -2 0.660 1999
2.05 47.9% 170.1% 0.68 196.5% 25.7* 3 0.629 1578
total 93.3% 15.7% 54.30 15.8% 100.0* 12* 1.217 42499
140-fold multiplicity: 16 crystals, 360° each, inverse beam, 7235 eV

## Slide 204: 140-fold multiplicity
18 σ
Phased anomalous difference Fourier
16 σ

## Slide 205: 140-fold multiplicity
15σ = PO4
Phased anomalous difference Fourier

## Slide 206: 140-fold multiplicity
~2σ = Mg?
Phased anomalous difference Fourier

## Slide 207: 140-fold multiplicity
8.2σ = Mg or Na
DELFAN residual anomalous difference

## Slide 208: non-isomorphism
Why doesn’t everyone do this?

## Slide 209: Non-isomorphism in lysozyme
RH: 84.2%
vs 71.9%
Riso = 44.5%
3aw6
3aw7
Δcell = 0.7 %
RMSD = 0.18 Å

## Slide 210
h,k,l | structure factors (F) |  |  | 
 | #1 | #2 | #3 | #4
5,3,4 | 523.7 | 559.8 | 579.9 | 603.2
5,4,4 | 168.2 | 166.6 | 177.2 | 196.1
5,5,4 | 34.9 | 26.4 | 19.2 | 17.3
6,1,4 | 305.7 | 301.1 | 298.1 | 296.3
6,2,4 | 353.0 | 353.9 | 356.2 | 366.9
6,3,4 | 300.9 | 285.3 | 273.5 | 259.4
6,3,5 | 223.8 | 226.3 | 234.6 | 251.4
… | … | … | … | …
X-ray Data Sets
h,k,l | 100% | 17 % | 13 % | 9 %
 | 1st | 2nd | 3rd | 4th
5,3,4 | -1.46 | -0.02 | 1.84 | -0.72
5,4,4 | -0.88 | -0.29 | -0.34 | 0.15
5,5,4 | -0.42 | -0.65 | 1.02 | 1.47
6,1,4 | -0.90 | -0.85 | 1.44 | -0.40
6,2,4 | -1.20 | -0.37 | 0.67 | 0.01
6,3,4 | -0.75 | 0.31 | 0.48 | 0.00
6,3,5 | -0.75 | -0.85 | 0.72 | -0.82
… | … | … | … | …
data
set
Singular value decomp.
SVD
vector
value
Singular values & vectors
Correlation
Coefficients
-0.68
CC2
CC3
CC1
CC1 CC2 CC3
data set #1
Data sets
Positioned
in
“Correlation
Space”
-0.24
data set #2
data set #3
0.32 …

## Slide 212
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 213
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 214
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 215: Bragg’s “minimum wavelength principle”
Perutz (1985). “Early Days of Cryst…” Methods in Enzymology, Vol. 114, 3-18.
Bragg & Perutz (1952)."external form haemoglobin I", Acta Cryst. 5, 277-283.

## Slide 216: DMMULTI – fake data 4 deg rotation: 8 “xtals”: before
CC = 0.02

## Slide 217
CC = 0.8
DMMULTI – fake data 4 deg rotation: 8 “xtals”: after

## Slide 218: Partiality > 25% error per spot!
Kabsch W (2014)."Processing of X-ray snapshots from crystals in random orientations", Acta Cryst D 70, 2204-2216.

## Slide 219: What is “partiality”?
Ewald sphere

## Slide 220: What is “partiality”?
Ewald sphere

## Slide 221: The “partiality problem”
0.006°
1 μm xtal
1 Å x-rays

## Slide 222: Multiplicity required to phase
Monte Carlo
  100% /obs → 10,000 fold
nXDS
  25% /obs → 625 fold
Synchrotron
  3% /obs → 9 fold
  Assuming ΔF/F ~ 1%
Beam time:
$2/s

## Slide 223: Can’t we just rotate the crystal?
1 μm
1°
100 fs
= 90 km/s
9 nm
17.26 km/s
(90 km/s)2
0.5 μm
= 1.5 x 1015 G
= 0.5 nN

## Slide 224: Can’t we just rotate the crystal?
NO
Why do we want to rotate the crystal?

## Slide 225: The “nanocrystal advantage”
Ispot = k Ncells
Ewald sphere
range
2
caveat: 100% error!

## Slide 226
Real XFEL still

## Slide 227: fastBragg program
http://bl831.als.lbl.gov/~jamesh/fastBragg/
Optimized for nanocrystals
Square or round
Takes h,k,l and F
Supports 1 unit cell
no “mosaicity”
arbitrary “source”
arbitrary “phi” steps

## Slide 228: nonBragg for background

## Slide 229: “fit” simulation to reality
Dispersion
Divergence
Mosaicity
Wavelength
Unit cell parameters (3)
Crystal orientation (3)
Mosaic domain size (3)
Beam center (2)
Beam direction (2)
Detector distance

## Slide 230: Simulation of XFEL stills

## Slide 231: Simulation of XFEL stills

## Slide 232
phiz
Simulation of XFEL stills
phiy
phiz
phix
phix
phiy
VS
real

## Slide 233
Angle about y axis (°)
Fraction pixels predicted
Fitting individual “mosaic domains”
Best of
262,140 trials

## Slide 234: The “Lorentz zone”

## Slide 235: The “partiality problem”
0.006°
1 μm xtal
1 Å x-rays
Lovelace et al. (2006)."topography", J. Appl. Cryst. 39, 425-432.

## Slide 236: mosaic spread
Ewald sphere
diffracted ray
F(h,k,l)
d*
λ*
λ*
F(0,0,0)

## Slide 237: mosaic spread
Ewald sphere
diffracted ray
λ*
λ*
d*
d*
F(h,k,l)
F(0,0,0)

## Slide 238: mosaic spread = 0 º

## Slide 239: mosaic spread = 0.1º

## Slide 240: mosaic spread = 0.2º

## Slide 241: mosaic spread = 0.4º

## Slide 242: mosaic spread = 0.6º

## Slide 243: mosaic spread = 0.8º

## Slide 244: mosaic spread = 1.0º

## Slide 245: mosaic spread = 1.5º

## Slide 246: mosaic spread = 2.0º

## Slide 247: mosaic spread = 2.5º

## Slide 248: mosaic spread = 3.2º

## Slide 249: mosaic spread = 6.4º

## Slide 250: mosaic spread = 12.8º

## Slide 251: beam divergence
F(h,k,l)
F(0,0,0)
Ewald sphere
diffracted ray
d*
λ*
λ*

## Slide 252: beam divergence
Ewald sphere
λ*
λ*
F(0,0,0)
d*
diffracted ray

## Slide 253: divergence = 0 º

## Slide 254: divergence = 0.3 º

## Slide 255: spectral dispersion
Ewald sphere
diffracted ray
d*
λ*
λ*
F(h,k,l)
F(0,0,0)

## Slide 256: spectral dispersion
Ewald sphere
diffracted ray
λ’*
λ’*
F(h,k,l)
F(0,0,0)
d*

## Slide 257: dispersion = 0

## Slide 258: dispersion = 0.014% (Si 111)

## Slide 259: dispersion = 0.25% (CuKα)

## Slide 260: dispersion = 0.6%

## Slide 261: dispersion = 1.3%

## Slide 262: dispersion = 2.6%

## Slide 263: dispersion = 5.1%

## Slide 264: spot shape
Ewald sphere
diffracted ray
d*
λ’*
λ’*
Ewald sphere
diffracted ray
d*
λ*
λ*
diffracted ray
d*
Ewald sphere
λ*
λ*
Ewald sphere
diffracted rays
d*
d*

## Slide 265: 0 mrad, 0.0% bw

## Slide 266: 1 mrad, 0.1% bw

## Slide 267
Simulation of XFEL stills
Beam center from autoindexing
Sauter (2015). JSR 22, 239.

## Slide 268
Simulation of XFEL stills
Beam center from autoindexing
Sauter (2015). JSR 22, 239.
Color is
time

## Slide 269: Sanity check on beam position?
~1000 m
0.3 m
100 μm
~1 m
pinhole

## Slide 270: Can’t we just widen the bandpass?

## Slide 271: Si(111) vs multilayers
0.014%
Si(111)
1%
multilayer
4 Å
1.9 Å
resolution
spectral
dispersion

## Slide 272: Wide-bandpass MX?
Mono | Si(111) | multilayer | Difference (%) | good
Energy (eV) | 11111 | 12027.5 | +8.2 | Same
Scale | 1.0000 | 1.0964 | +9.6 | Yes
Rmerge (%) | 7.5 | 8.4 | +12 | No
Ranom (%) | 5.6 | 5.5 | -1.8 | Same
I/sd | 13.2 | 12.3 | -6.8 | Same
I/sd (1.5Å) | 2.3 | 1.8 | -21.7 | No
Ano Patt | 5.96 | 4.75 | -20.3 | Same
Ano Phased | 41 | 39.33 | -4.1 | Same
FOM | 0.238 | 0.192 | -19.3 | Same
CC | 0.555 | 0.647 | -6.1 | Yes
Rcryst (%) | 26.70 | 26.48 | -0.2 | Same
Ligand peak | 8.213 | 8.250 | +0.4 | Same

## Slide 273: Wide bandpass reveals mosaicity from a still
Snell EH, Weisgerber S, Helliwell JR, Holzer K & Schroer K (1995)."Improvements in lysozyme protein crystal perfection through microgravity growth", Acta crystallographica. Section D, Biological crystallography 51, 1099-1102.
low mosaic
high mosaic
Δradial = 2ηD/cos22θ

## Slide 274: Narrow bandpass does not improve anomalous signal
Chart: Photon energy (eV)
| 12656 | 12657 | 12658 | 12658.1 | 12658.2 | 12658.6 | 12658.9 | 12659 | 12659.1 | 12659.2 | 12659.3 | 12659.4 | 12659.6 | 12659.7 | 12659.9 | 12660.4 | 12660.5 | 12660.6 | 12661 | 12656 | 12657 | 12658 | 12658.1 | 12658.2 | 12658.6 | 12658.9 | 12659 | 12659.1 | 12659.2 | 12659.3 | 12659.4 | 12659.6 | 12659.7 | 12659.9 | 12660.4 | 12660.5 | 12660.6 | 12661
I(+) | 159900 | 171800 | 190300 | 193800 | 195000 | 228800 | 232700 | 240200 | 253200 | 241400 | 260200 | 267800 | 243300 | 256400 | 251000 | 260200 | 233100 | 234600 | 247000
I(-) | 131500 | 100900 | 81560 | 76100 | 83960 | 69860 | 50120 | 60980 | 74270 | 66830 | 85140 | 76810 | 82330 | 69980 | 103800 | 106000 | 89630 | 108800 | 110400
vertical
divergence
(240 μRad)
100 μm
pinhole
Si(333)
Si(333)
Al
absorber
1rb5
h,k,l = 5,5,0

## Slide 275
Photon Energy (eV)
Anomalous f” (electrons)
2472.7 2473.5
Bohic et al. Anal. Chem. 2008; 80(24):9557. doi: 10.1021/ac801817k

## Slide 276: S-MAD Sample size Dilemma

## Slide 277
Ewald sphere 2
diffracted ray
λ*
λ*
θ
1
Ewald sphere
λ*
(h,k,l)
diffracted ray
λ*
θ
d*
(-h,-k,-l)
d*

## Slide 278
h,k,l
-h,-k,-l
Detector
Detector
Detector
Detector
λ = 5 Å
sample
injector
Si(111)
52.87deg
Si(111)
Si(111)
Si(111)
Si(111)
Si(111)
2 Multilayer mirrors
d=2nm, W/B4C
KB Horiz focus
KB vertical focus
~ 1m
Notes: Proposed 5-crystal monochromator for colliding-beam crystallography. The generation of two opposing Ewald spheres means that for every h,k,l index reflected from the protein crystal, the Friedel mate is reflected in the opposite direction, allowing for very accurate anomalous difference measurements. The wavelength need not be set precisely at the sulfur or phosphorous edge, but merely at a wavelength where the f” of those elements are strong. For fs-class pulses, the distances above will have to be precise to withing ~3 microns, and for accurate reproduction of the partiality of the Friedel mates, the angular precision of the colliding beams must be within ~1% of the sample crystal’s rocking width, or ~100 microrads.

## Slide 279: “sweet spot” for sample size ?
2 Å
2sin(90°)
3 Å
2sin(90°)
S
P
Mg
Na
C
F
N
O
Cl
Ar
K
Ca
Ne
Se
4 Å
2sin(90°)

## Slide 280: Small, soft beams

## Slide 281: Small, soft beams
Diamond
($100, reusable)

## Slide 282: Small, soft beams
Diamond
($100, reusable)
oil ?

## Slide 283: Small, soft beams
Diamond
($100, reusable)
oil ?

## Slide 284: Small, soft beams
oil ?
λ=2d sinθ
2.5 Å data
with 5 Å X-rays
Only analytic absorption correction:
International Tables for Crystallography, Vol. C, 2nd ed., chapter 6.3

## Slide 285: X-ray scattering “rules”:
1 μm crystal ≈ 1 μm water
≈ 1 μm plastic
≈ 0.1 μm glass
≈ 1000 μm air
~ 50 mm He
≈ 370 mm sat water vapor @ 4C
Optimum: support thickness = crystal thickness

## Slide 286
The number of photons scattered
before crystal is dead
is independent
of data collection time
1 um3 = 105 photons (roomT)
1 um3 = 106 photons (synch)
1 um3 = 108 photons (XFEL)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009
(synch)

## Slide 287
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.
No flux
No symmetry

## Slide 288
Crystal diameter (micron)
Resolution (Å)
B = 0
B = 20
B = 60
B = 170
B = 330
B = 560
B = 850
Bigger is better, but not by much

## Slide 289: B factor from image analysis
B = 500

## Slide 290: B factor from image analysis
B = 20

## Slide 291
Home Lab Resolution (Å)
Synchrotron Resolution (Å)
Predicting resolution limits

## Slide 292
Synchrotron Resolution (Å)
XFEL Resolution (Å)
Predicting resolution limits

## Slide 293: Muybridge’s galloping horse (1878)
Real space
reciprocal
“Time-resolved” diffraction

## Slide 294: Muybridge’s galloping horse (1878)
Real space
reciprocal
Average electron density

## Slide 295: Muybridge’s galloping horse (1878)
Real space
reciprocal
Average electron density: 1 sigma contour

## Slide 296: lysozyme: real and reciprocal

## Slide 297: lysozyme: thermal motion

## Slide 298: Sparse validation supporting a 4D model with 2D data

## Slide 299: URLs & Summary
Outrun radiation damage
25% error from partiality
Phasing limited by relative error
Resolution limited by disorder
“wet vacuum” for bio samples?
How do we make our molecules sit still?
http://bl831.als.lbl.gov/~jamesh/powerpoint/
SLAC_uxss_2016.pptx
http://bl831.als.lbl.gov/~jamesh/bin_stuff/
http://bl831.als.lbl.gov/~jamesh/mlfsom/