## Slide 1: Acknowledgements
In order of response:
David von Stetten
Meitian Wang
Manfred Weiss
Judith Juanhuix Gibert
Bill Shepard
Ilme Schlichting
Kunio Hirata
Armin Wanger
Tom Caradoc-Davies
UCSF LBNL SLAC
ALS 8.3.1: TomAlberTron
Astera.org diff-USE (Fraser)
NIH NIGMS R35 GM158447 (Holton)
NIH NIAID P50 AI150476 (Krogan)
NIH NIGMS P30 GM124169 (Adams)
DOE-BER IDAT (Hura)
NIH NIGMS P30 GM133894 (Hodgson)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.

## Slide 2: From round the world

## Slide 3: From round the world
Study function and dynamics
  Fixed target, “serial”, capture intermediates
Multi-crystal multi-data
  Fragment screening
  Time-resolved (laser?, mixer?, tape?)
“room” (core) temperature
Element identification
Very high resolution

## Slide 4: From round the world
“Fewer Beamlines” or industrialized?
cryoEM
  “interesting” things don’t crystallize
Alphafold is the new “low resolution”
Data curation, training students
Multilayers?, high energy? In-vacuum?
Source upgrades!
China?

## Slide 5: Main Challenges in Structural Biology
$$$
Predicting crystallization outcomes
Getting crystals to diffract better
Is the ligand there or not?
Anisotropic diffraction
Radiation damage
Phase problem
Metals (anaerobic)
What is “resolution”
Serial crystallography (processing)
Non-isomorphism & multi-crystal methods

## Slide 6: Magic Microscope
Visualize a single molecule
spatial resolution 1 Å
temporal resolution: ~100 fs
Watch same molecule indefinitely
No damage to molecule/patient
Ability to tap / tug
Handheld & common
Q: what would you look at first?
Q2: how long before end of disease?
second

## Slide 7: Goals of Methods Development
Impossible → Expensive
Expensive → Cheaper
  Difficult → Easier

## Slide 8
Because: the future of crystallography has alternate conformations
Single-conf models
poor resolution
Low signal/noise
Phase Problem
Dynamics?
Mechanism?
Small signal?
Overlapping states?
The last Å between prediction and reality

## Slide 9: The last Å: near, but far
ATOM 122 N LEU A 13 -3.244 25.808 19.998 1.00 16.96 N
ATOM 123 CA LEU A 13 -2.877 25.448 21.355 1.00 15.29 C
ATOM 124 C LEU A 13 -2.792 23.966 21.561 1.00 17.54 C
ATOM 125 O LEU A 13 -1.814 23.493 22.143 1.00 16.35 O
ATOM 126 CB LEU A 13 -3.907 26.164 22.268 1.00 18.72 C
ATOM 127 CG LEU A 13 -3.577 25.982 23.738 1.00 21.19 C
ATOM 128 CD1 LEU A 13 -2.283 26.820 24.019 1.00 19.43 C
ATOM 129 CD2 LEU A 13 -4.702 26.474 24.639 1.00 24.65 C
ATOM 130 N SER A 14 -3.677 23.149 20.979 1.00 15.96 N
ATOM 131 CA SER A 14 -3.646 21.711 21.061 1.00 18.26 C
ATOM 132 C SER A 14 -2.373 21.203 20.360 1.00 18.71 C
ATOM 133 O SER A 14 -1.747 20.315 20.930 1.00 17.47 O
ATOM 134 CB SER A 14 -4.875 21.077 20.419 1.00 17.62 C
ATOM 135 OG ASER A 14 -4.825 19.665 20.388 0.50 20.89 O
ATOM 136 OG BSER A 14 -6.027 21.408 21.164 0.50 18.67 O
ATOM 137 N LYS A 15 -2.045 21.772 19.215 1.00 18.03 N
ATOM 138 CA LYS A 15 -0.799 21.361 18.555 1.00 18.12 C
ATOM 139 C LYS A 15 0.446 21.707 19.351 1.00 18.81 C
ATOM 140 O LYS A 15 1.400 20.948 19.411 1.00 17.77 O
ATOM 141 CB LYS A 15 -0.700 22.034 17.177 1.00 14.49 C
ATOM 142 CG LYS A 15 -1.727 21.368 16.256 1.00 16.12 C
ATOM 143 CD LYS A 15 -1.663 22.147 14.936 1.00 19.40 C
ATOM 144 CE ALYS A 15 -2.725 21.614 13.986 0.50 17.42 C
ATOM 145 CE BLYS A 15 -1.750 21.211 13.750 0.50 17.01 C
ATOM 146 NZ ALYS A 15 -2.346 21.674 12.559 0.50 18.61 N
ATOM 147 NZ BLYS A 15 -3.052 20.513 13.741 0.50 18.76 N

## Slide 10: The last Å: near, but far
ATOM 122 N LEU A 13 -3.000 26.000 20.000 1.00 16.96 N
ATOM 123 CA LEU A 13 -3.000 25.000 21.000 1.00 15.29 C
ATOM 124 C LEU A 13 -3.000 24.000 22.000 1.00 17.54 C
ATOM 125 O LEU A 13 -2.000 23.000 22.000 1.00 16.35 O
ATOM 126 CB LEU A 13 -4.000 26.000 22.000 1.00 18.72 C
ATOM 127 CG LEU A 13 -4.000 26.000 24.000 1.00 21.19 C
ATOM 128 CD1 LEU A 13 -2.000 27.000 24.000 1.00 19.43 C
ATOM 129 CD2 LEU A 13 -5.000 26.000 25.000 1.00 24.65 C
ATOM 130 N SER A 14 -4.000 23.000 21.000 1.00 15.96 N
ATOM 131 CA SER A 14 -4.000 22.000 21.000 1.00 18.26 C
ATOM 132 C SER A 14 -2.000 21.000 20.000 1.00 18.71 C
ATOM 133 O SER A 14 -2.000 20.000 21.000 1.00 17.47 O
ATOM 134 CB SER A 14 -5.000 21.000 20.000 1.00 17.62 C
ATOM 135 OG ASER A 14 -5.000 20.000 20.000 0.50 20.89 O
ATOM 136 OG BSER A 14 -6.000 21.000 21.000 0.50 18.67 O
ATOM 137 N LYS A 15 -2.000 22.000 19.000 1.00 18.03 N
ATOM 138 CA LYS A 15 -1.000 21.000 19.000 1.00 18.12 C
ATOM 139 C LYS A 15 0.000 22.000 19.000 1.00 18.81 C
ATOM 140 O LYS A 15 1.000 21.000 19.000 1.00 17.77 O
ATOM 141 CB LYS A 15 -1.000 22.000 17.000 1.00 14.49 C
ATOM 142 CG LYS A 15 -2.000 21.000 16.000 1.00 16.12 C
ATOM 143 CD LYS A 15 -2.000 22.000 15.000 1.00 19.40 C
ATOM 144 CE ALYS A 15 -3.000 22.000 14.000 0.50 17.42 C
ATOM 145 CE BLYS A 15 -2.000 21.000 14.000 0.50 17.01 C
ATOM 146 NZ ALYS A 15 -2.000 22.000 13.000 0.50 18.61 N
ATOM 147 NZ BLYS A 15 -3.000 21.000 14.000 0.50 18.76 N

## Slide 11: Is it Real? Or is it MLFSOM
simulated
real
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 12: Stills should be better

## Slide 13: T-REXX beamline - Sample environment chamber
relative humidity: up to 98%
temperature: 8 – 70 °C
still a prototype, but in constant use
[Schulz et al., Nature Commun. 16, 6553 (2025)]

## Slide 14
Real XFEL still
Lyubimov et al. (2016).
eLife 5, e18740.

## Slide 15
phiz
Simulation fit to XFEL still
phiy
phiz
phix
phix
phiy
VS
real
https://pmc.ncbi.nlm.nih.gov/articles/PMC11801403/
“texture”

## Slide 16: Best “round relp” simulation

## Slide 17
Real XFEL still
Lyubimov et al. (2016).
eLife 5, e18740.

## Slide 18: 3-cluster texture simulation

## Slide 19: Texture sufficient for poor stats
texture | 1 cluster | 3 clusters
Rtrue* | 4% | 16%
Rmerge | 23% | 66%
I/σ | 32 (1.1) | 19 (1.2)
CC1/2 | 99 (69) | 99 (58)
resolution | 1.55 | 1.94
500 images Results from iota: cctbx & prime
*Agreement with F value fed into simulation

## Slide 20: Prediction:
Incorporating texture
in serial data processing will
reduce image count requirement
from ~1e4 to ~100
Why? Because rotation data lack texture error

## Slide 21: Non-isomorphism
is annoying
Caused by:
rad dam
humidity
temperature
Growth conditions
Cryo-cooling
Everything
means you:
can’t merge
can’t
add
can’t
subtract

## Slide 22: Cell clustering: 100 datasets
Reality:
Perfect isomorphism
(simulated data)
Holton, J. (2019). Acta Cryst. D 75, 113-122.

## Slide 23
0.5% cell change → 15%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.
Same structure, different cell

## Slide 24
Same structure, different cell
0.5% cell change → 15%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 25
Uniform stretch
5% change → 0%

## Slide 26
5% change → 0%
Uniform stretch

## Slide 27: Hygrostatic gradients
loop
jet
high
water activity
low

## Slide 28: Non-isomorphism in lysozyme
RH: 84.2%
vs 71.9%
Riso = 44.5%
3aw6
3aw7
Δcell = 0.7 %
RMSD = 1.70 Å
RMSD = 0.18 Å LSQ

## Slide 29: 3aw6

## Slide 30: 3aw6 3aw7

## Slide 31
Periodic Spatial Distortion Vector Field

## Slide 32: 3aw6 3aw7

## Slide 33: 3aw6, 3aw7, “bent” 3aw6

## Slide 34: 3aw7, “bent” 3aw6

## Slide 35: 3aw7

## Slide 36: “bent” 3aw7

## Slide 37: 3aw6

## Slide 38
Fobs-Fobs difference
3σ 1.8 Å
“unbent”

## Slide 39
Fobs-Fobs difference
3σ 1.8 Å
old way

## Slide 40: Prediction:
Correcting non-isomorphism
will allow
infinite averaging
allowing arbitrary signal/noise
Why? Because it works for cryoEM

## Slide 41: Radiation Damage

## Slide 42: 0 Gy

## Slide 43: 100 MGy

## Slide 44: What is the dose?
50 MGy ?

## Slide 45: Systematic error: Illumination contrast appears to “reverse” damage
0.35 MGy
Cys6
Cys127
Room temperature high-dose rate series
de la Mora, et al. (2020) PNAS USA 117, 4142-4151

## Slide 46: False Damage reversal: from “hole burning”
X-ray beam
crystal

## Slide 47: False “Damage reversal”: from beam profile
Cold beam
Hot beam
crystal

## Slide 48: False “Damage reversal”: from beam profile
Cold beam
Hot beam
crystal

## Slide 49: False “Damage reversal”: from beam profile
Cold beam
Hot beam
crystal

## Slide 50: False “Damage reversal”: from beam profile
Cold beam
Hot beam
crystal

## Slide 51: False “Damage reversal”: from beam profile
Cold beam
Hot beam
crystal

## Slide 52: False “Damage reversal”: from drift
X-ray beam
crystal

## Slide 53: Systematic error: Illumination contrast appears to “reverse” damage
Room temperature high-dose rate series
de la Mora, et al. (2020) PNAS USA 117, 4142-4151
occupancy
time
0
1
observed
cold
hot

## Slide 54
Holton (2009) J. Synchrotron Rad. 16 133-42
Radiation Damage World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
10/Å global damage Howells et al. (2009)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
4 R-C-COOH Garman et al. (2015)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
~1? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.06 putidaredoxin Corbett et al. (2007)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 55: “rastering” to find the crystal
Membrane
protein crystal
X-ray beam
ice

## Slide 56: “painting” for flat dose

## Slide 57: “painting” for virtual beam

## Slide 58: Painting with X-rays
0°
img_000045

## Slide 59: Painting with X-rays
0.2°
img_000100

## Slide 60: Painting with X-rays
30°
img_015000

## Slide 61: Painting with X-rays
90°
img_045000

## Slide 62: Painting with X-rays
360°
img_180000

## Slide 63: Painting with X-rays
1080°
img_540000

## Slide 64: Beam Shape Dichotomy
Flat-top beam
  Uniform dose in illuminated region
  Sharp edges: sensitive to drift
Gaussian beam
  Softer edges
  High dose contrast
Best of both?
  “dose flattening”

## Slide 65: How many images?
360° / 0.1° * ( 100 µm / 1 µm )2
= 36x106
28,000 photons/image

## Slide 66: Lossless data rate
The 1.2e-5 scattered photons per incident photon can be derived form the cross section of oxygen (0.2 cm^2/g) and the rough density of protein crystals (1.2 g/cm^3), and the fact that about half of all scattered photons hit a flat detector: 0.2*1.2*1e-4/2 = 1.155e-5 That is, flux*thickness*1.2e-5 is the rate of photon arrivals and log2(pixels) is the number of bits required to store the location of one photon in the entropy-limited regime. Lossless compression cannot be better than this because individual photon arrivals are genuinely random.
bits
s
= log2(pixels) * flux * thick * 1.2x10-5
where: bits/s = entropy-limited compressed data rate
pixels = number of pixels in the detector
flux = photons/s onto the sample thick = sample thickness in microns
EG: 1e12 ph/s * 100um thick = 3.4 GBytes/s

## Slide 67: How to lose information
long exposures
  >1 photon/image = order of arrivals
Wide phi slice
  sum over angle
Large beams
  sum over profile area
Pink/divergent beam
  sum over lambda/angle
Background
  non-crystal stuff
Systematics
  Dose contrast, drift, read-out gap

## Slide 68: Dose slicing: is that a spot?

## Slide 69: Dose slicing: is that a spot?

## Slide 70: Dose slicing: is that a spot?

## Slide 71: Dose slicing: is that a spot?

## Slide 72: Dose slicing: is that a spot?

## Slide 73: Dose slicing: is that a spot?

## Slide 74
photons
0
4
time
photons
0
4
photons
0
4
time
photons
0
4
Single Photons Carry Information
About Radiation Damage

## Slide 75: Prediction:
“painting mode” data collection =
damage-free data from synchrotron
zero-dose extrapolation that works
Why? Because everything is linear (to first order)

## Slide 76: Detector Calibration

## Slide 77
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel Pilatus detector
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 78: 140-fold multiplicity
7.4σ = Na
DELFAN residual anomalous difference
data Courtesy of Tom & Janet
I/Sa = 260

## Slide 79: Prediction:
Detector ultra-calibration will
Reveal identify of light metals
down to Na
(perhaps F?)
Why? Because ultra-high multiplicity can

## Slide 80: The R-factor Gap

## Slide 81
Rwork = 0.04
Rfree = 0.05
dmin = 3.5 Å
6σ = 1 e-
Simulation:
Realistic noise
“perfect” model
Hydrogen: visible at 3.5 Å resolution!

## Slide 84: The UNTANGLE Challenge
https://github.com/jmholton/UnTangle

## Slide 85: Prediction:
Untangling Ensemble Models will
Simultaneously reveal correlated motions and low-lying map features
down to 1 e-
Why? Because small molecules can

## Slide 86: Summary
Re-tool or die
Stills should be better
Ultra-calibration to see Na
Correct Rad Dam by “painting”
Correct non-isomorphism by “bending”
Correct ensemble for low-noise maps
The Last Å: where we live now

## Slide 87: Dominant source of error in MX: Cowtan’s Cat
http://www.ysbl.york.ac.uk/~cowtan/fourier/coeff.html
Amplitudes
Phases
2Fo-Fc
+
=

## Slide 88: key structural dynamical insight
https://cen.acs.org/pharmaceuticals/vaccines/tiny-tweak-behind-COVID-19/98/i38

## Slide 89
novocaine
1901 1902 1903 1904 1905 1906 1907 1908 1909 1910
1911 1912 1913 1914 1915 1916 1917 1918 1919 1920
1921 1922 1923 1924 1925 1926 1927 1928 1929 1930
Word War I
Pandemic
electron
X-ray
diffraction
Neutron
“Nature
of chem
Bond”
Curie
Genes on
Chromasomes
penicillin (1941)
mass
spec
e-
scope
DNA
conv.
plasma
Pavlov
insulin
Vitamin K
Svedberg
Titanic
hormones
X-rays
bakelite
victrola
relativity
tunguska
Bohr
USSR
Lucy
“how-to”
kleenex
Russia
vs
Ukra
polymer
Vitamin A
“giant
hereditary
molecule”

## Slide 90
2001 2002 2003 2004 2005 2006 2007 2008 2009 2010
2011 2012 2013 2014 2015 2016 2017 2018 2019 2020
2021 2022 2023 2024 2025 2026 2027 2028 2029 2030
iPhone
Pandemic
APS-U
ALS-U
Pandemic
16k PDBs: Protein Structure Initiative ->
AlphaFold2
AlphaFold
Diamond & Soleil
PSI ends
100k
PDBs
150k
PDBs
cryoEM
ribosome
Quasi
Xtals
9/11
iPod
firefox
wikipedia
LHC
Pandemic
iPad
H2O
CRISPR
CASP15
pluto
Rosetta
zika
grav wave