## Slide 1: PowerPoint File available:
http://bl831.als.lbl.gov/
~jamesh/powerpoint/
UCSF_DQvMI_2017.pptx

## Slide 2: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1: TomAlberTron
UC Multicampus Research Programs and Initiatives (MRPI)
NIH NIGMS R01 GM124149
NIH NIGMS P30 GM124169
Integrated Diffraction Analysis Technologies (IDAT)
Plexxikon, Inc.
Synchrotron Radiation Structural Biology Resource (SLAC)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser John Spence
Chris Nielsen Clemens Schulze-Briese Aina Cohen Ana Gonzalez

## Slide 3: signal vs noise
“If you don’t have good data, then you have no data at all.”
-Sung-Hou Kim

## Slide 4: signal vs noise
easy
hard
impossible

## Slide 5: signal vs noise
easy
hard
impossible
threshold of “solvability”

## Slide 6: signal vs noise
“If you don’t have good data, then you must learn statistics.”
-James Holton

## Slide 7: Adding noise

## Slide 8: Adding noise
12 + 12 = 1.42

## Slide 9: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 10: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 11: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 12: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
102 + 12 = 10.052

## Slide 13: What do we want?
Resolution
Low R factor
Mosaicity
Nice, round spots
No overlaps
No twinning
Lots of crystals
…

## Slide 15: What do we want?
Resolution
Low R-factor
Mosaicity
Nice, round spots
No overlaps
No twinning
Lots of crystals
…
2. Phases

## Slide 16: Phases
http://bl831.als.lbl.gov/~jamesh/movies/dephase.mpeg

## Slide 17
scattering from a structure
sample
detector
beam center
+

## Slide 18
forward Fourier Transform
inverse Fourier Transform
no phase
+

## Slide 19
scattering from a structure
colored by phase
sample
detector
inverse Fourier Transform
+

## Slide 20
scattering from a lattice
colored by phase
sample
detector
beam center
+

## Slide 21
scattering from a lattice
colored by phase
sample
detector
beam center
+

## Slide 22
scattering from a lattice
colored by phase
sample
detector
beam center
+

## Slide 23
scattering from a crystal structure
colored by phase
sample
detector
beam center
+

## Slide 24: Major Phasing techniques
Molecular Replacement
Multiple Isomorphous Replacement
Multiwavelength Anomalous Diffraction
Single-wavelength Anomalous Diffraction

## Slide 25: Molecular Replacement
?
correct structure and intensities
http://www.ysbl.york.ac.uk/~cowtan/fourier/coeff.html

## Slide 26: Molecular Replacement
Available model and intensities

## Slide 27: Molecular Replacement
?
correct structure and intensities

## Slide 28: Molecular Replacement
use something similar as a starting model

## Slide 29: Model Building
current model is missing something

## Slide 30: Model Building
phases from available model

## Slide 31: Model Building
missing bits show up, even if not in available model!

## Slide 32: Model Building
missing bits show up better in Fobs + (Fobs - Fcalc) map

## Slide 33: Phase errors: simplest possible case
fractional coordinate
electron density (e-/Å3)

## Slide 34: Phase errors: simplest possible case
fractional coordinate
electron density (e-/Å3)

## Slide 35: Phase errors: simplest possible case
fractional coordinate
electron density (e-/Å3)

## Slide 36: Phase errors: simplest possible case
fractional coordinate
electron density (e-/Å3)

## Slide 37: Phase errors: simplest possible case
fractional coordinate
electron density (e-/Å3)

## Slide 38: Phase errors: simplest possible case
fractional coordinate
electron density (e-/Å3)

## Slide 39: Phase errors: simplest possible case
fractional coordinate
electron density (e-/Å3)

## Slide 40: Phase errors: simplest possible case
fractional coordinate
electron density (e-/Å3)

## Slide 41: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 42: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 43: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 44: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 45: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 46: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 47: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 48: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 49: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 50: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 51: Phase errors: 3-atom case
fractional coordinate
electron density (e-/Å3)

## Slide 52: Phase errors: asymmetric case
fractional coordinate
electron density (e-/Å3)

## Slide 53: Phase errors: asymmetric case
fractional coordinate
electron density (e-/Å3)

## Slide 54: Phase errors: asymmetric case
fractional coordinate
electron density (e-/Å3)

## Slide 55: Phase errors: asymmetric case
fractional coordinate
electron density (e-/Å3)

## Slide 56: Phase errors: asymmetric case
fractional coordinate
electron density (e-/Å3)

## Slide 57: Phase errors: asymmetric case
fractional coordinate
electron density (e-/Å3)

## Slide 58: Phase errors: asymmetric case
fractional coordinate
electron density (e-/Å3)

## Slide 59: Phase errors: asymmetric case
fractional coordinate
electron density (e-/Å3)

## Slide 60: Phase errors: asymmetric case
fractional coordinate
electron density (e-/Å3)

## Slide 61: Molecular Dynamics Simulation
1aho
Scorpion toxin
0.96 Å resolution
64 residues
Solvent: H20 + acetate
Cerutti et al. (2010).J. Phys. Chem. B 114, 12811-12824.
using real
crystal’s lattice

## Slide 62: MD simulation: 30 conformers from 24,000
Cerutti et al. (2010).J. Phys. Chem. B 114, 12811-12824.

## Slide 63: Electron density from 24,000 conformers

## Slide 64: MLFSOM simulation
Holton, Classen, Frankel & Tainer (2014) "R-factor gap" FEBS 281 4046-60

## Slide 65: 2Fsim-Fcalc and Fsim-Fcalc maps
1.0 Å data
Rwork= 0.137
Rfree = 0.159
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc

## Slide 66: 2Fsim-Fcalc and “true difference” maps
1 “sigma” 2Fsim-Fc
Fright – (2Fsim-Fc)
1.0 Å data
Rwork= 0.137
Rfree = 0.159

## Slide 67: 30 conformers from 24,000

## Slide 68: Conventional model vs X-ray data
1 “sigma” 2Fobs-Fc
2.5 “sigma” Fobs-Fc
1.0 Å data
Rwork = 0.116
Rfree = 0.135

## Slide 69: How many conformers are needed?
Rwork = 0.0441
Rfree = 0.0516
vs Fsim
Answer: 2-14
MD-derived fake data

## Slide 70: How many conformers are needed?
Rwork = 0.135
Rfree = 0.158
vs Fobs
1aho:
Rwork = 0.1475
Rfree = 0.1685
Answer: 1-7
Observed x-ray data

## Slide 71: Adding noise
12%2 + 12%2 = 17%2
Rprotein + Rsolvent ≈ Rwork

## Slide 72: Adding noise
4%2 + 12%2 = 12.6%2
Rprotein + Rsolvent ≈ Rwork

## Slide 73: How many conformers are there?
All difference
features
are in
the solvent!
real data

## Slide 74: Solvent boundary problem

## Slide 75: Solvent boundary problem

## Slide 76: Solvent boundary problem

## Slide 77: Solvent boundary problem

## Slide 78: Current implementation

## Slide 79: Better implementation? (not available yet)

## Slide 80: Combined multi-conformer & cloud solvent
Rwork = 0.0309
Rfree = 0.0678
vs Fsim
Problem: diverges with more cycles

## Slide 81: Getting rid of “bias”
Throw out everything not 100% sure about
  Alt confs? Side chains? Loops?
  Can often cut down to 50% or more
Build biggest Fobs-Fcalc feature
Refine to convergence
  Atoms stop moving, not just R settling
Goto 2.
  Note: Repeating MR = rigid-body shift
  Solvent-flattened SAD phases not better

## Slide 82: Building back from mainchain
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.

## Slide 83: Building back from mainchain
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.
Fo-Fc difference map peak height

## Slide 84: Take-home lesson:
Always build into the
biggest
Fobs-Fcalc difference feature
(least likely to be noise)
If biggest feature is negative:
adjust bulk solvent parameters

## Slide 85: “R” factors
R = % error

## Slide 86: “R” factors
completely random: 0.59
starting MR solution: 0.4-0.55
something still wrong?: > 0.3
correct chain trace: < 0.2
small molecule: ~ 0.05

## Slide 87: “R” factors
Rcryst (or just “R”)
observed vs calculated data (Fs)
Rfree
cross-check with “random” subset of data
should be < 0.3 and < Rcryst + 0.1

## Slide 88
structure factor (F)
spot index (h)
Fitting data

## Slide 89
structure factor (F)
spot index (h)
Fitting data

## Slide 90
structure factor (F)
spot index (h)
Fitting data

## Slide 91
structure factor (F)
spot index (h)
Fitting data

## Slide 92: “R” factors
Rcryst (or just “R”)
observed vs calculated data (Fs)
Rfree
cross-check with “random” subset of data
should be < 0.3 and < Rcryst + 0.1
Rsym = Rmerge (self-consistency of data: Is)

## Slide 93: Rmerge
completely random: 0.59
weak data (high angle): 0.7- ∞
wrong symmetry choice?: ~0.2-0.55
small or disordered crystal: ~0.1-0.2
typical: ~ 0.05
blows up
as Iobs → 0

## Slide 94: R-factor Gap
Holton et al. (2014). FEBS J. 281, 4046-60.
R1 < 2*Rsigma
Publication criterion for chemical crystallography:
R1 = Fo vs Fc for I/σ(I) > 3
Rsigma = <σ(I)>/<I>
There are no PDB entries that pass this test!

## Slide 95: Why should you care?
dmax = 4.5 Å
Rcryst = 27%
Rfree = 38%

## Slide 96: Why should you care?
3a8n 4.5 Å Rmerge = 0.15 R/Rfree = 0.306/0.396
1grz 5 Å Rmerge = 0.052 R/Rfree = 0.369/0.428
1qzv 4.44 Å Rmerge = 0.099 R/Rfree = 0.41/0.42

## Slide 97: Why should you care?
1hvu 4.75 Å Rmerge = 0.064 R/Rfree = 0.34/0.413
2r6e 5.02 Å Rmerge = 0.058 R/Rfree = 0.394/0.397
1n8e 4.5 Å Rmerge = 0.138 R/Rfree = 0.415/0.416

## Slide 98: “R” factors
Rcryst (or just “R”)
observed vs calculated data (Fs)
Rfree
cross-check with “random” subset of data
should be < 0.3 and < Rcryst + 0.1
Rsym = Rmerge (self-consistency of data: Is)
Rrim Rpim Rmeas
Riso Ranom
Rdiff
Rsym is “unfair” to high multiplicity

## Slide 99: R-factor
http://bl831.als.lbl.gov/~jamesh/movies/rfactor.mpeg

## Slide 100: Overloads
http://bl831.als.lbl.gov/~jamesh/movies/overloads.mpeg

## Slide 101: Resolution: low-angle cutoff
http://bl831.als.lbl.gov/~jamesh/movies/lo_cut.mpeg

## Slide 102: Completeness: missing wedge
http://bl831.als.lbl.gov/~jamesh/movies/osc.mpeg

## Slide 103: Completeness: random deletion
http://bl831.als.lbl.gov/~jamesh/movies/completeness.mpeg

## Slide 104: And the dominant source of error is…
Resolution
  Disorder (including Radiation Damage)
  Background
Phases
  Non-isomorphism (including Radiation Damage)
  Vibration (beam, xtal, spindle, etc.)
  Detector calibration

## Slide 105: What is “disorder”?

## Slide 106: What is “disorder”?

## Slide 107: What is “disorder”?

## Slide 108: What is “disorder”?
order
order
disorder
B-factor

## Slide 109: “B” factors
ATOM 122 N LEU A 13 -3.244 25.808 19.998 1.00 16.96 N
ATOM 123 CA LEU A 13 -2.877 25.448 21.355 1.00 15.29 C
ATOM 124 C LEU A 13 -2.792 23.966 21.561 1.00 17.54 C
ATOM 125 O LEU A 13 -1.814 23.493 22.143 1.00 16.35 O
ATOM 126 CB LEU A 13 -3.907 26.164 22.268 1.00 18.72 C
ATOM 127 CG LEU A 13 -3.577 25.982 23.738 1.00 21.19 C
ATOM 128 CD1 LEU A 13 -2.283 26.820 24.019 1.00 19.43 C
ATOM 129 CD2 LEU A 13 -4.702 26.474 24.639 1.00 24.65 C
ATOM 130 N SER A 14 -3.677 23.149 20.979 1.00 15.96 N
ATOM 131 CA SER A 14 -3.646 21.711 21.061 1.00 18.26 C
ATOM 132 C SER A 14 -2.373 21.203 20.360 1.00 18.71 C
ATOM 133 O SER A 14 -1.747 20.315 20.930 1.00 17.47 O
ATOM 134 CB SER A 14 -4.875 21.077 20.419 1.00 17.62 C
ATOM 135 OG ASER A 14 -4.825 19.665 20.388 0.50 20.89 O
ATOM 136 OG BSER A 14 -6.027 21.408 21.164 0.50 18.67 O
ATOM 137 N LYS A 15 -2.045 21.772 19.215 1.00 18.03 N
ATOM 138 CA LYS A 15 -0.799 21.361 18.555 1.00 18.12 C
ATOM 139 C LYS A 15 0.446 21.707 19.351 1.00 18.81 C
ATOM 140 O LYS A 15 1.400 20.948 19.411 1.00 17.77 O
ATOM 141 CB LYS A 15 -0.700 22.034 17.177 1.00 14.49 C
ATOM 142 CG LYS A 15 -1.727 21.368 16.256 1.00 16.12 C
ATOM 143 CD LYS A 15 -1.663 22.147 14.936 1.00 19.40 C
ATOM 144 CE ALYS A 15 -2.725 21.614 13.986 0.50 17.42 C
ATOM 145 CE BLYS A 15 -1.750 21.211 13.750 0.50 17.01 C
ATOM 146 NZ ALYS A 15 -2.346 21.674 12.559 0.50 18.61 N
ATOM 147 NZ BLYS A 15 -3.052 20.513 13.741 0.50 18.76 N

## Slide 110: “B” factors
B ≈ 4d2 + 12
essentially, the “resolution” of an atom
d = resolution in Å

## Slide 111
electron density (e-/Å3)
position (Å)
“B” factors

## Slide 112
electron density (e-/Å3)
position (Å)
“B” factors

## Slide 113
electron density (e-/Å3)
position (Å)
“B” factors

## Slide 114
electron density (e-/Å3)
position (Å)
“B” factors

## Slide 115: The B factor
Bragg, W. H. (1914)."XCVII. The intensity of reflexion of X rays by crystals", Philosophical Magazine Series 6 27, 881-899. Published May 1 1914

## Slide 116: B factor from image analysis
B = 500

## Slide 117: B factor from image analysis
B = 20

## Slide 118
Crystal diameter (micron)
Resolution (Å)
B = 0
B = 20
B = 60
B = 170
B = 330
B = 560
B = 850
Bigger is better, but not by much

## Slide 119: The real problem is:
a grand challenge for structural biology in the 21st century
Averaging
+
Dynamics
=
Poor
resolution

## Slide 120: What Causes Disorder?
Function
Radiation damage
Mosaicity
Strain
Xtal abuse
Dehydration

## Slide 121: What Causes Disorder?
Function
Radiation damage
Mosaicity
Strain
Xtal abuse
Dehydration

## Slide 122: Muybridge’s galloping horse (1878)

## Slide 123: realistic “crystal” of horses

## Slide 124: average structure: galloping horse

## Slide 125: Ways to improve order
New crystal form
Purify
  - add a column
  - heat shock
Bind something
  - Known ligand
  - Silver bullets
Change the clone
  - chop off floppy bits
  - homolog
  - Ala -> Lys mutants
Make Protein Sit Still!!!
Newman J. (2006) Acta Cryst. D62 27-31.
8000 cases in PDB of resolution improvement
80% of these are different crystal forms
> 1 Å improvement → 94% different forms

## Slide 126: What Causes Disorder?
Function
Radiation damage
Mosaicity
Strain
Xtal abuse
Dehydration

## Slide 127: Types of radiation damage
Global
Specific

## Slide 128: Types of radiation damage
Global
  scale factor
  B factor
  non-isomorphism
Specific
  depends on chemistry
  destroys phasing signal

## Slide 129
Global damage
Howells, et al. (2009) J. Electron Spectrosc. Relat. Phenom. 170, 4-12.

## Slide 130: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12

## Slide 131: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12
10 MGy/Å

## Slide 132: what the is a MGy?
http://bl831.als.lbl.gov/
damage_rates.pdf
Holton J. M. (2009) J. Synchrotron Rad. 16 133-42
1 MGy = 106 J/kg

## Slide 133
How long will my crystal last?
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
ALS 4.2.2 MAD 2.2e11 75x80 3.7e+07 27.3 kGy/s 18 m 73 s
ALS 5.0.1 mono 1.6e11 100 2.0e+07 10.4 kGy/s 48 m 3.2 m
ALS 5.0.2 MAD 8e11 100 1.0e+08 51.8 kGy/s 9.6 m 39 s
ALS 5.0.3 mono 1.7e11 100 2.2e+07 11 kGy/s 45 m 3 m
ALS 8.2.1 MAD 1.8e11 100 2.3e+07 11.7 kGy/s 43 m 2.9 m
ALS 8.2.2 MAD 2.3e11 100 2.9e+07 14.9 kGy/s 34 m 2.2 m
ALS 8.3.1 MAD 9e11 70 2.3e+08 119 kGy/s 4.2 m 17 s
ALS 8.3.1 typical 6e11 70 1.6e+08 115 kGy/s 4.3 m 17 s
ALS 12.3.1 MAD 1.8e11 100 2.3e+07 11.7 kGy/s 43 m 2.9 m
ALS 12.3.1 ML 4.0e12 100 5.1e+08 513 kGy/s 58 s 3.9 s
APS 8-BM MAD 1e11 200 2.5e+06 1.27 kGy/s 6.6 h 26 m
APS 14-BM-C mono 5.8e10 200 1.4e+06 738 Gy/s 11 h 45 m
APS 14-BM-D MAD 3.3e9 200 8.2e+04 42 Gy/s 8.3 d 13 h
APS 14-ID-B MAD 6.0e10 200 1.5e+06 763 Gy/s 11 h 44 m
APS 17-BM MAD 1.1e11 200 2.8e+06 1.4 kGy/s 6 h 24 m
APS 17-ID MAD 2.3e11 200 5.8e+06 2.93 kGy/s 2.8 h 11 m
APS 19-BM MAD 2.0e11 70x60 4.8e+07 24.2 kGy/s 21 m 83 s
APS 19-ID MAD 1.3e13 80x40 4.1e+09 2.07 MGy/s 15 s 0.97 s
APS 19-ID typical 5.5e11 100x100 5.5e+07 28 kGy/s 18 m 71 s
APS 22-BM MAD 7e12 80x40 2.2e+09 1.23 MGy/s 24 s 1.6 s
APS 22-ID MAD 7e12 80x40 2.2e+09 1.23 MGy/s 24 s 1.6 s
APS 22-ID typical 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
APS 23-ID-B MAD 1e13 75x25 5.3e+09 3.01 MGy/s 10 s 0.66 s
APS 23-ID typical 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
APS 24-ID-C MAD 1.3e13 20x60 1.1e+10 5.23 MGy/s 5.7 s 0.38 s
APS 24-ID-E MAD 0.5e13 20x100 2.5e+09 1.19 MGy/s 25 s 1.7 s
APS 31-ID MAD 2e12 70 4.1e+08 194 kGy/s 2.6 m 10 s

## Slide 135
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 136: Specific damage
final, refined phases

## Slide 137: Specific damage
experimentally-obtained phases

## Slide 138
Holton, J. M. (2007) J. Synch. Rad. 14, 51-72.

## Slide 139
1.0
0.0
fraction
unconverted
Holton, J. M. (2007) J. Synch. Rad. 14, 51-72.

## Slide 140
Holton (2009) J. Synchrotron Rad. 16 133-42
Radiation Damage World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
10/Å global damage Howells et al. (2009)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
4 R-C-COOH Garman et al. (2015)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
~1? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.06 putidaredoxin Corbett et al. (2007)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 141: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 142: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 143: No Damage in the Dark!
Experiment time (hours)
Peak absorbance (electrons)
4.6 5.0 5.4 5.8 6.2 6.6
0 5 10 15 20 25

## Slide 144
Rad dam take-home lesson:
The number of photons scattered
before crystal is dead
is independent
of flux & time
1 um3 = 105 photons (roomT)
1 um3 = 106 photons (synch)
1 um3 = 108 photons (XFEL)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009
(synch)

## Slide 145: Dose slicing
crystal’s useful life
N
photons
N
photons
N
photons
unacceptable
completeness
unacceptable
read noise

## Slide 146: Dose slicing: is that a spot?

## Slide 147: Dose slicing: is that a spot?

## Slide 148: Dose slicing: is that a spot?

## Slide 149: Dose slicing: is that a spot?

## Slide 150: Dose slicing: is that a spot?

## Slide 151: Dose slicing: is that a spot?

## Slide 152: What if?
You only have a few small crystals…
Should you:
  Collect 360° from each?
  Collect 10° from each at 36x exposure?
  Glue 36 xtals together, then collect 360° ?
  Glue, and do 12960° faint exposures?

## Slide 153
Chart: 
Resolution (Å)
CC vs right answer
“true” resolution limit

## Slide 154
Dose slice collection scenario |  |  | 
fine | coarse | glue | Glue & fine
3.17700 | 3.14057 | 3.17604 | 3.12086
“true” resolution vs strategy
301,640,334 photons/xtal

## Slide 155
processing procedure | resolution limit |  |  | 
 | fine | coarse | glue | glue&fine
XDS/XSCALE | 3.17700 | 3.14057 | 3.17604 | 3.12086
XDS/aimless | 3.16251 | 3.15922 | 3.16675 | 3.12162
XDS/noscale | 3.27289 | 3.15617 | 3.38929 | 3.12162
MOSFLM-defaults | x | x | x | x
MOSFLM-cheat | 3.19755 | 3.18166 | 3.20354 | 3.19755
HKL2000-defaults | x | x | x | x
HKL2000-expert | 3.21803 | 3.12646 | 3.11551 | 3.21803
HKL2000-cheat | 3.16119 | 3.10338 | 3.10338 | 3.16300
DIALS-defaults | x | x | 3.42125 | x
DIALS-expert | 3.10296 | 3.09547 | 3.07653 | 3.08465
d*Trek | ? | ? | 4.34076 | ?
EVAL15 | 3.14352 | 3.10383 | 3.09936 | 3.14105
EVAL15-sadabs | 3.13920 | 3.10797 | 3.10171 | 3.13700

## Slide 156: Zero-dose extrapolation (ZDE)
Diederichs, K. (2006). "Some aspects of quantitative analysis and correction of radiation damage." Acta Cryst. D 62(1): 96-101.

## Slide 157: "error bar" for electron density
structure factor (e-/cell)
spot index

## Slide 158: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 159: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 160: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 161: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 162: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 163: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 164: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 165: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 166: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 167: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 168: "error bar" for electron density
structure factor (e-/cell)
spot index
fractional coordinate
electron density (e-/Å3)

## Slide 169: "error bar" for electron density
fractional coordinate
electron density (e-/Å3)
Refinement
Against
Perturbed
Input
Data

## Slide 170: How does the “error” compare to “sigma”?
Electron Number Density (e-/Å3)
normalized counts

## Slide 171: How does the “error” compare to “sigma”?
Electron Number Density (e-/Å3)
normalized counts

## Slide 172: How does the “error” compare to “sigma”?
Electron Number Density (e-/Å3)
normalized counts

## Slide 173: What is the “error” in 2Fo-Fc “sigma” units?
traditional “sigma” units (multples of rms(-) relative to )
normalized counts

## Slide 174: What is the “error” in Fo-Fc “sigma” units?
traditional “sigma” units (multples of rms(-) relative to )
normalized counts

## Slide 175: Tradition
fractional coordinate
electron density (e-/Å3)

## Slide 176: Better contour: derived from noise
fractional coordinate
electron density (e-/Å3)

## Slide 177: Basic Principles
“Hell, there are NO RULES here - we're trying to accomplish something.”
Thomas A. Edison – inventor
“You’ve got to have an ASSAY.”
Arthur Kornberg – Nobel Laureate
“Control, control, you must learn CONTROL!”
Yoda – Jedi Master

## Slide 178: Data quality vs Model Interpretation
Big difference features first
  Don’t build anything you don’t have to
Ligand bound or not?
  Omit maps, “polder” maps, chemistry
R factor good enough?
  Rules of thumb
  Nothing beats a “control”
Radiation damage?
  Only control: early vs late data

## Slide 179: PowerPoint File available:
http://bl831.als.lbl.gov/
~jamesh/powerpoint/
UCSF_DQvMI_2017.pptx

## Slide 180: Molecular Dynamics vs Observation
Fobs
1aho.cif
1aho.pdb
Fsim
Fcalc
Fcalc
Rwork= 0.137
Rwork= 0.116
Rvault = 0.69
refined_vs_Fsim.pdb
LSQ rmsd = 0.43Å
rmsd = 1.05 Å
1aho 64-residue scorpion toxin in water to 1.0 Å resolution
Rvault = 0.48 to 4 Å
Riso =

## Slide 181: Molecular Dynamics vs Observation
Fobs
fav8.fcf
fav8.cif
Fsim
Fcalc
Fcalc
Rwork= 0.13
Rwork= 0.16
Rvault= 0.23
refined_vs_Fsim.pdb
LSQ rmsd = 0.091Å & 0.15 Å
rmsd = 0.20 Å
“fav8” 8-residue aromatic peptide with 4 waters to 1.0 Å resolution
R1 = 0.041
With 4σ cutoff!
Rvault = 0.20 to 2Å

## Slide 182: Is the structure any good?
“do the data presented justify the conclusions drawn?”