## Slide 1: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1 creator: Tom Alber
UC Multicampus Research Programs and Initiatives (MRPI)
UCSF Program for Breakthrough Biomedical Research (PBBR)
one-time NIH-DOE Inter-agency agreement (IAA)
Integrated Diffraction Analysis Technologies (IDAT)
Plexxikon, Inc.
M D Anderson CRC
Synchrotron Radiation Structural Biology Resource (SLAC)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser Dave Case
Chris Nielsen Clemens Schulze-Briese Aina Cohen Ana Gonzalez
Christine Gee Tom Peat Janet Newman

## Slide 2: PowerPoint File available:
http://bl831.als.lbl.gov/
~jamesh/powerpoint/
UQ_averaging_2016.pptx

## Slide 3: Hot debate:
When a horse gallops, is there ever a moment where all four hooves leave the ground?
AD 1872

## Slide 4: average structure: galloping horse

## Slide 5: Anything is possible … with the right tools.

## Slide 6: Muybridge’s multi-camera

## Slide 7: Muybridge’s galloping horse (1878)

## Slide 8: Hot questions: 21st century how do molecules work?
Beernink, Endrizzi, Alber & Schachman (1999). PNAS USA 96, 5388-5393.

## Slide 9: a “crystal” of horses

## Slide 10: realistic “crystal” of horses

## Slide 11: Not enough light

## Slide 12: brighter light

## Slide 13: brighter light

## Slide 14: even brighter

## Slide 15: very bright light

## Slide 16: average structure: galloping horse

## Slide 17
Damage is done
by dose (MGy)
proportional to photons/area
not time
not heat
Sliz P, Harrison SC & Rosenbaum G (2003). Structure 11, 13-19.
Garman EF & McSweeney SM (2006). J. Sync. Rad. 14, 1-3.
Owen RL, Rudino-Pinera E & Garman EF (2006). PNAS 103, 4912-4917.
Leiros et al. (2006). Acta Cryst. D 62, 125-132.
Holton JM (2007). J. Synch Rad. 14, 51-72.

## Slide 18: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12

## Slide 19: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12
10 MGy/Å

## Slide 20
Holton (2009) J. Synchrotron Rad. 16 133-42
Radiation Damage
World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
4 R-C-COOH Garman et al. (2015)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
~1? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 21: what the is a MGy?
http://bl831.als.lbl.gov/
damage_rates.pdf
Holton J. M. (2009) J. Synchrotron Rad. 16 133-42
1 MGy = 106 J/kg

## Slide 22
How long will my crystal last?
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
ALS 4.2.2 MAD 2.2e11 75x80 3.7e+07 27.3 kGy/s 18 m 73 s
ALS 5.0.1 mono 1.6e11 100 2.0e+07 10.4 kGy/s 48 m 3.2 m
ALS 5.0.2 MAD 8e11 100 1.0e+08 51.8 kGy/s 9.6 m 39 s
ALS 5.0.3 mono 1.7e11 100 2.2e+07 11 kGy/s 45 m 3 m
ALS 8.2.1 MAD 1.8e11 100 2.3e+07 11.7 kGy/s 43 m 2.9 m
ALS 8.2.2 MAD 2.3e11 100 2.9e+07 14.9 kGy/s 34 m 2.2 m
ALS 8.3.1 MAD 9e11 70 2.3e+08 119 kGy/s 4.2 m 17 s
ALS 8.3.1 typical 6e11 70 1.6e+08 115 kGy/s 4.3 m 17 s
ALS 12.3.1 MAD 1.8e11 100 2.3e+07 11.7 kGy/s 43 m 2.9 m
ALS 12.3.1 ML 4.0e12 100 5.1e+08 513 kGy/s 58 s 3.9 s
APS 8-BM MAD 1e11 200 2.5e+06 1.27 kGy/s 6.6 h 26 m
APS 14-BM-C mono 5.8e10 200 1.4e+06 738 Gy/s 11 h 45 m
APS 14-BM-D MAD 3.3e9 200 8.2e+04 42 Gy/s 8.3 d 13 h
APS 14-ID-B MAD 6.0e10 200 1.5e+06 763 Gy/s 11 h 44 m
APS 17-BM MAD 1.1e11 200 2.8e+06 1.4 kGy/s 6 h 24 m
APS 17-ID MAD 2.3e11 200 5.8e+06 2.93 kGy/s 2.8 h 11 m
APS 19-BM MAD 2.0e11 70x60 4.8e+07 24.2 kGy/s 21 m 83 s
APS 19-ID MAD 1.3e13 80x40 4.1e+09 2.07 MGy/s 15 s 0.97 s
APS 19-ID typical 5.5e11 100x100 5.5e+07 28 kGy/s 18 m 71 s
APS 22-BM MAD 7e12 80x40 2.2e+09 1.23 MGy/s 24 s 1.6 s
APS 22-ID MAD 7e12 80x40 2.2e+09 1.23 MGy/s 24 s 1.6 s
APS 22-ID typical 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
APS 23-ID-B MAD 1e13 75x25 5.3e+09 3.01 MGy/s 10 s 0.66 s
APS 23-ID typical 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
APS 24-ID-C MAD 1.3e13 20x60 1.1e+10 5.23 MGy/s 5.7 s 0.38 s
APS 24-ID-E MAD 0.5e13 20x100 2.5e+09 1.19 MGy/s 25 s 1.7 s
APS 31-ID MAD 2e12 70 4.1e+08 194 kGy/s 2.6 m 10 s

## Slide 23
How long will my crystal last?
http://bl831.als.lbl.gov/damage_rates.pdf

## Slide 25
The number of photons scattered
before crystal is dead
is independent
of data collection time
1 um3 = 106 photons (synch)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009

## Slide 26: Dose slicing
crystal’s useful life
N
photons
N
photons
N
photons
unacceptable
damage
unacceptable
read noise

## Slide 27: What if…
You only have a few small crystals?
Should you:
  Collect 360° from each?
  Collect 10° from each at 36x exposure?
  Glue 36 xtals together, then collect 360° ?
  Glue together and do 12960° ?
  http://bl1231.als.lbl.gov/~jamesh/dose_slice/results.html
5 μm & 1 MGy = 301,640,334 photons

## Slide 28: Dose slicing: is that a spot?

## Slide 29: Dose slicing: is that a spot?

## Slide 30: Dose slicing: is that a spot?

## Slide 31: Dose slicing: is that a spot?

## Slide 32: Dose slicing: is that a spot?

## Slide 33: Dose slicing: is that a spot?

## Slide 34
Resolution (Å)
CC vs right answer
“true” resolution limit

## Slide 35
Dose slice collection scenario |  |  | 
fine | coarse | glue | Glue & fine
3.03874 | 3.02970 | 3.0270 | 3.02948
“true” resolution vs strategy
301,640,334 photons

## Slide 36: Optimal exposure time (faint spots on a CCD)
thr Optimal exposure time for data set (s)
tref exposure time of reference image (s)
bgref background level near weak spots on
reference image (ADU)
bg0 ADC offset of detector (ADU)
bghr optimal background level (via thr)
σ0 rms read-out noise (ADU)
gain ADU/photon
m multiplicity of data set (including partials)
adjust exposure
so this is ~100

## Slide 37: Optimal exposure time (faint spots on a PAD)
thr Optimal exposure time for data set (s)
tro read-out time (s)
2.03 ms on PILATUS3 S
3 μs on EIGER

## Slide 38: Optimal exposure time (anomalous on a PAD)
time
intensity
2.03 ms

## Slide 39: Optimal exposure time (anomalous on EIGER)
time
intensity
0.003 ms

## Slide 40: Optimal exposure time (anomalous on a PAD)
thr Optimal exposure time (s)
tro read-out time (s)
2.03 ms on PILATUS3 S
3 μs on EIGER
PILATUS
>0.2 s/frame
EIGER
>0.0003 s/frame
= 20,000 frames
350 GB/dataset
11 seconds

## Slide 41
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 42
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.
No flux
No symmetry

## Slide 43
Crystal diameter (micron)
Resolution (Å)
B = 0
B = 20
B = 60
B = 170
B = 330
B = 560
B = 850
Bigger is better, but not by much

## Slide 44: Increased exposure won’t make the target sit still

## Slide 45: Timescales of radiation damage
Garret et. al. (2005) Chem. Rev. 105, 355-389

## Slide 46: Timescales of radiation damage
Garret et. al. (2005) Chem. Rev. 105, 355-389
LCLS
synch
bunch

## Slide 47: LCLS: outrunning damage

## Slide 48: Realistic single-particle prediction
1012 photon/pulse
100 nm focus

## Slide 49: Realistic single-particle prediction
1012 photon/pulse
3 nm focus

## Slide 50: lysozyme: real and reciprocal

## Slide 51: lysozyme: thermal motion

## Slide 52: Muybridge’s galloping horse (1878)
Real space
reciprocal
Average electron density

## Slide 53: Muybridge’s galloping horse (1878)
Real space
reciprocal
“Time-resolved” diffraction

## Slide 54: Single-image model refinement? Supporting a 4D model with 2D data

## Slide 55: The R-factor Gap
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.

## Slide 56: MD simulation: 30 conformers from 24,000
Cerutti et al. (2010).J. Phys. Chem. B 114, 12811-12824.

## Slide 57: Electron density from 24,000 conformers

## Slide 58: How many “conformers” are needed?
Rwork = 0.0441
Rfree = 0.0516
vs Fsim
Answer: 2-14
No solvent!

## Slide 59: How do you model solvent?
Rwork = 0.0309
Rfree = 0.0678
vs Fsim
Problem: diverges with more cycles

## Slide 60: “R-factor Gap” for macromolecules
R1 < 2*Rsigma
Publication criterion for chemical crystallography:
R1 = Fo vs Fc for I/σ(I) > 3
Rsigma = <σ(I)>/<I>
There are no PDB entries that pass this test!
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.

## Slide 61: Status of macromolecular representation:
Even if we knew the “right answer”
it would blow up.

## Slide 62
Required signal-to-noise (I/σ)
Solve-able proteins (%)
Current
technology
Goal
Threshold of a revolution in phasing

## Slide 63: Can you count to 1,000,000 ?
= 0.1%
sqrt(1,000,000)
1,000,000
= 3%
sqrt(1,000)
1,000
> 1000 is a waste!
photon
spot
Theoretically:
In reality:
ISa ~ 33
Rmeas ≈ 0.1% ?
ISa = 1000
Rmeas = ≈ 3%

## Slide 64: Is it Real? Or is it MLFSOM
simulated
real
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 65
Source of error | realistic simulation | No SHSSS | Perfect detector
Photon counting | + | + | +
Shutter jitter | + | + | -
Beam flicker | + | + | -
Sample absorption | + | + | -
Radiation damage | + | + | -
Imperfect spindle | + | + | -
vignette | + | + | -
Corner correction | + | + | -
SHSSS | + | - | -
Rmeas (∞-10 Å) | 2.8% | 0.7% | 0.7%
I/σ asymptotic | 26.8 | 74.2 | 81.0
Threshold of a revolution in phasing
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 66: CCD calibration: 7235 eV

## Slide 67: CCD calibration: 7247 eV

## Slide 68: Gadox calibration vs energy
photon energy (keV)
Relative absorption depth
same = good!
bad!

## Slide 69: Data collection parameters:
16 crystals
360° each, inverse beam
7235 eV photon energy
< 1 MGy per xtal
Australian Synchrotron MX1
  35 kGy/s into 100 μm x 100 μm

## Slide 70
RESOLUTION COMPLETENESS R-FACTOR I/SIGMA R-meas CC(1/2) Anomal SigAno Nano
LIMIT OF DATA observed Corr
9.17 99.1% 3.9% 257.47 3.9% 100.0* 91* 5.024 450
6.49 100.0% 5.2% 214.33 5.2% 100.0* 86* 3.836 882
5.30 100.0% 7.2% 165.13 7.2% 100.0* 76* 3.257 1175
4.59 100.0% 7.2% 175.42 7.3% 100.0* 67* 2.589 1403
4.10 99.9% 7.7% 174.13 7.7% 100.0* 59* 2.264 1594
3.74 99.9% 9.4% 143.09 9.4% 100.0* 49* 1.953 1783
3.47 100.0% 11.2% 120.17 11.2% 100.0* 39* 1.696 1942
3.24 100.0% 14.1% 91.14 14.1% 100.0* 30* 1.333 2103
3.06 99.9% 19.5% 65.79 19.5% 100.0* 23* 1.117 2214
2.90 99.9% 29.0% 44.85 29.1% 99.9* 17* 1.008 2369
2.77 99.9% 40.5% 32.58 40.6% 99.8* 11* 0.901 2493
2.65 99.9% 52.8% 25.16 52.9% 99.8* 10* 0.866 2605
2.54 100.0% 67.4% 19.47 67.6% 99.6* 2 0.804 2705
2.45 100.0% 88.9% 14.58 89.2% 99.2* 4 0.831 2859
2.37 100.0% 109.3% 9.97 109.7% 98.1* 5 0.829 2925
2.29 100.0% 138.2% 6.87 138.9% 96.1* 1 0.760 3037
2.22 100.0% 197.1% 4.03 198.6% 83.5* -1 0.721 3159
2.16 100.0% 227.3% 2.41 230.8% 46.9* -1 0.677 3224
2.10 61.2% 154.4% 1.28 163.6% 47.0* -2 0.660 1999
2.05 47.9% 170.1% 0.68 196.5% 25.7* 3 0.629 1578
total 93.3% 15.7% 54.30 15.8% 100.0* 12* 1.217 42499
140-fold multiplicity: 16 crystals, 360° each, inverse beam, 7235 eV

## Slide 71: 140-fold multiplicity
18 σ
Phased anomalous difference Fourier
16 σ

## Slide 72: 140-fold multiplicity
15σ = PO4
Phased anomalous difference Fourier

## Slide 73: 140-fold multiplicity
~2σ = Mg?
Phased anomalous difference Fourier

## Slide 74: 140-fold multiplicity
8.2σ = Mg or Na
DELFAN residual anomalous difference

## Slide 75
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel
Pilatus: subtract smooth baseline

## Slide 76
3.5
3.0
2.5
2.0
1.5
1.0
0.5
SHSSS
Systematic component of Rsseparate (%)
distance between spots (mm)
0.1 1 10 100
CCD detector
anomalous mates are always on
different modules
different
modules
New
Pilatus
SN113
Pilatus
SN001
Notes: Comparision of SHSSS measured by the detector-shift experiment on three different detectors:
The Q315R in ALS 8.3.1
The first Pilatus detector at the Swiss Light Soruce
A newer Pilatus detector at Stanford
Improvements in calibration technology have finally made
Pilatus competitive with calibration on CCDs

## Slide 77: non-isomorphism
Why doesn’t everyone do
Multi-crystal averaging?

## Slide 78
Dear James
The story of the two forms of lysozyme crystals goes back to about 1964 when it was found that the diffraction patterns from different crystals could be placed in one of two classes depending on their intensities. This discovery was a big set back at the time and I can remember a lecture title being changed from the 'The structure of lysozyme' to 'The structure of lysozyme two steps forward and one step back'. Thereafter the crystals were screened based on intensities of the (11,11,l) rows to distinguish them (e.g. 11,11,4 > 11,11,5 in one form and vice versa in another). Data were collected only for those that fulfilled the Type II criteria. (These reflections were easy to measure on the linear diffractometer because crystals were mounted to rotate about the diagonal axis). As I recall both Type I and Type II could be found in the same crystallisation batch . Although sometimes the external morphology allowed recognition this was not infallible.
The structure was based on Type II crystals. Later a graduate student Helen Handoll examined Type I. The work, which was in the early days and before refinement programmes, seemed to suggest that the differences lay in the arrangement of water or chloride molecules (Lysozyme was crystallised from NaCl). But the work was never written up. Keith Wilson at one stage was following this up as lysozyme was being used to test data collection strategies but I do not know the outcome.
An account of this is given in International Table Volume F (Rossmann and Arnold edited 2001) p760.
Tony North was much involved in sorting this out and if you wanted more info he would be the person to contact. I hope this is helpful. Do let me know if you need more.
Best wishes
Louise
Non-isomorphism in lysozyme

## Slide 79
Johnson’s ratio
Structure factor (e-)
Non-isomorphism in lysozyme

## Slide 80
Johnson’s ratio
Structure factor (e-)
Non-isomorphism in lysozyme

## Slide 82: Non-isomorphism in lysozyme
RH: 84.2%
vs 71.9%
Riso = 44.5%
3aw6
3aw7
Δcell = 0.7 %
RMSD = 0.18 Å

## Slide 83
h,k,l | structure factors (F) |  |  | 
 | #1 | #2 | #3 | #4
5,3,4 | 523.7 | 559.8 | 579.9 | 603.2
5,4,4 | 168.2 | 166.6 | 177.2 | 196.1
5,5,4 | 34.9 | 26.4 | 19.2 | 17.3
6,1,4 | 305.7 | 301.1 | 298.1 | 296.3
6,2,4 | 353.0 | 353.9 | 356.2 | 366.9
6,3,4 | 300.9 | 285.3 | 273.5 | 259.4
6,3,5 | 223.8 | 226.3 | 234.6 | 251.4
… | … | … | … | …
X-ray Data Sets
h,k,l | 100% | 17 % | 13 % | 9 %
 | 1st | 2nd | 3rd | 4th
5,3,4 | -1.46 | -0.02 | 1.84 | -0.72
5,4,4 | -0.88 | -0.29 | -0.34 | 0.15
5,5,4 | -0.42 | -0.65 | 1.02 | 1.47
6,1,4 | -0.90 | -0.85 | 1.44 | -0.40
6,2,4 | -1.20 | -0.37 | 0.67 | 0.01
6,3,4 | -0.75 | 0.31 | 0.48 | 0.00
6,3,5 | -0.75 | -0.85 | 0.72 | -0.82
… | … | … | … | …
data
set
Singular value decomp.
SVD
vector
value
Singular values & vectors
Correlation
Coefficients
-0.68
CC2
CC3
CC1
CC1 CC2 CC3
data set #1
Data sets
Positioned
in
“Correlation
Space”
-0.24
data set #2
data set #3
0.32 …

## Slide 85
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 86
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 87
Correlation to 2nd & 3rd singular vectors
Structure factor (electrons)

## Slide 88: Bragg’s “minimum wavelength principle”
Perutz (1985). “Early Days of Cryst…” Methods in Enzymology, Vol. 114, 3-18.
Bragg & Perutz (1952)."external form haemoglobin I", Acta Cryst. 5, 277-283.

## Slide 89: DMMULTI – fake data 4 deg rotation: 8 “xtals”: before
CC = 0.02

## Slide 90
CC = 0.8
DMMULTI – fake data 4 deg rotation: 8 “xtals”: after

## Slide 91
Dear James
The story of the two forms of lysozyme crystals goes back to about 1964 when it was found that the diffraction patterns from different crystals could be placed in one of two classes depending on their intensities. This discovery was a big set back at the time and I can remember a lecture title being changed from the 'The structure of lysozyme' to 'The structure of lysozyme two steps forward and one step back'. Thereafter the crystals were screened based on intensities of the (11,11,l) rows to distinguish them (e.g. 11,11,4 > 11,11,5 in one form and vice versa in another). Data were collected only for those that fulfilled the Type II criteria. (These reflections were easy to measure on the linear diffractometer because crystals were mounted to rotate about the diagonal axis). As I recall both Type I and Type II could be found in the same crystallisation batch . Although sometimes the external morphology allowed recognition this was not infallible.
The structure was based on Type II crystals. Later a graduate student Helen Handoll examined Type I. The work, which was in the early days and before refinement programmes, seemed to suggest that the differences lay in the arrangement of water or chloride molecules (Lysozyme was crystallised from NaCl). But the work was never written up. Keith Wilson at one stage was following this up as lysozyme was being used to test data collection strategies but I do not know the outcome.
An account of this is given in International Table Volume F (Rossmann and Arnold edited 2001) p760.
Tony North was much involved in sorting this out and if you wanted more info he would be the person to contact. I hope this is helpful. Do let me know if you need more.
Best wishes
Louise
Non-isomorphism in lysozyme

## Slide 92: Elastic deformation = non-isomorphism

## Slide 93: Elastic deformation = non-isomorphism

## Slide 94: Plastic deformation = poor diffraction

## Slide 95: Plastic deformation = poor diffraction

## Slide 96: Dehydration: 1934
100 μm
2 mm
= 1.5 μL
= 1.0 nL
10 μm
= 1.0 pL
and 2016?
1 μm
= 1.0 fL

## Slide 97: OK! OK! Now I am afraid!
What should I do?

## Slide 98: … but does it work for membrane proteins?
Efremov, R. G. & Sazanov, L. A. (2011)."Structure of the membrane domain of respiratory complex I", Nature 476, 414-420.
“To improve diffraction properties, crystals were slowly cooled to 4 C, placed into micro-dialysis buttons, and mother liquor was exchanged by dialysis for 0.1 M sodium acetate (pH 4.8), 0.15 M sodium tartrate (pH 5.0), 30% PEG4000, 0.1% sodium cholate and 12.5% glycerol over a period of 5 days.”
CCP4BB:
“We used it for a large membrane protein complex and diffraction improved from ~7 to 2.7 A. The crystal is fished out and put into mother liquor solution in the button, sealed with dialysis membrane and the button is then placed into about 5 mls of mother liquor with slightly higher PEG concentration. Then you just exchange outside buffer every day or so for solutions containing higher concentrations of PEG. We went from ~9 to 30 % PEG4000 in about a week. You can easily observe crystal under microscope and if it cracks - you went too far/too quickly with PEG and need to use a bit less next time. Also, this method allows you to control all other components of the dehydrating solution - we needed to decrease salt concentration at the same time as increasing PEG. You can also introduce/increase cryo-protectant concentration at the same time. With these crystals, otherwise excellent dehydration machines already mentioned did not work, possibly because the process had to be really slow.”

## Slide 99: oil is your friend

## Slide 100: opened drop: you have ~30 seconds!
oil

## Slide 101: oiled drop: you have ~3 hours
oil

## Slide 102: Dabbing to remove excess
clean surface

## Slide 103: Dabbing to remove excess
clean surface

## Slide 104: Dabbing to remove excess
clean surface

## Slide 105: Dabbing to remove excess
clean surface

## Slide 106: Dabbing to remove excess
clean surface

## Slide 107: Dabbing to remove excess
clean surface

## Slide 108: Dabbing to remove excess
clean surface

## Slide 109: X-ray scattering “rules”:
1 μm crystal ≈ 1 μm water
≈ 1 μm plastic
≈ 0.1 μm glass
≈ 1000 μm air
you want:
air gap < 1000x xtal size

## Slide 110: Non-crystal stuff in the beam
Too much
Too little
Just right

## Slide 111: Sources of error for weak spots
Beam intensity sqrt(seconds)
Radiation damage (10 MGy/Å)
Illuminated volume (size3)
Background sqrt(Ispot+Ibg)
Disorder (e-B)

## Slide 112: Fine Slicing
Pflugrath, J. W. (1999)."The finer things in X-ray diffraction data collection", Acta Cryst. D 55, 1718-1725.
background
background

## Slide 113: Background scattering

## Slide 114: Mosquito tips cost $0.15 each
So do EIGER pixels!
You just bought 18x106
Use them!
(they are reusable)

## Slide 115
X-ray beam size (μm)
Resolution (Å)
too big
too small
just right
Always better to match beam to target size

## Slide 116: Now What?
10 Å

## Slide 117: Ways to improve diffraction
New crystal form
Purify
  - add a column
  - heat shock
Bind something
  - Known ligand
  - Silver bullets
Change the clone
  - chop off floppy bits
  - homolog
  - Ala -> Lys mutants
Make Protein Sit Still!!!
Newman J. (2006) Acta Cryst. D62 27-31.
Heras B & Martin JL (2005) Acta Cryst. D61, 1173-1180.

## Slide 118: Basic Principles
“Hell, there are NO RULES here - we're trying to accomplish something.”
Thomas A. Edison – inventor
“You’ve got to have an ASSAY.”
Arthur Kornberg – Nobel Laureate
“Control, control, you must learn CONTROL!”
Yoda – Jedi Master

## Slide 119: URL Summary
Averaging is good for phasing
Averaging + disorder destroys resolution
Averaging + isomorphism = good for resolution
Humidity = isomorphism
Dose-slice with EIGER
The future = better models for “disorder”
http://bl831.als.lbl.gov/~jamesh/powerpoint/
UQ_averaging_2016.pptx
http://bl831.als.lbl.gov/xtalsize.html
http://bl831.als.lbl.gov/xtallife.html

## Slide 120: The Future of Structural Biology
grand challenge for the 21st century
We need
better
models
We need
better
data

## Slide 121: Grand Challenges in Structural Biology
Phase Problem
Better detector calibration
non-isomorphism phasing?
Amplitude Problem
    Revolution in sample handling
    Get around averaging (better models)
R-factor Gap
    Better models for “disorder” (function)
    If we had right answer, it would blow up!

## Slide 122: Suggested anomalous protocol:
2 wavelengths are better than 1
- (peak + inf)/2, and remote
MAD, not M-SAD!
360° in < 5 MGy
move detector
4X exposure
goto 2

## Slide 123
Real XFEL still

## Slide 124: Simulation of XFEL still

## Slide 125: XFEL: “fit” simulation to reality
Dispersion
Divergence
Mosaicity
Wavelength
Unit cell parameters (3)
Crystal orientation (3)
Mosaic domain size (3)
Beam center (2)
Beam direction (2)
Detector distance

## Slide 126
phiz
Simulation of XFEL still
phiy
phiz
phix
phix
phiy
VS
real

## Slide 127: Systematic error does not “average out”