## Slide 1: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1: TomAlberTron
UC Multicampus Research Programs and Initiatives (MRPI)
NIH NIGMS R01 GM124149
NIH NIGMS P30 GM124169
Integrated Diffraction Analysis Technologies (IDAT)
Plexxikon, Inc.
Synchrotron Radiation Structural Biology Resource (SLAC)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser John Spence
Chris Nielsen Clemens Schulze-Briese Aina Cohen Ana Gonzalez

## Slide 2: PowerPoint File available:
http://bl831.als.lbl.gov/
~jamesh/powerpoint/
Uruguay_datacoll_2017.pptx

## Slide 3: The “success rate” of data collection
100 s/dataset
200 days/year
~150 beamlines
~26,000,000 datasets/year
~10,000 PDBs in 2016

## Slide 4: signal vs noise
“If you don’t have good data, then you have no data at all.”
-Sung-Hou Kim

## Slide 5: signal vs noise
easy
hard
impossible

## Slide 6: signal vs noise
easy
hard
impossible
threshold of “solvability”

## Slide 7: signal vs noise
“If you don’t have good data, then you must learn statistics.”
-James Holton

## Slide 8: Adding noise

## Slide 9: Adding noise
12 + 12 = 1.42

## Slide 10: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 11: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 12: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
σtotal2 = σ12 + σ22

## Slide 13: Adding noise
12 + 12 = 1.42
32 + 12 = 3.22
102 + 12 = 10.052

## Slide 14: MR simulation
Rmsd from perfect search model (Å)
corrupted model
Correlation coefficient to correct density

## Slide 15: The “threshold of solvability” is sharp!
How can we predict success/failure?
Know Thy Experiment

## Slide 16: Where do photons go?
beamstop
Transmitted (98%)
Protein
1A x-rays

## Slide 17: Elastic scattering

## Slide 18: Elastic scattering

## Slide 19: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
Protein
1A x-rays

## Slide 20: Elastic scattering

## Slide 21: Inelastic scattering

## Slide 22: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
Protein
1A x-rays

## Slide 23: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays

## Slide 24: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 25: Photoelectric absorption

## Slide 26: Photoelectric absorption
e-
+

## Slide 27: Fluorescence
+

## Slide 28: Fluorescence
e-
+

## Slide 29: Metal identification

## Slide 30: Auger emission
+

## Slide 31: Auger emission
++
e-

## Slide 32: Sample atoms

## Slide 33: Sample atoms

## Slide 34: Primary ionization
e-
+

## Slide 35: Secondary ionizations
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+

## Slide 36: Ionization track
e-
e-
e-
e-
e-
e-
e-
e-
e-
+
+
+
+
+
+
+
+
+
e-
+

## Slide 39: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 40: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (99%)
Absorbed (~0%)

## Slide 41: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (~0%)
Absorbed (99%)
Re-emitted (99%)
Absorbed (~0%)

## Slide 42: Where do photons go?
beamstop
elastic scattering (6%)
Transmitted (98%)
useful/absorbed energy: 7.3%
inelastic scattering (7%)
Photoelectric (87%)
Protein
1A x-rays
Re-emitted (~0%)
Absorbed (99%)
Re-emitted (99%)
Absorbed (~0%)

## Slide 43: What do we want?
Resolution
Mosaicity
Nice, round spots
No overlaps
No twinning
Lots of crystals
…

## Slide 45: What do we want?
Resolution
Mosaicity
Nice, round spots
No overlaps
No twinning
Lots of crystals
…
2. Phases

## Slide 46: Phases
http://bl831.als.lbl.gov/~jamesh/movies/dephase.mpeg

## Slide 47: And the dominant source of error is…
Resolution
  Disorder (including Radiation Damage)
  Background
Phases
  Non-isomorphism (including Radiation Damage)
  Vibration (beam, xtal, spindle, etc.)
  Detector calibration

## Slide 48: What is “disorder”?

## Slide 49: What is “disorder”?

## Slide 50: What is “disorder”?

## Slide 51: What is “disorder”?
order
order
disorder
B-factor

## Slide 52: “B” factors
ATOM 122 N LEU A 13 -3.244 25.808 19.998 1.00 16.96 N
ATOM 123 CA LEU A 13 -2.877 25.448 21.355 1.00 15.29 C
ATOM 124 C LEU A 13 -2.792 23.966 21.561 1.00 17.54 C
ATOM 125 O LEU A 13 -1.814 23.493 22.143 1.00 16.35 O
ATOM 126 CB LEU A 13 -3.907 26.164 22.268 1.00 18.72 C
ATOM 127 CG LEU A 13 -3.577 25.982 23.738 1.00 21.19 C
ATOM 128 CD1 LEU A 13 -2.283 26.820 24.019 1.00 19.43 C
ATOM 129 CD2 LEU A 13 -4.702 26.474 24.639 1.00 24.65 C
ATOM 130 N SER A 14 -3.677 23.149 20.979 1.00 15.96 N
ATOM 131 CA SER A 14 -3.646 21.711 21.061 1.00 18.26 C
ATOM 132 C SER A 14 -2.373 21.203 20.360 1.00 18.71 C
ATOM 133 O SER A 14 -1.747 20.315 20.930 1.00 17.47 O
ATOM 134 CB SER A 14 -4.875 21.077 20.419 1.00 17.62 C
ATOM 135 OG ASER A 14 -4.825 19.665 20.388 0.50 20.89 O
ATOM 136 OG BSER A 14 -6.027 21.408 21.164 0.50 18.67 O
ATOM 137 N LYS A 15 -2.045 21.772 19.215 1.00 18.03 N
ATOM 138 CA LYS A 15 -0.799 21.361 18.555 1.00 18.12 C
ATOM 139 C LYS A 15 0.446 21.707 19.351 1.00 18.81 C
ATOM 140 O LYS A 15 1.400 20.948 19.411 1.00 17.77 O
ATOM 141 CB LYS A 15 -0.700 22.034 17.177 1.00 14.49 C
ATOM 142 CG LYS A 15 -1.727 21.368 16.256 1.00 16.12 C
ATOM 143 CD LYS A 15 -1.663 22.147 14.936 1.00 19.40 C
ATOM 144 CE ALYS A 15 -2.725 21.614 13.986 0.50 17.42 C
ATOM 145 CE BLYS A 15 -1.750 21.211 13.750 0.50 17.01 C
ATOM 146 NZ ALYS A 15 -2.346 21.674 12.559 0.50 18.61 N
ATOM 147 NZ BLYS A 15 -3.052 20.513 13.741 0.50 18.76 N

## Slide 53: The B factor
Bragg, W. H. (1914)."XCVII. The intensity of reflexion of X rays by crystals", Philosophical Magazine Series 6 27, 881-899. Published May 1 1914

## Slide 54: B factor from image analysis
B = 500

## Slide 55: B factor from image analysis
B = 20

## Slide 56
Crystal diameter (micron)
Resolution (Å)
B = 0
B = 20
B = 60
B = 170
B = 330
B = 560
B = 850
Bigger is better, but not by much

## Slide 57
disorder
+ averaging
= poor resolution
Diffraction Take-Home Lesson:

## Slide 58: What Causes Disorder?
Function
Radiation damage
Mosaicity
Strain
Xtal abuse
Dehydration

## Slide 59: What Causes Disorder?
Function
Radiation damage
Mosaicity
Strain
Xtal abuse
Dehydration

## Slide 60: Muybridge’s galloping horse (1878)

## Slide 61: realistic “crystal” of horses

## Slide 62: average structure: galloping horse

## Slide 63: Ways to improve order
New crystal form
Purify
  - add a column
  - heat shock
Bind something
  - Known ligand
  - Silver bullets
Change the clone
  - chop off floppy bits
  - homolog
  - Ala -> Lys mutants
Make Protein Sit Still!!!
Newman J. (2006) Acta Cryst. D62 27-31.
8000 cases in PDB of resolution improvement
80% of these are different crystal forms
> 1 Å improvement → 94% different forms

## Slide 64: What Causes Disorder?
Function
Radiation damage
Mosaicity
Strain
Xtal abuse
Dehydration

## Slide 65: Types of radiation damage
Global
Specific

## Slide 66: Types of radiation damage
Global
  scale factor
  B factor
  non-isomorphism
Specific
  depends on chemistry
  destroys phasing signal

## Slide 67
Global damage
Howells, et al. (2009) J. Electron Spectrosc. Relat. Phenom. 170, 4-12.

## Slide 68: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12

## Slide 69: resolution dependence of global damage
resolution (Å)
maximum tolerable dose (MGy)
1 2 3 5 7 10 20 40 70 100
1
10
100
103
Howells et al. (2009) J. Electron. Spectrosc. Relat. Phenom. 170 4-12
10 MGy/Å

## Slide 70: what the is a MGy?
http://bl831.als.lbl.gov/
damage_rates.pdf
Holton J. M. (2009) J. Synchrotron Rad. 16 133-42
1 MGy = 106 J/kg

## Slide 71
How long will my crystal last?
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
BESSY 14.1 MAD 1.6e11 340x800 5.9e+05 298 Gy/s 28 h 1.9 h
BESSY 14.2 MAD 1.9e11 190x90 1.1e+07 5.63 kGy/s 89 m 5.9 m
BESSY 14.3 mono 0.9e11 255x40 8.8e+06 3.18 kGy/s 2.6 h 10 m
BSRF 3W1A MAD 5e10? 800x600 1.0e+05 53 Gy/s 6.6 d 10 h
CLSI 08ID-1 MAD 1e12 200x100 5.0e+07 28.2 kGy/s 18 m 71 s
DIAMOND I02 MAD 1e12 100 1.0e+08 50.9 kGy/s 9.8 m 39 s
DIAMOND I03 MAD 1e12 100 1.0e+08 50.9 kGy/s 9.8 m 39 s
DIAMOND I04 MAD 1e12 100 1.0e+08 50.9 kGy/s 9.8 m 39 s
DIAMOND I04.1 MAD 1e12 100 1.0e+08 50.9 kGy/s 9.8 m 39 s
ESRF BM14 MAD 1.5e10 100 1.5e+06 704 Gy/s 12 h 47 m
ESRF ID14-1 MAD ?
ESRF ID14-2 MAD ?
ESRF ID14-3 MAD ?
ESRF ID14-4 MAD ?
ESRF BM30A MAD 0.5e11 300 5.6e+05 275 Gy/s 30 h 2 h
LNLS W01B-MX2 MAD 5e11 250x500 3.8e+06 7.7 kGy/s 1.0 h 4 m
MAXLAB I711 mono 2e11 300 2.2e+06 613 Gy/s 14 h 54 m
MAXLAB I911-1 mono 3e10 300x100 1.0e+06 1.03 kGy/s 8.1 h 32 m
MAXLAB I911-2 mono 1e11 300 1.1e+06 1.15 kGy/s 7.3 h 29 m
MAXLAB I911-3 MAD 3e11 250x150 8.0e+06 4.07 kGy/s 2 h 8.2 m
MAXLAB I911-4 mono 5e11 400x200 6.2e+06 3.18 kGy/s 2.6 h 10 m
MAXLAB I911-5 mono 5e10 300x200 8.3e+05 424 Gy/s 20 h 79 m
NSRRC BL13B1 MAD 4e11 200 1.3e+07 6.05 kGy/s 83 m 5.5 m
NSRRC BL13C1 MAD 4e10 200 1.3e+06 598 Gy/s 14 h 56 m
NSRRC BL17B1 MAD 4e9 200 1.3e+05 71.8 Gy/s 4.8 d 7.7 h

## Slide 73
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 74: Multi-crystal strategies
Kendrew et al. (1960) "Structure of Myoglobin” Nature 185, 422-427.

## Slide 75: Specific damage
final, refined phases

## Slide 76: Specific damage
experimentally-obtained phases

## Slide 77
Holton, J. M. (2007) J. Synch. Rad. 14, 51-72.

## Slide 78
1.0
0.0
fraction
unconverted
Holton, J. M. (2007) J. Synch. Rad. 14, 51-72.

## Slide 79
Holton (2009) J. Synchrotron Rad. 16 133-42
Radiation Damage World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
10/Å global damage Howells et al. (2009)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
4 R-C-COOH Garman et al. (2015)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
~1? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.06 putidaredoxin Corbett et al. (2007)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 80: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 81: Life-halving concentration
Na | 44
Mg | 27
P | 9
S | 7
Cl | 5
K | 3.3
Ca | 2.7
Fe | 1.0
Cu | 0.67
Zn | 0.58
molar, at the Se edge based on RADDOSE
As | 0.44
Se | 0.42
Br | 2.9
I | 0.47
Gd | 0.21
Ta | 0.13
Pt | 0.17
Au | 0.16
Hg | 0.16
U | 0.23

## Slide 82: No Damage in the Dark!
Experiment time (hours)
Peak absorbance (electrons)
4.6 5.0 5.4 5.8 6.2 6.6
0 5 10 15 20 25

## Slide 83
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.
No flux
No symmetry
No exposure time

## Slide 84
The number of photons scattered
before crystal is dead
is independent
of flux & time
1 um3 = 105 photons (roomT)
1 um3 = 106 photons (synch)
1 um3 = 108 photons (XFEL)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009
(synch)

## Slide 85: Dose slicing
crystal’s useful life
N
photons
N
photons
N
photons
unacceptable
completeness
unacceptable
read noise

## Slide 86: X-ray data are 3D!

## Slide 87: Data collection “strategy”
Dauter, Z. (1999). "Data-collection strategies." Acta Cryst. D 55(10): 1703-1717.
The “American Method”:
360° no matter what
(shoot first, questions later)

## Slide 88: Dose slicing: is that a spot?

## Slide 89: Dose slicing: is that a spot?

## Slide 90: Dose slicing: is that a spot?

## Slide 91: Dose slicing: is that a spot?

## Slide 92: Dose slicing: is that a spot?

## Slide 93: Dose slicing: is that a spot?

## Slide 94: What if?
You only have a few small crystals…
Should you:
  Collect 360° from each?
  Collect 10° from each at 36x exposure?
  Glue 36 xtals together, then collect 360° ?
  Glue, and do 12960° faint exposures?

## Slide 95
Chart: 
Resolution (Å)
CC vs right answer
“true” resolution limit

## Slide 96
Dose slice collection scenario |  |  | 
fine | coarse | glue | Glue & fine
3.17700 | 3.14057 | 3.17604 | 3.12086
“true” resolution vs strategy
301,640,334 photons/xtal

## Slide 97
processing procedure | resolution limit |  |  | 
 | fine | coarse | glue | glue&fine
XDS/XSCALE | 3.17700 | 3.14057 | 3.17604 | 3.12086
XDS/aimless | 3.16251 | 3.15922 | 3.16675 | 3.12162
XDS/noscale | 3.27289 | 3.15617 | 3.38929 | 3.12162
MOSFLM-defaults | x | x | x | x
MOSFLM-cheat | 3.19755 | 3.18166 | 3.20354 | 3.19755
HKL2000-defaults | x | x | x | x
HKL2000-expert | 3.21803 | 3.12646 | 3.11551 | 3.21803
HKL2000-cheat | 3.16119 | 3.10338 | 3.10338 | 3.16300
DIALS-defaults | x | x | 3.42125 | x
DIALS-expert | 3.10296 | 3.09547 | 3.07653 | 3.08465
d*Trek | ? | ? | 4.34076 | ?
EVAL15 | 3.14352 | 3.10383 | 3.09936 | 3.14105
EVAL15-sadabs | 3.13920 | 3.10797 | 3.10171 | 3.13700

## Slide 98: Minimum exposure time:
~1 photon/pixel
  PAD w XDS, DIALS
~10 photon/pixel
PAD w HKL2k, MOSFLM
~30 photon/pixel
CCD detector

## Slide 99: Optimal exposure time (faint spots on CCD or IP)
thr Optimal exposure time for data set (s)
tref exposure time of reference image (s)
bgref background level near weak spots on
reference image (ADU)
bg0 ADC offset of detector (ADU)
bghr optimal background level (via thr)
σ0 rms read-out noise (ADU)
gain ADU/photon
m multiplicity of data set (including partials)
adjust exposure
so this is ~15

## Slide 100: What Causes Disorder?
Function
Radiation damage
Mosaicity
Strain
Xtal abuse
Dehydration

## Slide 101
Ewald’s “mosaic” picture

## Slide 102
Ewald’s “mosaic” picture

## Slide 103
Ewald’s “mosaic” picture
What is
this stuff?

## Slide 104
Darwin’s original picture

## Slide 105
“mosaicity” with visible light

## Slide 106: mosaic spread = 0 º

## Slide 107: mosaic spread = 0.1º

## Slide 108: mosaic spread = 0.2º

## Slide 109: mosaic spread = 0.4º

## Slide 110: mosaic spread = 0.6º

## Slide 111: mosaic spread = 0.8º

## Slide 112: mosaic spread = 1.0º

## Slide 113: mosaic spread = 1.5º

## Slide 114: mosaic spread = 2.0º

## Slide 115: mosaic spread = 2.5º

## Slide 116: mosaic spread = 3.2º

## Slide 117: mosaic spread = 6.4º

## Slide 118: mosaic spread = 12.8º

## Slide 119: What Causes Disorder?
Function
Radiation damage
Mosaicity
Strain
Xtal abuse
Dehydration

## Slide 120
stress and strain
radiation damage = defects
What about
undamaged crystals?

## Slide 121: Purity is crucial!
McPherson, A., Malkin, A. J., Kuznetsov, Y. G. & Plomp, M. (2001)."Atomic force microscopy applications in macromolecular crystallography", Acta Cryst. D 57, 1053-1060.
not important for
initial hits
important for
resolution

## Slide 122: What can I improve?
Purity!
is 95% good enough? 99%?
Purity!
conformational (homogeneous)
Purity!
kinetic (stable over time)

## Slide 123: What Causes Disorder?
Function
Radiation damage
Mosaicity (η) > ~3 μm
Strain (B) < ~3 μm
Xtal abuse
Dehydration

## Slide 124: What Causes Disorder?
Function
Radiation damage
Mosaicity > ~3 μm
Strain < ~3 μm
Xtal abuse
Dehydration

## Slide 125: Xtal Abuse
physical contact
don’t touch the part you intend to shoot
osmotic shock
equilibrate, or calculate matching solution
changes in dielectric constant
Petsko (1975) J. Mol. Biol. 96, 381-388.
cooled density mismatch
Juers & Matthews (2004) Acta Cryst. D 60, 412-421.
basically: no sudden moves!

## Slide 126: What Causes Disorder?
Function
Radiation damage
Mosaicity > ~3 μm
Strain < ~3 μm
Xtal abuse
Dehydration

## Slide 127: opened drop: you have ~30 seconds!
equilibrated drop

## Slide 128: OK! OK! Now I am afraid!
What should I do?

## Slide 129: Basic Principles
“Hell, there are NO RULES here - we're trying to accomplish something.”
Thomas A. Edison – inventor
“You’ve got to have an ASSAY.”
Arthur Kornberg – Nobel Laureate
“Control, control, you must learn CONTROL!”
Yoda – Jedi Master

## Slide 130: The Best Assay

## Slide 131: And the dominant source of error is…
Resolution
  Disorder (including Radiation Damage)
  Background
Phases
  Non-isomorphism (including Radiation Damage)
  Vibration (beam, xtal, spindle, etc.)
  Detector calibration

## Slide 132: beam size vs xtal size
  Put your crystal into the beam

## Slide 133: Get thee to a microbeam?
Evans et al. (2011)."Macromolecular microcrystallography", Crystallography Reviews 17, 105-142.

## Slide 134: beam size vs xtal size
  Put your crystal into the beam
  Shoot the whole crystal

## Slide 135: shoot the whole crystal

## Slide 136: shoot the whole crystal

## Slide 137: shoot the whole crystal

## Slide 138: beam size vs xtal size
  Put your crystal into the beam
  Shoot the whole crystal
  Shoot nothing but the crystal

## Slide 139: scattering/absorptoin “rules”:
1 μm crystal ≈ 1 μm water
≈ 1 μm plastic
≈ 0.1 μm glass
≈ 1000 μm air
Optimum: support thickness = crystal thickness

## Slide 140
X-ray beam size (μm)
Resolution (Å)
too big
too small
just right

## Slide 141: shoot nothing but the crystal

## Slide 142: shoot nothing but the crystal

## Slide 143: shoot nothing but the crystal

## Slide 144: shoot nothing but the crystal

## Slide 145: shoot nothing but the crystal

## Slide 146: Tipping point for µfocus:
10 µm
~10 mm
~1 mrad =0.06°

## Slide 147: Gaussian beam
50% of flux
the other 50%

## Slide 148: Collimated beam
100% of flux
0%

## Slide 149: beam size vs xtal size
  Put your crystal into the beam
  Shoot the whole crystal
  Shoot nothing but the crystal
  Back off!

## Slide 150: Background scattering

## Slide 151: Background scattering
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
$100,000.00
real estate is
expensive
use it!

## Slide 152: Mosquito tips cost $0.15 each
So do Pilatus pixels!
We bought 6,224,001
Use them!
(they are reusable)

## Slide 153: Fine Slicing
Pflugrath, J. W. (1999)."The finer things in X-ray diffraction data collection", Acta Cryst. D 55, 1718-1725.
background
background

## Slide 154: beam size vs xtal size
  Put your crystal into the beam
  Shoot the whole crystal
  Shoot nothing but the crystal
  Back off!
  The crystal must rotate

## Slide 155: The crystal rotates!

## Slide 156: The crystal rotates!
Membrane Protein Expression Center © 2012

## Slide 157: avoiding overlaps
c
c

## Slide 158: avoiding overlaps
c

## Slide 159: avoiding overlaps
c
http://www.mitegen.com/mic_catalog.php?c=DTMicroMounts

## Slide 160: avoiding overlaps
c
http://www.mitegen.com/mic_catalog.php?c=orientedmounts

## Slide 161: One xtal, no idea? Suggested native protocol:
Do strategy
Start at specified phi
Complete fast as you can
Keep going to 360°
Move detector
Advance phi 10-30 deg
Increase photons/image 4x
goto 4

## Slide 162: Adding images
% cat << EOF > MERGE2CBF.INP
NAME_TEMPLATE_OF_DATA_FRAMES= /data/you/weak_?????.cbf
DATA_RANGE= 1 10
NAME_TEMPLATE_OF_OUTPUT_FRAMES=/data/you/sum_???.cbf
NUMBER_OF_DATA_FRAMES_COVERED_BY_EACH_OUTPUT_FRAME= 10
EOF
% merge2cbf
Which is better?:
% xds_runme.com /data/you/weak_?????.cbf
% xds_runme.com /data/you/sum_?????.cbf
“lossy”
compression

## Slide 163: Native Summary
100 ADU/pixel
10 μm for lysozyme
Do “strategy”
Follow by “American Method”
“Attenu-wait”: dose slicing
Assay, control and open mind
http://bl831.als.lbl.gov/xtalsize.html
http://bl831.als.lbl.gov/xtallife.html
http://bl831.als.lbl.gov/~jamesh/powerpoint/Uruguay_dtacoll_2017.pptx

## Slide 164: And the dominant source of error is…
Resolution
  Disorder (including Radiation Damage)
  Background
Phases
  Non-isomorphism (including Radiation Damage)
  Vibration (beam, xtal, spindle, etc.)
  Detector calibration

## Slide 165
anomalous signal
Crick, F. H. C. & Magdoff, B. S. (1956) Acta Crystallogr. 9, 901-908.
Hendrickson, W. A. & Teeter, M. M. (1981) Nature 290, 107-113.
# sites
MW (Da)
ΔF
F
≈ 1.2 f”
√
World record!
ΔF/F = 0.5%
Wang, Dauter & Dauter (2006) Acta Cryst. D 62, 1475-1483.

## Slide 166: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.

## Slide 167: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.
Riso ≈ 0.7 %/MGy

## Slide 168: First diffraction from protein xtal
Bernal, J. & Crowfoot, D. (1934). "X-ray photographs of crystalline pepsin", Nature 133, 794-795.
1934

## Slide 169: Dehydration: 1934
100 μm
2 mm
= 1.5 μL
= 1.0 nL
10 μm
= 1.0 pL
and 2017?
1 μm
= 1.0 fL

## Slide 170
Dear James
The story of the two forms of lysozyme crystals goes back to about 1964 when it was found that the diffraction patterns from different crystals could be placed in one of two classes depending on their intensities. This discovery was a big set back at the time and I can remember a lecture title being changed from the 'The structure of lysozyme' to 'The structure of lysozyme two steps forward and one step back'. Thereafter the crystals were screened based on intensities of the (11,11,l) rows to distinguish them (e.g. 11,11,4 > 11,11,5 in one form and vice versa in another). Data were collected only for those that fulfilled the Type II criteria. (These reflections were easy to measure on the linear diffractometer because crystals were mounted to rotate about the diagonal axis). As I recall both Type I and Type II could be found in the same crystallisation batch . Although sometimes the external morphology allowed recognition this was not infallible.
The structure was based on Type II crystals. Later a graduate student Helen Handoll examined Type I. The work, which was in the early days and before refinement programmes, seemed to suggest that the differences lay in the arrangement of water or chloride molecules (Lysozyme was crystallised from NaCl). But the work was never written up. Keith Wilson at one stage was following this up as lysozyme was being used to test data collection strategies but I do not know the outcome.
An account of this is given in International Table Volume F (Rossmann and Arnold edited 2001) p760.
Tony North was much involved in sorting this out and if you wanted more info he would be the person to contact. I hope this is helpful. Do let me know if you need more.
Best wishes
Louise
Non-isomorphism in lysozyme

## Slide 171
Johnson’s ratio
Structure factor (e-)
Non-isomorphism in lysozyme

## Slide 172
Johnson’s ratio
Structure factor (e-)
Non-isomorphism in lysozyme

## Slide 174: Non-isomorphism in lysozyme
RH: 84.2%
vs 71.9%
Riso = 44.5%
3aw6
3aw7
Δcell = 0.7 %
RMSD = 1.70 Å
RMSD = 0.18 Å

## Slide 175
0.5% cell change → 15%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.
Same structure, different cell

## Slide 176
Same structure, different cell
0.5% cell change → 15%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 177
Same cell, rotated protein
0.5° rotation → 16%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 178
Same cell, rotated protein
0.5° rotation → 16%
Crick & Magdoff (1956) “theory method isomorphous replacement”, Acta Cryst. 9, 901-8.

## Slide 179
Uniform stretch
5% change → 0%

## Slide 180
5% change → 0%
Uniform stretch

## Slide 181
Magdoff & Crick (1955) “Ribonuclease II. Accuracy of measurement and shrinkage”, Acta Cryst. 8, 461-8.
Crick & Magdoff (1956) “The theory of the method of isomorphous replacement for protein crystals”, Acta Cryst. 9, 901-8.

## Slide 182: Elastic deformation = non-isomorphism

## Slide 183: Elastic deformation = non-isomorphism

## Slide 184: Plastic deformation = poor diffraction

## Slide 185: Plastic deformation = poor diffraction

## Slide 186: … but does it work for membrane proteins?
Efremov, R. G. & Sazanov, L. A. (2011)."Structure of the membrane domain of respiratory complex I", Nature 476, 414-420.
“To improve diffraction properties, crystals were slowly cooled to 4 C, placed into micro-dialysis buttons, and mother liquor was exchanged by dialysis for 0.1 M sodium acetate (pH 4.8), 0.15 M sodium tartrate (pH 5.0), 30% PEG4000, 0.1% sodium cholate and 12.5% glycerol over a period of 5 days.”
CCP4BB:
“We used it for a large membrane protein complex and diffraction improved from ~7 to 2.7 A. The crystal is fished out and put into mother liquor solution in the button, sealed with dialysis membrane and the button is then placed into about 5 mls of mother liquor with slightly higher PEG concentration. Then you just exchange outside buffer every day or so for solutions containing higher concentrations of PEG. We went from ~9 to 30 % PEG4000 in about a week. You can easily observe crystal under microscope and if it cracks - you went too far/too quickly with PEG and need to use a bit less next time. Also, this method allows you to control all other components of the dehydrating solution - we needed to decrease salt concentration at the same time as increasing PEG. You can also introduce/increase cryo-protectant concentration at the same time. With these crystals, otherwise excellent dehydration machines already mentioned did not work, possibly because the process had to be really slow.”

## Slide 187: And the dominant source of error is…
Resolution
  Disorder (including Radiation Damage)
  Background
Phases
  Non-isomorphism (including Radiation Damage)
  Vibration (beam, xtal, spindle, etc.)
  Detector calibration

## Slide 188: Optimal exposure time (anomalous on a PAD)
time
intensity
2.03 ms

## Slide 189: PAD full vs partial
iteration
Summed intensity

## Slide 190: Optimal exposure time (anomalous on a PAD)
tmad Optimal exposure time (s)
tro read-out time (s)
2.03 ms on Pilatus3 S
0.95 ms on Pilatus3 X
0.003 ms on Eiger
Attenuate for MAD
PILATUS
>0.2 s/frame
EIGER
>0.0003 s/frame

## Slide 191: And the dominant source of error is…
Resolution
  Disorder (including Radiation Damage)
  Background
Phases
  Non-isomorphism (including Radiation Damage)
  Vibration (beam, xtal, spindle, etc.)
  Detector calibration

## Slide 192: Detector calibration: 7235 eV

## Slide 193: Detector calibration: 7247 eV

## Slide 194: Gadox calibration vs energy
photon energy (keV)
Relative absorption depth
same = good!
bad!

## Slide 195
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel Pilatus detector
Spatial Heterogeneity in Sharp Spot Sensitivity

## Slide 196: Systematic error does not “average out”

## Slide 197
Required signal-to-noise (I/σ)
Solve-able proteins (%)
CCD
old Pilatus
Goal
Threshold of a revolution in phasing
Best
Pilatus

## Slide 198: Can you count to 1,000,000 ?
= 0.1%
sqrt(1,000,000)
1,000,000
= 3%
sqrt(1,000)
1,000
> 1000 is a waste!
photon
spot
Theoretically:
In reality:
ISa ~ 33
Rmeas ≈ 0.1% ?
ISa = 1000
Rmeas = ≈ 3%

## Slide 199: Fractional error
mult > (—)2
~3%
<ΔF/F>

## Slide 200
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 201: S-SAD merging 20 xtals
Knott et al. (2017). "Guide-bound CRISPR-Cas13a." Nature S&MB online

## Slide 202
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
F+ | 52.3965 | 57.5371 | 48.523 | 47.5964 | 34.153 | 48.9106 | 70.3415 | 52.7871 | 59.3327 | 50.0622
F- | 46.3965 | 51.5371 | 42.523 | 41.5964 | 28.153 | 42.9106 | 64.3415 | 46.7871 | 53.3327 | 44.0622
observation
intensity
Systematic vs random error

## Slide 203: Data collection parameters:
16 crystals
360° each, inverse beam
7235 eV photon energy
< 1 MGy per xtal
Australian Synchrotron MX1
  35 kGy/s into 100 μm x 100 μm

## Slide 204
RESOLUTION COMPLETENESS R-FACTOR I/SIGMA R-meas CC(1/2) Anomal SigAno Nano
LIMIT OF DATA observed Corr
9.17 99.1% 3.9% 257.47 3.9% 100.0* 91* 5.024 450
6.49 100.0% 5.2% 214.33 5.2% 100.0* 86* 3.836 882
5.30 100.0% 7.2% 165.13 7.2% 100.0* 76* 3.257 1175
4.59 100.0% 7.2% 175.42 7.3% 100.0* 67* 2.589 1403
4.10 99.9% 7.7% 174.13 7.7% 100.0* 59* 2.264 1594
3.74 99.9% 9.4% 143.09 9.4% 100.0* 49* 1.953 1783
3.47 100.0% 11.2% 120.17 11.2% 100.0* 39* 1.696 1942
3.24 100.0% 14.1% 91.14 14.1% 100.0* 30* 1.333 2103
3.06 99.9% 19.5% 65.79 19.5% 100.0* 23* 1.117 2214
2.90 99.9% 29.0% 44.85 29.1% 99.9* 17* 1.008 2369
2.77 99.9% 40.5% 32.58 40.6% 99.8* 11* 0.901 2493
2.65 99.9% 52.8% 25.16 52.9% 99.8* 10* 0.866 2605
2.54 100.0% 67.4% 19.47 67.6% 99.6* 2 0.804 2705
2.45 100.0% 88.9% 14.58 89.2% 99.2* 4 0.831 2859
2.37 100.0% 109.3% 9.97 109.7% 98.1* 5 0.829 2925
2.29 100.0% 138.2% 6.87 138.9% 96.1* 1 0.760 3037
2.22 100.0% 197.1% 4.03 198.6% 83.5* -1 0.721 3159
2.16 100.0% 227.3% 2.41 230.8% 46.9* -1 0.677 3224
2.10 61.2% 154.4% 1.28 163.6% 47.0* -2 0.660 1999
2.05 47.9% 170.1% 0.68 196.5% 25.7* 3 0.629 1578
total 93.3% 15.7% 54.30 15.8% 100.0* 12* 1.217 42499
140-fold multiplicity: 16 crystals, 360° each, inverse beam, 7235 eV

## Slide 205: 140-fold multiplicity
18 σ
Phased anomalous difference Fourier
16 σ

## Slide 206: 140-fold multiplicity
15σ = PO4
Phased anomalous difference Fourier

## Slide 207: 140-fold multiplicity
~2σ = Mg?
Phased anomalous difference Fourier

## Slide 208: 140-fold multiplicity
8.2σ = Mg?
DELFAN residual anomalous difference

## Slide 209: Discerning Na+ from Mg++
f’’ (electrons)
DELFAN peak height (σ)
Mg
Ne
Na
F
O
N

## Slide 210: 140-fold multiplicity
7.4σ = Na
DELFAN residual anomalous difference

## Slide 211
FOM from “dm”
Correlation to final map
XFEL Phasing success vs Figure of Merit
Hunter et al. (2016)."Selenium anomalous phasing XFEL", Nature Comm. 7, 13388.
http://cxidb.org/id54-SfjMJjaBny/id-54.html http://cxidb.org/id55-BWuBDSUrBy/id-55.html
Adjusting:
Solvent content
Resolution
SDfac Sdadd
Cycles of dm
“mode”
“scheme”
NCS radius
NCS cycles
Phase blur

## Slide 212: Phasing Summary
~3% error per spot, 1%/MGy
7235 eV for S-SAD
Multiplicity multiplicity multiplicity
“Attenu-wait”: dose slicing
>1000 photons/spot is a waste
http://bl831.als.lbl.gov/xtalsize.html
http://bl831.als.lbl.gov/xtallife.html
http://bl831.als.lbl.gov/~jamesh/powerpoint/Uruguay_datacoll_2017.pptx

## Slide 213: But my reviewer says…
Rmerge in high-resolution bin is >100% !
Answer: this is expected

## Slide 214: Expected Rmerge as Iobs → 0

## Slide 215
Average value
Averaging Gaussian error
Number of samples averaged

## Slide 216
Average value
Averaging Gauss/Gauss error
Number of samples averaged

## Slide 217
Average outer-shell Rmerge
Rmerge at the resolution limit in PDB
Year

## Slide 218: Take-home lesson:
R factors are
undefined
as Iobs → 0
Report as “ – “ in outer bin

## Slide 219: Re-indexing cheat sheet
Dauter, Z. (1999). "Data-collection strategies." Acta Cryst. D 55(10): 1703-1717.

## Slide 220: Adding noise
12 + 12 = 1.42

## Slide 221: 100% SeMet incorporation
Trivial to solve

## Slide 222: 100% S -Met incorporation
Impossible to solve

## Slide 223: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 224: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 225: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 226: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 227: Phase Problem: Se vs S
fraction Sulfur
correlation coefficient

## Slide 228
29% Se 71% S

## Slide 229
28% Se 72% S

## Slide 230
21% Se 79% S

## Slide 231
11% Se 89% S

## Slide 232: Finding sites
fraction Sulfur
Number of correct sites

## Slide 233: Finding sites
fraction Sulfur
Number of correct sites

## Slide 234: Finding sites
fraction Sulfur
Number of correct sites

## Slide 235: Finding sites
fraction Sulfur
Number of correct sites
25
20
15
10
5
0
peak height ()

## Slide 236: Finding sites
fraction Sulfur
Number of correct sites

## Slide 237: CCP4: aimless log
$TABLE: Analysis against resolution, XDSdataset:
$GRAPHS:I/sigma, Mean Mn(I)/sd(Mn(I)):0|0.216023x0|137.14:2,13,14:
:Rmerge, Rfull, Rmeas, Rpim v Resolution:0|0.216023x0|1.70834:2,4,5,6,7:
:Average I, RMSdeviation and Sd:0|0.216023x0|1650.8:2,10,11,12:
:Fractional bias:0|0.216023x0|0:2,15:
$$
N 1/d^2 Dmid Rmrg Rfull Rcum Rmeas Rpim Nmeas AvI RMSdev sd I/RMS Mn(I/sd) FrcBias $$ $$
1 0.0064 12.55 0.020 0.020 0.020 0.021 0.006 13115 1651 57 42 29.2 137.1 -
2 0.0191 7.24 0.027 0.027 0.024 0.028 0.008 24753 1171 47 42 25.0 105.2 -
3 0.0318 5.61 0.038 0.038 0.029 0.040 0.012 32197 857 46 43 18.4 79.6 -
4 0.0445 4.74 0.034 0.034 0.031 0.035 0.010 37743 1212 57 53 21.4 91.2 -
5 0.0572 4.18 0.036 0.036 0.032 0.038 0.011 42642 1181 59 57 19.9 83.8 -
6 0.0699 3.78 0.049 0.049 0.036 0.052 0.015 47224 883 59 57 15.1 65.1 -
7 0.0826 3.48 0.065 0.065 0.040 0.068 0.020 51052 685 59 58 11.7 50.9 -
8 0.0953 3.24 0.096 0.096 0.045 0.100 0.029 54636 448 56 56 8.0 35.0 -
9 0.1080 3.04 0.151 0.151 0.050 0.158 0.046 58072 268 53 53 5.1 22.7 -
10 0.1207 2.88 0.229 0.229 0.056 0.240 0.070 60731 171 51 51 3.3 15.4 -
11 0.1334 2.74 0.314 0.314 0.063 0.329 0.097 63807 125 51 51 2.4 11.3 -
12 0.1461 2.62 0.406 0.406 0.070 0.425 0.125 66241 98 51 52 1.9 8.7 -
13 0.1588 2.51 0.537 0.537 0.078 0.562 0.166 68272 76 53 53 1.4 6.5 -
14 0.1715 2.41 0.685 0.685 0.084 0.727 0.237 54170 61 53 54 1.1 4.4 -
15 0.1843 2.33 0.886 0.886 0.088 0.950 0.333 39781 48 55 56 0.9 3.1 -
16 0.1970 2.25 1.249 1.249 0.092 1.355 0.508 29754 35 57 59 0.6 2.1 -

## Slide 238: CCP4: aimless log
$TABLE: Correlations CC(1/2) within dataset, XDSdataset:
$GRAPHS: Anom & Imean CCs v resolution:0|0.216023x0|1:2,4,7:
: RMS correlation ratio :0|0.216023x0|2.20344:2,6:
$$
N 1/d^2 Dmid CCanom Nanom RCRanom CC1/2 NImean $$ $$
1 0.0064 12.55 0.659 499 2.203 1.000 669
2 0.0191 7.24 0.550 975 1.853 1.000 1155
3 0.0318 5.61 0.527 1295 1.798 1.000 1479
16 0.1970 2.25 0.037 2123 1.038 0.711 2275
17 0.2097 2.18 0.043 1682 1.044 0.460 1877

## Slide 239: XDS: CORRECT.LP or XSCALE.LP
SUBSET OF INTENSITY DATA WITH SIGNAL/NOISE >= -3.0 AS FUNCTION OF RESOLUTION
RESOLUTION NUMBER OF REFLECTIONS COMPLETENESS R-FACTOR R-FACTOR COMPARED I/SIGMA R-meas CC(1/2) Anomal SigAno Nano
LIMIT OBSERVED UNIQUE POSSIBLE OF DATA observed expected Corr
6.39 4103 2517 3135 80.3% 1.7% 1.8% 3018 33.77 2.3% 99.9* 21* 1.012 533
4.54 7339 4970 5544 89.6% 2.6% 2.6% 4585 22.56 3.6% 99.8* 9 0.914 796
3.72 9442 6724 7186 93.6% 2.8% 2.9% 5327 19.99 4.0% 99.7* 9 0.859 877
3.22 11077 7997 8486 94.2% 4.8% 4.9% 6094 12.27 6.8% 99.3* -1 0.784 913
2.88 12408 8851 9595 92.2% 10.0% 10.1% 7068 6.01 14.2% 97.8* -2 0.799 1012
2.63 13673 9561 10662 89.7% 20.8% 20.8% 8185 3.10 29.4% 88.8* -4 0.776 1274
2.44 14360 9852 11510 85.6% 34.5% 34.7% 8981 1.90 48.8% 75.9* 2 0.765 1525
2.28 9501 6495 12416 52.3% 61.8% 59.6% 5991 1.14 87.3% 53.5* -2 0.722 1031
2.15 4567 3307 13210 25.0% 120.5% 120.3% 2520 0.59 170.4% 21.9* 4 0.693 408
total 86470 60274 81744 73.7% 6.7% 6.7% 51769 8.97 9.5% 99.5* 2 0.804 8369

## Slide 240: XDS: CORRECT.LP or XSCALE.LP
******************************************************************************
CORRECTION PARAMETERS FOR THE STANDARD ERROR OF REFLECTION INTENSITIES
******************************************************************************
The variance v0(I) of the intensity I obtained from counting statistics is
replaced by v(I)=a*(v0(I)+b*I^2). The model parameters a, b are chosen to
minimize the discrepancies between v(I) and the variance estimated from
sample statistics of symmetry related reflections. This model implicates
an asymptotic limit ISa=1/SQRT(a*b) for the highest I/Sigma(I) that the
experimental setup can produce (Diederichs (2010) Acta Cryst D66, 733-740).
a b ISa
3.806E+00 1.080E-04 49.32

## Slide 241: Major Phasing techniques
Molecular Replacement
Multiple Isomorphous Replacement
Multiwavelength Anomalous Diffraction
Single-wavelength Anomalous Diffraction

## Slide 242: Molecular Replacement
?
correct structure and intensities
http://www.ysbl.york.ac.uk/~cowtan/fourier/coeff.html

## Slide 243: Molecular Replacement
use something similar as a starting model

## Slide 244: Model Building
current model is missing something

## Slide 245: Model Building
phases from model

## Slide 246: Model Building
missing bits show up in “difference map”

## Slide 247: Model Building
missing bits show up better in FO + (FO - FC) map