## Slide 1: Acknowledgements
UCSF LBNL SLAC
ALS 8.3.1 creator: Tom Alber
UC Multicampus Research Programs and Initiatives (MRPI)
UCSF Program for Breakthrough Biomedical Research (PBBR)
one-time NIH-DOE Inter-agency agreement (IAA)
GM117126 to Sauter (DIALS)
Integrated Diffraction Analysis Technologies (IDAT)
Plexxikon, Inc.
Synchrotron Radiation Structural Biology Resource (SLAC)
The Advanced Light Source is supported by the Director, Office of Science, Office of Basic Energy Sciences, Materials Sciences Division, of the US Department of Energy under contract No. DE-AC02-05CH11231 at Lawrence Berkeley National Laboratory.
Robert Stroud James Fraser
Nick Sauter John Tainer Aina Cohen Ana Gonzalez

## Slide 2: How low can you dose?
Stay below World Record
Look up dose rate
  http://bl831.als.lbl.gov/damage_rates.pdf
Know your limits
  10 MGy/Å reso, 5 = SeMet, 20 kGy?
R-factor Gap
  A perfect model would blow up
Resolution: optimum cutoff is 0 Å
http://bl831.als.lbl.gov/~jamesh/
powerpoint/WCPCW_lodose_2017.pptx

## Slide 3: What do I do?
You only have a few small crystals…
Should you:
  Collect 360° from each?
  Collect 10° from each at 36x exposure?
  Glue 36 xtals together, then collect 360° ?
  Glue together and do 12960° ?
  http://bl1231.als.lbl.gov/~jamesh/dose_slice/results.html

## Slide 4
Where:
IDL - average damage-limited intensity (photons/hkl) at a given resolution
105 - converting R from μm to m, re from m to Å, ρ from g/cm3 to kg/m3 and MGy to Gy
re - classical electron radius (2.818 x 10-15 m/electron)
h - Planck’s constant (6.626 x 10-34 J∙s)
c - speed of light (299792458 m/s)
fdecayed - fractional progress toward completely faded spots at end of data set
ρ - density of crystal (~1.2 g/cm3)
R - radius of the spherical crystal (μm)
λ - X-ray wavelength (Å)
fNH - the Nave & Hill (2005) dose capture fraction (1 for large crystals)
nASU - number of proteins in the asymmetric unit
Mr - molecular weight of the protein (Daltons or g/mol)
VM - Matthews’s coefficient (~2.4 Å3/Dalton)
H - Howells’s criterion (10 MGy/Å)
θ - Bragg angle
a2 - number-averaged squared structure factor per protein atom (electron2)
Ma - number-averaged atomic weight of a protein atom (~7.1 Daltons)
B - average (Wilson) temperature factor (Å2)
μ - attenuation coefficient of sphere material (m-1)
μen - mass energy-absorption coefficient of sphere material (m-1)
Self-calibrated damage limit
Holton & Frankel (2010) Acta D 66 393-408.
No flux
No symmetry
No exposure time

## Slide 5
The number of photons scattered
before crystal is dead
is independent
of data collection time
1 um3 = 105 photons (roomT)
1 um3 = 106 photons (synch)
1 um3 = 108 photons (XFEL)
Henderson, 1990; Gonzalez & Nave, 1994; Glaeser et al., 2000; Sliz et al., 2003; Leiros et al., 2006; Owen et al., 2006; Garman & McSweeney, 2006; Garman & Nave, 2009; Holton, 2009
(synch)

## Slide 6: Dose slicing
crystal’s useful life
N
photons
N
photons
N
photons
unacceptable
damage
unacceptable
read noise

## Slide 7: Dose slicing: is that a spot?

## Slide 8: Dose slicing: is that a spot?

## Slide 9: Dose slicing: is that a spot?

## Slide 10: Dose slicing: is that a spot?

## Slide 11: Dose slicing: is that a spot?

## Slide 12: Dose slicing: is that a spot?

## Slide 13
Resolution (Å)
CC vs right answer
“true” resolution limit

## Slide 14
Dose slice collection scenario |  |  | 
fine | coarse | glue | Glue & fine
3.17700 | 3.14057 | 3.17604 | 3.12086
“true” resolution vs strategy
301,640,334 photons/xtal

## Slide 15
processing procedure | resolution limit |  |  | 
 | fine | coarse | glue | glue&fine
XDS/XSCALE | 3.17700 | 3.14057 | 3.17604 | 3.12086
XDS/aimless | 3.16251 | 3.15922 | 3.16675 | 3.12162
XDS/noscale | 3.27289 | 3.15617 | 3.38929 | 3.12162
MOSFLM-defaults | x | x | x | x
MOSFLM-cheat | 3.19755 | 3.18166 | 3.20354 | 3.19755
HKL2000-defaults | x | x | x | x
HKL2000-expert | 3.21803 | 3.12646 | 3.11551 | 3.21803
HKL2000-cheat | 3.16119 | 3.10338 | 3.10338 | 3.16300
DIALS-defaults | x | x | 3.42125 | x
DIALS-expert | 3.10296 | 3.09547 | 3.07653 | 3.08465
d*Trek | ? | ? | 4.34076 | ?
EVAL15 | 3.14352 | 3.10383 | 3.09936 | 3.14105
EVAL15-sadabs | 3.13920 | 3.10797 | 3.10171 | 3.13700

## Slide 16
Holton (2009) J. Synchrotron Rad. 16 133-42
Radiation Damage World Records
MGy reaction reference
~45 global damage Owen et al. (2006)
10/Å global damage Howells et al. (2009)
5 Se-Met Holton (2007)
4 Hg-S Ramagopal et al. (2004)
4 R-C-COOH Garman et al. (2015)
3 S-S Murray et al. (2002)
1 Br-RNA Olieric et al. (2007)
~1? Cl-C ???
0.5 Mn in PS II Yano et al. (2005)
0.06 putidaredoxin Corbett et al. (2007)
0.02 Fe in myoglobin Denisov et al. (2007)

## Slide 17: what the is a MGy?
http://bl831.als.lbl.gov/
damage_rates.pdf
Holton J. M. (2009) J. Synchrotron Rad. 16 133-42

## Slide 18
How long will my crystal last?
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime
ALS 4.2.2 MAD 1e12 75x80 1.7e+08 124 kGy/s 4 m 16 s
ALS 5.0.1 mono 2e11 100 2.5e+07 13 kGy/s 39 m 2.6 m
ALS 5.0.2 MAD 1.5e12 100 1.5e+08 76.3 kGy/s 6.6 m 26 s
ALS 5.0.3 mono 3e11 100 3.8e+07 19.4 kGy/s 26 m 1.7 m
ALS 8.2.1 MAD 3.5e11 100 4.5e+07 22.7 kGy/s 22 m 88 s
ALS 8.2.2 MAD 3.5e11 100 4.5e+07 22.7 kGy/s 22 m 88 s
ALS 8.3.1 MAD 9e11 70 2.3e+08 119 kGy/s 4.2 m 17 s
ALS 12.3.1 MAD 2e11 65x90 3.4e+07 17.4 kGy/s 29 m 1.9 m
ALS 12.3.1 ML 4.0e13 65x90 6.8e+09 6.89 MGy/s 4.4 s 0.29 s
SSRL 1-5 MAD 1.7e10 200 4.2e+05 202 Gy/s 41 h 2.8 h
SSRL 7-1 mono 2.6e11 200 6.5e+06 3.09 kGy/s 2.7 h 11 m
SSRL 9-1 mono 3.9e10 200 9.8e+05 463 Gy/s 18 h 72 m
SSRL 9-2 MAD 4.8e11 200 1.2e+07 5.7 kGy/s 88 m 5.8 m
SSRL 11-1 MAD 3.9e11 200 9.8e+06 4.63 kGy/s 1.8 h 7.2 m
SSRL 11-3 mono 2.6e10 200 6.5e+05 302 Gy/s 28 h 1.8 h
SSRL 12-2 MAD 4e12 90x5 8.9e+09 5.01 MGy/s 6 s 0.4 s
SSRL 12-1 MAD 4e12 5x5 1.6e+11 90 MGy/s 0.35 s 22 ms
SSRL 12-1 ML 3e14 5x5 1.1e+13 6.4 GGy/s 5 ms 300 us
APS 24-ID-C MAD 1.3e13 20x60 1.1e+10 5.23 MGy/s 5.7 s 0.38 s
APS "typical" MAD 1.5e12 80 2.3e+08 119 kGy/s 4.2 m 17 s
synch line type flux beamsize flux density dose max xtal min site
ph/s μm ph/μm2/s rate lifetime lifetime

## Slide 20
Holton & Frankel (2010) Acta D 66 393-408.

## Slide 21: How low can you dose?
Stay below World Record
Look up dose rate
  http://bl831.als.lbl.gov/damage_rates.pdf
Know your limits
  10 MGy/Å reso, 5 = SeMet, 20 kGy?
R-factor Gap
  A perfect model would blow up
Resolution: optimum cutoff is 0 Å
http://bl831.als.lbl.gov/~jamesh/
powerpoint/WCPCW_lodose_2017.pptx

## Slide 22: Optimum resolution cutoff is:
Too optimistic: add nothing but noise
Too pessimistic: series-termination error
Happy medium?
Simulate:
  Random atoms, compute F2
  Add Gaussian noise, RMS = 1
  Truncate
  Subtract “right” map, RMS difference

## Slide 23
Resolution cutoff (Å)
Error in map (rms e-)
Optimal resolution cutoff

## Slide 24
Resolution cutoff (Å)
Correlation Coefficient
Optimal resolution cutoff

## Slide 25
Resolution cutoff (Å)
Correlation Coefficient
Optimal resolution cutoff

## Slide 26
Resolution cutoff (Å)
Error in map (rms e-)
Optimal resolution cutoff

## Slide 27
log( intensity )
Wilson Plot
2.2 1.6 1.3 1.1 1.0 0.9 0.85 0.8 0.75 0.7
resolution (Å)
8
2

## Slide 28: Optimum resolution cutoff is:
0.0 Å

## Slide 29: “R-factor Gap” for macromolecules
R1 < 2*Rsigma
Publication criterion for chemical crystallography:
R1 = Fo vs Fc for I/σ(I) > 3
Rsigma = <σ(I)>/<I>
There are no PDB entries that pass this test!
Holton et al. (2014) "The R-factor gap", FEBS J. 281, 4046-4060.

## Slide 30: What if we knew everything?
How would we store it?
    30,000 conformers will crash coot
Take an MD simulation of a crystal
Average electron density of cell
Build conventional model
  Look at “true” difference
Build noise-limited model
  Drop into real data

## Slide 31: MD simulation: 30 conformers from 24,000
Cerutti et al. (2010).J. Phys. Chem. B 114, 12811-12824.

## Slide 32: Electron density from 24,000 conformers

## Slide 33: 2Fsim-Fcalc and Fsim-Fcalc maps
1.0 Å data
Rcryst= 0.137
Rfree = 0.159
1 “sigma” 2Fsim-Fc
2.5 “sigma” Fsim-Fc

## Slide 34: 2Fsim-Fcalc and (Fsim Φsim) - (Fcalc Φcalc) maps
1 “sigma” 2Fsim-Fc
Fright – (2Fsim-Fc)
1.0 Å data
Rcryst= 0.137
Rfree = 0.159

## Slide 35: 30 conformers from 24,000

## Slide 36: How many conformers are there?
Rcryst = 0.0441
Rfree = 0.0516
vs Fsim
Answer: 2-14

## Slide 37: How many conformers are there?
Rcryst = 0.1546
Rfree = 0.1749
vs Fobs
1aho:
Rcryst = 0.1630
Rfree = n/d
Answer: 1-7

## Slide 38: How many conformers are there?
All difference
features
are in
the solvent!
real data

## Slide 39: Combined multi-conformer & explicit solvent
Rwork = 0.0309
Rfree = 0.0678
vs Fsim
Problem: diverges with more cycles

## Slide 40: How low can you dose?
Stay below World Record
Look up dose rate
  http://bl831.als.lbl.gov/damage_rates.pdf
Know your limits
  10 MGy/Å reso, 5 = SeMet, 20 kGy?
R-factor Gap
  A perfect model would blow up
Resolution: optimum cutoff is 0 Å
http://bl831.als.lbl.gov/~jamesh/
powerpoint/WCPCW_lodose_2017.pptx

## Slide 41: Fractional error
mult > (—)2
~3%
<ΔF/F>

## Slide 42: Can you count to 1,000,000 ?
= 0.1%
sqrt(1,000,000)
1,000,000
= 3%
sqrt(1,000)
1,000
> 1000 is a waste!
photon
spot
Theoretically:
In reality:
ISa ~ 33
Rmeas ≈ 0.1% ?
ISa = 1000
Rmeas = ≈ 3%

## Slide 43
Required signal-to-noise (I/σ)
Solve-able proteins (%)
Current
technology
Goal
Threshold of a revolution in phasing

## Slide 44
Source of error | realistic simulation | No SHSSS | Perfect detector
Photon counting | + | + | +
Shutter jitter | + | + | -
Beam flicker | + | + | -
Sample absorption | + | + | -
Radiation damage | + | + | -
Imperfect spindle | + | + | -
vignette | + | + | -
Corner correction | + | + | -
SHSSS | + | - | -
Rmeas (∞-10 Å) | 2.8% | 0.7% | 0.7%
I/σ asymptotic | 26.8 | 74.2 | 81.0
Threshold of a revolution in phasing
Holton et al (2014) "R-factor gap", FEBS Journal 281, 4046-4060.

## Slide 45
Pick-up tool mark
Bragg
glitch
oxygen
inclusions
“tree rings”
1% high
average
1% low
~3x105 photon/pixel
Pilatus: subtract smooth baseline

## Slide 46: nonBragg extracts background
Flux
Exposure
Density
Thickness
Gain, offset
spot remover

## Slide 47
FOM from “dm”
Correlation to final map
Phasing success vs Figure of Merit
Hunter et al. (2016)."Selenium anomalous phasing XFEL", Nature Comm. 7, 13388.
http://cxidb.org/id54-SfjMJjaBny/id-54.html http://cxidb.org/id55-BWuBDSUrBy/id-55.html
Adjusting:
Solvent content
Resolution
SDfac Sdadd
Cycles of dm
“mode”
“scheme”
NCS radius
NCS cycles
Phase blur

## Slide 48: Riso vs dose
Riso (%)
change in dose (MGy)
data taken from Banumathi, et al. (2004) Acta Cryst. D 60, 1085-1093.
Riso ≈ 0.7 %/MGy